## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 1: Forces Acting on a Moving Vehicle'

## Slide 2: Forces Acting on a Moving Vehicle
Session 1 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Automotive Vehicles. Over the next 20 sessions, we're going to build your understanding of how vehicles work from the ground up. And I mean that literally – we start with the ground.

## Slide 4: The Question That Drives Everything
Let me ask you something. When you press the accelerator in a car, what's actually happening? Most people say 'the engine speeds up.' That's not wrong, but it's incomplete. Today, I want to share with you a different way of thinking about vehicles – one that starts with a simple physics question: How much force does it take to move this car?

## Slide 5: Why This Matters (Personal Connection)
I remember when I first started studying automotive engineering, I was overwhelmed by all the systems – engines, transmissions, electronics. But my professor told me something that changed everything: 'Before you can understand how to generate power, you need to understand why we need it.' That's what we're doing today.

## Slide 6: Our Learning Journey Today
Here's our path today. We'll start with basic physics you already know – Newton's laws, force calculations. Then we'll apply them to real vehicles. By the end, you'll be able to calculate exactly how much force any vehicle needs in any situation. No black boxes, no magic – just physics and math.

## Slide 7: Real-World Scenario
Let me give you a challenge. This is a Honda Civic. Mass: 1,300 kg. It's driving on a level highway at 100 km/h. Question: What force is the engine fighting against right now?
By the end of today, you won't just guess – you'll calculate the exact answer. And more importantly, you'll understand where every Newton of that force comes from.

## Slide 8: The Three Resistance Forces
Here's what I'm going to teach you today. Every moving vehicle fights three forces:
Rolling Resistance — from the tires
Aerodynamic Drag — from pushing through air
Gradient Resistance — from climbing slopes
Understand these three, and you understand why vehicles need power.

## Slide 9: What is Rolling Resistance?
Imagine pushing a shopping cart. Even on flat ground, you need force to keep it moving. Why? The wheels resist motion. Same with car tires.
When a tire rolls, it deforms slightly – it's not perfectly rigid. This deformation eats energy. That's rolling resistance.

## Slide 10: The Formula (Simplified)
The formula is beautifully simple:
Frolling = Crr × W
Where:
F_rolling = rolling resistance force (N)
C_rr = coefficient of rolling resistance (dimensionless, ~0.01 for cars)
W = vehicle weight (N) = mg
That's it. Weight times a small coefficient.

## Slide 11: Example Calculation (Live)
Let me show you with our Honda Civic:
Mass (m) = 1,300 kg
Weight (W) = mg = 1,300 × 9.81 = 12,753 N
C_rr = 0.012 (typical for car tires on asphalt)
F_rolling = 0.012 × 12,753 = 153 N
That's the force just to overcome tire resistance. Write that number down – we'll use it later.

## Slide 12: Factors Affecting Rolling Resistance
Quick note on what affects C_rr:
Tire pressure (lower = higher resistance)
Tire material (harder rubber = lower resistance)
Road surface (smooth asphalt vs rough gravel)
Temperature
For most calculations, we use 0.01 to 0.015 for cars.

## Slide 13: Practice Problem
Your turn. Calculate rolling resistance for:
Truck: 3,500 kg, C_rr = 0.008
SUV: 2,200 kg, C_rr = 0.012
Take 2 minutes. I'll show the solution after.
[Include solution on next slide or as animation]

## Slide 14
#### Part 2: Aerodynamic Drag (Slides 14-18, ~20 minutes)

## Slide 15: Air Resistance - The Hidden Force
Rolling resistance is constant – same force at 10 km/h or 100 km/h. But there's another resistance that grows dramatically with speed. You've felt it if you've ever stuck your hand out of a car window at highway speeds.
Air resistance. And it follows a fascinating relationship with velocity.

## Slide 16: The Drag Equation
This equation looks more complex, but let me break it down for you:
Fdrag = ½ ρ Cd A v² — F_drag = aerodynamic drag force (N)
ρ = air density (1.225 kg/m³ at sea level)
C_d = drag coefficient (0.25-0.35 for modern cars)
A = frontal area (m²)
v = velocity (m/s)
Notice that v² at the end? That's the key. Double your speed, quadruple the drag force.

## Slide 17: Understanding Each Term
Let me explain each term:
ρ (rho) - Air Density: 1.225 kg/m³ at sea level, 20°C. Lower at high altitudes.
C_d - Drag Coefficient: How 'slippery' the car is. Sports cars: 0.25-0.30. SUVs: 0.35-0.40. It's all about shape.
A - Frontal Area: How much air the car pushes. Measure the face of the car. Sedans: ~2-2.5 m². SUVs: ~3 m².
v - Velocity: Speed in m/s. Remember: 100 km/h = 27.8 m/s.

## Slide 18: Example Calculation (The Power of v²)
Back to our Honda Civic:
C_d = 0.30 (pretty aerodynamic)
A = 2.2 m²
ρ = 1.225 kg/m³
v = 100 km/h = 27.8 m/s
F_drag = 0.5 × 1.225 × 0.30 × 2.2 × (27.8)²
F_drag = 0.5 × 1.225 × 0.30 × 2.2 × 772
F_drag = 312 N at 100 km/h
But watch what happens at 50 km/h (13.9 m/s):
F_drag = 0.5 × 1.225 × 0.30 × 2.2 × (13.9)²
F_drag = 78 N at 50 km/h
Half the speed = quarter the drag. This is why highway fuel economy is so different from city driving.

## Slide 19: Practice Problem + Discussion
Calculate drag force for the same car at:
60 km/h
120 km/h
Then think: At what speed does aerodynamic drag equal rolling resistance (153 N)?
This is practical engineering thinking.

## Slide 20
#### Part 3: Gradient Resistance (Slides 19-22, ~15 minutes)

## Slide 21: Climbing Hills - Gravity Fights Back
Flat roads are the easy case. But what about climbing a hill? Now we're fighting gravity directly.
This is where your trigonometry becomes useful.

## Slide 22: The Gradient Force Equation
When a vehicle climbs a slope at angle θ:
F_gradient = mg sin(θ)
Or, if you know the grade percentage:
F_gradient = mg × (grade/100)
For small angles (which most roads are), grade percentage is approximately the angle in degrees × 1.75.

## Slide 23: Example - Climbing a 5% Grade
Our Honda Civic climbing a 5% grade (about 3 degrees):
Method 1 (using percentage):
F_gradient = 1,300 × 9.81 × (5/100)
F_gradient = 627 N
Method 2 (using angle):
θ = 2.86° (from arctan(0.05))
F_gradient = 12,753 × sin(2.86°)
F_gradient = 636 N (slightly more accurate)
That's more than rolling resistance and drag combined at moderate speeds!

## Slide 24: Total Resistance Force
Here's the moment it all comes together. The total resistance force a vehicle faces is:
Ftotal = Frolling + Fdrag + Fgradient
Three independent forces, one total force the engine must overcome.
Let me show you a complete scenario.

## Slide 25: Complete Example - The Full Picture
Honda Civic, 100 km/h, climbing 3% grade:
F_rolling = 0.012 × 12,753 = 153 N
F_drag = 0.5 × 1.225 × 0.30 × 2.2 × (27.8)² = 312 N
F_gradient = 12,753 × (3/100) = 383 N
F_total = 153 + 312 + 383 = 848 N
That's the answer. 848 Newtons of force, continuously, just to maintain 100 km/h up a 3% grade.
This is the force the powertrain must provide through the tires. Everything else in the car – the engine, transmission, differential – exists to deliver this force to the road.

## Slide 26: Real-World Application Exercise
Let's apply what we've learned. Calculate total resistance for:
City driving: 50 km/h, flat road
Highway cruising: 120 km/h, flat road
Mountain driving: 80 km/h, 8% uphill grade
Use the same Honda Civic parameters. You have all the tools now.
[Include worked solutions]

## Slide 27: Key Formulas Summary
Here are your takeaway formulas:
| Force Type | Formula | Typical Values |
|------------|---------|----------------|
| Rolling | Frr = Crr × mg | C_rr: 0.01-0.015 |
| Drag | Fd = ½ρCdAv² | C_d: 0.25-0.40 |
| Gradient | F_g = mg sin(θ) | θ: 0-15° typical |
| Total | Ft = Frr + Fd + Fg | Sum of all |
Master these, and you understand vehicle motion fundamentals.

## Slide 28: Performance Metrics Preview
One more thing before we finish. You can now answer questions like:
Why do electric cars have excellent city range but lower highway range?
Why does fuel economy drop dramatically above 100 km/h?
Why do trucks struggle on hills?
All of these are explained by the forces we calculated today. The math tells the story.

## Slide 29: Assignment & Next Session Preview
Your assignment:
Choose any vehicle (give me make, model, mass). Calculate total resistance at three scenarios of your choice. Show all work.
Next session: We move to the tires – the only part of the vehicle touching the road. How do they generate the forces we calculated today? How much force can they actually provide? What happens at the limit?
This is where things get really interesting.

## Slide 30: Q&A Prompts
We have 30 minutes for questions. Some things to think about:
How would these forces change at high altitudes?
What about electric vehicles vs IC engines?
How do engineers optimize for different scenarios?
What questions do you have?

## Slide 31: 📊 PPT DESIGN GUIDANCE
Technical Diagrams:
Professional engineering aesthetic: Clean layouts, technical diagrams
Color scheme: Blues and grays (professional), highlight key equations in orange
Consistent: Same template throughout
Slide 2 (The Question) - Hook students immediately
Slide 10, 15, 20 (Formulas) - Make these crystal clear
Slide 24 (Complete Example) - The "aha" moment
Slide 27 (Summary) - Students will photograph this
Minimal and professional
Use build animations for multi-step calculations
Highlight key terms as you mention them
Reveal solutions to practice problems after pause
Use clean, labeled free-body diagrams
Show force vectors clearly
Include units on all calculations

## Slide 32: 🎯 INSTRUCTOR NOTES
Engagement Points:
This session uses Teacher-Led Narrative to:
Build confidence: Start with "you already know this
Demystify complexity: Break down into three simple forces
Provide tools: Every formula is immediately applied
Connect to experience: Highway driving, hill climbing are relatable
Unit conversion (km/h to m/s): Emphasize early, practice often
When to use sin vs percentage: Show both methods
Understanding v²: Use the comparison table (Slide 17)
If running short: Skip one practice problem
If running long: Move detailed gradient discussion to Q&A
Core content: Slides 1-25 (must cover)
Slide 6: Pause for guesses before revealing challenge
Slide 13, 18: Student calculation time (active learning)
Slide 24: "Let's calculate together" - work through live
Slide 26: Can be homework if time is tight

## Slide 33: ✅ Session Success Criteria
Students leave able to:
✓ Calculate rolling resistance for any vehicle
✓ Calculate aerodynamic drag at any speed
✓ Calculate gradient force on any slope
✓ Determine total resistance for combined scenarios
✓ Understand why performance varies with speed and terrain
Most importantly: Students feel confident that automotive engineering is accessible physics, not black magic.

## Slide 34
End of Framework
Next: Generate framework for Session 2 (Tires & Friction Fundamentals)