## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 2: Tires & Friction Fundamentals'

## Slide 2: Tires & Friction Fundamentals
Session 2 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome back. Last session, we calculated the forces a vehicle must overcome. Today, we answer the next critical question: How do tires actually provide those forces?

## Slide 4: Recap & The Missing Link
Last time, we calculated that our Honda Civic at 100 km/h needs 848 N of force to overcome resistance. But here's what we didn't answer: Where does that force come from?
The engine generates torque, the transmission multiplies it, but ultimately, all that power must become force at one place: the contact patch between tire and road.
This tiny area – about the size of your hand – is where physics meets the road. Literally.

## Slide 5: The Four Contact Patches
Think about this. Right now, your entire car – all 1,300 kg – is supported by four patches of rubber, each roughly 15cm × 20cm. That's it. Four areas smaller than this textbook.
Through these patches:
All acceleration force
All braking force
All cornering force
All weight transfer
Everything depends on tire-road friction. Today, we master this.

## Slide 6: The Maximum Force Limit
Here's a question that will drive everything today: Why can't tires provide unlimited force?
If I asked you to accelerate at 5 m/s², you might do it easily. But if I asked for 15 m/s², your tires would just spin. Why? What's the limit?
The answer is in the physics of friction. Let me show you.

## Slide 7: What's Inside a Tire?
Before we talk friction, let's understand what we're working with. A modern tire is engineering marvel. Let me show you what's inside.
[Point to diagram layers]:
Tread: Rubber that contacts road
Belt: Steel or fabric reinforcement
Carcass: Fabric plies that give structure
Bead: Steel wire that seals to rim
Two main types: Radial (modern standard) vs Bias-ply (older, some specialty uses).

## Slide 8: Radial vs Bias-Ply
Radial tires (what you drive on):
Cords run radially (perpendicular to direction of travel)
Better heat dissipation
Longer life, better fuel economy
Less rolling resistance
Bias-ply tires (rare today):
Cords run at angles
Stiffer sidewalls
Still used in some agricultural and aircraft applications
For this course, assume radial unless stated otherwise.

## Slide 9: Tire Nomenclature - Reading the Sidewall
When you see 205/55 R16 91V:
205: Width in mm (205 mm)
55: Aspect ratio (height is 55% of width)
R: Radial construction
16: Wheel diameter in inches
91: Load index (615 kg capacity)
V: Speed rating (up to 240 km/h)
Engineers use this to select appropriate tires for vehicle loads and speeds.

## Slide 10: Quick Exercise
Decode this: 245/40 R18 97Y
[Pause for students]
245 mm wide
Height = 40% of 245 = 98 mm
Radial, 18-inch wheel
730 kg load capacity per tire
Speed rated to 300 km/h (performance tire)
Moving on to forces.

## Slide 11
#### Part 2: Normal Force & Load Distribution (Slides 11-14, ~12 minutes)

## Slide 12: Normal Force - The Foundation of Friction
Here's a critical concept from physics: The maximum friction force depends on the normal force.
Normal force (N) is the force pressing the tire into the road. For a stationary car on flat ground:
N = Weight on that tire
But it's not always equal on all four tires. Load distribution matters.

## Slide 13: Load Distribution Basics
Most cars are front-heavy (engine in front). Typical distribution:
Front axle: 60% of weight
Rear axle: 40% of weight
For our 1,300 kg Honda Civic:
Total weight (W) = 1,300 × 9.81 = 12,753 N
Front axle: 0.60 × 12,753 = 7,652 N (3,826 N per tire)
Rear axle: 0.40 × 12,753 = 5,101 N (2,551 N per tire)
This asymmetry affects braking, acceleration, and handling. We'll see why in later sessions.

## Slide 14: Calculation Example
Let's calculate normal force for each tire:
Front tires (assuming equal left/right):
N_front = 7,652 N / 2 = 3,826 N per tire
Rear tires:
N_rear = 5,101 N / 2 = 2,551 N per tire
Remember these numbers. They determine maximum friction force at each tire.

## Slide 15: Load Transfer Teaser
Quick note: This is for static conditions. When the car accelerates, brakes, or turns, weight transfers between tires. We'll dive deep into that in Session 9 (Vehicle Dynamics).
For today, assume static loading. But keep in mind: real-world normal forces change dynamically.

## Slide 16
#### Part 3: Friction Fundamentals (Slides 15-18, ~15 minutes)

## Slide 17: The Friction Equation
Here it is. The equation that governs every force a tire can generate:
F_friction = μ × N
Where:
F_friction = maximum friction force (N)
μ (mu) = coefficient of friction (dimensionless)
N = normal force (N)
Simple, powerful, fundamental. Let me break down each part.

## Slide 18: Coefficient of Friction (μ)
The coefficient of friction depends on two surfaces in contact:
Typical Values: — Dry asphalt + rubber: μ ≈ 0.8 - 1.0 — Wet asphalt + rubber: μ ≈ 0.5 - 0.7 — Ice + rubber: μ ≈ 0.1 - 0.2 — Racing slicks on track: μ ≈ 1.2 - 1.5 (hot)
Higher μ = more grip = more force available.
Note: These are simplified. Reality is complex (temperature, slip angle, etc.). But for our calculations, these work.

## Slide 19: Maximum Tire Force Calculation
Let's calculate maximum force from one front tire on dry asphalt:
Given:
N_front = 3,826 N
μ_dry = 0.9 (good tire, dry road)
F_max = μ × N
F_max = 0.9 × 3,826
F_max = 3,443 N
This is the absolute maximum force this tire can provide in any direction – braking, accelerating, or cornering.
Exceed this, and the tire breaks traction (slides).

## Slide 20: All Four Tires Combined
Maximum total force from all four tires:
Front: 2 × 3,443 N = 6,886 N
Rear (using N_rear = 2,551 N): 2 × (0.9 × 2,551) = 4,592 N
Total available friction force = 11,478 N
Compare this to Session 1: At 100 km/h on flat road, we only needed ~465 N to maintain speed (rolling + drag). We have massive margin.
But what about acceleration? Braking? Cornering at the limit? That's where it gets interesting.

## Slide 21
#### Part 4: Tire Slip & Force Generation (Slides 19-20, ~6 minutes)

## Slide 22: Slip - The Surprising Truth
Here's something that surprises most people: Tires must slip slightly to generate force.
[Show graph of friction force vs slip %]
0% slip = no force (tire rolling freely)
5-15% slip = maximum force (optimal)
100% slip = wheel locked or spinning (lower force, no control)
This is why:
ABS prevents wheel lock (keeps slip in optimal range)
Traction control prevents wheelspin
Skilled drivers 'feel' the limit
We'll use this in future sessions.

## Slide 23: Longitudinal vs Lateral Slip
Two types of slip:
Longitudinal slip: Forward/backward (acceleration/braking)
Wheel rotating faster or slower than vehicle speed
Lateral slip (slip angle): Sideways (cornering)
Direction tire points vs direction it travels
Both generate force. Both can't be maximized simultaneously. That leads us to the friction circle.

## Slide 24
#### Part 5: The Friction Circle (Slides 21-22, ~5 minutes)

## Slide 25: The Friction Circle Concept
This is one of the most important concepts in vehicle dynamics. Let me show you why.
[Show friction circle]:
Radius = maximum friction force (μN)
X-axis = longitudinal force (braking/accelerating)
Y-axis = lateral force (cornering)
Rule: The resultant force vector must stay inside the circle.
What does this mean?

## Slide 26: Complete Example - Emergency Braking While Turning
Let's apply everything. Emergency scenario:
Situation: Front tire, dry road, turning + braking simultaneously
N = 3,826 N (we calculated this)
μ = 0.9
F_max = 3,443 N (circle radius)
Currently using 2,000 N for cornering (lateral)
Question: How much braking force can you add without losing grip?
Solution:
Using Pythagorean theorem (forces are perpendicular):
Flateral² + Fbraking² ≤ F_max²
(2,000)² + F_braking² ≤ (3,443)²
F_braking² ≤ 11,854,249 - 4,000,000
F_braking ≤ 2,801 N
Answer: Maximum 2,801 N of braking force available. Beyond that, tire slides.

## Slide 27: Summary - The Tire Force Chain
Here's the complete picture:
Weight (mg) →
Normal Force (N = portion of weight) →
Friction (F_max = μN) →
Available Force (can be longitudinal, lateral, or combined)
This chain determines every performance limit:
How fast you can accelerate
How quickly you can stop
How fast you can corner
Master this, and you understand vehicle limits.

## Slide 28: Connection to Session 3
We now know:
Session 1: Forces the vehicle must overcome
Session 2 (today): Forces the tires can provide
Next session: Converting force to torque and power. We'll answer: How much engine power do we actually need?
That's when everything clicks together.

## Slide 29: Practice Problems
Assignment:
Calculate maximum braking force for all four tires on:
Dry asphalt (μ = 0.9)
Wet asphalt (μ = 0.6)
Compare to total vehicle weight
Using friction circle, if a tire is using 60% of maximum friction for cornering, what percentage is available for braking?
Why do performance cars have wider tires? (Hint: Think about contact patch and normal force distribution)
Show all work. Due next session.

## Slide 30: Q&A Prompts
Questions to ponder:
How do tire warmers help race cars?
Why are winter tires different from summer tires?
What's the physics behind drifting?
How does ABS actually work at the friction level?
30 minutes for your questions.

## Slide 31: 📊 PPT DESIGN GUIDANCE
Include Real Images:
Tire cross-sections: Use clean technical diagrams
Friction circle: Make it prominent and clear (Slide 21-22)
Force vectors: Color-code (green = within limit, red = exceeds)
Slide 3 (Contact patches) - Visual impact
Slide 15 (Friction equation) - Core formula
Slide 21-22 (Friction circle) - Most important concept
Slide 25 (Summary chain) - Complete understanding
Slide 21: Animate friction circle with example vectors
Slide 23: Step-by-step calculation reveal
Force diagrams: Build elements as you explain them
Tire tread patterns (Slide 7)
Actual tire sidewall (Slide 9)
Contact patch under load (Slide 3)
Race car vs regular tire comparison

## Slide 32: 🎯 INSTRUCTOR NOTES
Engagement Points:
Build on Session 1: Explicit connections throughout
Hands-on concept: Friction is tangible, relatable
Friction circle: Spend extra time here - it's crucial for understanding all dynamics
Safety message: Implicit throughout (wet roads, worn tires)
μ vs N: Emphasize μ is property, N is force
Friction circle: Practice with multiple examples
Slip concept: Counterintuitive that slip is needed
Friction circle (Slides 21-22): Don't rush - critical concept
Can skip Slide 10 exercise if running short
Slide 19 (slip) can be brief with promise to revisit in dynamics module
Slide 5: Ask for examples of losing traction
Slide 23: Work through together on board
Slide 27: Can start in class

## Slide 33: ✅ Session Success Criteria
Students leave able to:
✓ Read tire specifications
✓ Calculate normal forces on tires
✓ Apply friction equation (F = μN)
✓ Understand friction circle for combined forces
✓ Identify factors affecting tire grip
Critical outcome: Students understand that tires are the performance bottleneck — everything else (engine, brakes, suspension) is limited by tire-road friction.

## Slide 34
End of Framework
Next: Session 3 (From Forces to Power Requirements)