## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 3: From Forces to Power Requirements'

## Slide 2: From Forces to Power Requirements
Session 3 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 3. Today is special. Today, everything we've learned comes together, and you'll understand exactly how engineers size powertrains.

## Slide 4: The Story So Far
Let me tell you where we've been:
Session 1: We calculated the forces resisting vehicle motion
Rolling resistance
Aerodynamic drag
Gradient resistance
You can now tell me exactly how much force any vehicle needs in any scenario.
Session 2: We learned how tires generate force
F = μN (the friction equation)
Friction circle
You understand the maximum force tires can provide.
But we left a critical question unanswered...

## Slide 5: Real-World Design Problem
Here's a real engineering challenge. You're designing a new SUV:
Mass: 2,000 kg
Top speed target: 180 km/h
0-100 km/h target: 8 seconds
Must climb 15% grade at 60 km/h
Question: How much power does the engine need?
Today, I'm going to show you how to calculate the exact answer. No guessing, no rules of thumb - just physics and math.

## Slide 6: Understanding Torque
First, let's be clear about what torque is. You know force (F, in Newtons). Torque (τ, tau) is force applied at a distance from rotation point.
Torque = Force × Distance
Or more specifically for wheels:
τ = F × r
Where:
τ = torque (N⋅m)
F = force at tire contact patch (N)
r = wheel radius (m)
Let me show you why this matters.

## Slide 7: The Wheel as a Lever
Think of the wheel as a lever. The axle applies torque at the center. This creates force at the circumference (where tire touches road).
[Show diagram]:
Torque at axle (τ)
Radius (r)
Force at contact patch (F)
Relationship: F = τ/r
Or rearranged: τ = F × r
Bigger wheel (larger r) needs more torque for same force. That's why off-road trucks with huge tires need more torque.

## Slide 8: Example - Calculating Required Wheel Torque
Back to our Honda Civic from Session 1. Remember:
At 100 km/h on flat road: F_total = 465 N (rolling + drag)
Wheel radius: r = 0.32 m (typical for 16" wheel + tire)
Required torque at ONE wheel (4-wheel drive):
τ = F × r = (465/4) × 0.32 = 37.2 N⋅m per wheel
For rear-wheel drive (power to 2 wheels):
τ = (465/2) × 0.32 = 74.4 N⋅m per rear wheel
This is the wheel torque needed to maintain 100 km/h.

## Slide 9: Practice Calculation
Your turn. Calculate wheel torque for:
Vehicle mass: 1,500 kg
Climbing 5% grade at constant 80 km/h
4-wheel drive
Wheel radius: 0.35 m
Assume: Frolling = 180 N, Fdrag = 200 N, F_gradient = 736 N
[Pause for calculation]
Solution:
F_total = 180 + 200 + 736 = 1,116 N
τ per wheel = (1,116/4) × 0.35 = 97.7 N⋅m per wheel
Good. Now let's connect this to engine torque.

## Slide 10: Transmission Multiplies Torque
Here's the key: Engine doesn't directly drive wheels. Transmission sits in between and multiplies torque.
Simple relationship:
τwheel = τengine × G_total
Where G_total = gear ratio × final drive ratio
Example: If G_total = 10:
Engine torque = 200 N⋅m
Wheel torque = 200 × 10 = 2,000 N⋅m
We'll cover transmissions in detail in Sessions 7-8. For now, know that we can multiply engine torque through gearing.
Implication: Smaller engines can move heavy vehicles if transmission ratios are right.

## Slide 11
#### Part 2: Torque to Power Conversion (Slides 11-16, ~20 minutes)

## Slide 12: What is Power?
Torque tells us force capability at a wheel. But torque doesn't include speed. That's where power comes in.
Power = How fast you can do work
In rotational systems:
P = τ × ω
Where:
P = power (Watts)
τ = torque (N⋅m)
ω (omega) = angular velocity (rad/s)
Or, if you have RPM instead:
P = (τ × N) / 9,549
Where N = rotational speed in RPM
Let me show you why this matters.

## Slide 13: Understanding the Power Equation
Look at this graph. If engine maintains 200 N⋅m of torque:
At 1,000 RPM: P = (200 × 1,000) / 9,549 = 20.9 kW — At 3,000 RPM: P = (200 × 3,000) / 9,549 = 62.8 kW — At 5,000 RPM: P = (200 × 5,000) / 9,549 = 104.7 kW
Same torque, different power!
This is why:
High RPM = high power (sports cars)
High torque at low RPM = good for acceleration (diesel engines, electric motors)
Power and torque are related but different.

## Slide 14: Converting Linear to Rotational Terms
We need to connect linear motion (vehicle speed) to rotational motion (wheel speed).
Linear velocity to angular velocity:
ω = v / r
Where:
v = linear velocity (m/s)
r = wheel radius (m)
ω = angular velocity (rad/s)
Example: 100 km/h (27.8 m/s) with 0.32 m radius wheel:
ω = 27.8 / 0.32 = 86.9 rad/s = 830 RPM (at the wheel)
If transmission ratio is 5:1, engine spins at 4,150 RPM.

## Slide 15: Power Requirement Calculation
Let's calculate power needed for our Honda Civic at 100 km/h:
Given:
F_total = 465 N (from Session 1)
v = 27.8 m/s (100 km/h)
Method 1 - Direct:
P = F × v
P = 465 × 27.8 = 12,927 W = 12.9 kW
Method 2 - Through torque:
τ_wheel = 465 × 0.32 = 148.8 N⋅m (for RWD)
ω_wheel = 27.8 / 0.32 = 86.9 rad/s
P = τ × ω = 148.8 × 86.9 = 12,933 W ≈ 12.9 kW
Both methods give the same answer (as they must!).
This is the power just to maintain 100 km/h. To accelerate, we need more.

## Slide 16: Accounting for Losses
Real-world complication: Not all engine power reaches the wheels.
Drivetrain losses:
Transmission friction: ~5-15%
Differential friction: ~2-5%
Total losses: ~15-20% for manual, ~20-25% for automatic
Efficiency factor (η):
Pengine = Pwheel / η
For our Civic (manual transmission, η = 0.85):
P_engine = 12.9 kW / 0.85 = 15.2 kW
So we need ~15 kW of engine power just to cruise at 100 km/h on flat road.

## Slide 17: Why Cars Have Much More Power
If we only need 15 kW to cruise, why do cars have 80-150 kW engines?
Because we also need power for:
Acceleration (much higher forces)
Hill climbing (gradient resistance)
Passing maneuvers (quick acceleration at highway speeds)
Air conditioning (can use 2-5 kW)
Reserve (don't want to run engine at 100% continuously)
Let me show you acceleration calculations.

## Slide 18
#### Part 3: Performance Calculations (Slides 17-24, ~20 minutes)

## Slide 19: Acceleration Performance
During acceleration, we need force for:
Overcoming resistance (rolling + drag)
Accelerating the mass (F = ma)
Total force needed:
Ftotal = Fresistance + ma
Where:
m = vehicle mass (kg)
a = desired acceleration (m/s²)
Higher acceleration = more force = more torque = more power.

## Slide 20: Example - 0-100 km/h Calculation
Let's calculate 0-100 km/h time for Honda Civic (simplified):
Assumptions:
Mass: 1,300 kg
Available power: 80 kW
Ignore changing resistance (simplification)
Assume average force during acceleration
Step 1: Convert speed
v_final = 100 km/h = 27.8 m/s
Step 2: Calculate average power during acceleration
Assuming average speed = 50 km/h = 13.9 m/s
Favailable = P / vavg = 80,000 / 13.9 = 5,755 N
Step 3: Account for resistance (estimate)
Fresistanceavg = 250 N
F_net = 5,755 - 250 = 5,505 N
Step 4: Calculate acceleration
a = F/m = 5,505 / 1,300 = 4.23 m/s²
Step 5: Calculate time
t = v / a = 27.8 / 4.23 = 6.6 seconds
Real-world: ~8-9 seconds (our simplifications were optimistic). But this shows the method!

## Slide 21: Maximum Gradeability
Another performance metric: Gradeability — steepest hill the vehicle can climb.
At the limit:
Favailable = Frolling + F_gradient (ignore drag at low speed)
For maximum grade:
Fgradient = Favailable - F_rolling
mg sin(θmax) = (P/v) - Crr × mg
Example (Civic at 60 km/h = 16.7 m/s):
F_available = 80,000 / 16.7 = 4,790 N
F_rolling = 0.012 × 12,753 = 153 N
F_gradient = 4,790 - 153 = 4,637 N
sin(θ_max) = 4,637 / 12,753 = 0.364
θ_max = 21.3 degrees = 39% grade
That's steep! Real-world lower due to other factors, but shows potential.

## Slide 22: Maximum Speed Calculation
Top speed occurs when all available power is consumed by resistance:
Pavailable = Ftotal × v_max
Where Ftotal = Frolling + F_drag (ignore gradient on flat road)
Problem: F_drag depends on v² which we're solving for!
Solution: Iterative or algebraic solving.
For our Civic with 80 kW power (simplified):
[Show iterative approach or use quadratic solution]
Result: v_max ≈ 185 km/h
(Real Honda Civic: ~195 km/h - our assumptions were conservative)

## Slide 23: Power-to-Weight Ratio
A useful metric: Power-to-Weight Ratio (kW/kg or hp/ton)
Honda Civic: 80 kW / 1,300 kg = 0.062 kW/kg = 62 W/kg
Comparison:
Economy car: 40-60 W/kg
Sports car: 100-150 W/kg
Supercar: 200-300 W/kg
Formula 1: 800+ W/kg
Higher ratio = better acceleration, higher top speed.
Quick estimate: For every 10 W/kg increase, 0-100 km/h improves by ~0.5-1 second.

## Slide 24: Electric vs IC Engine Power Delivery
Quick note on electric motors vs IC engines:
IC Engine:
Torque peaks at specific RPM
Must use gears to match torque to speed
Electric Motor:
Maximum torque from 0 RPM
Constant power across wide speed range
Why EVs accelerate so well
Both ultimately limited by:
Tire friction (Session 2)
Available power
We'll revisit in Session 8.

## Slide 25: Practice Problem - Design Challenge
Design challenge: Delivery van specification
Mass (loaded): 2,500 kg
Required top speed: 120 km/h
Required 0-100 km/h: <15 seconds
Must climb 12% grade at 40 km/h
Task: Calculate minimum power requirement.
Consider:
Resistance forces at top speed
Acceleration needs
Hill climbing needs
Take the maximum of these
[Work through together or assign as homework]

## Slide 26: Force → Torque → Power Chain
Let me show you the complete chain we've built over three sessions:
Session 1: FORCES
Ftotal = Frolling + Fdrag + Fgradient
Session 2: FRICTION LIMIT
F_max = μ × N (tire limit)
Session 3 (Today): TORQUE & POWER
τ = F × r (force to torque)
P = τ × ω = F × v (power requirement)
From this, we can calculate:
Required engine power for any performance target
Vehicle acceleration, top speed, gradeability
Transmission ratios needed
You now have the complete physics of vehicle motion and performance.

## Slide 27: Summary of Key Equations
Your reference card:
Force to Torque:
τ = F × r
Torque to Power:
P = τ × ω (rad/s)
P = (τ × N) / 9,549 (RPM)
P = F × v (linear)
Performance Metrics:
Acceleration: a = (P/v - F_resistance) / m
Top speed: Solve P = Ftotal × vmax
Gradeability: sin(θmax) = (P/v - Frolling) / mg
Power-to-Weight:
P/m (kW/kg or W/kg)
These equations solve most vehicle performance questions.

## Slide 28: Foundation Module Complete
Congratulations. You've completed the foundation module.
Session 1: You learned to calculate resistance forces
Session 2: You learned tire force generation limits
Session 3: You learned power requirements
You can now:
Calculate total resistance for any driving scenario
Determine maximum forces tires can provide
Specify power requirements for any vehicle
This is the physics foundation for everything else in automotive engineering.
Starting next session, we'll explore how vehicles actually generate and deliver this power. But you already understand why they need it.

## Slide 29: Comprehensive Assignment
Major Assignment (combines all three sessions):
Choose a real vehicle (provide specifications). Calculate:
Total resistance at 60, 100, and 140 km/h on flat road
Maximum friction force available (all tires, dry road)
Power required to maintain each speed
Predicted 0-100 km/h time
Maximum gradeability at 60 km/h
Theoretical top speed
Compare your calculations to published specifications. Discuss differences.
Due: Beginning of Session 5 (you have one session break).
This shows you can apply everything we've learned.

## Slide 30: Q&A and Looking Ahead
30 minutes for questions. Also, preview of what's coming:
Module 2 (Sessions 4-8): Powertrain
How do engines generate torque?
How do we keep them cool and lubricated?
How do transmissions multiply torque?
Module 3 (Sessions 9-12): Chassis Dynamics
Vehicle dynamics in detail
Braking systems
Steering and suspension
But for today, let's discuss what we covered. What questions do you have?

## Slide 31: 📊 PPT DESIGN GUIDANCE
Include:
Equation-heavy slides: Use large, clear fonts
Calculation slides: Step-by-step reveal with build animations
Graphs: Power vs speed, torque vs speed (reference for comparisons)
Slide 3 (Missing link) - Sets up the session
Slide 14 (Power calculation) - Core method
Slide 25 (Complete chain) - Integration of all three sessions
Slide 27 (Equation summary) - Students will photograph this
Slide 25: Build the complete chain step-by-step
Calculation slides: Reveal answers after pause for student work
Slide 26: Animate different vehicle examples
Actual vehicle specs: Use real examples (Honda Civic, Ford F-150, etc.)
Comparison tables: Power-to-weight ratios across vehicle classes
Performance graphs: Show how power affects performance

## Slide 32: 🎯 INSTRUCTOR NOTES
Critical Success Factor:
Integration focus: Constantly reference Sessions 1 & 2
Practical emphasis: Every equation applied immediately to real examples
Building confidence: "You can now calculate what engineers calculate
Transition moment: End of foundation, beginning of systems
Unit conversions: km/h ↔ m/s, kW ↔ W - practice extensively
Torque vs Power: Emphasize they're related but different
Simplified vs real calculations: Acknowledge approximations
Slides 17-24 (Performance): This is the meat - don't rush
Can condense Slide 22 (EV vs IC) if time is tight
Ensure time for Slide 25 (integration) - it's the payoff
Slide 9, 23: Student calculation opportunities
Slide 26: Discuss real vehicles they know
Slide 29: Can start assignment discussion in class
Students must leave feeling they've achieved mastery. This is the end of foundation - they should feel confident about their ability to apply physics and math to automotive problems.

## Slide 33: ✅ Session Success Criteria
Students leave able to:
✓ Convert force to torque (τ = F × r)
✓ Calculate power from torque and speed
✓ Determine power requirements for any scenario
✓ Calculate 0-100 km/h time, top speed, gradeability
✓ Understand complete force → torque → power chain
Most importantly: Students understand that vehicle performance is quantifiable — not magic, not guesswork, but physics and mathematics they can apply.
Emotional outcome: Students should feel empowered and confident entering the next module. The hardest conceptual work is done.

## Slide 34
End of Framework - Foundation Module Complete
Next: Template for remaining sessions + Example (Session 4: IC Engines)