## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 4: Introduction to IC Engines (Simplified)'

## Slide 2: Introduction to IC Engines (Simplified)
Session 4 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 4. Today we transition from understanding what power a vehicle needs to understanding how we generate that power.

## Slide 4: Connection to Previous Sessions
Let's connect the dots from the past three sessions:
Session 1: We calculated the forces a vehicle must overcome – rolling resistance, drag, gradient forces.
Session 2: We learned about tires and friction – the interface that delivers force to the road.
Session 3: We calculated power requirements – we know exactly how much power a vehicle needs to accelerate, climb hills, reach top speed.
Today's question: Where does that power come from?

## Slide 5: The Fundamental Question
Think about this for a moment. You pull up to a petrol station and pump liquid fuel into your tank. Minutes later, your wheels are spinning at 1000 RPM, delivering torque to the road.
How does chemical energy in liquid fuel become rotational mechanical energy at the wheels?
The answer is the Internal Combustion Engine – and today, I want to show you how it works, not as a thermodynamics problem, but as a mechanical torque-generating device.

## Slide 6: Why This Matters
Here's why understanding engines matters for automotive electronics engineers:
Modern engines are controlled entirely by electronics (ECU, sensors, actuators)
You can't design engine control systems without understanding what you're controlling
Performance, fuel efficiency, emissions – all depend on engine operation
But here's the good news: You don't need to be a thermodynamics expert. You need to understand the mechanical operation and what the electronics must control.

## Slide 7: Real-World Scenario
Let me give you a concrete example. This is the engine from a Honda Civic:
Engine: 1.5L 4-cylinder petrol
Maximum Power: 127 PS @ 6600 RPM
Maximum Torque: 145 Nm @ 4600 RPM
Questions: — What do these numbers actually mean?
Why does maximum torque occur at 4600 RPM but maximum power at 6600 RPM?
How does this engine deliver the 30-40 kW we calculated you need for highway cruising?
By the end of today, these specifications will make complete sense to you.

## Slide 8: What is an Internal Combustion Engine?
At its most basic level, an IC engine is a device that:
Takes in fuel and air
Burns them inside a cylinder (that's why 'internal' combustion)
Converts the expanding gas pressure into mechanical motion
Outputs rotational torque at a shaft
Think of it as an energy converter: Chemical energy (fuel) → Thermal energy (combustion) → Mechanical energy (rotation).
Today, we focus on step 3 and 4 – the mechanics. Thermodynamics comes much later.

## Slide 9: The Core Principle – Pressure Pushing Piston
Here's the fundamental principle:
When fuel-air mixture burns inside a sealed cylinder, it creates high pressure gas. This pressure pushes a piston downward. The piston is connected to a crankshaft via a connecting rod.
[Show animation]:
Pressure pushes piston DOWN (linear motion)
Piston pushes connecting rod
Connecting rod rotates crankshaft (rotational motion)
Linear motion → Rotational motion – that's the magic.

## Slide 10: From Piston to Wheels
Let me connect this back to what you already know from Session 3:
Session 3: You learned F = τ/r and P = τω
The engine creates torque (τ) at the crankshaft. This torque flows through:
Transmission (changes torque/speed ratio)
Driveshaft
Differential
Wheels
And ultimately creates the force at the tire contact patch that overcomes resistance and accelerates the vehicle.
Today's focus: How does the engine create that torque?

## Slide 11: Engine as a System
Let's think of the engine as a system:
Inputs: — Fuel (petrol or diesel)
Air
Spark (for petrol engines) or Compression (for diesel)
Outputs: — Mechanical Torque (what we want!)
Heat (needs cooling – Session 5 next week)
Exhaust gases (emissions control – Session 6)
Control: ECU controls fuel, air, spark timing (Sessions 13-15)
Everything is interconnected.

## Slide 12
#### Part 2: Major Engine Components (Slides 12-16, ~15 minutes)

## Slide 13: The Main Players – Components Overview
An IC engine has many parts, but today we focus on the essential mechanical components. Let me introduce them:
Cylinder – The chamber where combustion happens
Piston – Moves up and down inside the cylinder
Connecting Rod – Links piston to crankshaft
Crankshaft – Converts linear to rotational motion
Valves – Control air/fuel intake and exhaust exit
Camshaft – Opens and closes valves at right time
Let's examine each one.

## Slide 14: Cylinder and Piston
Cylinder: — A precisely machined tube (typically cast iron or aluminum)
Sealed at the top by the cylinder head
Houses the piston
Piston: — Fits snugly inside cylinder with piston rings for sealing
Moves up and down (reciprocating motion)
Connected to connecting rod via piston pin
Key point: The space above the piston is the combustion chamber – where the magic happens.

## Slide 15: Connecting Rod and Crankshaft
This is where linear motion becomes rotation:
Connecting Rod (Con-Rod): — Small end connects to piston (piston pin)
Big end connects to crankshaft (crankpin)
Transmits force from piston to crankshaft
Crankshaft: — Converts reciprocating motion to rotational motion
Like your bicycle pedal crank – your leg goes up/down, crank rotates
Has offset 'throws' (crankpins) where con-rods attach
[Show animation]: As piston moves down, con-rod pushes crankpin in circular path → shaft rotates.

## Slide 16: Valves and Camshaft
Valves control what goes in and out of the cylinder:
Intake Valve: — Opens to let air-fuel mixture into cylinder
Closes during compression and combustion
Exhaust Valve: — Opens to let burnt gases exit
Closed during intake, compression, and power stroke
Camshaft: — Driven by crankshaft (via timing belt or chain)
Has lobes that push on valve stems
Opens/closes valves at precisely the right time
Timing is critical – if valves open at wrong time, engine won't work!

## Slide 17: Putting It All Together – Engine Block Assembly
Let's see how everything fits:
Engine Block – Main structure, houses cylinders
Cylinder Head – Bolted on top, contains valves and combustion chamber
Crankcase – Bottom part of block, houses crankshaft
Oil Pan (Sump) – Underneath, stores engine oil
Modern cars typically have 3, 4, or 6 cylinders all in one engine block. Each cylinder operates independently but all connected to the same crankshaft.

## Slide 18
#### Part 3: The 4-Stroke Cycle (Mechanical Perspective) (Slides 17-21, ~15 minutes)

## Slide 19: Why 4 Strokes?
Here's a key concept: It takes 4 strokes of the piston (2 complete crankshaft rotations) to complete one power cycle.
4 Strokes:
Intake – Pull in air-fuel mixture
Compression – Compress it
Power – Burn it, extract energy
Exhaust – Push out burnt gases
Then repeat. Only 1 out of every 4 strokes produces power!
Let me show you each stroke in detail.

## Slide 20: Stroke 1 – Intake
Intake Stroke:
What happens: — Piston moves DOWN (from top to bottom of cylinder)
Intake valve OPEN
Exhaust valve CLOSED
Air-fuel mixture is sucked into cylinder (like a syringe pulling fluid)
Result: Cylinder is now filled with fresh air-fuel mixture, ready to compress.
Crankshaft rotation: 0° to 180°

## Slide 21: Stroke 2 – Compression
Compression Stroke:
What happens: — Piston moves UP
BOTH valves CLOSED (cylinder sealed)
Air-fuel mixture is compressed into small space (combustion chamber)
Pressure and temperature increase
Why compress? Higher compression → more efficient combustion → more power
At top: Spark plug fires (petrol engine) or fuel injected (diesel)
Crankshaft rotation: 180° to 360° (one full rotation complete)

## Slide 22: Stroke 3 – Power (Combustion)
Power Stroke – This is where the action is!
What happens: — Spark ignites compressed air-fuel mixture (or diesel self-ignites)
Rapid combustion creates HIGH PRESSURE (up to 60-100 bar!)
Pressure pushes piston DOWN with great force
Piston pushes con-rod → rotates crankshaft → TORQUE is generated
This is the only stroke that produces power. The other 3 are preparation.
Crankshaft rotation: 360° to 540°

## Slide 23: Stroke 4 – Exhaust
Exhaust Stroke:
What happens: — Piston moves UP
Intake valve CLOSED
Exhaust valve OPEN
Burnt gases are pushed out through exhaust valve into exhaust manifold
Result: Cylinder is cleared of exhaust, ready for next intake stroke.
Crankshaft rotation: 540° to 720° (two full rotations complete)
Then the cycle repeats – intake, compression, power, exhaust, intake...

## Slide 24
#### Part 4: Engine Terminology & Calculations (Slides 22-24, ~10 minutes)

## Slide 25: Key Engine Terms
Let me teach you the language engineers use to describe engines:
Bore (B): Diameter of the cylinder (mm)
Stroke (S): Distance piston travels from top to bottom (mm)
TDC (Top Dead Center): Piston's highest position
BDC (Bottom Dead Center): Piston's lowest position
Displacement: Volume swept by piston in one stroke
These define the engine's size and geometry.

## Slide 26: Calculating Engine Capacity (Displacement)
Here's how to calculate engine displacement (capacity):
For one cylinder:
V_cylinder = (π/4) × B² × S
Where:
B = Bore (mm)
S = Stroke (mm)
V_cylinder = Volume in mm³ (convert to cc or liters)
For entire engine:
Vengine = Vcylinder × Number of cylinders
Example: Honda Civic 1.5L engine
Bore = 73 mm
Stroke = 89.5 mm
Cylinders = 4
V_cylinder = (π/4) × 73² × 89.5 = 374,500 mm³ = 374.5 cc
V_engine = 374.5 × 4 = 1,498 cc ≈ 1.5 L

## Slide 27: Engine Torque vs Power Curves
Now we arrive at the heart of engine performance. Let me show you how to read these curves:
[Point to torque curve]:
Torque Curve (Nm vs RPM): — Shows how much twisting force the engine produces at each speed
Peak torque: 145 Nm @ 4600 RPM — At low RPM: Lower torque (engine struggles)
At very high RPM: Torque drops (breathing limitations)
[Point to power curve]:
Power Curve (PS vs RPM): — Remember: P = τ × ω (Session 3!)
Power = Torque × Angular velocity
Peak power: 127 PS @ 6600 RPM
Notice: Peak power occurs at HIGHER RPM than peak torque. Why?

## Slide 28: Why Peak Power ≠ Peak Torque RPM
This confuses many people, so let me explain clearly:
Remember: Power = Torque × RPM (essentially)
At 4600 RPM (peak torque):
Torque = 145 Nm (maximum)
RPM = 4600
Power = 145 × 4600 = ~100 PS
At 6600 RPM (peak power):
Torque = 130 Nm (slightly lower)
RPM = 6600 (much higher!)
Power = 130 × 6600 = 127 PS (maximum!)
Key insight: Even though torque drops at high RPM, the engine is spinning so much faster that power increases.
For vehicle performance: — Peak torque → Best for acceleration from low speeds
Peak power → Best for top speed

## Slide 29: Key Takeaways Summary
Let's summarize what you've learned today:
✓ Engine Function: IC engine converts fuel energy into rotational torque via combustion
✓ Key Components: Cylinder, piston, con-rod, crankshaft, valves, camshaft
✓ 4-Stroke Cycle: Intake → Compression → Power → Exhaust (only power stroke generates torque)
✓ Engine Specifications: Displacement = (π/4) × B² × S × n_cylinders
✓ Performance Curves: Torque curve shows force, power curve shows torque × RPM
✓ Engine Types: Classified by fuel (petrol/diesel), cylinders (3/4/6), configuration (inline/V/flat)
You can now understand engine specifications and interpret performance curves!

## Slide 30: Connection to Next Session
Today, we learned how engines generate torque through combustion. But we glossed over something critical:
Combustion generates enormous heat – temperatures reach 2000°C inside cylinders!
Moving parts create friction – piston, crankshaft, camshaft all rubbing at high speed.
Next Session (Session 5): Engine Support Systems – Cooling & Lubrication
You'll learn:
Why cooling is critical (what happens if engine overheats?)
How cooling systems work (radiator, thermostat, water pump)
Why lubrication is essential (engine oil functions)
How oil circulates through the engine
We're building a complete picture of the powertrain, piece by piece.

## Slide 31: 📊 PPT DESIGN GUIDANCE
Visual Elements to Include:
Assignment (Due before Session 5):
Problem 1: An engine has bore = 86 mm, stroke = 94 mm, 4 cylinders. Calculate:
a) Displacement of one cylinder (in cc)
b) Total engine capacity (in liters)
Problem 2: An engine produces 180 Nm torque at 3000 RPM. Calculate power output in kW and PS.
Problem 3: Study the torque and power curves of any one engine (find online or in textbook). Identify:
Peak torque value and RPM
Peak power value and RPM
Explain why peak power occurs at higher RPM than peak torque
Discussion Questions for Q&A: — What are the trade-offs between small displacement high-RPM engines vs large displacement low-RPM engines?
Why do diesel engines have higher compression ratios than petrol engines?
How does the 4-stroke cycle relate to the need for a flywheel?
30 minutes for your questions. —--
Consistency: Use same professional engineering template as Sessions 1-3
Technical Professionalism: Clean mechanical diagrams, cutaway views, labeled components
Color coding: — Blue for intake stroke
Orange for compression/combustion
Gray for exhaust
Green for mechanical components
Font sizes: Component labels and formulas in large, readable fonts (18-24pt)
Slide 9: Core principle (pressure pushing piston) – Foundation concept
Slide 14: Connecting rod and crankshaft animation – How linear becomes rotational
Slides 18-21: 4-stroke cycle animations – Heart of understanding
Slide 25: Torque and power curves – Industry standard way to describe engines
Slide 28: Summary – Students will photograph this
Slide 9, 14: Smooth animation of piston motion and crankshaft rotation
Slides 18-21: Build animation for 4-stroke cycle (step through each stroke)
Slide 25: Animated pointer tracing along curves as you explain
Keep mechanical animations smooth – helps visualize motion
Cutaway diagrams: Real engine cutaways showing internal components
Animated GIFs: 4-stroke cycle animation (use existing high-quality animations if available)
Component photos: Real parts (piston, crankshaft, camshaft) if possible
Graphs: Actual torque/power curves from real engines (Honda, Toyota, etc.)
Comparison tables: Engine classifications (inline vs V vs flat)

## Slide 32: 🎯 INSTRUCTOR NOTES
Safety/Ethics Notes:
Build on Session 3: Explicitly connect engine power output to power requirements calculated earlier
Mechanical focus only: NO thermodynamics yet – treat combustion as "pressure source
Visualize motion: Use animations heavily – students must "see" how parts move
Real examples: Use familiar engines (Honda Civic, Toyota Corolla) throughout
Prepare for Session 5: Set up the need for cooling and lubrication
Challenge 1: "Why 4 strokes? Why not generate power every stroke?"
How to address: Explain physical requirements – need to: 1) bring in fresh mixture, 2) compress it, 3) extract energy, 4) clear exhaust. Can't skip steps. Mention 2-stroke engines briefly (power every 2 strokes but less efficient, used in small engines).
Challenge 2: "How does crankshaft keep rotating during non-power strokes?"
How to address: Introduce flywheel concept – heavy rotating disc stores kinetic energy from power stroke, carries engine through other 3 strokes. Also, in multi-cylinder engines, other cylinders fire at different times.
Challenge 3: "Why peak power at higher RPM than peak torque?"
How to address: Use the mathematical relationship P = τ × ω explicitly. Show that even if torque decreases, if RPM increases proportionally more, power increases. Use numerical examples.
Challenge 4: "What's the difference between petrol and diesel engines mechanically?"
How to address: Today focus on similarities. Briefly mention: diesel has no spark plug (compression ignition), higher compression ratio, more robust construction. Details in Session 6.
If running short: — Condense Slide 16 (engine block assembly) – not critical
Combine compression ratio explanation into terminology slide
Reduce time on engine classification (Slide 6 outcome)
If running long: — Move detailed compression ratio calculations to assignment
Defer engine classification details to Session 6
Move flywheel discussion to Q&A
Core content (must cover): — Slides 8-10 (engine fundamentals)
Slides 13-15 (key components)
Slides 17-21 (4-stroke cycle – absolutely critical)
Slide 23 (displacement calculation)
Slide 25-26 (torque/power curves)
Slide 3: Pause and ask "Has anyone thought about this before? How does fuel become wheel rotation?
Slide 14: Work through the crank-slider mechanism together on board – draw it, show geometry
Slide 21: After showing 4 strokes, ask "In a 4-cylinder engine, how are firing intervals arranged?" (Answer: 180° apart, so one cylinder always powering)
Slide 23: Have students calculate displacement with you in real-time
Slide 26: Ask "If you want quick acceleration, what RPM range should you use?" (Answer: Near peak torque RPM)
Q&A: Be ready for questions about:
Turbochargers (briefly mention: forces more air in, increases power; details later)
Electric motors vs IC engines (mention: instant torque, covered in Session 8)
Engine efficiency (typical IC engine ~30-35% efficient; rest is heat)
Engine emissions: Mention that combustion produces pollutants (CO, NOx, HC) – why emission controls matter (Session 6 preview)
Fuel efficiency: More efficient engines = less fuel consumption = lower environmental impact
Standards: Reference BS4, BS6 emission standards (India-specific)

## Slide 33: ✅ Session Success Criteria
Students leave able to:
✓ Explain IC engine as device converting fuel energy to rotational torque
✓ Identify and explain functions of major engine components
✓ Describe 4-stroke cycle from mechanical perspective
✓ Calculate engine displacement and understand compression ratio
✓ Interpret torque and power curves and relate to vehicle performance
✓ Classify engines by fuel type, cylinder count, and configuration
Most importantly: Students understand engines as torque generators that deliver the power calculated in Session 3, and feel confident they can understand how engines work without needing deep thermodynamics knowledge.

## Slide 34: 📝 ADDITIONAL NOTES
Balance Simplification with Accuracy:
This session is the pivotal transition from "vehicle needs power" to "engine supplies power." Make this connection explicit and clear.
Throughout the session, mention heat generation and friction occasionally. At the end, create anticipation: "Now we know how engines work, but there's a problem – all this combustion and motion creates heat and friction. Next time, we solve that problem.
Use specific engine examples throughout:
Honda Civic 1.5L (inline-4 petrol)
Toyota Fortuner 2.8L (inline-4 diesel)
Maruti Suzuki Alto 0.8L (inline-3 petrol)
BMW 3.0L (inline-6 petrol)
Students relate better to engines they've heard of or seen.
We simplify by avoiding thermodynamics, but don't oversimplify mechanics
Valve timing, overlap, and advanced topics briefly mentioned but not detailed
Focus: Mechanical operation that electronics will control

## Slide 35
End of Session 4 Framework