## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 5: Engine Support Systems - Cooling & Lubrication'

## Slide 2: Engine Support Systems - Cooling & Lubrication
Session 5 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 5. Last week, we learned how engines generate torque through combustion. Today, we address the consequences of that combustion.

## Slide 4: Connection to Session 4
In Session 4, you learned the 4-stroke cycle. Let me remind you what happens during the power stroke:
Compressed air-fuel mixture ignites
Combustion temperature: ~2000-2500°C — Pressure: 60-100 bar pushing piston down
This happens thousands of times per minute (at 3000 RPM = 1500 combustion events per minute in a 4-cylinder engine!)
Question: What happens to all that heat?

## Slide 5: The Problem We Must Solve
Here's the harsh reality: Without proper cooling and lubrication, your engine would destroy itself in minutes.
Heat problems: — Aluminum pistons melt at ~660°C
Oil breaks down above ~200°C
Metal expands → parts seize together
Friction problems: — Piston sliding in cylinder: 10-20 meters per second
Crankshaft spinning at 3000-6000 RPM
Without oil: Metal-on-metal contact → catastrophic wear
Today's mission: Understand the systems that keep engines alive.

## Slide 6: Why This Matters for Automotive Electronics Engineers
As electronics engineers, why should you care about cooling and lubrication?
Because modern systems are electronically controlled: — Cooling fan – ECU-controlled based on coolant temperature sensor
Thermostat – Electronic thermostats now common
Oil pressure monitoring – Sensors and warning systems
Variable oil pumps – Electronic control for efficiency
You design the control systems. You must understand what you're controlling.

## Slide 7: Real-World Scenario
Picture this: You're driving on a highway. Suddenly, the temperature warning light comes on. Within 2 minutes, steam pours from under the hood. You pull over.
What happened? Cooling system failed.
What got damaged? — Cylinder head gasket blown → coolant leaked into engine
Engine overheated → piston rings damaged
Repair cost: ₹50,000 - ₹1,00,000
All because: One component in the cooling system failed – maybe just a ₹200 thermostat.
Understanding these systems isn't academic – it's economically critical.

## Slide 8: Why Engines Need Cooling
Let's talk numbers. In a typical gasoline engine:
Fuel Energy (100%) breaks down as:
~30-35% → Useful mechanical work (powering vehicle)
~30-35% → Lost as exhaust heat
~25-30% → Lost as engine heat (cooling system removes this)
~5-10% → Friction losses
That means nearly 1/3 of fuel energy becomes heat that must be removed.
For a 100 HP (75 kW) engine, cooling system must remove ~60-70 kW of heat – equivalent to running 60-70 electric room heaters!

## Slide 9: What Happens If We Don't Cool?
Let me show you the failure timeline without cooling:
0-2 minutes: Temperature rises from 90°C → 150°C
Oil viscosity drops → increased wear
2-5 minutes: 150°C → 250°C
Coolant boils → steam pockets form
Oil starts breaking down
5-10 minutes: 250°C → 400°C+
Piston rings lose tension → compression lost
Aluminum components start deforming
10+ minutes: Catastrophic failure
Pistons seize in cylinders
Cylinder head warps
Engine destroyed
Cooling isn't optional – it's survival.

## Slide 10: Two Cooling Approaches
There are two fundamental approaches:
AIR-COOLED: — Heat dissipates directly to air via fins on cylinder
Airflow (from vehicle motion or fan) carries heat away
Simple, lightweight, no coolant needed
LIQUID-COOLED: — Coolant (water + antifreeze) circulates through engine
Absorbs heat from engine → releases heat at radiator
More complex, but more effective
Let's compare them.

## Slide 11: Air-Cooled vs Liquid-Cooled Analysis
AIR-COOLED SYSTEMS:
Advantages:
✓ Simple – fewer parts, less maintenance
✓ Lightweight – no radiator, hoses, coolant
✓ No coolant leaks or freezing issues
Disadvantages:
✗ Less effective cooling – limited heat transfer
✗ Temperature control difficult – depends on airflow
✗ Noisy – need large cooling fins
✗ Limited to smaller engines
LIQUID-COOLED SYSTEMS:
Advantages:
✓ Very effective – water absorbs heat well
✓ Precise temperature control – thermostat regulation
✓ Quieter operation
✓ Works for high-power engines
Disadvantages:
✗ Complex – more components
✗ Heavier – radiator, coolant, hoses
✗ Maintenance required – coolant replacement
✗ Potential leaks
Modern cars: 99% use liquid cooling. Motorcycles: Mix of both.

## Slide 12: Liquid Cooling System Overview
Here's the complete liquid cooling system. Let me walk you through it:
Components (we'll detail each):
Water jacket – Passages around cylinders and combustion chambers
Water pump – Circulates coolant through system
Thermostat – Controls coolant flow based on temperature
Radiator – Heat exchanger that cools the coolant
Cooling fan – Forces air through radiator (when needed)
Coolant – Water + antifreeze mixture
Hoses – Connect components
Expansion tank – Handles coolant expansion/contraction
Flow path: Engine → Thermostat → Radiator → Back to engine (cycle repeats)
Let's examine each component.

## Slide 13
#### Part 2: Cooling System Components (Slides 13-17, ~15 minutes)

## Slide 14: Water Jacket & Water Pump
Water Jacket: — Network of passages cast into engine block and cylinder head
Surrounds cylinders and combustion chambers (hottest areas)
Coolant flows through, absorbing heat from metal walls
Water Pump: — Centrifugal pump (impeller design)
Driven by engine via belt from crankshaft
Pumps coolant through entire system at ~40-60 liters per minute — Modern cars: Some use electric pumps (ECU controlled for efficiency)

## Slide 15: Thermostat – The Temperature Controller
The thermostat is brilliant in its simplicity:
Function: Control coolant flow to maintain optimal engine temperature (~90-95°C)
Operation: — Cold engine (below ~85°C): Thermostat CLOSED
→ Coolant circulates only within engine (bypass circuit)
→ Engine warms up quickly
Hot engine (above ~95°C): Thermostat OPENS
→ Coolant flows to radiator
→ Heat is released to atmosphere
Mechanism: — Contains wax pellet that expands with heat
Expansion pushes valve open
Purely mechanical – no electronics needed (traditional design)
Modern: Electronic thermostats with heater element – ECU can control opening temperature for efficiency.

## Slide 16: Radiator – The Heat Exchanger
Radiator Design: — Thin metal tubes carry hot coolant
Fins attached to tubes increase surface area
Air flows through fins (from vehicle motion or fan)
Heat transfers from coolant → tubes → fins → air
Materials: — Tubes: Aluminum or copper
Fins: Aluminum (good heat conductor, lightweight)
Tanks: Plastic or aluminum
Performance: — Coolant enters at ~95-100°C (top)
Exits at ~75-85°C (bottom)
ΔT ~ 15-20°C in one pass
Capacity: Sized to dissipate engine's heat rejection at maximum power.

## Slide 17: Cooling Fan & Control
Cooling Fan Function: — Provides airflow when vehicle speed is low or stopped
Not needed at highway speeds (ram air sufficient)
Types:
Mechanical fan (older vehicles)
Belt-driven from engine
Always spinning (inefficient)
Viscous coupling can modulate speed
Electric fan (modern vehicles) ✓
Driven by electric motor
ECU-controlled based on coolant temperature sensor
Control Logic: — Coolant temp < 95°C → Fan OFF
Coolant temp > 100°C → Fan ON
AC compressor ON → Fan ON (helps condenser cooling too)
Benefits: Reduces engine load, improves fuel efficiency, precise control.

## Slide 18: Coolant & Expansion Tank
Coolant Composition: — Not pure water! Mixture of:
50% water
50% ethylene glycol (antifreeze)
Why antifreeze? — Lowers freezing point: ~0°C → —37°C
Raises boiling point: 100°C → 129°C (under pressure)
Corrosion protection: Additives prevent rust
Lubrication: Protects water pump seal
Expansion Tank (Overflow Reservoir): — Coolant expands when hot, contracts when cold
Tank accommodates volume changes
Maintains system pressure (~1.0-1.3 bar)
Fill level: Check when engine cold
Maintenance: Replace coolant every 2-3 years (additives degrade).

## Slide 19
#### Part 3: Lubrication Systems Fundamentals (Slides 18-21, ~12 minutes)

## Slide 20: Why Engines Need Lubrication
Let's shift to the second critical support system: Lubrication.
The friction problem:
Even polished metal surfaces are rough at microscopic level. When metal slides on metal at high speed:
Extreme friction → Heat generation
Rapid wear → Surface damage
Seizing → Parts weld together
Examples in engine: — Piston sliding in cylinder: 10-20 m/s — Crankshaft journal in bearing: 3000-6000 RPM — Camshaft lobes pushing valves: High pressure contact
Solution: Create a thin film of oil between surfaces → prevents metal-to-metal contact.

## Slide 21: Engine Oil Functions (Beyond Lubrication)
Engine oil does much more than reduce friction. It has 5 critical functions:
1. FRICTION REDUCTION (Primary function) — Creates oil film between moving parts
Reduces friction coefficient from ~0.3 (dry) to ~0.01 (lubricated)
Reduces power loss due to friction
2. HEAT DISSIPATION — Oil absorbs heat from pistons, bearings, etc.
Carries heat to oil pan (sump) where it dissipates
Removes ~10-15% of engine heat
3. CLEANING — Detergent additives suspend carbon deposits and soot
Prevents sludge buildup on engine parts
Contaminants removed by oil filter
4. SEALING — Oil film between piston rings and cylinder wall seals combustion chamber
Improves compression and prevents blowby
5. CORROSION PROTECTION — Additives prevent rust and corrosion
Protects parts during engine-off periods
One fluid, five functions – that's why oil quality matters!

## Slide 22: What Happens Without Proper Lubrication?
Let's see the failure timeline without oil:
0-30 seconds: Oil pressure drops to zero
Metal-to-metal contact begins at bearings
Friction increases → heat generation accelerates
30 seconds - 2 minutes: — Bearings start melting (babbit metal softens)
Piston rings score cylinder walls
Loud knocking noises (bearing knock)
2-5 minutes: — Bearings seize
Crankshaft stops rotating → connecting rod breaks
Catastrophic failure
Real-world: Some race engines can survive ~10 seconds without oil (at reduced load). Street engines? Maybe 1 minute before serious damage.
Bottom line: Never drive with low oil pressure warning on!

## Slide 23: Lubrication System Overview
Here's the complete lubrication system:
Components:
Oil sump (pan) – Reservoir holds 4-6 liters of oil
Oil pump – Pressurizes and circulates oil
Oil filter – Removes contaminants
Oil galleries – Passages in engine block/head delivering oil
Oil pressure sensor – Monitors system pressure
PCV valve – Handles blowby gases
Flow path:
Sump → Pump → Filter → Main gallery → Bearings/Camshaft/Pistons → Drains back to sump
Pressure: Typically 3-5 bar at operating temperature
Let's examine the components.

## Slide 24
#### Part 4: Lubrication System Components & Oil Specifications (Slides 22-24, ~10 minutes)

## Slide 25: Oil Pump, Filter & Galleries
Oil Pump: — Type: Usually gear pump (two meshing gears) or rotor pump
Drive: Driven by crankshaft or camshaft
Pressure: Maintains 3-5 bar (higher at cold start, lower when hot)
Relief valve: Opens if pressure too high (protects system)
Oil Filter: — Function: Removes particles down to ~10-30 microns
Type: Spin-on cartridge or replaceable element
Bypass valve: If filter clogs, oil bypasses (dirty oil better than no oil!)
Replacement: Every 5,000-10,000 km (depends on oil type)
Oil Galleries: — Main oil gallery: Large passage in engine block
Branch passages: Deliver oil to specific locations
Crankshaft main bearings
Connecting rod bearings (via drilled holes in crankshaft!)
Camshaft bearings
Piston cooling jets (high-performance engines)
Oil drains back to sump by gravity

## Slide 26: Engine Oil Specifications – Viscosity Grades
When you see '5W-30' on an oil bottle, what does it mean?
Understanding Viscosity Grades:
Format: XW-Y (e.g., 5W-30, 10W-40)
'XW' (Winter viscosity):
Number before 'W' = cold temperature performance
Lower number = flows better when cold
5W = Good to -30°C
10W = Good to -25°C
15W = Good to -20°C
'Y' (High temperature viscosity):
Number after hyphen = viscosity at 100°C
Higher number = thicker oil at operating temperature
30 = Thinner (better fuel economy)
40 = Medium
50 = Thicker (better protection under heavy load)
Example:
5W-30: — Flows like 5-weight oil when cold (easy cold starts)
Protects like 30-weight oil when hot (normal operation)
Choosing: — Cold climate (Ladakh): 0W-30 or 5W-30
Hot climate (Rajasthan): 10W-40 or 15W-40
Severe service (racing): 10W-50 or 20W-50
Always follow manufacturer recommendation!

## Slide 27: Cooling & Lubrication Working Together
Here's the big picture: Cooling and lubrication are interconnected systems working together to manage engine heat and friction.
Heat Generation Sources:
Combustion → ~60-70% of heat (cooling system removes)
Friction → ~10% of heat (oil removes)
Heat Removal Paths: — Cooling system: 60-65% of total heat rejection
Lubrication system: 10-15% (oil carries heat from pistons/bearings)
Exhaust: 25-30%
They work together: — Oil temperature controlled by cooling system (some engines have oil cooler using coolant)
Coolant temperature affects oil viscosity
Both must maintain optimal temperature range (oil: ~90-110°C, coolant: ~90-95°C)
If either fails → Engine fails.

## Slide 28: Solving Today's Challenges
Remember our challenges from the beginning? Let's solve them:
Challenge 1: Design cooling system for 100 HP engine (-20°C to +45°C operation)
Solution: — Liquid cooling system (air-cooling inadequate for 100 HP)
Radiator size: ~0.5-0.6 m² frontal area (dissipates ~60 kW)
Coolant: 50/50 mix ethylene glycol/water (freeze protection to -37°C, boil protection to ~130°C)
Thermostat: 85-90°C opening temp (ensures warm-up in winter, cooling in summer)
Electric fan: ECU-controlled with temperature sensor (on above 100°C)
Expansion tank: 10-15% of system capacity
Challenge 2: Select oil for Delhi vs Ladakh
Delhi (hot summers, cool winters): — 5W-30 or 10W-40 (good all-year performance)
Fully synthetic (handles temperature swings better)
Ladakh (extreme cold, can reach -30°C): — 0W-30 or 0W-40 (critical for cold starts)
Fully synthetic (flows at extreme low temps)
Both: API SN or higher for modern engines.

## Slide 29: Key Takeaways Summary
Let's summarize what you've mastered today:
COOLING SYSTEMS:
✓ Engines reject ~60-70 kW of heat (must be removed to prevent damage)
✓ Liquid cooling more effective than air cooling for automotive use
✓ Key components: Water jacket, pump, thermostat, radiator, fan, coolant
✓ Coolant: 50/50 water/antifreeze mix (freeze protection + boil protection)
✓ Thermostat maintains optimal 90-95°C operating temperature
LUBRICATION SYSTEMS:
✓ Oil has 5 functions: friction reduction, heat dissipation, cleaning, sealing, corrosion protection
✓ Key components: Sump, pump, filter, oil galleries
✓ Oil pressure: 3-5 bar at operating temperature
✓ Viscosity grade (e.g., 5W-30): Cold flow (5W) + Hot protection (30)
✓ API/ACEA ratings indicate oil quality and application suitability
You can now explain why engines need support systems and how they work!

## Slide 30: Connection to Next Session
Today we covered how to keep the engine alive. Next session, we focus on optimizing engine performance:
Session 6: Engine Performance & Fuel Systems
You'll learn:
How to interpret engine performance maps (torque curves, power curves, BSFC)
How fuel is delivered to the engine (carburetor vs fuel injection)
Multi-Point Fuel Injection (MPFI) and Direct Injection (GDI) systems
Air-fuel ratio control and emissions basics
Connection: Cooling/lubrication keep engine running. Fuel systems optimize how efficiently it runs.
Building towards: Complete understanding of powertrain systems (Sessions 4-6 form a cluster).

## Slide 31: 📊 PPT DESIGN GUIDANCE
Visual Elements to Include:
Assignment (Due before Session 6):
Problem 1: A 4-cylinder, 2.0L engine produces 150 HP (110 kW) at maximum power. Assuming 30% thermal efficiency, calculate:
a) Total fuel energy input rate (kW)
b) Heat rejection rate that cooling system must handle (kW)
c) If coolant flow rate is 60 L/min and temperature rise is 15°C, verify that cooling system capacity is adequate (use: Q = ṁ × cp × ΔT, where cp = 4.18 kJ/kg·K for water)
Problem 2: Select appropriate engine oil for the following scenarios:
a) Taxi in Mumbai (high mileage, frequent stops, hot climate)
b) Truck in Manali-Leh route (cold climate, heavy load)
c) Sports car used for weekend track days (high RPM, high load)
Justify your viscosity grade choice and synthetic vs mineral recommendation.
Problem 3: Research and sketch the lubrication path in a 4-cylinder engine from oil sump to crankshaft main bearing and back. Label all components.
Discussion Questions for Q&A: — Why do electric cooling fans improve fuel efficiency compared to belt-driven fans?
What are the trade-offs between long oil change intervals (15,000 km) vs short intervals (5,000 km)?
How do turbocharged engines modify cooling requirements?
30 minutes for your questions. —--
Consistency: Maintain professional engineering template from Sessions 1-4
Technical Professionalism: Clear system diagrams, component cutaways, flow charts
Color coding: — Red/Orange for hot coolant, heat flow, friction points
Blue for cool coolant, oil flow
Gray for mechanical components
Green for sensors/electronic control
Font sizes: Labels on diagrams should be large and readable (18-24pt)
Slide 3: The problem (overheating/seizure) – Establishes urgency
Slide 12: Complete cooling system diagram – Students will photograph this
Slide 19: Five functions of engine oil – Core concept
Slide 23: Viscosity grade interpretation – Practical application
Slide 28: Summary – Comprehensive reference
Slide 12: Build animation showing coolant flow path through system
Slide 14: Thermostat opening/closing animation
Slide 21: Oil circulation path animation (sump → pump → filter → galleries → back)
Slide 22: Gear pump operation animation
Keep flow animations smooth – helps visualize circulation
Cutaway diagrams: Real engines showing water jacket passages, oil galleries
Component photos: Real radiator, thermostat, oil filter, oil pump
System schematics: Flow diagrams with arrows showing fluid circulation
Comparison tables: Air-cooled vs liquid-cooled, synthetic vs mineral oil
Temperature/pressure graphs: Show operating ranges
Oil bottle labels: Real examples of 5W-30, API SN markings

## Slide 32: 🎯 INSTRUCTOR NOTES
Safety/Ethics Notes:
Consequence-driven: Start with "what happens if we don't" (failure modes create urgency)
System thinking: Show how cooling and lubrication interconnect
Real-world relevance: Use actual vehicle examples (Honda Civic, Toyota, etc.)
Practical application: Oil selection, coolant maintenance – skills students can use
Connect to electronics: Emphasize ECU control, sensors throughout (their domain)
Challenge 1: "Why 50/50 coolant mix? Why not 100% antifreeze for better protection?"
How to address: Explain that pure antifreeze (ethylene glycol) has worse heat transfer properties than water. 50/50 mix balances freeze/boil protection with heat transfer effectiveness. Show data: water cp = 4.18 kJ/kg·K, antifreeze cp = 2.4 kJ/kg·K.
Challenge 2: "Can I use thicker oil (like 20W-50) for 'better protection'?"
How to address: Explain trade-offs: Thicker oil → more friction → power loss + worse fuel economy + harder cold starts. Modern engines designed for specific viscosity – using wrong grade can cause oil starvation (oil passages sized for specific flow). Always follow manufacturer spec.
Challenge 3: "How does oil get to top of engine (cylinder head) if pump is at bottom?"
How to address: Explain pressurized system – pump creates 3-5 bar pressure, forces oil up through galleries against gravity. Show oil gallery diagram. Drainback is gravity-fed.
Challenge 4: "Why does oil pressure drop when engine is hot?"
How to address: Viscosity decreases with temperature → oil flows more easily → less resistance → lower pressure. This is normal. Oil pressure warning typically set to ~0.5 bar – if it drops below that, insufficient lubrication.
If running short: — Condense Slide 11 (air-cooled vs liquid-cooled comparison) – briefly mention, don't dwell
Combine oil pump and filter into single slide (Slide 22)
Reduce time on API/ACEA classifications (just mention they exist)
If running long: — Move oil specification details (Slide 23-24) to assignment reading
Defer oil cooler discussion to Q&A
Reduce time on expansion tank details
Core content (must cover): — Slides 8-9 (why cooling needed – critical understanding)
Slides 12-16 (cooling system components – complete system)
Slides 18-21 (lubrication fundamentals and system – critical understanding)
Slide 23 (viscosity grades – practical skill)
Slide 3: Ask "Has anyone experienced engine overheating? What happened?
Slide 11: Poll students: "Who has seen an air-cooled engine? Where?" (motorcycles, old VW Beetles)
Slide 14: Draw thermostat operation on board – show wax pellet expansion concept
Slide 19: Ask "If oil only reduced friction, what would happen to all the heat and dirt in the engine?
Slide 23: Interactive: Given climate conditions, have students select oil grade together
Q&A: Be ready for questions about:
Oil additives: Mention ZDDP (zinc) for wear protection, detergents/dispersants for cleaning, friction modifiers
Coolant colors: Green, orange, pink – different formulations, DO NOT MIX different types
Oil change intervals: How to determine (oil analysis, manufacturer recommendation, driving conditions)
Turbocharger cooling: Brief mention of oil cooling for turbo bearings, some have water cooling too
Environmental: Used engine oil is hazardous waste – must be disposed properly, NOT down drains
Coolant toxicity: Ethylene glycol is toxic – handle carefully, sweet taste attracts animals/children
Maintenance importance: Regular oil/coolant changes prevent costly failures – false economy to skip maintenance
Oil quality: Counterfeit oil is a problem in some markets – buy from reputable sources

## Slide 33: ✅ Session Success Criteria
Students leave able to:
✓ Explain why engines generate heat and need cooling systems
✓ Compare air-cooled and liquid-cooled systems with analysis of suitability
✓ Identify all cooling system components and explain their operation
✓ Explain need for lubrication and all five functions of engine oil
✓ Describe lubrication system components and oil circulation path
✓ Interpret oil specifications (5W-30, API SN) and select appropriate oil for given conditions
Most importantly: Students understand that cooling and lubrication are critical support systems without which engines would destroy themselves, and they can apply this knowledge to real-world scenarios (selecting oil, diagnosing cooling issues, understanding ECU control requirements).

## Slide 34: 📝 ADDITIONAL NOTES
Common Misconceptions to Address:
Session 4: Introduced engine as torque generator – Session 5 shows support systems needed for that generator to survive
Sessions 1-3: Calculated power requirements – Session 5 explains how to manage the heat generated when producing that power
Throughout session, mention fuel delivery and efficiency occasionally. At end: "We know how to keep engine alive (Session 5). Next: How to optimize its performance through fuel delivery and management.
Cooling failures: Blown head gasket symptoms, overheating on hills (inadequate cooling capacity)
Lubrication failures: Low oil pressure warning, engine knock, seized engines
Maintenance: Oil change process, coolant flush, why regular service matters economically
Performance modifications: Oil coolers for track cars, upgraded radiators for towing
Emphasize throughout that modern systems are electronically managed:
Cooling fan – PWM control for variable speed
Thermostat – Electric heating element for faster/ECU-controlled opening
Oil pump – Variable displacement pumps (ECU-controlled pressure)
Sensors – Temperature, pressure sensors feed ECU for monitoring and control
This connects mechanical understanding to their electronics engineering background.
"More oil is better" – No, overfilling causes aeration, foaming, pressure issues
"Thicker oil is always better protection" – No, modern tight tolerances need specified viscosity
"Flush radiator with water is same as proper coolant" – No, loses antifreeze and corrosion protection
"Oil looks clean, so it's still good" – No, additives deplete even if oil looks clean

## Slide 35
End of Session 5 Framework