## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 6: Engine Performance & Fuel Systems'

## Slide 2: Engine Performance & Fuel Systems
Session 6 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 6. We're now at the final piece of the powertrain puzzle: How do we optimize engine performance through fuel management?

## Slide 4: Connection to Sessions 4-5
Let's trace our journey through the powertrain:
Session 4: How engines convert fuel energy into torque
Learned 4-stroke cycle, mechanical components
Understood torque vs power relationship
Session 5: How to keep engines alive
Cooling removes heat
Lubrication reduces friction
Today (Session 6): How to optimize engine performance
How to measure and interpret performance (maps and curves)
How to deliver fuel precisely (injection systems)
How to control emissions (environmental responsibility)
The goal: Maximum efficiency, minimum emissions.

## Slide 5: The Fundamental Challenge
Here's the engineering challenge that every engine designer faces:
Three competing objectives:
High Power – Customers want performance
Good Fuel Economy – Customers want low running costs
Low Emissions – Regulations demand clean exhaust
The problem: These three goals contradict each other!
More power → More fuel consumption
Lean mixture (economy) → High NOx emissions
Rich mixture (power) → High CO and HC emissions
Solution: Precise fuel control through electronic fuel injection + understanding performance maps to operate in optimal regions.
Today you learn how engineers balance these trade-offs.

## Slide 6: Why This Matters for Electronics Engineers
This session is CRITICAL for automotive electronics engineers because:
Modern fuel systems are 100% electronically controlled: — ECU determines exact fuel quantity (millisecond-level precision)
Sensors measure air flow, oxygen content, throttle position, temperature
Actuators = fuel injectors (solenoid-controlled valves)
Closed-loop control using oxygen sensor feedback
You design these control systems. You must understand:
What the engine needs (air-fuel ratio requirements)
How to measure it (sensor inputs)
How to control it (injection timing and duration)
This is where electronics meets combustion!

## Slide 7: Real-World Scenario
Let me show you a real puzzle:
Two identical Honda Civic 1.5L engines:
Driver A: — Fuel economy: 12 km/L (city driving)
Emissions: Borderline BS6 compliance
Driver B: — Fuel economy: 18 km/L (same city route!)
Emissions: Well within BS6 limits
Question: Same engine, same route, same fuel. Why such different results?
Answer: Driver B understands engine performance maps and drives in optimal regions (2000-3000 RPM where BSFC is lowest). Driver A accelerates hard, uses high RPM, operates where engine is inefficient.
By the end of today, you'll know how to read those maps and understand the optimal regions.

## Slide 8: Recap – Torque vs Power Curves
Let's start by revisiting what you learned in Session 4:
Torque Curve (Nm vs RPM): — Shows engine's ability to do work at each speed
Peak torque typically at mid-range RPM (e.g., 4000 RPM)
Power Curve (kW or PS vs RPM): — Power = Torque × RPM (remember: P = τω)
Peak power at higher RPM than peak torque (e.g., 6000 RPM)
For vehicle performance: — Torque → Acceleration (especially from standstill)
Power → Top speed and sustained performance
But there's a third curve that's even more important for real-world driving...

## Slide 9: Introducing BSFC (Brake Specific Fuel Consumption)
BSFC = Brake Specific Fuel Consumption
Definition: How much fuel the engine consumes to produce one unit of power for one hour.
Formula:
BSFC = (Fuel consumption rate) / (Power output)
Units: g/kW·h (grams of fuel per kilowatt-hour)
What it tells us: — Lower BSFC = More efficient (less fuel for same power)
Higher BSFC = Less efficient (more fuel for same power)
Typical values: — Best BSFC (modern gasoline engine): ~220-250 g/kW·h — Best BSFC (diesel engine): ~200-220 g/kW·h (diesel more efficient)
Poor operating point (high RPM, light load): >400 g/kW·h
Why it matters: This tells you WHERE to operate the engine for best fuel economy.

## Slide 10: The BSFC Map Explained
This is a BSFC map – the most important performance tool for understanding engine efficiency:
How to read it: — X-axis: Engine speed (RPM)
Y-axis: Engine torque (Nm)
Contour lines: BSFC values (g/kW·h)
Colors: Often blue = efficient, red = inefficient
The 'island' in the middle: — Lowest BSFC region (e.g., 220-240 g/kW·h)
This is the 'sweet spot' – most efficient operation
Typically occurs at: ~2000-3000 RPM, ~50-80% of max torque
Why an island? — Too low RPM: Mechanical friction dominates (% of output)
Too high RPM: Pumping losses, valve train friction increase
Too low load: Throttling losses (pumping air past throttle)
Too high load: Combustion efficiency decreases
Optimal region: Medium RPM, medium-high load.

## Slide 11: Operating Points on BSFC Map
Let me show you where different driving conditions fall on this map:
Scenario 1: Highway cruising at 100 km/h — Engine RPM: ~2500 RPM
Torque required: ~60 Nm (low load – just overcoming drag)
BSFC: ~260 g/kW·h (pretty good, near optimal island)
Result: Good fuel economy
Scenario 2: City driving, idling in traffic — Engine RPM: 800 RPM (idle)
Torque: ~10 Nm (very light load)
BSFC: >500 g/kW·h (terrible efficiency!)
Result: Poor fuel economy (engine running but doing little work)
Scenario 3: Aggressive acceleration — Engine RPM: 5000-6000 RPM
Torque: Maximum available (~120 Nm)
BSFC: ~350-400 g/kW·h (inefficient region)
Result: High power but poor fuel economy
Key insight: You want to operate in the low-BSFC island as much as possible.

## Slide 12: How Transmission Helps Optimize BSFC
Here's why modern cars have 6, 7, or even 8 gears:
Purpose of multiple gears: Keep engine operating in efficient BSFC region for various vehicle speeds.
Example: — Vehicle speed: 60 km/h
If in 3rd gear: Engine at 3500 RPM, torque 40 Nm → BSFC = 340 g/kW·h (inefficient)
If in 5th gear: Engine at 2000 RPM, torque 60 Nm → BSFC = 240 g/kW·h (efficient!)
Modern solution: Continuously Variable Transmission (CVT) or 8+ speed automatics
Can always keep engine at optimal RPM/torque combination
ECU chooses gear to minimize BSFC for given power demand
This is why hybrid cars are efficient: Electric motor assists so engine can stay in optimal BSFC island always (Sessions 7-8 cover transmissions).

## Slide 13: Practice – Reading Performance Maps
Let's practice reading a real map:
[Show actual BSFC map]
Questions:
At what RPM and torque is BSFC minimum? (Answer: ~2500 RPM, ~120 Nm, BSFC ~230 g/kW·h)
You're cruising at 3500 RPM, 50 Nm torque. Is this efficient? (Check map – probably ~280 g/kW·h, not optimal)
How would you improve efficiency? (Shift to higher gear → reduce RPM to ~2500, increase torque to ~70 Nm)
This is real engine optimization! —--
#### Part 2: Fuel Delivery Systems (Slides 14-20, ~25 minutes)

## Slide 14: The Air-Fuel Mixture Requirement
Before we discuss HOW to deliver fuel, let's understand WHAT the engine needs:
Complete combustion requires precise air-fuel ratio.
Gasoline combustion (simplified):
C₈H₁₈ (octane) + 12.5 O₂ → 8 CO₂ + 9 H₂O + Energy
Mass ratio: — For complete combustion: Need 14.7 kg of air for every 1 kg of fuel
Stoichiometric Ratio = 14.7:1 (for gasoline)
Air-Fuel Ratio (AFR) terminology: — AFR = 14.7 → Stoichiometric (ideal combustion, λ = 1)
AFR > 14.7 → Lean mixture (excess air, λ > 1)
AFR < 14.7 → Rich mixture (excess fuel, λ < 1)
Why it matters: Different AFR for different needs!

## Slide 15: Air-Fuel Ratio for Different Operating Conditions
Here's what the engine needs in different situations:
Normal cruising (best economy): — AFR = 16:1 (lean)
λ ≈ 1.09
Burns all fuel efficiently, minimal CO and HC emissions
Slightly lower power output (acceptable for cruising)
Maximum power (full throttle): — AFR = 12:1 to 13:1 (rich)
λ ≈ 0.85
Extra fuel cools combustion chamber, prevents knock
Maximum power output
Higher emissions (CO and HC increase)
Cold start: — AFR = 9:1 to 11:1 (very rich)
Compensates for poor fuel evaporation when cold
High emissions (temporarily)
Idle: — AFR = 14.7:1 (stoichiometric)
Smooth running, catalytic converter works best
Challenge: How to deliver the RIGHT amount of fuel for each condition? That's where fuel injection comes in.

## Slide 16: Evolution of Fuel Delivery – Carburetor
Let's trace the evolution of fuel delivery systems:
CARBURETOR (Technology: 1890s-1990s)
How it works: — Air flows through venturi (narrow section)
Venturi creates vacuum (Bernoulli's principle)
Vacuum sucks fuel from float chamber through jet
Fuel mixes with air → enters engine
Advantages:
✓ Simple, mechanical (no electronics)
✓ Cheap to manufacture
✓ Easy to repair
Disadvantages:
✗ Imprecise AFR control (mechanical jets can't adapt well)
✗ Poor cold start performance
✗ Altitude sensitive (air density changes)
✗ Cannot meet modern emission standards
✗ Poor fuel economy
Result: Phased out in cars by 2000s (still used in small engines like lawn mowers, older motorcycles).

## Slide 17: Electronic Fuel Injection – The Revolution
Electronic Fuel Injection (EFI) revolutionized automotive engineering:
Core principle: — ECU calculates exact fuel quantity needed (every engine cycle!)
Fuel injectors spray precise fuel quantity into air stream
Sensors provide feedback for closed-loop control
Advantages over carburetor:
✓ Precise AFR control (±1% accuracy)
✓ Adapts to all conditions (temperature, altitude, load)
✓ Better fuel economy (~15-20% improvement)
✓ Lower emissions (can meet BS6/Euro 6)
✓ Better performance (optimal AFR for every condition)
✓ No altitude adjustment needed
Disadvantages:
✗ More complex (requires ECU, sensors, electrical system)
✗ More expensive
✗ Requires skilled technicians for repair
Timeline: Introduced 1980s, mandatory in developed countries by 1995-2000, universal in India post-BS3 (2005+).

## Slide 18: Multi-Point Fuel Injection (MPFI)
MPFI = Multi-Point Fuel Injection (most common system in modern cars)
Configuration: — One injector per cylinder (4-cylinder engine = 4 injectors)
Injector located in intake manifold, just before intake valve (port injection)
Fuel sprays onto intake valve, mixes with air, enters cylinder
How it works:
Sensors measure: — Air flow (MAF sensor)
Throttle position (TPS)
Engine RPM (crankshaft sensor)
Coolant temperature (temp sensor)
Oxygen in exhaust (O₂ sensor)
ECU calculates: — Required fuel quantity based on air mass
Base fuel = Air mass / AFR target
Adjustments for temperature, altitude, acceleration, etc.
Injector delivers: — ECU sends electrical pulse to injector solenoid
Pulse width (milliseconds) determines fuel quantity
Typical: 2-10 ms pulse width
Injector opens → fuel sprays → injector closes
Result: Precise AFR control for every cylinder, every engine cycle!

## Slide 19: Gasoline Direct Injection (GDI)
GDI = Gasoline Direct Injection (latest technology, premium cars)
Key difference from MPFI: — MPFI: Fuel injected into intake manifold (outside cylinder)
GDI: Fuel injected directly into combustion chamber (like diesel engines)
Advantages of GDI:
✓ Higher compression ratio possible (fuel injection cools cylinder → less knock)
✓ Better fuel economy (~5-10% improvement over MPFI)
✓ More power (denser air charge)
✓ Stratified charge possible (lean-burn at low load)
Challenges:
✗ Higher injection pressure needed (~200 bar vs ~3-5 bar for MPFI)
✗ More expensive (high-pressure pump, precise injectors)
✗ Carbon buildup on intake valves (no fuel washing them)
✗ Particulate emissions (requires Gasoline Particulate Filter for BS6)
Used in: Premium cars (BMW, Audi, Mercedes), some Hyundai/Kia models
Future: Most engines moving to GDI for efficiency and emission compliance.

## Slide 20: The Fuel Injector – How It Works
Let's zoom in on the fuel injector itself:
Construction: — Solenoid coil: Electromagnetic coil
Pintle (needle valve): Seals fuel nozzle
Spring: Keeps valve closed (normally closed)
Nozzle: Atomizes fuel into fine spray
Operation:
ECU sends pulse (e.g., 5V for 4 ms)
Solenoid energized → Creates magnetic field
Pintle lifts → Opens nozzle
Fuel sprays under pressure (atomized)
Pulse ends → Solenoid de-energizes
Spring closes pintle → Fuel flow stops
Precision: — Typical injector can meter 0.5 mg of fuel accurately
Response time: <1 ms (open/close)
Operates millions of times over vehicle life (very reliable)
Control: Injector is purely ON/OFF device. Quantity controlled by pulse duration.

## Slide 21
#### Part 3: Air Intake Systems & Emissions (Slides 21-24, ~10 minutes)

## Slide 22: Air Intake System Components
Fuel is only half the equation. We need AIR (which contains oxygen for combustion):
Air Intake System Components:
1. Air Filter: — Removes dust and particles from intake air
Paper or foam element
Critical: Prevents cylinder/piston wear
Clogged filter → Reduced power, poor fuel economy
Replace every 10,000-15,000 km
2. Mass Air Flow (MAF) Sensor: — Measures mass of air entering engine (kg/h)
Hot-wire or vane-type sensor
ECU uses this to calculate fuel quantity
3. Throttle Body & Valve: — Controls air flow into engine (driver's accelerator pedal)
Traditional: Cable-operated
Modern: Electronic Throttle Control (Drive-by-wire) – no cable, ECU-controlled motor
4. Intake Manifold: — Distributes air to each cylinder evenly
Variable geometry in some engines (optimize for different RPM ranges)
Air path: Atmosphere → Filter → MAF → Throttle → Manifold → Cylinders

## Slide 23: Emissions – What Comes Out?
When fuel burns, we get energy – but also emissions. Let's understand what comes out:
Exhaust Composition: — ~71% Nitrogen (N₂): Inert, from air (air is 78% N₂) – harmless
~14% CO₂ (Carbon Dioxide): Complete combustion product – greenhouse gas but not toxic
~13% H₂O (Water vapor): Complete combustion product – harmless
~1-2% Other gases: Oxygen (excess air), other compounds
Pollutants (harmful):
CO (Carbon Monoxide) → From incomplete combustion (rich mixture) → Toxic
HC (Hydrocarbons) → Unburned fuel → Smog precursor
NOx (Nitrogen Oxides) → From high temperature combustion → Acid rain, respiratory issues
PM (Particulate Matter) → Soot particles (mainly from diesel, some from GDI) → Respiratory issues, cancer risk
Goal: Minimize these four pollutants while maintaining performance and fuel economy.

## Slide 24: Emission Standards – BS4 vs BS6
Bharat Stage (BS) Standards – India's emission regulations (based on Euro standards)
Timeline: — BS4 (Euro 4): Implemented 2017
BS6 (Euro 6): Implemented April 2020 (skipped BS5)
BS6 vs BS4 – Key Differences:
| Pollutant | BS4 Limit (Petrol) | BS6 Limit (Petrol) | Reduction |
|-----------|-------------------|-------------------|-----------|
| NOx | 60 mg/km | 60 mg/km | - |
| HC + NOx | 100 mg/km | 100 mg/km | - |
| PM | - | 4.5 mg/km | NEW |
| CO | 1000 mg/km | 1000 mg/km | - |
For Diesel (Stricter):
| Pollutant | BS4 Limit | BS6 Limit | Reduction |
|-----------|----------|----------|-----------|
| NOx | 250 mg/km | 80 mg/km | —68% |
| PM | 25 mg/km | 4.5 mg/km | —82% |
Technologies Required for BS6: — Gasoline: GDI engines need Gasoline Particulate Filter (GPF)
Diesel: Selective Catalytic Reduction (SCR) for NOx, Diesel Particulate Filter (DPF)
Both: Improved catalytic converters, advanced O₂ sensors, precise fuel injection
Impact: Cleaner air, but higher vehicle costs (~₹20,000-40,000 more per vehicle).

## Slide 25: Complete Fuel Management System
Let's see the complete picture of modern engine fuel management:
INPUT SENSORS: — MAF sensor → Air mass flow
TPS → Throttle position (driver demand)
Crankshaft sensor → Engine RPM
Coolant temp → Engine temperature
O₂ sensor → Exhaust oxygen (AFR feedback)
ECU PROCESSING: — Calculates base fuel quantity (mass airflow / target AFR)
Applies corrections (temp, altitude, acceleration, etc.)
Determines injection timing and duration
Adjusts based on O₂ sensor feedback (closed-loop)
ACTUATORS: — Fuel injectors → Precise fuel delivery (pulse width control)
(Ignition coils → Spark timing – related system)
EMISSIONS CONTROL: — 3-way catalytic converter → Reduces CO, HC, NOx
O₂ sensor ensures λ=1 for optimal conversion
Performance Optimization: — BSFC map guides transmission gear selection
ECU optimizes for: Power (when needed) or Economy (when possible)
This is a complete control system – sensing, computation, actuation, and feedback!

## Slide 26: Solving Today's Challenges
Let's solve the challenges from the beginning:
Challenge 1: Identify optimal regions on BSFC map
[Point to actual BSFC map]:
Best fuel economy: 2000-3000 RPM, 60-80% max torque → BSFC ~230-250 g/kW·h
Maximum power: 5000-6500 RPM, 100% max torque → BSFC ~350-400 g/kW·h
Why max power wastes fuel: Operating far from optimal BSFC island → 40-50% more fuel per kW
Driving recommendation: Use highest gear that allows smooth acceleration → keeps engine in low-BSFC zone.
Challenge 2: Fuel injection strategy for different conditions
| Condition | AFR Target | λ | Fuel Pulse Width | Why |
|-----------|------------|---|------------------|-----|
| Cruising | 16:1 | 1.09 | ~3 ms | Lean for economy |
| Normal driving | 14.7:1 | 1.00 | ~4 ms | Stoichiometric for cat converter |
| Full power | 12.5:1 | 0.85 | ~6 ms | Rich for power + cooling |
| Cold start | 10:1 | 0.68 | ~8 ms | Rich for poor evaporation |
Control: — MAF measures 8 g/s air flow
For λ=1: Need 8/14.7 = 0.544 g/s fuel
Injector delivers ~10 mg/pulse → Need 54.4 pulses/sec → Matches 4-cyl engine at 2720 RPM ✓
ECU does this calculation every engine cycle!

## Slide 27: Key Takeaways Summary
Let's summarize today's learning:
ENGINE PERFORMANCE MAPS:
✓ BSFC map shows fuel efficiency at every RPM/torque combination
✓ Optimal zone (low BSFC island): ~2000-3000 RPM, medium-high load
✓ Operating in optimal zone improves fuel economy by 30-40% vs random driving
✓ Transmission helps keep engine in optimal zone
FUEL DELIVERY SYSTEMS:
✓ Air-fuel ratio: 14.7:1 stoichiometric for gasoline
✓ Rich mixture (~12:1) for max power, lean mixture (~16:1) for economy
✓ Evolution: Carburetor → MPFI → GDI (increasing precision and efficiency)
✓ MPFI: One injector per cylinder, port injection
✓ GDI: Direct injection into cylinder, higher efficiency but more complex
AIR INTAKE & EMISSIONS:
✓ Air intake: Filter → MAF → Throttle → Manifold
✓ Four main pollutants: CO, HC, NOx, PM
✓ BS6 (2020): Much stricter than BS4, especially NOx and PM for diesel
✓ 3-way catalytic converter: >95% reduction when λ=1
✓ Closed-loop control with O₂ sensor essential for emission compliance
You can now understand complete engine optimization from performance to emissions!

## Slide 28: Connection to Next Sessions
We've now completed the engine module (Sessions 4-6):
Session 4: How engines generate torque (mechanical operation)
Session 5: How to keep them alive (cooling + lubrication)
Session 6 (today): How to optimize performance (fuel management + emissions)
Next: Transmission Systems (Sessions 7-8)
Session 7: Transmission Fundamentals
Why we need gearboxes (connect back to BSFC maps!)
Gear ratio calculations
Manual vs automatic transmissions
Differential and final drive
Session 8: Advanced Transmission & Electric Powertrains
CVT, DCT (Dual-Clutch Transmission)
Hybrid powertrains (Toyota Prius architecture)
Electric vehicle powertrains (Tesla, Nissan Leaf)
Comparison: ICE vs Hybrid vs BEV
Connection: Engine generates torque → Transmission adapts it to wheels → Complete powertrain understanding.

## Slide 29: 📊 PPT DESIGN GUIDANCE
Visual Elements to Include:
Assignment (Due before Session 7):
Problem 1: An engine is operating at 3000 RPM, producing 100 Nm torque. Fuel consumption rate is 8 kg/h.
a) Calculate power output (kW)
b) Calculate BSFC (g/kW·h)
c) Is this efficient operation? (Compare to typical BSFC values)
Problem 2: For a 4-cylinder MPFI engine at 4000 RPM, intake air mass flow is 60 kg/h.
a) Calculate required fuel mass flow rate for λ=1 (stoichiometric) operation
b) If each cylinder fires once per 2 crankshaft revolutions, how many injections per second per cylinder?
c) If injector delivers 10 mg fuel per pulse, calculate required pulse width in ms (assume steady flow during pulse)
Problem 3: Research and compare:
a) Find BS4 and BS6 emission limits for one pollutant of your choice (petrol or diesel)
b) Calculate percentage reduction from BS4 to BS6
c) What technology changes are needed to meet the stricter limits?
Discussion Questions for Q&A: — Why can't we always operate at the best BSFC point?
What are the trade-offs between MPFI and GDI systems?
How do turbochargers affect the BSFC map? (Preview: They allow downsizing while maintaining power)
Why is cold-start emission control challenging?
30 minutes for your questions. —--
Consistency: Maintain professional engineering template from Sessions 1-5
Technical Professionalism: Clear performance maps, system diagrams, chemical equations
Color coding: — Blue for efficiency zones on BSFC maps
Red for high BSFC (inefficient) zones
Green for emission control components
Orange for sensors/actuators
Font sizes: BSFC map labels must be very readable (20pt minimum)
Slide 10: BSFC map explanation – Students must understand how to read this
Slide 15: AFR requirements table – Core reference
Slide 18: MPFI system diagram – Most common system
Slide 23: BS4 vs BS6 comparison – India-specific relevance
Slide 25: Complete system integration – Big picture
Slide 28: Summary – Comprehensive reference
Slide 11: Animated pointer showing different operating points on BSFC map as you discuss scenarios
Slide 20: Fuel injector animation (solenoid actuation, fuel spray)
Slide 24: Catalytic converter reaction animation
Slide 25: Build animation showing sensor → ECU → actuator → emissions flow
Use color highlighting for emphasis on BSFC maps
Real BSFC maps: From Honda, Toyota, or other manufacturers (find in technical papers or SAE documents)
Component photos: Fuel injectors, throttle body, MAF sensor, catalytic converter cutaway
System diagrams: Complete fuel system schematic with all sensors and actuators
Graphs: Torque/power curves overlaid on BSFC contours
Comparison tables: Carburetor vs MPFI vs GDI, BS4 vs BS6
Chemical equations: Combustion reaction, catalytic converter reactions

## Slide 30: 🎯 INSTRUCTOR NOTES
Safety/Ethics Notes:
Performance-driven: Start with BSFC maps – show WHY precise fuel control matters (efficiency!)
Evolution narrative: Carburetor → MPFI → GDI shows technological progression
System integration: Emphasize sensors-ECU-actuators-feedback loop (electronics engineering!)
Real-world relevance: BS6 compliance, fuel economy, real driving scenarios
Balance theory and application: Chemical equations explained simply, then applied to control strategies
Challenge 1: "What's the difference between rich and lean? Why not always use stoichiometric?"
How to address: Use performance triangle (power/economy/emissions) – different goals need different AFR. Stoichiometric best for emissions (cat converter), rich for power (cooling + more fuel energy), lean for economy (burn all fuel efficiently). Show data: power increases ~10% with rich mixture.
Challenge 2: "How does ECU 'know' how much fuel to inject?"
How to address: Walk through calculation step-by-step:
MAF measures air (e.g., 10 g/s)
Target AFR set (e.g., 14.7:1)
Required fuel = 10/14.7 = 0.68 g/s
Convert to injector pulse width based on injector flow rate
Show that it's pure math, done in real-time.
Challenge 3: "Why do GDI engines have particulate emissions? I thought that was only diesel!"
How to address: Explain that direct injection can cause localized rich zones if fuel doesn't mix perfectly with air → incomplete combustion → soot formation. MPFI has more time for air-fuel mixing (in intake manifold). GDI trades mixing time for efficiency gains. BS6 requires GPF to capture particles.
Challenge 4: "If λ=1 is best for emissions, why not always use it?"
How to address: Cat converter works best at λ=1, but:
Full power needs rich (λ=0.85) for cooling and maximum energy release
Cold start needs rich (poor fuel evaporation)
Cruising can use lean (λ=1.05-1.10) for economy IF you have NOx trap (expensive)
Most modern cars stay at λ=1 most of the time (best compromise).
If running short: — Condense BSFC map practice (Slide 13) – show solution without student work time
Combine carburetor history (Slide 16) with EFI intro (Slide 17)
Reduce detail on GDI challenges (Slide 19)
Move BS4 vs BS6 detailed table to assignment reading
If running long: — Move AFR calculation practice to assignment
Defer fuel injector mechanical details to Q&A
Reduce time on emission chemistry (just show reactions, don't explain mechanisms)
Core content (must cover): — Slides 9-12 (BSFC maps – absolutely critical for understanding efficiency)
Slides 14-15 (AFR requirements – foundation)
Slide 18 (MPFI system – most common)
Slide 23 (BS6 standards – India-specific and current)
Slide 25 (System integration – big picture)
Slide 6: Ask "Has anyone tracked their fuel economy? What factors affect it?" (driving style, maintenance, traffic)
Slide 10: Work through BSFC map reading together – point to different zones, ask students to estimate BSFC values
Slide 15: Poll: "What AFR would you use for: highway cruising? Climbing steep hill? Starting in winter?" (Get student predictions first)
Slide 18: Ask "How does ECU know which cylinder to inject into right now?" (Crankshaft position sensor!)
Slide 26: Interactive calculation: Given air flow, calculate fuel pulse width together
Q&A: Be ready for questions about:
Turbocharging: How it affects BSFC (allows downsizing, can improve efficiency in optimal zone)
Hybrid systems: How they keep engine in optimal BSFC (preview of Session 8)
Flex-fuel engines: How ECU adapts to ethanol blends (E10, E85) – different stoichiometric ratio
Diesel vs petrol: Why diesel engines more efficient (higher compression, diesel BSFC ~200 vs petrol ~240)
Emissions impact: Show connection between NOx and respiratory health, PM and cancer risk – why regulations matter
Fuel economy: Economic impact (fuel costs ~40-50% of vehicle operating cost in India)
Tampering: Illegal to remove catalytic converters or modify emission controls (BS6 compliance required by law)
Real-time emissions monitoring: BS6 vehicles must have OBD-II with emissions fault detection

## Slide 31: ✅ Session Success Criteria
Students leave able to:
✓ Interpret BSFC maps and identify optimal operating regions for efficiency
✓ Explain air-fuel ratio requirements and stoichiometric combustion concept
✓ Compare carburetor and fuel injection systems with advantages/disadvantages
✓ Describe MPFI and GDI systems and their operation
✓ Explain air intake system components and their functions
✓ Describe main emission types and BS4 vs BS6 requirements
Most importantly: Students understand the complete fuel management system as an integrated control problem (sensors → ECU → actuators → emissions), can read performance maps to identify efficient operation, and appreciate the engineering trade-offs between power, economy, and emissions.

## Slide 32: 📝 ADDITIONAL NOTES
Electronic Control Deep Dive:
Session 4: Introduced engine torque/power – Session 6 shows how to optimize power delivery through fuel control
Session 5: Cooling system – Session 6 explains how rich AFR for max power requires extra cooling
Sessions 1-3: Power requirements calculated – Session 6 shows how BSFC determines fuel consumption to deliver that power
Throughout session, mention gear selection for BSFC optimization. At end: "We know optimal RPM zones exist (BSFC maps). But vehicle speed varies from 0-120 km/h. Next sessions: How transmissions let us stay in optimal zones regardless of vehicle speed.
Eco-driving: How understanding BSFC improves real fuel economy (accelerate gently, use high gears, anticipate stops)
BS6 transition: What changed in 2020 (vehicles more expensive but cleaner)
Fuel quality: How poor fuel (low octane, contamination) affects performance and emissions
Diagnostics: How to interpret Check Engine Light related to fuel system (lean/rich fault codes)
For electronics students, emphasize:
Closed-loop control: O₂ sensor feedback is classic control system (measure → compare → adjust)
Real-time processing: ECU updates fuel calculation every engine cycle (~100 Hz at 3000 RPM)
Sensor fusion: Combining MAF, TPS, temp, RPM to infer engine state
Actuator control: PWM-like pulse width control of injectors
Fault tolerance: How ECU handles sensor failures (backup strategies, limp-home mode)
This bridges mechanical and electrical domains perfectly.

## Slide 33
End of Session 6 Framework