## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 7: Transmission Systems - Part 1'

## Slide 2: Transmission Systems - Part 1
Session 7 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 7. Today we answer a critical question: Why can't we connect the engine directly to the wheels? Why do we need this complex device called a transmission?

## Slide 4: The Problem - Engine vs Wheel Requirements
Let me show you the fundamental mismatch between what engines produce and what wheels need:
ENGINE CHARACTERISTICS (from Sessions 4-6):
Operates from ~800 RPM (idle) to ~6000 RPM (redline)
Peak torque at ~4000 RPM (let's say 150 Nm)
Can't produce significant torque below ~1500 RPM
Problem: Needs to be spinning to make torque!
WHEEL REQUIREMENTS: — At standstill: Need MAXIMUM torque to overcome inertia
At 120 km/h: Wheels spinning at ~800 RPM
At 20 km/h: Wheels spinning at ~130 RPM
Problem: Wheels need high torque at low speeds, low torque at high speeds
The mismatch: Engine makes power at high RPM, but vehicle needs torque at low wheel speeds.
Solution: A transmission – a mechanical device that multiplies torque and changes speed ratios.

## Slide 5: Real-World Demonstration
Let me illustrate with a real car – Honda Civic:
Accelerating from 0-100 km/h:
WITHOUT transmission (impossible, but hypothetically):
At 0 km/h: Engine at 0 RPM → No torque → Car doesn't move!
To move: Need to keep engine at 4000 RPM while wheels at 0 RPM → Impossible!
WITH 6-speed transmission: — 0-20 km/h: 1st gear → Engine at 3000 RPM → Wheels at 130 RPM → High torque
20-40 km/h: 2nd gear → Engine at 3000 RPM → Wheels at 260 RPM → Good torque
40-60 km/h: 3rd gear → Engine at 3000 RPM → Wheels at 390 RPM
60-80 km/h: 4th gear → Engine at 2800 RPM → Wheels at 520 RPM
80-100 km/h: 5th gear → Engine at 2600 RPM → Wheels at 650 RPM
See the pattern? Engine stays in optimal RPM range (2500-4000), while wheels continuously accelerate. That's what transmission does!

## Slide 6: Connection to Session 6 (BSFC Maps)
Remember in Session 6 we learned about BSFC maps? We found the 'optimal efficiency island' at 2000-3000 RPM, medium-high load.
Here's the connection:
Without a transmission, you can't stay in that optimal zone. The transmission lets you choose the right gear to:
Keep engine RPM in efficient range
Match torque requirement at wheels
Maximize fuel economy OR maximize acceleration (depending on your goal)
Modern transmissions (6, 7, 8 speeds): More gears = more opportunities to stay in optimal BSFC zone.
Today you'll learn how these gears work and how to calculate the ratios.

## Slide 7: Real-World Scenario
Here's a real engineering challenge:
Vehicle: Light commercial vehicle (think Tata Ace)
Engine: 700 cc, peak torque 38 Nm @ 4500 RPM
Vehicle mass: 900 kg (loaded)
Wheel radius: 0.28 m
Requirements:
Must be able to climb 20° slope from standstill (loaded)
Must reach 80 km/h top speed on flat road
Questions: — What torque do we need at wheels to climb 20° slope?
What gear ratio do we need in 1st gear?
What gear ratio do we need in top gear (5th)?
How many intermediate gears and what ratios?
By the end of today: You'll solve this problem completely.

## Slide 8: The Simple Gear Pair
Let's start with the simplest transmission: Two gears meshing together.
Setup: — Driver gear (input): 20 teeth, connected to engine
Driven gear (output): 60 teeth, connected to wheels
When driver rotates 1 revolution: — Driver gear: 20 teeth pass through mesh
Driven gear: Receives 20 teeth → Rotates 20/60 = 0.333 revolutions
Speed relationship: — If driver spins at 3000 RPM
Driven spins at 3000 × (20/60) = 1000 RPM
We've achieved speed reduction of 3:1 (or gear ratio = 3.0).

## Slide 9: Where Did the 'Lost' Speed Go? (Torque Multiplication!)
Here's the beautiful principle: Energy is conserved (ignoring friction).
Power in = Power out
Remember from Session 3: Power = Torque × Angular velocity
P = τ × ω
At input (driver gear): — Torque: τ_in = 50 Nm (from engine)
Speed: ω_in = 3000 RPM
Power: P_in = 50 × 3000 = 150,000 units
At output (driven gear): — Speed: ω_out = 1000 RPM (we reduced it by 3x)
Power: Pout = Pin = 150,000 units (conserved!)
Torque: τ_out = P / ω = 150,000 / 1000 = 150 Nm
Torque multiplied by 3x! (from 50 Nm to 150 Nm)
The Rule: — Gear ratio 3:1 → Speed reduction 3x → Torque multiplication 3x
τout = τin × Gear Ratio — ωout = ωin / Gear Ratio

## Slide 10: Defining Gear Ratio Mathematically
Let's formalize the math:
GEAR RATIO (GR) = ωin / ωout = Ndriven / Ndriver
Where:
ω_in = Input speed (RPM)
ω_out = Output speed (RPM)
N_driven = Number of teeth on driven gear
N_driver = Number of teeth on driver gear
For our example:
GR = 60 teeth / 20 teeth = 3.0
Relationships: — Speed: ωout = ωin / GR
Torque: τout = τin × GR × η (where η = efficiency, ~0.95-0.98 for gears)
Key insight: Higher gear ratio = More torque, Less speed (good for acceleration, hill climbing).
Lower gear ratio = Less torque, More speed (good for cruising, top speed).

## Slide 11: Example Calculation
Let's practice with a real example:
Given: — Engine speed: 4000 RPM
Engine torque: 120 Nm
Driver gear: 18 teeth
Driven gear: 54 teeth
Find: Output speed and torque
Solution:
Step 1: Calculate Gear Ratio
GR = Ndriven / Ndriver = 54 / 18 = 3.0
Step 2: Calculate Output Speed
ωout = ωin / GR = 4000 / 3.0 = 1333 RPM
Step 3: Calculate Output Torque (assuming η = 0.96)
τout = τin × GR × η = 120 × 3.0 × 0.96 = 345.6 Nm
Result: We've tripled the torque (120 → 346 Nm) while reducing speed to 1/3.

## Slide 12
#### Part 2: Transmission System Calculations (Slides 12-16, ~18 minutes)

## Slide 13: Complete Transmission Chain
A real vehicle transmission has multiple stages:
Power flow:
1. ENGINE → Torque: τengine, Speed: ωengine
2. CLUTCH → (When engaged, just passes power through)
3. GEARBOX → Gear ratio: GR_gearbox (e.g., 3.5 in 1st gear)
Speed: ωgearboxout = ωengine / GRgearbox
Torque: τgearboxout = τengine × GRgearbox
4. DIFFERENTIAL → Gear ratio: GR_diff (typically 3.5 to 4.5)
Speed: ωwheel = ωgearboxout / GRdiff
Torque: τwheel = τgearboxout × GRdiff
5. WHEELS → Convert torque to force: F = τwheel / rwheel
Overall Ratio = GRgearbox × GRdiff
Let's calculate a complete example!

## Slide 14: Complete Example - 1st Gear Acceleration
Scenario: Honda Civic accelerating in 1st gear
Given: — Engine torque: 145 Nm @ 4000 RPM
1st gear ratio: 3.6
Differential ratio: 4.1
Wheel radius: 0.32 m
Transmission efficiency: 94%
Find: Force at road from one wheel (assuming 2WD, power to 2 wheels)
Solution:
Step 1: Torque after gearbox
τ_gearbox = 145 × 3.6 = 522 Nm
Step 2: Torque after differential
τ_diff = 522 × 4.1 = 2,140 Nm
Step 3: Torque per wheel (power to 2 wheels)
τ_wheel = 2,140 / 2 = 1,070 Nm per wheel
Step 4: Apply efficiency
τwheelactual = 1,070 × 0.94 = 1,006 Nm per wheel
Step 5: Force at road
F = τwheel / rwheel = 1,006 / 0.32 = 3,144 N per wheel
Total force (both drive wheels): ~6,300 N
That's enough to accelerate a 1,300 kg car at ~4.8 m/s²! (Good acceleration)

## Slide 15: Practice Problem - You Try It!
Your turn! Try this:
Given: — Engine: 2000 RPM, 180 Nm torque
Transmission in 3rd gear, ratio = 1.8
Differential ratio = 4.3
Wheel radius = 0.30 m
Efficiency = 95%
Calculate:
Wheel RPM
Torque per wheel (assume 2WD)
Force at road per wheel
Take 2 minutes. I'll show the solution after.
[Pause for student work]
Solution:
Wheel RPM = 2000 / (1.8 × 4.3) = 258 RPM
Torque per wheel = 180 × 1.8 × 4.3 × 0.95 / 2 = 660 Nm
Force per wheel = 660 / 0.30 = 2,200 N

## Slide 16: Designing Transmission Ratios - Requirements
Now let's flip the problem: HOW to choose gear ratios?
Two constraints define the extremes:
CONSTRAINT 1: Hill Climbing (determines 1st gear) — Must produce enough wheel torque to climb steepest slope
Calculation: F_required = m × g × sin(θ) + Rolling resistance + Drag
Work backwards: F → τwheel → τengine × Ratios
This gives MINIMUM 1st gear ratio
CONSTRAINT 2: Top Speed (determines final gear) — At top speed, engine at redline (e.g., 6500 RPM)
Wheel speed must match top speed requirement
Calculation: ωwheel = vmax / r_wheel
This gives MAXIMUM top gear ratio (actually minimum value, around 0.7-1.0)
Intermediate gears: Spaced between these extremes to keep engine in optimal RPM range.
Let's work through real design example...

## Slide 17: Design Example - Small Commercial Vehicle
Design Challenge: (Remember from Slide 6?)
Vehicle: 900 kg, wheel radius 0.28 m
Engine: 38 Nm @ 4500 RPM (peak torque)
Differential ratio: 5.0 (typical for commercial vehicle)
Requirements: Climb 20° slope, 80 km/h top speed
DESIGNING 1st GEAR:
Force needed to climb 20° slope:
F = m × g × sin(20°) + F_rolling
F = 900 × 9.81 × 0.342 + (900 × 9.81 × 0.02)
F ≈ 3,020 + 177 = 3,200 N
Torque needed at wheels (both drive wheels):
τwheel = F × rwheel = 3,200 × 0.28 = 896 Nm
Working backwards to find 1st gear ratio:
τwheel = τengine × GR1st × GRdiff × η
896 = 38 × GR_1st × 5.0 × 0.94
GR_1st = 896 / (38 × 5.0 × 0.94) = 5.0
DESIGNING 5th GEAR (top gear):
Top speed = 80 km/h = 22.2 m/s
Wheel RPM at top speed: ω_wheel = v / (2πr) = 22.2 / (2π × 0.28) = 12.6 rev/s = 757 RPM
Engine at redline: 6000 RPM
Overall ratio needed: GR_overall = 6000 / 757 = 7.93
Since differential = 5.0:
GR_5th = 7.93 / 5.0 = 1.59
Summary: — 1st gear: 5.0 (for hill climbing)
5th gear: 1.59 (for top speed)
Intermediate gears (2nd, 3rd, 4th): Geometrically spaced → ~3.5, ~2.5, ~2.0
You've just designed a transmission! —--
#### Part 3: Clutch System (Slides 17-19, ~10 minutes)

## Slide 18: Why Do We Need a Clutch?
Before we look inside the gearbox, we need to understand the CLUTCH.
The problem: Engine must keep running (~800 RPM idle) even when vehicle is stopped (wheels at 0 RPM).
Without clutch: — Stop vehicle → Wheels stop → Transmission locked → Engine forced to stop → Engine stalls
To start moving: Can't shift gears while engine running (gears spinning at different speeds would clash!)
Clutch solution: Temporary disconnection device between engine and transmission
Allows engine to run while vehicle stopped
Allows gear shifting (disconnect, shift, reconnect)
Allows smooth engagement (gradually connect engine to wheels)
Operation: — Clutch engaged (pedal released): Engine connected to transmission → Power flows
Clutch disengaged (pedal pressed): Engine disconnected → Engine free, wheels free

## Slide 19: Single-Plate Clutch Construction
SINGLE-PLATE CLUTCH (most common in cars)
Key Components:
1. Flywheel: — Attached to engine crankshaft (always rotating with engine)
Heavy disc, smooths engine power pulses
Provides friction surface
2. Clutch Disc (Friction Disc): — Friction material both sides (like brake pads)
Splined hub connects to transmission input shaft
Can slide on splines but rotates with input shaft
3. Pressure Plate: — Spring-loaded plate that presses clutch disc against flywheel
Provides clamping force via diaphragm spring
4. Release Bearing: — Pushes on diaphragm spring when clutch pedal pressed
Releases clamping force
OPERATION:
Engaged (pedal released): — Diaphragm spring pushes pressure plate
Clutch disc clamped between flywheel and pressure plate
Friction connects engine to transmission → Power flows
Disengaged (pedal pressed): — Release bearing pushes diaphragm spring center inward
Pressure plate pulls back
Clutch disc free → Engine and transmission disconnected

## Slide 20: Clutch Engagement - The Friction Zone
The 'biting point' or 'friction zone':
When you slowly release clutch pedal:
Fully pressed: No contact → 0% torque transfer
Friction zone (~20-40% release): Partial contact → 20-80% torque transfer (slipping)
Fully released: Full clamping → 100% torque transfer (locked)
Why slipping is useful: — Starting from standstill: Engine at 1500 RPM, wheels at 0 RPM
Gradual engagement lets speeds synchronize smoothly
Prevents stall or violent jerk
Torque capacity:
Tmax = μ × N × Fclamp × R_mean
Where:
μ = friction coefficient (~0.3-0.4)
N = number of friction surfaces (2 for single-plate)
F_clamp = clamping force from spring (~3000-5000 N)
R_mean = mean radius of friction surface
Typical clutch capacity: 250-400 Nm (must exceed peak engine torque!)

## Slide 21
#### Part 4: Manual Gearbox Internals (Slides 20-24, ~12 minutes)

## Slide 22: Manual Transmission Overview
Let's look inside a manual transmission:
Main Components:
1. Input Shaft: — Connected to clutch disc
Receives power from engine (when clutch engaged)
2. Output Shaft: — Delivers power to differential/wheels
Parallel to input shaft
3. Gear Sets: — Multiple pairs of gears, always meshing (constant mesh design)
Different sized pairs for each gear ratio
Example: 1st gear pair (20T/60T), 2nd gear pair (25T/50T), etc.
4. Synchronizers (Synchromesh): — Allow smooth gear engagement
Match speeds before locking
5. Shift Forks & Mechanism: — Moved by gear lever
Slide synchronizers to select gears
Key Principle: Gears are ALWAYS meshing and spinning. Selection is done by locking the right gear to the output shaft.

## Slide 23: Constant Mesh Gearbox Operation
CONSTANT MESH principle (all modern manuals):
Setup: — Input shaft has gears fixed to it (rotate with input shaft always)
Output shaft has gears that free-wheel on bearings (not locked)
Synchronizers on output shaft can lock selected gear
Example - Selecting 2nd Gear:
Before selection (in neutral): — Input shaft spinning at engine speed
All gears on input shaft spinning
Output shaft gears spinning (driven by meshing input gears) BUT freewheeling
Output shaft stationary (no gear locked)
Shifting to 2nd:
Press clutch → Disconnect engine
Move shift lever → Shift fork moves 2nd gear synchronizer
Synchronizer matches speeds → Friction brings output shaft to 2nd gear speed
Synchronizer locks → 2nd gear now locked to output shaft
Release clutch → Power flows: Engine → Input shaft → 2nd gear pair → Output shaft → Wheels
Result: 2nd gear ratio now active!

## Slide 24: Synchromesh Mechanism
SYNCHROMESH = Synchronizer Mechanism
Problem it solves:
When shifting (e.g., from 2nd to 3rd):
3rd gear on output shaft spinning at one speed (freewheeling)
Output shaft spinning at different speed (locked to 2nd gear)
Can't just lock them together → Would clash, grind gears!
Synchromesh operation:
Stage 1: Synchronizing (friction cone contact) — Shift fork pushes synchronizer sleeve toward 3rd gear
Friction cone on synchro ring contacts friction cone on gear
Friction gradually matches speeds (synchro ring rotates slightly)
Stage 2: Locking (dog teeth engagement) — Once speeds matched (synchro ring aligns)
Continued push slides sleeve further
Dog teeth on sleeve engage dog teeth on gear
Gear now locked to output shaft
Benefits:
✓ Smooth, clash-free shifting
✓ No need to match speeds manually (like old non-synchro boxes)
✓ Fast shifts possible
Modern transmissions: All forward gears have synchros (reverse often doesn't, hence the 'crunch' if you don't stop completely!)

## Slide 25: Power Flow Analysis - 1st Gear Example
Let's trace power flow with 1st gear engaged:
Power Path:
Engine → Clutch (engaged) → Input shaft spinning
Input shaft → 1st gear on input shaft (fixed to shaft) → 1st gear spinning
1st gear (input) meshes with 1st gear (output) → 1st gear on output shaft driven
1st gear (output) → Synchronizer locked → Output shaft forced to rotate with 1st gear
Output shaft → Differential → Wheels
Meanwhile: — All other gears on input shaft also spinning (constant mesh)
All other gears on output shaft freewheeling (not locked)
Only 1st gear pair is transmitting power (because only 1st is locked to output shaft)
Shift to 2nd: — Unlock 1st synchronizer
Lock 2nd synchronizer
Now 2nd gear pair transmits power
Elegant design: Simple mechanical selection determines which ratio is active.

## Slide 26: Designing a Complete 5-Speed Manual Transmission
Let's design a complete transmission system for a passenger car:
Vehicle Specifications: — Mass: 1,200 kg
Engine: Peak torque 180 Nm @ 4000 RPM, Redline 6500 RPM
Wheel radius: 0.32 m
Performance requirements:
0-100 km/h: <10 seconds
Top speed: 180 km/h
Climb 15° slope in 1st gear
STEP 1: Determine Differential Ratio
Choose: GR_diff = 4.1 (typical for passenger car)
STEP 2: Calculate 1st Gear Ratio (hill climbing requirement)
Force for 15° slope: F = 1200 × 9.81 × sin(15°) + rolling ≈ 3,200 N — Torque at wheels: τwheel = 3200 × 0.32 = 1,024 Nm — Required GR1st: 1024 = 180 × GR_1st × 4.1 × 0.95
GR_1st = 1024 / (180 × 4.1 × 0.95) = 1.46... round to 3.5
STEP 3: Calculate 5th Gear Ratio (top speed)
Top speed 180 km/h = 50 m/s
Wheel RPM: ω_wheel = 50 / (2π × 0.32) = 24.8 rev/s = 1,490 RPM — Engine at 6500 RPM
Overall ratio: 6500 / 1490 = 4.36
GR_5th = 4.36 / 4.1 = 1.06 ≈ 1.0 (close to 1:1, common for 5th gear)
STEP 4: Design Intermediate Gears (geometric progression)
2nd: 2.4
3rd: 1.7
4th: 1.3
Final Ratios:
| Gear | Ratio | Overall (with diff) |
|------|-------|---------------------|
| 1st | 3.5 | 14.35 |
| 2nd | 2.4 | 9.84 |
| 3rd | 1.7 | 6.97 |
| 4th | 1.3 | 5.33 |
| 5th | 1.0 | 4.10 |
| Reverse | 3.8 | 15.58 |

## Slide 27: Analyzing the Design - RPM Drop During Shifts
Let's verify our design by checking RPM at different vehicle speeds:
At 100 km/h (27.8 m/s): — Wheel RPM = 27.8 / (2π × 0.32) = 828 RPM
Engine RPM in each gear: — 1st gear: 828 × 14.35 = 11,882 RPM → Way over redline! (Can't reach 100 km/h in 1st)
2nd gear: 828 × 9.84 = 8,147 RPM → Over redline (Can't sustain 100 km/h in 2nd)
3rd gear: 828 × 6.97 = 5,771 RPM → Below redline ✓ (Can reach 100 in 3rd)
4th gear: 828 × 5.33 = 4,413 RPM → Good RPM ✓
5th gear: 828 × 4.10 = 3,395 RPM → Optimal for cruising ✓
Shift points for acceleration (at redline 6500 RPM): — 1st → 2nd shift at: 6500 / 14.35 = 453 wheel RPM = 57 km/h — 2nd → 3rd shift at: 84 km/h — 3rd → 4th shift at: 112 km/h — 4th → 5th shift at: 147 km/h
RPM drop per shift: — 1st → 2nd: 6500 → (6500 × 9.84/14.35) = 4,458 RPM (drop 2042 RPM)
2nd → 3rd: 6500 → 4,603 RPM (drop 1897 RPM)
Design is good: Smooth progression, keeps engine in power band during acceleration!

## Slide 28: Key Takeaways Summary
Let's consolidate what you've mastered today:
WHY TRANSMISSIONS:
✓ Engine operates in narrow RPM range (1500-6500 RPM), wheels need 0-1500 RPM
✓ Transmission multiplies torque at low speeds, allows high speed at top end
✓ Keeps engine in optimal BSFC zone for fuel economy (Session 6 connection!)
GEAR RATIO MATHEMATICS:
✓ GR = Ndriven / Ndriver = ωin / ωout
✓ τout = τin × GR × η (torque multiplication)
✓ ωout = ωin / GR (speed reduction)
✓ Overall ratio = GRgearbox × GRdifferential
CLUTCH SYSTEM:
✓ Disconnects engine from transmission for gear shifting and stopping
✓ Single-plate clutch: Flywheel + Friction disc + Pressure plate
✓ Friction zone allows smooth engagement
MANUAL GEARBOX:
✓ Constant mesh design: All gears always meshing, select by locking to output shaft
✓ Synchromesh matches speeds for smooth, clash-free shifting
✓ Power flows through selected gear pair only
TRANSMISSION DESIGN:
✓ 1st gear ratio determined by hill climbing requirement
✓ Top gear ratio determined by top speed and redline RPM
✓ Intermediate gears spaced geometrically
You can now design and analyze complete manual transmissions!

## Slide 29: Connection to Next Session
Today we mastered manual transmissions – driver controls gear selection.
Next Session (Session 8): Advanced Transmissions & Powertrain Alternatives
Part 1: Automatic Transmissions — Torque converter (replaces clutch)
Planetary gear sets (compact, multiple ratios)
Hydraulic/electronic control (no clutch pedal!)
Part 2: Modern Transmission Technologies — CVT (Continuously Variable Transmission) – infinite ratios!
DCT/DSG (Dual-Clutch Transmission) – fast shifts, no power loss
AMT (Automated Manual Transmission) – robotized manual
Part 3: Differential & Drivetrain — How differential allows wheels to spin at different speeds (cornering)
FWD vs RWD vs AWD configurations
Part 4: Electric Powertrains (Preview) — Electric motors: Instant torque from 0 RPM
Do EVs even need multi-speed transmissions? (Mostly single-speed!)
Hybrid architectures (Toyota Prius example)
Connection: Manual transmission fundamentals (gears, ratios, torque multiplication) apply to ALL transmission types – today's foundation supports everything!

## Slide 30: 📊 PPT DESIGN GUIDANCE
Visual Elements to Include:
Assignment (Due before Session 8):
Problem 1: A vehicle has the following specifications:
Mass: 1,500 kg
Engine peak torque: 200 Nm @ 3500 RPM, Redline: 6000 RPM
Wheel radius: 0.33 m
Must climb 18° slope from standstill
Top speed requirement: 150 km/h
Design a 5-speed manual transmission:
a) Calculate required 1st gear ratio (assume differential ratio = 4.2, efficiency = 95%)
b) Calculate required 5th gear ratio
c) Design intermediate gear ratios (2nd, 3rd, 4th) using geometric progression
d) At what vehicle speed should you shift from 2nd to 3rd if accelerating at redline?
Problem 2: For a gear pair with driver gear (25 teeth) and driven gear (75 teeth):
a) Calculate gear ratio
b) If input is 3600 RPM and 150 Nm torque, find output RPM and torque (assume 96% efficiency)
c) If driver gear has pitch circle diameter 80 mm, what is driven gear diameter?
Problem 3: Explain in your own words:
a) Why does engine RPM drop when you shift to a higher gear at constant vehicle speed?
b) What would happen if you tried to shift from 5th to 1st at 100 km/h? (Hint: Calculate engine RPM)
c) Why is synchromesh necessary in modern transmissions?
Bonus: Research and sketch the gear arrangement (number of teeth for each gear pair) for any real car's transmission. Calculate the overall ratios and verify against published specs.
Discussion Questions for Q&A: — Why are modern cars moving to 6, 7, 8 or even 10-speed transmissions?
What are the advantages and disadvantages of manual vs automatic transmissions?
How do motorcycles achieve 6 speeds in such a small gearbox? (Sequential shifting)
What is double-clutching and why was it necessary in old trucks?
30 minutes for your questions. —--
Consistency: Maintain professional engineering template from Sessions 1-6
Technical Professionalism: Clear gear diagrams, cutaway illustrations, calculation worksheets
Color coding: — Blue for input shaft and components
Orange for output shaft and components
Green for power flow arrows (when gear engaged)
Gray for freewheeling components
Font sizes: Calculation steps must be clear (18-20pt minimum)
Slide 2: Engine vs wheel mismatch problem – Establishes need
Slide 10: Gear ratio formulas – Core mathematics
Slide 16: Complete design example – Real application
Slide 21: Constant mesh operation – Understanding internals
Slide 25: Full 5-speed design – Integration of all concepts
Slide 28: Summary – Comprehensive reference
Slide 8-9: Animated gear meshing showing speed reduction and torque multiplication
Slide 18: Clutch engagement/disengagement animation (pressure plate movement)
Slide 21: Synchronizer sliding and locking animation
Slide 23: Power flow highlighting (show power path lighting up in one gear)
Use color highlighting to trace power flow through transmission
Gear diagrams: Clear spur gear illustrations with teeth counts labeled
Cutaway photos: Real manual transmission cutaways (ZF, Getrag, etc.)
Component photos: Real clutch assembly, synchromesh, shift forks
Calculation worksheets: Step-by-step calculations with boxes and arrows
Comparison tables: Gear ratio comparisons, Honda Civic example
Power flow diagrams: Show which components rotate in each gear

## Slide 31: 🎯 INSTRUCTOR NOTES
Safety/Ethics Notes:
Problem-driven: Start with mismatch between engine and wheel needs (why?)
Mathematics-heavy: This is calculation-intensive – work through examples step-by-step
Build from simple to complex: Single gear pair → Complete transmission
Real-world validation: Compare designs to actual vehicles (Honda Civic)
Hands-on feel: If possible, bring real gears, clutch disc, synchromesh to show students
Challenge 1: "Why does higher gear ratio mean more torque but lower speed? Shouldn't 'higher' mean faster?"
How to address: Clarify terminology: "Higher gear ratio" (e.g., 3.5) means more reduction, not higher gear number. "5th gear" has LOWER ratio (~1.0) than "1st gear" (3.5). Emphasize: Gear ratio = reduction ratio. Higher reduction = more torque, less speed.
Challenge 2: "In calculations, when do I multiply and when do I divide by gear ratio?"
How to address: Always work from definitions:
Speed: ωout = ωin / GR (divide to reduce speed)
Torque: τout = τin × GR (multiply to increase torque)
Make students write this on every problem.
Challenge 3: "Why are all gears meshing? Doesn't that cause power loss and noise?"
How to address: Explain constant mesh advantages:
Smoother shifting (synchro can match speeds before locking)
Stronger (gears always engaged, no shock loading)
Modern design minimizes losses through good bearings and lubrication
Trade-off: Slight efficiency loss (~2-4%) vs improved reliability and shift quality
Challenge 4: "I don't understand how synchronizer works – there are so many parts!"
How to address: Simplify to two stages:
Friction stage: Cone surfaces match speeds through friction (like mini-clutch)
Locking stage: Once matched, dog teeth engage mechanically
Use animation or physical model if available.
If running short: — Condense clutch details (Slide 19) – just show operation, skip torque capacity calculation
Combine Slides 20-21 (gearbox overview and constant mesh operation)
Move synchromesh details (Slide 22) to assignment reading
Reduce time on shift mechanism (Slide 24)
If running long: — Move complete design example (Slide 25) calculations to assignment (just show results)
Defer RPM drop analysis (Slide 26) to Q&A discussion
Reduce time on Honda Civic comparison (Slide 27)
Core content (must cover): — Slides 2-3 (Why transmission needed – critical motivation)
Slides 8-11 (Gear ratio fundamentals – absolute core)
Slide 13 (Complete calculation example – must work through)
Slide 16 (Design example – application)
Slides 17-18 (Clutch basics)
Slides 20-21 (Constant mesh operation)
Slide 2: Ask "Has anyone driven a car without enough power for a hill? What happens?" (Engine bogs down, need lower gear)
Slide 11: Work through calculation together on board – pause between steps, ask students for next step
Slide 14: Give students 2 minutes to try problem – competitive element
Slide 16: Interactive design – give parameters, ask students to estimate 1st gear ratio before calculation
Slide 23: Trace power flow together – point at diagram, ask "where does power go next?
Q&A: Be ready for questions about:
Sequential gearboxes: How motorcycles and race cars shift (linear pattern, no searching for gears)
Dog-leg gearboxes: Why some sports cars have 1st gear in unusual position
Gear whine: Why race cars and straight-cut gears make noise (no helical teeth)
Reverse gear: Why it doesn't have synchro (crashes if you don't stop first)
Clutch abuse: Riding clutch (partial engagement) causes wear, overheating, premature failure
Money shifting: Accidentally shifting to wrong gear (e.g., 2nd instead of 4th) can over-rev engine → catastrophic damage
Maintenance: Transmission fluid change intervals, clutch replacement indicators
Driving efficiency: Proper gear selection saves fuel – connection to BSFC maps (Session 6)

## Slide 32: ✅ Session Success Criteria
Students leave able to:
✓ Explain need for transmission in matching engine characteristics to wheel requirements
✓ Calculate gear ratios and analyze effect on torque and speed
✓ Describe clutch construction and operation
✓ Explain manual gearbox construction (constant mesh, synchromesh)
✓ Design transmission gear ratios for given performance requirements
✓ Analyze power flow through manual transmission in any gear
Most importantly: Students understand the complete manual transmission system as a mechanical solution to the engine-wheel mismatch problem, can perform gear ratio calculations confidently, and can design transmissions for real vehicle requirements.

## Slide 33: 📝 ADDITIONAL NOTES
Connection to Electronics:
Session 3: Calculated power requirements → Session 7 shows how transmission delivers that power at different speeds
Session 4: Engine torque curves → Session 7 uses those to determine gear ratios
Session 6: BSFC maps and optimal operating zones → Session 7 shows how transmission keeps engine in those zones
Throughout session, mention limitations of manual transmission:
Driver must shift (attention, skill required)
Shift interrupts power delivery (acceleration pause)
Only discrete ratios available (5-6 options)
Session 8 will show how modern transmissions address these limitations.
Sports cars: Close-ratio gearboxes (smaller ratio steps) keep engine in power band
Trucks: Wider 1st gear (5.0+) for heavy loads and steep hills
Economy cars: Taller gearing (lower numerical ratio) for better highway fuel economy
Track days: How proper gear selection improves lap times (staying in power band)
Bring real gears: Show two gears meshing, count teeth, calculate ratio
Clutch disc: Show friction material, splined hub, explain wear
Synchromesh unit: Disassembled synchro showing friction cone and dog teeth
Shift mechanism: Model or actual linkage showing how gear lever connects to forks
These make abstract concepts concrete and memorable.
Manual transmission sensors: Gear position sensor (for ECU to know current gear)
Clutch position sensor: For engine torque management during shifts
Rev-matching systems: Modern manuals with auto-blip on downshift (electronics controlling throttle)
Hill start assist: Uses sensors and brakes to prevent rollback
Manual transmissions are increasingly electronically assisted even though mechanically operated!

## Slide 34
End of Session 7 Framework