## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 8: Transmission Systems - Part 2 & Powertrain Alternatives'

## Slide 2: Transmission Systems - Part 2 & Powertrain Alternatives
Session 8 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 8 – the final session of our Powertrain Systems module. Today we explore modern transmission technologies and look ahead to the future: electric powertrains.

## Slide 4: The Evolution of Transmissions
Let's trace the evolution:
Session 7 (Last week): Manual transmission
Driver controls gear selection (skill required)
Power interruption during shifts (clutch disengagement)
5-6 discrete gear ratios
Advantages: Driver control, simplicity, lower cost
Disadvantages: Requires skill, interrupted power delivery, tiring in traffic
Today's technologies solve these limitations:
1. AUTOMATIC TRANSMISSION (1940s+)
No clutch pedal, auto gear selection
Smooth, uninterrupted power (torque converter)
2. CVT (Continuously Variable, 1990s+)
INFINITE gear ratios (not discrete!)
Always optimal ratio for efficiency
3. DCT/DSG (Dual-Clutch, 2000s+)
Fast shifts (<100ms) with no power loss
Combines manual efficiency with automatic convenience
4. ELECTRIC POWERTRAINS (2010s+)
Often SINGLE-SPEED (no multi-gear transmission needed!)
Instant torque from 0 RPM
Today you'll understand all of them.

## Slide 5: The Differential Puzzle
But before modern transmissions, let me show you a problem we haven't solved yet:
Scenario: Car turning a corner
[Show diagram]:
Inside wheel (left, turning left): Travels shorter distance, needs to spin SLOWER
Outside wheel (right): Travels longer distance, needs to spin FASTER
Problem: If both wheels on same axle connected to same transmission output shaft (rigidly), they'd be FORCED to spin at same speed!
Result: — Inside wheel would slip/drag (forced to spin too fast)
Outside wheel would slip (forced to spin too slow)
Tire wear, poor handling, binding forces
Solution: A device called the DIFFERENTIAL – allows two wheels to spin at different speeds while both receive power.
We'll understand how this mechanical marvel works today!

## Slide 6: Why This Matters for Electronics Engineers
Why do automotive electronics engineers need to understand transmissions?
Because modern transmissions are electronically controlled:
Automatic Transmission: — TCU (Transmission Control Unit) controls shifts based on:
Throttle position
Vehicle speed
Engine load
Driver mode selection (Eco / Sport / Manual)
Solenoid-controlled valves manage hydraulic pressure
CVT: — Stepper motor controls pulley ratio
ECU optimizes for target engine RPM (BSFC sweet spot!)
DCT/DSG: — Dual clutches electronically actuated
Predictive shift logic (pre-selects next gear)
Electric Powertrains: — Inverter controls motor speed and torque
Battery Management System (BMS)
Regenerative braking control
You'll design these control systems – must understand the mechanics you're controlling!

## Slide 7: Real-World Scenario
Let me give you three very different vehicle scenarios:
Scenario A: Luxury Sedan (Mercedes S-Class)
Requirement: Smooth, effortless driving in city traffic
Challenge: Frequent stop-start, must be comfortable, imperceptible shifts
Question: What transmission type is best?
Scenario B: Performance Sports Car (Porsche 911)
Requirement: Fastest possible acceleration, minimal shift time
Challenge: Track use, aggressive driving, maximum performance
Question: What transmission technology?
Scenario C: City Electric Car (Nissan Leaf)
Electric motor produces 320 Nm torque from 0 RPM
Top speed: 140 km/h
Question: How many gears do we need?
By the end of today: You'll be able to select the optimal transmission for each scenario and justify your choice with engineering reasoning.

## Slide 8: Automatic Transmission Overview
AUTOMATIC TRANSMISSION – the most popular transmission type worldwide.
Key Difference from Manual: — No clutch pedal (torque converter replaces clutch)
Automatic gear selection (driver doesn't shift, TCU does)
Planetary gear sets (instead of parallel shaft gears like manual)
Two Main Components:
Torque Converter – Fluid coupling for smooth power transfer
Planetary Gear Sets – Compact gears providing multiple ratios
Let's understand each.

## Slide 9: Torque Converter – The Fluid Clutch
TORQUE CONVERTER replaces the clutch in automatic transmissions.
Three Main Components:
1. Impeller (Pump): — Connected to engine crankshaft (always spinning with engine)
Centrifugal pump that throws transmission fluid outward
2. Turbine: — Connected to transmission input shaft
Receives fluid from impeller → Spins → Powers transmission
3. Stator: — Stationary (or one-way clutch)
Redirects fluid flow from turbine back to impeller efficiently
Key function: Provides TORQUE MULTIPLICATION!
How It Works:
Vehicle Stopped (Engine Idling): — Impeller spinning (engine running)
Turbine stationary (brakes holding vehicle)
Fluid circulates but turbine doesn't spin (stator redirects flow)
No rigid connection → Engine doesn't stall!
Accelerating: — Driver releases brake, presses accelerator
Engine speeds up → Impeller pumps more fluid
Turbine starts spinning → Transmission engages
Stator redirects fluid → Torque multiplication (~2-2.5x at stall!)
Cruising (Lockup): — Lockup clutch engages (mechanical connection)
Eliminates fluid slippage → Improved efficiency
Acts like rigid coupling (like manual clutch fully engaged)

## Slide 10: Torque Converter Performance Characteristics
Torque Converter Performance:
Torque Multiplication: — At stall (0 speed): Torque multiplication ~2.0-2.5x
As turbine speeds up: Multiplication decreases
At coupling point (~90% impeller speed): Multiplication = 1.0x
Efficiency: — At stall: ~0% efficient (all energy creating fluid motion)
At coupling: ~85-90% efficient (fluid slippage losses)
With lockup clutch: ~98% efficient (mechanical connection)
Why Lockup Clutch? — Above ~40-50 km/h (cruising): Lockup engages
Eliminates slippage → Better fuel economy
Modern autos lock up as early as 2nd or 3rd gear
Trade-off: — Torque converter provides smoothness and torque multiplication
But: Less efficient than manual clutch (even with lockup)
This is why autos traditionally had worse fuel economy than manuals

## Slide 11: Planetary Gear Sets – Compact Multi-Ratio System
PLANETARY GEAR SET – the heart of automatic transmission.
Components:
Sun Gear (center, small gear)
Planet Gears (typically 3-4 small gears meshing with sun and ring)
Planet Carrier (holds planet gears, can rotate)
Ring Gear (outer gear, internal teeth, meshes with planets)
The Magic: By holding one component stationary and driving another, you get different ratios!
Example Ratios:
Configuration 1: 1st Gear (Reduction ~2.5:1)
Input: Sun gear (from torque converter)
Output: Carrier
Held: Ring gear (clutch/brake holds it stationary)
Planets walk around inside ring → Carrier rotates slowly → Speed reduction, torque multiplication
Configuration 2: Direct Drive (1:1 ratio)
Input: Sun gear
Output: Carrier
Locked: All components locked together (clutches)
Entire set rotates as one unit → No reduction
Configuration 3: Reverse (~2:1 reduction, opposite direction)
Input: Ring gear
Output: Carrier
Held: Sun gear
Carrier rotates opposite direction
Advantages:
✓ Compact (coaxial, nested design)
✓ Multiple ratios from single gear set (by changing what's held/driven)
✓ Smooth (always in mesh, no shift shock like manuals)
Real transmissions: Use 2-3 planetary sets to achieve 6-10 speeds!

## Slide 12: Shift Control – Hydraulics + Electronics
How does automatic transmission shift gears?
Shift Mechanism: — Different gear ratios achieved by engaging/disengaging clutches and brakes (bands)
These are hydraulically actuated (pressurized ATF – Automatic Transmission Fluid)
Control System:
Traditional (Pre-1990s): Purely Hydraulic — Governor (centrifugal valve) senses speed
Modulator senses throttle position
Hydraulic logic circuits determine shift points
Problem: Fixed shift logic, not adaptive
Modern (1990s+): Electronic Control — TCU (Transmission Control Unit) – Dedicated ECU for transmission
Sensors: — Transmission input speed (turbine speed)
Output speed (vehicle speed)
Throttle position (TPS)
Transmission fluid temperature
Gear position (PRNDL sensor)
Actuators: Solenoid valves control hydraulic pressure to clutches
Shift Logic:
TCU monitors speed and throttle
Determines optimal gear (based on shift map programmed in ECU)
Energizes solenoid → Opens valve → Hydraulic pressure engages clutch
Smooth shift achieved by modulating pressure (ramp up/down)
Modern Features: — Adaptive shift logic: Learns driver behavior
Driver modes: Sport (shift at higher RPM), Eco (shift early for economy)
Manual mode: Driver controls shifts (via paddles or shifter)
Skip shifts: 1st → 3rd → 6th (intelligent skipping)
This is where electronics meets mechanics!

## Slide 13: Modern Multi-Speed Automatics (8, 9, 10 speeds!)
Evolution: More Speeds = Better Efficiency
Historical: — 1950s-1980s: 3-speed autos
1990s-2000s: 4-5 speed autos
2010s: 6-8 speed autos
Today: 8-10 speed autos common (Ford-GM: 10-speed!)
Why More Speeds?
Advantage 1: Closer Ratio Steps — Engine stays in optimal RPM range (BSFC sweet spot – Session 6!)
Example: 4-speed might have ratio steps 1.5x apart, 8-speed only 1.2x
Smoother acceleration (less RPM jump per shift)
Advantage 2: Wider Overall Ratio Spread — 4-speed: Overall spread ~4:1 (e.g., 1st = 3.2, 4th = 0.8)
8-speed: Overall spread ~7:1 (e.g., 1st = 4.7, 8th = 0.67)
Lower 1st gear → Better acceleration from standstill
Taller top gear → Lower RPM at highway speeds → Better fuel economy
Result: — Modern 8-speed auto can achieve BETTER fuel economy than manual!
Example: BMW 8-speed ZF transmission ~5-8% better economy than old 6-speed manual
Complexity: — More gears = More clutches and planetary sets
Sophisticated TCU software (thousands of shift combinations)
Higher cost (~₹50,000-100,000 more than manual)

## Slide 14
#### Part 2: Modern Transmission Technologies (Slides 14-18, ~15 minutes)

## Slide 15: CVT – Continuously Variable Transmission
CVT = Continuously Variable Transmission
Fundamental Difference: NO DISCRETE GEARS! Infinite ratios.
How It Works:
Components: — Two pulleys: Drive pulley (input) and Driven pulley (output)
Metal belt or chain connecting pulleys
Variable diameter: Pulley halves move together/apart to change effective diameter
Operation: — Low ratio (like 1st gear): — Drive pulley: Small diameter (halves apart)
Driven pulley: Large diameter (halves together)
Belt rides on small radius of drive, large radius of driven → Speed reduction
High ratio (like top gear): — Drive pulley: Large diameter (halves together)
Driven pulley: Small diameter (halves apart)
Belt rides on large radius of drive, small radius of driven → Speed increase (overdrive)
Infinite intermediate ratios: — Pulley halves move continuously
No shift points! Ratio changes smoothly
Control: Stepper motor or hydraulic actuators move pulley halves
Advantages:
✓ Optimal efficiency: ECU can keep engine at exact optimal RPM (BSFC sweet spot)
✓ Smooth acceleration: No shift shock
✓ Simple: Fewer parts than multi-speed auto
Disadvantages:
✗ Torque limit: Belt/chain can slip under high torque (~250-300 Nm max)
✗ Driving feel: Constant RPM (rubber band effect) feels unnatural to some
✗ Efficiency: Slightly lower than manual/DCT due to belt friction losses (~5-8%)
Used in: Honda Jazz, Nissan Micra, many Nissan/Toyota hybrids

## Slide 16: DCT/DSG – Dual-Clutch Transmission
DCT/DSG = Dual-Clutch Transmission / Direct Shift Gearbox (VW's name)
Concept: TWO manual gearboxes in one! TWO clutches!
How It Works:
Architecture: — Clutch 1 controls odd gears (1st, 3rd, 5th, 7th) via Input Shaft 1
Clutch 2 controls even gears (2nd, 4th, 6th) and Reverse via Input Shaft 2
Both input shafts are concentric (one inside the other)
Single output shaft
Shifting Process (e.g., 1st → 2nd):
In 1st gear: — Clutch 1 engaged → 1st gear active, power flowing
Clutch 2 disengaged
BUT: 2nd gear already pre-selected on Input Shaft 2!
Shifting: — Clutch 1 opens (releases 1st gear)
Simultaneously: Clutch 2 closes (engages 2nd gear)
Happens in 50-100 milliseconds! — No power interruption (one clutch closing as other opens)
Next gear already prepared: While in 2nd, 3rd is pre-selected and ready
Advantages:
✓ Very fast shifts: Faster than manual, faster than auto (<100ms vs ~200-300ms)
✓ No power loss during shift: Seamless
✓ High efficiency: ~98-99% (like manual, better than auto/CVT)
✓ Performance: Used in supercars (Ferrari, Lamborghini, Porsche PDK)
Disadvantages:
✗ Complex: Two clutches, complex control logic
✗ Expensive: ₹1,50,000-2,00,000 more than manual
✗ Low-speed jerkiness: Dual wet clutches can be jerky in stop-start traffic
✗ Maintenance: More expensive than manual
Used in: VW/Audi (DSG), Porsche (PDK), Ford (PowerShift)

## Slide 17: AMT – Automated Manual Transmission
AMT = Automated Manual Transmission (Also called Semi-Automatic)
Concept: Regular manual gearbox + Automated clutch and shift actuators
How It Works: — Base: Standard manual transmission (like Session 7)
Added: Electric or hydraulic actuators for:
Clutch operation (instead of pedal)
Gear shifting (instead of shift lever)
Control: TCU monitors speed/throttle, commands shifts
Operation: — Driver selects Drive (D) mode
TCU decides when to shift (based on speed, throttle)
Actuator presses clutch → Actuator moves shift mechanism → Actuator releases clutch
Same as manual transmission, just automated!
Advantages:
✓ Low cost: Only add actuators to existing manual (~₹30,000-50,000 extra vs manual)
✓ Fuel efficiency: Same as manual (no torque converter losses)
✓ Easy to maintain: Based on proven manual transmission
Disadvantages:
✗ Slow shifts: ~400-600ms (much slower than DCT or even auto)
✗ Power interruption: Clutch disengages during shift (like manual)
✗ Jerky: Shift shock, especially at low speeds
✗ Not suitable for performance: Mainly used in budget cars
Used in: Maruti Suzuki (AGS), Tata (AMT), many budget Indian cars

## Slide 18: Transmission Technology Comparison Table
Let's compare all transmission technologies side-by-side:
| Aspect | Manual | Auto (TC) | CVT | DCT/DSG | AMT |
|--------|--------|-----------|-----|---------|-----|
| Shift Speed | ~500ms | ~200ms | N/A | <100ms | ~500ms |
| Efficiency | 98% | 92-95% | 93-95% | 98-99% | 98% |
| Cost | Low | High | Medium | Very High | Low |
| Driving Ease | Skill needed | Very easy | Very easy | Very easy | Easy |
| Performance | Good | Good | Moderate | Excellent | Moderate |
| Traffic Use | Tiring | Excellent | Excellent | Good | Fair |
| Fuel Economy | Very Good | Good | Very Good | Very Good | Very Good |
| Reliability | Excellent | Good | Fair | Good | Good |
| Maintenance Cost | Low | High | Medium | High | Low |
| Torque Capacity | Very High | Very High | Limited | High | High |
Recommendations:
Manual: Enthusiasts, budget, maximum control
Automatic (TC): Comfort, reliability, luxury cars
CVT: Fuel economy focus, city driving, small cars
DCT/DSG: Performance, fast shifts, sports cars
AMT: Budget automatic option, Indian market
Global Trend: Manual declining in developed markets, DCT and Auto gaining

## Slide 19: Selecting the Right Transmission (Solve Scenario from Slide 6)
Let's solve our earlier scenarios:
Scenario A: Luxury Sedan (Mercedes S-Class)
Requirement: Smooth, effortless, comfortable
Recommendation: 9-speed Torque Converter Automatic — Why: Smoothest operation, proven reliability, imperceptible shifts, excellent low-speed refinement
Mercedes uses 9G-TRONIC (9-speed auto)
Scenario B: Performance Sports Car (Porsche 911)
Requirement: Fastest shifts, maximum performance
Recommendation: 7/8-speed DCT/PDK — Why: Fastest shifts (<100ms), no power interruption, launch control capable, manual mode with paddle shifters
Porsche PDK (7-speed DCT) standard in 911
Scenario C: City Electric Car (Nissan Leaf)
Electric motor, instant torque, 140 km/h top speed
Recommendation: SINGLE-SPEED FIXED GEAR — Why: (We'll explore in Part 5!)
Engineering decision depends on: Performance goals, cost targets, customer expectations, driving environment.

## Slide 20
#### Part 3: Differential & Final Drive (Slides 19-22, ~12 minutes)

## Slide 21: The Differential Problem and Solution
Now let's solve the cornering problem from Slide 3: How to power both wheels while allowing different speeds?
THE DIFFERENTIAL
Function: — Splits torque equally between two wheels (left and right)
Allows wheels to rotate at different speeds
How It Works:
Components: — Ring gear: Driven by transmission output (pinion gear meshes with ring)
Differential case: Attached to ring gear, rotates with it
Spider gears (pinion gears): Inside case, on a cross shaft
Side gears: One for each axle shaft (left wheel, right wheel)
Operation:
Straight Line Driving: — Ring gear rotates differential case
Spider gears don't rotate relative to case (they orbit with case)
Both side gears rotate at same speed
Both wheels rotate at same speed → Equal torque to each
Turning (e.g., left turn): — Ring gear still rotates case at constant speed
Left wheel (inside) must slow down (shorter path)
Right wheel (outside) must speed up (longer path)
Spider gears rotate on their axis → Allow side gears to spin at different speeds
Side gear speeds adjust automatically! (based on resistance/traction)
Key principle: Spider gears act as a speed compensator
Torque Split: ALWAYS 50:50 to each wheel (in open differential)

## Slide 22: Differential Ratio (Final Drive Ratio)
DIFFERENTIAL RATIO (Also called Final Drive Ratio)
Definition: Gear ratio between transmission output (pinion) and differential (ring gear)
Calculation:
GRdiff = Nring / N_pinion
Example: — Ring gear: 72 teeth
Pinion gear: 18 teeth
GR_diff = 72/18 = 4.0
What This Means: — Transmission output shaft rotates 4 times → Wheels rotate 1 time
This is the final torque multiplication stage
From Session 7, remember:
Overall ratio = GRtransmission × GRdifferential
Effect on Performance:
Higher Diff Ratio (e.g., 4.5):
More torque at wheels
Better acceleration
Lower top speed (engine hits redline at lower vehicle speed)
Worse fuel economy (higher RPM at cruising speed)
Lower Diff Ratio (e.g., 3.5):
Less torque at wheels
Slower acceleration
Higher top speed
Better fuel economy (lower RPM at cruising)
Typical Values: — Economy cars: 3.5-4.0
Performance cars: 3.0-3.5 (taller for high top speed)
Trucks/SUVs: 4.0-5.0 (shorter for towing and off-road)

## Slide 23: Final Drive Ratio Calculation Example
Complete Example:
Vehicle: Sports sedan
Engine redline: 7000 RPM
Transmission 6th gear ratio: 0.8 (overdrive)
Wheel radius: 0.33 m
Two differential options being considered:
Option A: 3.5 final drive
Option B: 4.1 final drive
Calculate: Top speed in 6th gear for each option
Solution:
Option A (3.5 diff ratio):
Overall ratio in 6th = 0.8 × 3.5 = 2.8
Wheel RPM at redline:
ω_wheel = 7000 / 2.8 = 2,500 RPM = 41.67 rev/s
Vehicle speed:
v = ω × 2πr = 41.67 × 2π × 0.33 = 86.4 m/s = 311 km/h ✓
Option B (4.1 diff ratio):
Overall ratio in 6th = 0.8 × 4.1 = 3.28
Wheel RPM at redline:
ω_wheel = 7000 / 3.28 = 2,134 RPM = 35.57 rev/s
Vehicle speed:
v = 35.57 × 2π × 0.33 = 73.7 m/s = 265 km/h
Conclusion: — Option A (3.5): Higher top speed, better for autobahn cruising
Option B (4.1): Better acceleration (more torque multiplication), better for city/mountain driving
Engineering choice depends on vehicle purpose!

## Slide 24: Limited-Slip Differential (LSD)
Problem with Open Differential:
Scenario: One wheel on ice, one on pavement
Wheel on ice has NO traction (can spin freely)
Differential splits torque 50:50
ALL power goes to the slipping wheel! (path of least resistance)
Wheel on pavement gets same torque but it's not enough to move car
Result: Car stuck, one wheel spinning uselessly
SOLUTION: LIMITED-SLIP DIFFERENTIAL (LSD)
Concept: Limit the speed difference between wheels
Types:
1. Clutch-type LSD: — Friction clutch packs between side gears and case
Preload keeps them partially engaged
If one wheel spins faster → Clutch resists → Transfers some torque to other wheel
2. Viscous LSD: — Silicone fluid between plates
Speed difference creates shear heating → Fluid thickens → Couples wheels
3. Torsen (Torque-Sensing): — Worm gears instead of spider gears
Mechanically biases torque to wheel with more traction
4. Electronic (e-Diff): — Uses brakes to slow down spinning wheel
Forces torque to other wheel (part of ESC system)
Used in: Sports cars (better cornering), trucks (off-road traction), performance sedans

## Slide 25
#### Part 4: Drivetrain Configurations (Slides 23-24, ~8 minutes)

## Slide 26: FWD vs RWD vs AWD Configurations
DRIVETRAIN CONFIGURATION: Which wheels receive power?
1. FWD – Front-Wheel Drive
Layout: Engine and transmission at front, power to front wheels
Advantages:
✓ Compact (engine, transmission, differential all in front)
✓ More interior space (no driveshaft tunnel)
✓ Better traction in snow/rain (engine weight over drive wheels)
✓ Lower cost (simpler, fewer parts)
✓ Better fuel economy (lighter, less drivetrain loss)
Disadvantages:
✗ Front wheels do steering AND power → Torque steer (pulling to one side under hard acceleration)
✗ Weight distribution (60:40 front:rear) → Understeer tendency
✗ Limited high-performance applications
Used in: Most economy and mid-size cars (Honda Civic, Toyota Corolla, Maruti Suzuki)
2. RWD – Rear-Wheel Drive
Layout: Engine at front (or rear), transmission at front or rear, driveshaft to rear differential, power to rear wheels
Advantages:
✓ Better weight distribution (50:50 possible)
✓ Better handling (neutral steering, less understeer)
✓ No torque steer (steering wheels not driven)
✓ Better for high-power applications
Disadvantages:
✗ Less traction in snow/rain (light rear end)
✗ More complex (driveshaft needed)
✗ Less interior space (driveshaft tunnel)
✗ Slightly higher cost
Used in: Luxury cars (BMW, Mercedes), sports cars (Mazda MX-5), trucks
3. AWD – All-Wheel Drive
Layout: Power to all four wheels (front and rear differentials, transfer case)
Advantages:
✓ Best traction (all wheels powered)
✓ Better acceleration (can use all four contact patches)
✓ Safer in adverse conditions (snow, rain, off-road)
Disadvantages:
✗ Heavier (extra differentials, transfer case, driveshafts)
✗ More complex and expensive
✗ Worse fuel economy (~10-15% penalty)
✗ Higher maintenance cost
Used in: SUVs, performance cars (Audi Quattro, Subaru), luxury sedans

## Slide 27: 4WD vs AWD Explained
4WD vs AWD: Often confused, but different!
AWD (All-Wheel Drive): — Always active (all wheels always powered)
Automatic: System distributes power as needed
Center differential: Allows front and rear axles to spin at different speeds (for normal roads)
Variable torque split: Can send more power to front or rear as needed (e.g., 60:40 or 40:60)
Used for: On-road performance and all-weather capability
Example: Audi Quattro, Subaru Symmetrical AWD
4WD (Four-Wheel Drive / 4x4): — Part-time: Driver selects 2WD or 4WD mode (lever or button)
Locked: In 4WD mode, front and rear axles locked together (usually 50:50 split)
Transfer case: Simple dog clutch or chain, no center differential
Low range: Often has low-range gearing for off-road crawling
Only for off-road: Should NOT use 4WD on dry pavement (axles locked → binding)
Used for: Serious off-road capability
Example: Jeep Wrangler, Mahindra Thar, Toyota Land Cruiser
Summary: — AWD: Sophisticated, on-road, always active, automatic
4WD: Rugged, off-road, selectable, low-range gearing

## Slide 28
#### Part 5: Electric Powertrains (Slides 25-27, ~12 minutes)

## Slide 29: Electric Motor vs IC Engine – Torque Characteristics
ELECTRIC POWERTRAINS – The future of automotive
Fundamental Difference: Torque Delivery
IC Engine Torque Curve (from Session 4):
Zero torque at 0 RPM (engine must be spinning)
Low torque at low RPM (~1000-1500 RPM)
Peak torque at ~3000-4000 RPM
Falling torque at high RPM (>5000)
Narrow operating range
Electric Motor Torque Curve: — MAXIMUM torque from 0 RPM! (instant torque)
Constant torque from 0 to ~5000 RPM (base speed)
Above base speed: Torque decreases (field weakening mode)
Usable range: 0-15,000+ RPM
Very wide operating range
Implications:
For ICE: NEED multi-speed transmission
Low RPM: Insufficient torque → Need 1st/2nd gear for torque multiplication
High vehicle speed: Engine can't spin fast enough → Need multiple gears
For EV: Single-speed transmission often sufficient!
0 RPM: Already have full torque → Don't need 1st gear!
Top speed: Motor can spin to 15,000+ RPM → One gear covers entire speed range
Example: Tesla Model 3
Motor: 350 Nm constant from 0-5000 RPM
Single-speed fixed gear ratio ~9:1
0-100 km/h: 3.3 seconds (instant torque!)
Top speed: 225 km/h (motor at ~14,000 RPM)

## Slide 30: Electric Powertrain Components
ELECTRIC POWERTRAIN ARCHITECTURE
Main Components:
1. Battery Pack (Energy Storage) — Lithium-ion cells (typically NCM or LFP chemistry)
High voltage: 400V (most EVs) or 800V (premium EVs like Porsche Taycan)
Capacity: 40-100 kWh (determines range)
Example: Nissan Leaf 40 kWh, Tesla Model 3 Long Range 82 kWh
2. BMS – Battery Management System — Monitors cell voltages, temperatures
Balances cells (ensures all cells at same state of charge)
Protects battery (thermal management, overcharge/over-discharge protection)
3. Inverter (Power Electronics) — Converts DC (battery) to 3-phase AC (motor)
Controls motor speed and torque
Bidirectional: Motor mode (drive) or Generator mode (regenerative braking)
This is the 'brain' – like ECU for ICE
4. Electric Motor — Typically Permanent Magnet Synchronous Motor (PMSM) or AC Induction Motor
Power: 50-500 kW (67-670 HP equivalent)
Peak torque: 200-1000 Nm
Efficiency: 90-95% (much better than ICE ~30-35%!)
5. Single-Speed Reducer (Transmission) — Fixed gear ratio ~8:1 to 10:1
No shifting, always engaged
Simple, reliable, ~98% efficient
6. Differential — Same as ICE vehicles
Distributes power to left/right wheels
Power Flow:
Battery (DC) → Inverter (DC to AC) → Motor (mechanical rotation) → Reducer → Differential → Wheels
Regenerative Braking:
Wheels → Differential → Reducer → Motor (acts as generator) → Inverter (AC to DC) → Battery (charges)
Recovers ~20-30% of energy during braking
Extends range significantly

## Slide 31: Connection to Next Module
We've completed MODULE 2: POWERTRAIN SYSTEMS (Sessions 4-8).
What we've mastered: — How engines generate power (Session 4)
How to keep engines alive (Session 5)
How to optimize performance (Session 6)
How to deliver power to wheels (Sessions 7-8)
Next: MODULE 3: CHASSIS DYNAMICS & CONTROL (Sessions 9-12)
Session 9: Vehicle Dynamics Fundamentals — Longitudinal dynamics (acceleration, braking)
Load transfer calculations
Weight distribution effects
Math-heavy! (Applying Sessions 1-3 physics to chassis)
Session 10: Braking Systems — Friction calculations (using Session 2 tire knowledge!)
Hydraulic brake systems
ABS (Anti-lock Braking System)
Session 11: Steering Systems — Ackermann geometry
Steering ratio calculations
Power steering (hydraulic and electric)
Session 12: Suspension Systems — Spring-mass-damper physics
Suspension types and trade-offs
Electronic suspension control
Connection: Powertrain generates forces → Chassis systems CONTROL those forces (braking, cornering, ride quality).

## Slide 32: 📊 PPT DESIGN GUIDANCE
Visual Elements to Include:
Assignment (Due before Session 9):
Problem 1: Compare transmission technologies:
Create a table comparing Manual, Automatic (TC), CVT, DCT, and AMT for:
a) City taxi (high mileage, frequent stops)
b) Performance sports car (track use)
c) Luxury sedan (comfort priority)
d) Budget hatchback (cost-conscious buyer)
Justify each recommendation with specific advantages for each application.
Problem 2: Final drive ratio calculations:
A vehicle has:
Engine redline: 6800 RPM
Transmission top gear ratio: 0.75
Wheel radius: 0.32 m
Top speed requirement: 210 km/h
a) Calculate required final drive ratio
b) If differential ratio chosen is 3.8, calculate acceleration in 1st gear (1st gear ratio = 3.5, engine torque = 200 Nm, efficiency = 94%)
c) Which gear should you use to cruise at 120 km/h for best fuel economy? (Assume BSFC optimal zone is 2000-3000 RPM)
Problem 3: Electric vs ICE comparison:
Compare a Tesla Model 3 (electric, 350 Nm from 0 RPM, single-speed) with a BMW 3-Series (ICE, 350 Nm @ 4000 RPM, 8-speed auto).
a) Why can Tesla achieve 0-100 km/h in 3.3s vs BMW's 5.6s despite same peak torque?
b) Sketch torque vs RPM curves for both
c) Explain why Tesla doesn't need multiple gears
Bonus: Research Porsche Taycan's 2-speed transmission. Why did Porsche add a 2nd gear when most EVs use single-speed? What performance advantage does it provide?
Discussion Questions for Q&A: — Will manual transmissions disappear completely? Why or why not?
How do hybrid powertrains (like Toyota Prius) combine ICE and electric motors? (Preview for future)
What is torque vectoring and how do modern AWD systems implement it?
Why are some manufacturers developing multi-speed EVs (e.g., Porsche Taycan 2-speed)?
How does regenerative braking work in EVs and how much energy can be recovered?
30 minutes for your questions. —--
Consistency: Maintain professional engineering template from all previous sessions
Technical Professionalism: Clear system diagrams, cutaway illustrations, comparison tables
Color coding: — Blue for mechanical components
Orange for hydraulic/fluid components
Green for electronic control systems
Purple for electric powertrain components
Font sizes: Comparison tables must be very readable (16pt minimum)
Slide 9: Torque converter operation – Core of automatic transmission
Slide 11: Planetary gears – Unique to automatics
Slide 17: Transmission comparison table – Critical reference
Slide 19: Differential operation – How it allows different wheel speeds
Slide 25: EV vs ICE torque curves – Fundamental difference
Slide 28: Complete powertrain summary – Module integration
Slide 30: Assignment problems – Comprehensive application
Slide 9: Torque converter fluid flow animation (impeller → turbine → stator)
Slide 11: Planetary gear set operation (different configurations for different ratios)
Slide 14: CVT pulley width changing (show ratio change smoothly)
Slide 15: DCT dual-clutch shifting (show overlap)
Slide 19: Differential spider gears rotating during cornering
Slide 26: Electric powertrain power flow (battery → inverter → motor → wheels)
Cutaway photos: Real automatic transmission, torque converter, differential
Component photos: Planetary gear set, CVT pulleys, DCT clutches, electric motor
System diagrams: Complete powertrain layouts (FWD/RWD/AWD configurations)
Comparison tables: All transmission types, drivetrain configurations
Graphs: Torque curves (ICE vs EV), transmission efficiency comparisons
Calculation worksheets: Final drive ratio examples

## Slide 33: 🎯 INSTRUCTOR NOTES
Safety/Ethics Notes:
Technology comparison: Present multiple solutions to same problem (getting power to wheels)
Evolution narrative: Manual → Auto → Modern (CVT/DCT) → Electric (shows progression)
Application-driven: Match technology to use case (luxury vs performance vs budget)
Integration: Connect back to Sessions 4-7 throughout (BSFC maps, gear ratios, etc.)
Forward-looking: Electric powertrains preview the future
Challenge 1: "How does torque converter multiply torque without gears?"
How to address: Explain stator function carefully – it redirects fluid flow to give impeller a "push" from turbine exit flow. This creates reaction torque on stator (held stationary), which allows turbine to produce MORE torque than impeller puts in. Draw fluid flow paths clearly.
Challenge 2: "Why are there so many transmission types? Isn't one 'best'?"
How to address: Emphasize trade-offs – no perfect solution. Each type optimizes different priorities (cost, efficiency, performance, comfort). Use comparison table extensively. Real-world selection depends on application, market, and customer expectations.
Challenge 3: "If electric motors have instant torque, why does Porsche Taycan have 2-speed transmission?"
How to address: Explain that single-speed works for most EVs, but for extreme performance:
1st gear: Even higher torque multiplication for 0-100 km/h (sub-3 second acceleration)
2nd gear: Allows higher top speed (>250 km/h)
Trade-off: Added complexity and weight for marginal performance gains. Only makes sense for premium performance EVs.
Challenge 4: "How does differential 'know' to send power to the wheel that needs it?"
How to address: Clarify misconception – OPEN differential doesn't "send" power intelligently. It ALWAYS splits torque 50:50. The wheel with less traction will spin faster (because it can), but receives same torque as other wheel. LIMITED-SLIP differentials address this by resisting speed difference, which does transfer more torque to higher-traction wheel. Electronic systems (using brakes) can actively manage this.
If running short: — Condense torque converter details (Slide 10) – show operation, skip efficiency graphs
Combine CVT and AMT into single slide (Slides 14+16)
Reduce differential details (Skip LSD Slide 22, just mention it exists)
Move drivetrain configurations (Slides 23-24) to assignment reading
If running long: — Move final drive calculations (Slide 21) to assignment (just show formula)
Defer 4WD vs AWD details (Slide 24) to Q&A
Reduce electric powertrain details (combine Slides 26-27)
Core content (must cover): — Slides 8-11 (Automatic transmission fundamentals – torque converter and planetary gears)
Slide 17 (Transmission comparison table – critical reference)
Slide 19 (Differential operation – resolves cornering puzzle)
Slides 25-26 (Electric powertrain basics – future technology)
Slide 28 (Module summary – integration)
Slide 3: Ask "When was the last time you noticed wheels spinning at different speeds during a turn? What would happen without a differential?
Slide 9: Draw torque converter fluid flow on board together – trace path from impeller to turbine to stator
Slide 17: Poll students: "Which transmission would YOU choose for your personal car? Why?" (Gets them thinking about trade-offs)
Slide 19: If possible, bring a differential (salvaged from junkyard) to physically demonstrate – rotate input, show wheels spin at different rates
Slide 25: Ask "Why do electric cars accelerate so much faster than gas cars with same torque?" (Instant torque from 0 RPM!)
Q&A: Be ready for questions about:
Hybrid transmissions: How Toyota Prius combines ICE and electric (eCVT with planetary gears)
Launch control: How DCTs and autos achieve maximum acceleration (slip clutch/converter at optimal RPM)
Torque vectoring: How modern AWD systems send different torque to each wheel (via clutches or electric motors at each wheel)
EV multi-motor setups: Dual motor (front + rear) or quad motor (one per wheel)
Transmission fluid maintenance: Regular ATF changes extend transmission life (~60,000-100,000 km intervals)
Differential fluid: Often neglected but critical (change every ~50,000 km)
EV high voltage safety: 400-800V systems are LETHAL – only trained technicians should work on them
Environmental impact: EV lifecycle emissions depend on electricity source (coal vs renewable)

## Slide 34: ✅ Session Success Criteria
Students leave able to:
✓ Explain automatic transmission operation (torque converter and planetary gears)
✓ Compare all transmission technologies (Manual, Auto, CVT, DCT, AMT) with advantages/disadvantages
✓ Describe differential operation and speed difference allowance
✓ Calculate final drive ratio and analyze impact on performance/economy
✓ Compare drivetrain configurations (FWD, RWD, AWD, 4WD)
✓ Explain electric powertrain components and why EVs use single-speed transmissions
Most importantly: Students understand the complete powertrain module (Sessions 4-8) as an integrated system, can compare different technological approaches to same problems, and appreciate the fundamental differences between ICE and electric powertrains.

## Slide 35: 📝 ADDITIONAL NOTES
Connection to Electronics (Throughout):
This session completes Module 2 (Powertrain Systems). Students should now understand:
How power is generated (ICE engines or electric motors)
How power is managed (cooling, lubrication, fuel/battery systems)
How power is delivered to wheels (transmissions, differentials, drivetrain)
How to optimize the complete system (BSFC maps, gear selection, efficiency)
Next module shifts focus from power generation/delivery to power CONTROL:
Braking (controlling deceleration)
Steering (controlling direction)
Suspension (controlling ride and handling)
All use the physics foundations from Sessions 1-3.
Transmission choices: Why Ferrari uses DCT, Mercedes uses auto, budget cars use AMT
Differential types: Why sports cars have LSD, luxury cars have electronic torque vectoring
EV architecture: Tesla (single-speed), Porsche Taycan (2-speed), Rivian (quad-motor)
Hybrid systems: Toyota (eCVT), Honda (multi-mode), plug-in hybrids (combined operation)
In-wheel motors: Electric motor in each wheel (eliminates differential!)
eCVT: Planetary gear set with electric motors (Toyota Prius system)
48V mild hybrid: Electric assist to ICE (belt-starter-generator)
Solid-state batteries: Next-gen EV batteries (higher energy density, faster charging)
TCU programming: Shift maps, adaptive logic, sport/eco modes
Inverter control: PWM control of electric motors, regenerative braking algorithms
BMS design: Cell balancing, thermal management, state of charge estimation
Torque vectoring: ECU coordinating brakes/clutches/motors for optimal traction
This bridges mechanical and electrical engineering domains comprehensively.

## Slide 36
End of Session 8 Framework
End of Module 2 (Powertrain Systems) - Sessions 4-8 Complete!