## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 9: Vehicle Dynamics Fundamentals'

## Slide 2: Vehicle Dynamics Fundamentals
Session 9 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 9. Today we begin Module 3: Chassis Dynamics & Control. We're going to apply everything you learned in Sessions 1-3 to understand how vehicles actually behave when they accelerate, brake, and corner.

## Slide 4: The Journey So Far - Connecting Modules
Let's trace our learning journey:
MODULE 1 (Sessions 1-3): FOUNDATION — We calculated forces: Rolling resistance, drag, gradient forces
We learned about friction: μ × N at tire-road interface
We calculated power requirements: P = F × v
MODULE 2 (Sessions 4-8): POWERTRAIN — How to generate power (engines)
How to deliver power (transmissions, differential)
How to optimize performance (fuel systems)
MODULE 3 (Today - Sessions 9-12): CHASSIS DYNAMICS — How to control that power (braking)
How to direct the vehicle (steering)
How to manage vehicle motion (suspension, dynamics)
Today's focus: The physics of vehicle motion - what happens when forces act on a real vehicle with mass, suspension, and multiple wheels.

## Slide 5: The Puzzle - Why Does the Car Nose-Dive When Braking?
Let me show you something you've all experienced but maybe never analyzed:
[Show photo]: Car braking hard
Front end: Suspension compressed, nose pointing down
Rear end: Suspension extended, rear lifted up
Why does this happen?
Think about it: You press the brake pedal, friction at tires creates braking force. The force acts at the ground level (tire contact patch). But the car's mass is up high (center of gravity).
This creates a moment! (Torque trying to rotate the car)
Result: Weight transfers from rear to front. Front suspension compresses under extra load, rear suspension extends as load decreases.
Today you'll learn: How to calculate EXACTLY how much weight transfers, why it happens, and what it means for vehicle performance and safety.

## Slide 6: Real-World Implications
Why does this matter?
For braking performance: — Front wheels get more load during braking → Can generate more friction force → Good!
Rear wheels get less load → Can lock up easily → ABS needed
For vehicle design: — Sports car: Low center of gravity → Less weight transfer → More stable
SUV: High center of gravity → More weight transfer → Easier to pitch/roll → Needs electronic stability control
For safety systems (Sessions 10-12): — Understanding load transfer is CRITICAL for:
Brake force distribution (proportioning valve)
ABS tuning (when do wheels lock?)
Electronic Stability Control (ESC) algorithms
For automotive electronics engineers: You'll program these control systems. You MUST understand the physics you're controlling.

## Slide 7: Real-World Scenario
Here's a real engineering challenge:
Vehicle: Honda Civic 1.5L Turbo
Mass: 1,300 kg
Wheelbase: 2.7 m
Center of gravity height: 0.55 m
CG position: 1.20 m from front axle, 1.50 m from rear axle
Track width: 1.52 m
Coefficient of friction (dry road): μ = 0.85
Requirements:
Acceleration: Achieve 0-100 km/h in under 8 seconds
Braking: Stop from 100 km/h in under 40 meters
Cornering: Navigate 30 m radius turn at 50 km/h without sliding
Questions: — Is this vehicle capable of meeting these targets?
How much weight transfers during each maneuver?
Which wheels are critical for each maneuver?
How would increasing CG height affect performance?
By the end of today: You'll calculate answers to all these questions!

## Slide 8: Vehicle as a Rigid Body - Coordinate System
Before we calculate, let's establish our coordinate system:
Vehicle Fixed Coordinate System: — X-axis: Longitudinal (forward/backward) - Roll axis
Y-axis: Lateral (left/right) - Pitch axis
Z-axis: Vertical (up/down) - Yaw axis
Center of Gravity (CG): — Point where all mass can be considered concentrated
Located at: (x_cg, 0, h) where h = height above ground
Typically: ~40-45% of wheelbase from front (passenger cars)
Height h: ~0.5-0.6 m (cars), ~0.8-1.0 m (SUVs)
Key Parameters: — L = Wheelbase (front axle to rear axle)
a = Distance from front axle to CG
b = Distance from rear axle to CG (L = a + b)
h = CG height above ground
t = Track width (left wheel to right wheel)
Note: Lower h = better (less load transfer). Longer L = better (less pitch).

## Slide 9: Free-Body Diagram - Acceleration
Scenario: Vehicle accelerating forward
Forces in Free-Body Diagram:
At Front Wheels: — W_f = Normal force on front axle (downward on ground, upward on wheel)
F_drag,f = Aerodynamic drag (small portion)
F_roll,f = Rolling resistance
(Usually no drive force for FWD during hard accel, weight transferred off front)
At Rear Wheels: — W_r = Normal force on rear axle
F_drive = Tractive force (driving force from engine/transmission)
F_roll,r = Rolling resistance
At CG: — mg = Weight (downward)
F_drag = Aerodynamic drag (horizontal, rearward)
Equations of Motion (Newton's 2nd Law):
Longitudinal (X-direction):
ΣFx = m × ax
Fdrive - Fdrag - Froll,total = m × ax
Vertical (Z-direction):
ΣF_z = 0 (no vertical acceleration)
Wf + Wr - mg = 0
→ Wf + Wr = mg (total load equals weight)
Moments about CG (Pitch):
ΣM_cg = 0 (no angular acceleration, assuming steady-state)
Wf × a - Wr × b + F_drive × h = 0
This moment equation tells us how weight distributes between front and rear!

## Slide 10: Static Weight Distribution vs Dynamic
STATIC (Vehicle at rest, a = 0):
Taking moments about front axle:
W_r × L - mg × a = 0
W_r = mg × (a/L)
Similarly:
W_f = mg × (b/L)
Example: Honda Civic
m = 1300 kg, L = 2.7 m, a = 1.2 m, b = 1.5 m
W_f,static = 1300 × 9.81 × (1.5/2.7) = 7,095 N (55.6%)
W_r,static = 1300 × 9.81 × (1.2/2.7) = 5,671 N (44.4%)
Front-heavy distribution (common for FWD cars - engine at front)
DYNAMIC (Vehicle accelerating, a = 2 m/s²):
Load transfers from front to rear!
ΔW = (m × a_x × h) / L (load transfer formula - we'll derive this!)
For our example:
ΔW = (1300 × 2.0 × 0.55) / 2.7 = 530 N
W_f,dynamic = 7,095 - 530 = 6,565 N (lighter!)
W_r,dynamic = 5,671 + 530 = 6,201 N (heavier!)
Weight shifted rearward → Rear tires more loaded → Can generate more traction

## Slide 11: Practice - Identify Forces (Braking & Cornering)
Quick practice: Identify forces for other maneuvers
BRAKING: — Braking forces at front and rear tires (Fbrake,f and Fbrake,r)
Weight transfers FORWARD (opposite of acceleration)
Front wheels get more load → Can brake harder
Rear wheels get less load → Can lock up easily
CORNERING (turning left): — Centrifugal force at CG (acts outward, to the right)
Normal forces change: Right wheels (outside) get MORE load
Left wheels (inside) get LESS load (can even lift off ground!)
Lateral friction forces at tires (pointing left, toward turn center)
We'll calculate all of these today! —--
#### Part 2: Longitudinal Dynamics - Acceleration (Slides 12-17, ~18 minutes)

## Slide 12: Deriving Load Transfer Formula (Acceleration)
Let's derive the load transfer formula rigorously:
Given: Vehicle accelerating at a_x (m/s²)
Apply Newton's 2nd Law:
Longitudinal:
Fdrive - Fresist = m × a_x
Vertical:
Wf + Wr = mg
Moments about CG (taking counter-clockwise as positive):
Wf × a - Wr × b - F_drive × h = 0
But we know: Fdrive = m × ax + F_resist
Substituting:
Wf × a - Wr × b - (m × ax + Fresist) × h = 0
For simplified analysis, assume Fresist is small compared to m × ax:
Wf × a - Wr × b - m × a_x × h ≈ 0
From vertical equilibrium: Wr = mg - Wf
Substituting:
Wf × a - (mg - Wf) × b - m × a_x × h = 0
Wf × a - mg × b + Wf × b - m × a_x × h = 0
Wf × (a + b) = mg × b + m × ax × h
Wf × L = mg × b + m × ax × h
Wf = (mg × b)/L + (m × ax × h)/L
Compare to static: W_f,static = (mg × b)/L
Load transfer: ΔW = (m × a_x × h)/L
Wf,accel = Wf,static - ΔW (front loses weight)
Wr,accel = Wr,static + ΔW (rear gains weight)
Key insight: Load transfer proportional to:
Acceleration (a_x) - harder accel → more transfer
CG height (h) - higher CG → more transfer
Inversely proportional to wheelbase (L) - longer wheelbase → less transfer

## Slide 13: Maximum Acceleration Calculation
Question: What's the maximum acceleration for Honda Civic (RWD for this example)?
Given: — m = 1,300 kg, L = 2.7 m, h = 0.55 m
a = 1.2 m, b = 1.5 m
μ = 0.85 (dry road)
Assume RWD (rear wheels drive)
Solution:
Step 1: Calculate static rear axle load
W_r,static = mg × (a/L) = 1300 × 9.81 × (1.2/2.7) = 5,671 N
Step 2: Calculate dynamic rear load during acceleration
At maximum acceleration, using load transfer:
Wr,dynamic = Wr,static + ΔW
Wr,dynamic = Wr,static + (m × a_max × h)/L
Step 3: Maximum tractive force limited by friction
Fdrive,max = μ × Wr,dynamic
Step 4: Set up equation
Fdrive,max = m × amax (ignoring resistances for max case)
μ × Wr,dynamic = m × amax
μ × [Wr,static + (m × amax × h)/L] = m × a_max
Step 5: Solve for a_max
μ × Wr,static + μ × (m × amax × h)/L = m × a_max
μ × Wr,static = m × amax - μ × (m × a_max × h)/L
μ × Wr,static = m × amax × [1 - μ × h/L]
amax = (μ × Wr,static) / [m × (1 - μ × h/L)]
Step 6: Calculate
a_max = (0.85 × 5671) / [1300 × (1 - 0.85 × 0.55/2.7)]
a_max = 4821 / [1300 × (1 - 0.173)]
a_max = 4821 / (1300 × 0.827)
a_max = 4821 / 1075
a_max = 4.48 m/s²
Result: Maximum acceleration ~4.5 m/s² (0.46 g)
0-100 km/h time ≈ 27.8/4.48 ≈ 6.2 seconds (not accounting for gear shifts and engine torque curve - actual will be slower)

## Slide 14: Effect of Weight Distribution on Acceleration
Why sports cars aim for 50:50 weight distribution:
Scenario: Same vehicle, different weight distributions (for RWD)
Front-heavy (60:40): — Static W_r = 40% × mg = 0.4 × 12,753 = 5,101 N
Less static rear load → Less initial traction
a_max = 4.10 m/s² (lower!)
50:50 distribution: — Static W_r = 50% × mg = 0.5 × 12,753 = 6,377 N
More static rear load → More traction
a_max = 5.12 m/s² (higher!)
Rear-heavy (40:60): — Static W_r = 60% × mg = 0.6 × 12,753 = 7,652 N
Even more rear load
a_max = 6.15 m/s² (best for RWD!)
BUT: Rear-heavy hurts braking (less front load) and understeer in corners
Trade-off: 50:50 is compromise for balanced performance in all maneuvers
Examples: — BMW 3-Series: 50:50 (RWD, balanced)
Porsche 911: Rear-heavy (~40:60) → Amazing acceleration, challenging handling
Honda Civic: Front-heavy (~60:40) → FWD, good braking, moderate accel

## Slide 15: AWD vs RWD vs FWD Acceleration
Drive configuration affects maximum acceleration:
RWD (Rear-Wheel Drive): — Uses rear weight + weight transfer → Good for acceleration
But: Front-heavy car wastes front weight during accel
Max accel ≈ 0.4-0.5 g
FWD (Front-Wheel Drive): — Uses front weight
Problem: Weight transfers AWAY from drive wheels during accel!
W_f decreases with acceleration → Traction decreases!
Max accel ≈ 0.3-0.4 g (worse than RWD)
Why FWD exists: Cheaper, better packaging, better snow traction
AWD (All-Wheel Drive): — Uses ALL four wheels
Can utilize full vehicle weight
Max accel ≈ 0.8-0.9 g (limited only by total μ × mg!)
Examples: Audi Quattro, Subaru WRX (famous for launch acceleration)
This is why drag racing cars: — Are RWD (or AWD)
Have weight shifted to rear (big engine in back, or long wheelbase with weight transfer)
Have low CG (reduce load transfer magnitude)

## Slide 16: Practice Problem - Your Turn!
Practice Problem:
Given: — Vehicle mass: 1,500 kg
Wheelbase: 3.0 m
CG position: 1.4 m from front, 1.6 m from rear
CG height: 0.6 m
Coefficient of friction: 0.80 (wet road)
RWD vehicle
Calculate:
Static weight distribution (front and rear axle loads)
Maximum acceleration possible (traction-limited)
Weight on rear axle at maximum acceleration
If this were FWD instead, what would maximum acceleration be?
Take 3 minutes. I'll show the solution after.
[Pause for student work]
Solution:
W_f,static = 1500 × 9.81 × (1.6/3.0) = 7,848 N (53.3%)
W_r,static = 1500 × 9.81 × (1.4/3.0) = 6,867 N (46.7%)
amax,RWD = (μ × Wr,static) / [m × (1 - μ × h/L)]
a_max,RWD = (0.80 × 6867) / [1500 × (1 - 0.80 × 0.6/3.0)]
a_max,RWD = 5494 / [1500 × 0.84]
a_max,RWD = 4.36 m/s²
ΔW = (1500 × 4.36 × 0.6)/3.0 = 1,308 N
W_r,accel = 6,867 + 1,308 = 8,175 N
For FWD: Weight transfers AWAY from front wheels
Wf,accel = Wf,static - ΔW = 7,848 - 1,308 = 6,540 N
a_max,FWD = (0.80 × 6540)/1500 / (1 + 0.80 × 0.6/3.0) ≈ 3.72 m/s² (worse!)

## Slide 17: Real-World Validation
Theory vs Reality:
Our simplified calculations assume:
Constant friction coefficient
Instant torque at wheels (no wheel spin, perfect traction control)
No gear shifts
No aerodynamic drag
Real-world factors: — Engine torque curve (not constant)
Gear ratios and shift times
Tire slip (optimal is ~10-15% slip, not 0%)
Drag increases with speed²
| Vehicle | Calculated a_max | Calc 0-100 | Actual 0-100 | Difference |
|---------|------------------|------------|--------------|------------|
| Honda Civic FWD | ~3.5 m/s² | ~8.0 s | 8.2 s | Good! |
| BMW 3-Series RWD | ~4.8 m/s² | ~5.8 s | 5.5 s | Decent (LC helps) |
| Audi Quattro AWD | ~7.5 m/s² | ~3.7 s | 3.9 s | Close! |
LC = Launch Control (electronic system that manages wheel slip for optimal accel)
Our calculations give good first-order estimates! —--
#### Part 3: Longitudinal Dynamics - Braking (Slides 18-22, ~18 minutes)

## Slide 18: Braking - Weight Transfers Forward
Braking is opposite of acceleration:
Free-Body Diagram (Braking):
Forces: — F_brake,f = Braking force at front wheels
F_brake,r = Braking force at rear wheels
Wf, Wr = Normal loads (change due to load transfer)
Moment about CG:
Wf × a - Wr × b + (Fbrake,f + Fbrake,r) × h = 0
Load Transfer Formula (Braking):
ΔW = (m × a_brake × h) / L
But now: — Wf,brake = Wf,static + ΔW (front GAINS weight!)
Wr,brake = Wr,static - ΔW (rear LOSES weight!)
Implications: — Front wheels more loaded → Can brake harder → Most braking done by front
Rear wheels less loaded → Can lock easily → ABS critical for rear
Typical brake force distribution: 70-80% front, 20-30% rear

## Slide 19: Maximum Braking Deceleration
Question: Maximum braking deceleration for Honda Civic?
Given: Same Honda Civic (m=1300 kg, L=2.7 m, h=0.55 m, a=1.2 m, b=1.5 m, μ=0.85)
Solution:
At maximum braking, ALL wheels at friction limit:
Fbrake,total = μ × (Wf + W_r) = μ × mg
But wait! Weight transfers to front. Front can brake harder, rear might lock first.
Ideal scenario (perfect brake distribution, no locking):
Deceleration:
abrake,max = Fbrake,total / m = μ × mg / m = μ × g
a_brake,max = 0.85 × 9.81 = 8.34 m/s² (0.85 g!)
This is independent of vehicle mass! (Just like free fall)
But depends on: — Road condition (μ): Dry = 0.8-0.9, Wet = 0.5-0.7, Ice = 0.1-0.3
Tire condition
Load transfer at max braking:
ΔW = (1300 × 8.34 × 0.55)/2.7 = 2,208 N
W_f,brake = 7,095 + 2,208 = 9,303 N (73% of weight on front!)
W_r,brake = 5,671 - 2,208 = 3,463 N (27% of weight on rear)
This is why: — Front brakes are LARGER than rear (need to handle more force)
Rear brakes can be smaller (often drum brakes on economy cars)
Proportioning valve limits rear brake pressure to prevent lockup

## Slide 20: Stopping Distance Calculation
Stopping Distance has two components:
1. Reaction Distance: — Time from seeing obstacle to pressing brake pedal
Typical reaction time: 1.5 seconds
dreaction = v × treaction
2. Braking Distance: — From brake application to full stop
Using kinematics: v² = v₀² + 2×a×d
At stop: v = 0
dbrake = -v₀² / (2×abrake)
Total: dtotal = dreaction + d_brake
Example: 100 km/h (27.8 m/s) on dry road (μ = 0.85)
Reaction distance:
d_reaction = 27.8 × 1.5 = 41.7 m
Braking distance:
a_brake = -0.85 × 9.81 = -8.34 m/s²
d_brake = -(27.8)² / (2 × -8.34) = 772 / 16.68 = 46.3 m
Total stopping distance = 41.7 + 46.3 = 88 m
Nearly a football field! (100m)
On wet road (μ = 0.6): — d_brake = 772 / (2 × 0.6 × 9.81) = 65.6 m — Total ≈ 107 m (30% longer!)
This is why: Speed limits lower in rain, following distance critical

## Slide 21: Brake Force Distribution Problem
Challenge: How to distribute brake force between front and rear?
Ideal case: Both axles reach friction limit simultaneously
Fbrake,f = μ × Wf,brake
Fbrake,r = μ × Wr,brake
But Wf and Wr change with deceleration! (load transfer)
Fixed distribution (simple cars): — Brake line pressure same front and rear (or fixed ratio)
Problem: At light braking, rear locks first (has less weight)
At heavy braking, distribution not optimal
Solution: Proportioning valve (reduces rear pressure above threshold)
Active distribution (ABS): — Wheel speed sensors detect impending lockup
ECU modulates brake pressure (pump cycles 5-15 times per second!)
Each wheel independently controlled
Result: Maximum braking force, no lockup, steering maintained
Electronic Brake Distribution (EBD): — Uses ABS hardware
Actively adjusts front/rear distribution based on deceleration
Optimal under all conditions (empty vs loaded, uphill vs downhill)
This is automotive electronics! Session 10 covers ABS in detail.

## Slide 22: Practice - Stopping Distance
Practice Problem:
A truck (mass 8,000 kg, L = 4.5 m, h = 1.2 m) is traveling at 80 km/h on a wet road (μ = 0.6).
Calculate:
Maximum braking deceleration
Braking distance (ignore reaction time)
Load transfer
Percentage of weight on front axle during maximum braking
Take 2 minutes.
Solution:
a_brake = μ × g = 0.6 × 9.81 = 5.89 m/s²
v = 80 km/h = 22.2 m/s
d_brake = v² / (2 × a) = 22.2² / (2 × 5.89) = 41.9 m
ΔW = (8000 × 5.89 × 1.2) / 4.5 = 12,565 N
Assume 50:50 static (common for trucks)
W_static = 8000 × 9.81 / 2 = 39,240 N each axle
W_f,brake = 39,240 + 12,565 = 51,805 N
Percentage = 51,805 / (8000 × 9.81) = 66% on front!
High CG (1.2 m) causes large load transfer → Rear axle only has 34% of weight during hard braking → Rear locks easily without ABS —--
#### Part 4: Lateral Dynamics - Cornering (Slides 23-26, ~12 minutes)

## Slide 23: Cornering Forces - Centrifugal Force
When vehicle corners, it requires centripetal acceleration:
Circular Motion: — Radius R, velocity v
Centripetal acceleration: a_c = v² / R (directed toward center)
Required force: Fc = m × ac = m × v² / R
From vehicle's perspective (rotating reference frame): — Centrifugal force appears to act outward at CG
F_cf = m × v² / R (outward, at height h)
This force must be balanced by: — Lateral friction forces at tires (Flat,front + Flat,rear)
Flat,total = μ × (Wleft + W_right) = μ × mg
Maximum cornering speed:
When friction force reaches limit:
m × v²_max / R = μ × mg
v_max = √(μ × g × R)
Example: R = 50 m turn, μ = 0.85
v_max = √(0.85 × 9.81 × 50) = √417 = 20.4 m/s = 73 km/h
Exceed this speed → Vehicle slides outward!

## Slide 24: Lateral Load Transfer (Roll)
Centrifugal force acts at CG (height h above ground):
Creates moment about roll axis: — Roll axis: Roughly at ground level
Moment arm: CG height h
Roll moment: Mroll = Fcf × h = (m × v²/R) × h
This causes vehicle to lean outward (body roll)
Weight transfers from inside wheels to outside wheels:
Lateral Load Transfer:
ΔWlat = (m × alateral × h) / t
Where:
a_lateral = v²/R (lateral acceleration)
h = CG height
t = track width (left wheel to right wheel distance)
Inside wheels: Winside = Wstatic - ΔW_lat
Outside wheels: Woutside = Wstatic + ΔW_lat
Example: Honda Civic at 50 km/h, R = 30 m
m = 1300 kg, h = 0.55 m, t = 1.52 m
a_lat = (13.9)² / 30 = 6.43 m/s²
ΔW_lat = (1300 × 6.43 × 0.55) / 1.52 = 3,022 N
Static: Each side carries ~6,377 N
Cornering: — Inside: 6,377 - 3,022 = 3,355 N (much lighter!)
Outside: 6,377 + 3,022 = 9,399 N (much heavier!)
Inside wheels near liftoff point! (In extreme case, can leave ground)

## Slide 25: Rollover Threshold
Vehicle rolls over when inside wheels lift completely:
Condition: W_inside = 0
From lateral load transfer:
Wstatic - ΔWlat = 0
(mg/2) - (m × a_lat × h)/t = 0
Solving for critical lateral acceleration:
a_lat,rollover = (g × t) / (2 × h)
Critical speed:
v²_rollover / R = (g × t) / (2 × h)
v_rollover = √(R × g × t / (2h))
Example 1: Honda Civic (t = 1.52 m, h = 0.55 m)
a_lat,rollover = (9.81 × 1.52) / (2 × 0.55) = 13.5 m/s² (1.38 g)
At R = 30 m: v_rollover = √(30 × 13.5) = 20.1 m/s = 72 km/h
Example 2: SUV (t = 1.6 m, h = 0.9 m - higher CG!)
a_lat,rollover = (9.81 × 1.6) / (2 × 0.9) = 8.7 m/s² (0.89 g)
At R = 30 m: v_rollover = √(30 × 8.7) = 16.2 m/s = 58 km/h
SUV rolls over at much lower speed! (Higher h, similar t)
This is why: — SUVs have Electronic Stability Control (ESC) mandatory
Sports cars are low to ground (low h)
Track width (t) important for stability

## Slide 26: Key Takeaways Summary
Let's consolidate today's physics:
FORCES & FREE-BODY DIAGRAMS:
✓ Identify all forces (normal, friction, weight, drag)
✓ Apply ΣF = ma in X and Z directions
✓ Apply ΣM = 0 for moments (assuming no angular acceleration)
LONGITUDINAL DYNAMICS (ACCELERATION):
✓ Load transfer: ΔW = (m × a_x × h) / L
✓ Wf,accel = Wf,static - ΔW (front loses weight)
✓ Wr,accel = Wr,static + ΔW (rear gains weight)
✓ Max accel (RWD): amax = (μ × Wr,static) / [m × (1 - μh/L)]
✓ Max accel (AWD): a_max ≈ μ × g (uses all weight)
LONGITUDINAL DYNAMICS (BRAKING):
✓ Load transfer: ΔW = (m × a_brake × h) / L (same formula!)
✓ Wf,brake = Wf,static + ΔW (front gains weight)
✓ Wr,brake = Wr,static - ΔW (rear loses weight)
✓ Max decel: a_brake,max = μ × g (independent of mass!)
✓ Stopping distance: d = v² / (2 × μ × g)
✓ Typical distribution: 70-80% front, 20-30% rear
LATERAL DYNAMICS (CORNERING):
✓ Centripetal accel: a_c = v² / R
✓ Lateral load transfer: ΔWlat = (m × alat × h) / t
✓ Max cornering speed: v_max = √(μ × g × R)
✓ Rollover threshold: a_lat,rollover = (g × t) / (2h)
✓ Lower CG (h) and wider track (t) → Better stability
KEY INSIGHTS: — Load transfer proportional to: acceleration, CG height, inversely to wheelbase/track
Weight distribution critical for balanced performance
Electronics (ABS, ESC) manage these physics in real-time
You can now analyze complete vehicle dynamics behavior!

## Slide 27: Connection to Next Sessions
Today: We analyzed the physics. Next 3 sessions: The systems that control it.
Session 10: Braking Systems — Today: Calculated how much load transfers during braking (ΔW)
Session 10: Design brake systems to handle that load
Hydraulic brake components (master cylinder, calipers)
Disc vs drum brakes
ABS: How it prevents wheel lockup using load transfer knowledge
Brake force distribution (proportioning valve)
Session 11: Steering Systems — Today: Calculated lateral forces during cornering
Session 11: Design steering systems to control direction
Ackermann geometry (prevent tire scrub)
Steering ratio calculations
Power steering (hydraulic and EPAS)
Understeer/oversteer management
Session 12: Suspension Systems — Today: Analyzed load transfer (longitudinal and lateral)
Session 12: Design suspension to manage that transfer
Spring-mass-damper systems
Suspension types (McPherson, double wishbone, etc.)
Anti-roll bars (reduce lateral load transfer!)
Electronic adaptive suspension
Foundation complete: Physics → Systems → Electronic Control
All three sessions apply today's load transfer calculations!

## Slide 28: 📊 PPT DESIGN GUIDANCE
Visual Elements to Include:
Assignment (Due before Session 10):
Problem 1: A sports car has the following specifications:
Mass: 1,400 kg
Wheelbase: 2.5 m
CG height: 0.48 m
CG position: 1.15 m from front axle
Track width: 1.55 m
Coefficient of friction: 0.90 (dry road, performance tires)
RWD vehicle
Calculate:
a) Static weight distribution (% front, % rear)
b) Maximum acceleration and load transfer
c) Weight on each axle at maximum acceleration
d) Maximum braking deceleration and load transfer
e) Weight on each axle at maximum braking
f) Maximum cornering speed for R = 40 m turn without sliding
g) Critical speed for rollover in the same turn
Problem 2: Comparative analysis
For the same vehicle in Problem 1:
a) If CG height increased to 0.60 m (like adding roof rack), recalculate max acceleration and braking
b) Calculate percentage change in performance
c) Calculate new rollover threshold
d) Explain why lowering CG improves all aspects of dynamics
Problem 3: Real-world application
Research one production vehicle's specifications (mass, wheelbase, CG height estimate, track width).
a) Calculate theoretical maximum acceleration (assume AWD, μ = 0.85)
b) Compare to manufacturer's claimed 0-100 km/h time
c) Explain discrepancies (hint: engine power, gear ratios, drag)
d) Calculate stopping distance from 100 km/h
Discussion Questions for Q&A: — Why do drag racing cars have wheelie bars? (prevent front lifting due to extreme load transfer)
Why are Formula 1 cars so low to the ground? (minimize h → minimize load transfer → maximum grip)
How does load transfer affect ABS operation? (rear wheels more prone to locking → need different control)
Why do sports cars have wider rear tires than front (on RWD)? (more load during accel, need more contact patch)
What is \"lift-off oversteer\" and why is it dangerous? (rapid weight transfer forward when releasing throttle mid-corner)
30 minutes for your questions. —--
Consistency: Maintain professional engineering template from all previous sessions
Math-heavy focus: Large, clear equations (24pt minimum)
Free-body diagrams: Clean, labeled, with force vectors in different colors
Color coding: — Red for forces (Fdrive, Fbrake, F_cf)
Blue for normal loads (Wf, Wr)
Green for resulting accelerations
Orange for load transfer (ΔW)
Arrows showing direction clearly
Slide 3: Nose-dive during braking photo – Establishes real-world phenomenon
Slide 9: Free-body diagram for acceleration – Foundation
Slide 12: Load transfer derivation – Core mathematics
Slide 13: Maximum acceleration calculation – Complete example
Slide 19: Maximum braking deceleration – Critical safety calculation
Slide 24: Lateral load transfer – 3D dynamics
Slide 27: Complete challenge solution – Integration
Slide 28: Summary of all formulas – Reference sheet
Slide 9: Build FBD step-by-step (add forces one at a time)
Slide 10: Animate weight shift during acceleration (show ΔW transfer)
Slide 12: Step-through derivation (one equation line at a time)
Slide 18: Animate braking weight transfer (forward shift)
Slide 24: Show vehicle rolling, weight shifting to outside wheels
Slide 25: Animated rollover sequence (dramatic but educational!)
Free-body diagrams: Professional engineering style (forces as arrows, labeled magnitudes)
Photos: Real vehicles accelerating (front lift), braking (nose dive), cornering (body roll)
Calculation worksheets: Step-by-step solutions with boxes highlighting key steps
Comparison tables: RWD vs FWD vs AWD, Car vs SUV dynamics
Graphs: Load distribution (static vs dynamic), stopping distance vs speed

## Slide 29: 🎯 INSTRUCTOR NOTES
Safety/Ethics Notes:
Physics application: Directly applies Sessions 1-3 foundation (forces, friction, Newton's laws)
Math-intensive: Multiple derivations and complete calculations (like Session 1-3)
Real-world grounding: Every concept tied to observable vehicle behavior
Build complexity: Start simple FBD → Add load transfer → Apply to 3 maneuvers
Problem-solving focus: Multiple complete examples, practice problems
Challenge 1: "Why does weight transfer happen? Weight doesn't change!"
How to address: Clarify terminology - total weight (mg) stays constant, but DISTRIBUTION between front/rear (or left/right) changes. Use moment analysis - force at ground level, mass at CG height creates moment that redistributes normal forces.
Challenge 2: "In braking formula, why does load transfer use same equation as acceleration?"
How to address: The formula ΔW = (mah)/L is general for any longitudinal acceleration (positive or negative). Sign of 'a' determines direction of transfer. Positive a (accel) → rearward transfer. Negative a (braking) → forward transfer. Physics is symmetric.
Challenge 3: "Why is max braking = μg independent of mass?"
How to address: Show the algebra: F_brake,max = μ × mg. Then a = F/m = (μ × mg)/m → mass cancels! This is like free fall - all objects fall at same rate regardless of mass. Here, all vehicles brake at same rate (if same μ) regardless of mass.
Challenge 4: "Lateral load transfer formula uses track width 't', but longitudinal uses wheelbase 'L'. Why?"
How to address: Moment arm is different! Longitudinal: weight distributed front-to-rear (spacing = L). Lateral: weight distributed left-to-right (spacing = t). The axis of rotation is different for pitch (longitudinal) vs roll (lateral).
If running short: — Condense acceleration example (Slide 13) - show final answer without full derivation
Combine AWD vs RWD vs FWD (Slide 15) into quick comparison table
Skip practice problem Slide 16 (assign as homework instead)
Reduce cornering section (Slides 23-26) - cover basics only, defer details to Session 12
If running long: — Move derivation (Slide 12) to appendix or assignment reading
Skip real-world validation (Slide 17) - just state "theory matches reality well
Reduce practice problem time (show solutions immediately)
Defer understeer/oversteer (Slide 26) entirely to Session 12
Core content (must cover): — Slides 8-10 (FBD and static vs dynamic weight)
Slide 12 or 13 (Load transfer - derivation OR application, at least one)
Slide 18-19 (Braking dynamics and load transfer)
Slide 20 (Stopping distance - critical safety topic)
Slide 23-24 (Lateral dynamics basics)
Slide 28 (Summary formulas)
Slide 3: Show video of car braking hard (slow motion if possible) - students see nose-dive
Slide 6: Poll: "Has anyone done 0-100 km/h timing in their car? How close to manufacturer claim?
Slide 12: Derive together on board - pause between steps, ask "what's next?
Slide 13: Work calculation in real-time, show each arithmetic step (don't just jump to answer)
Slide 20: Reaction time experiment - have someone try to catch ruler (measure reaction ~200-250ms)
Slide 24: Demonstrate with chair - push at top (high 'h') vs bottom → show toppling easier when pushed high
Q&A: Be ready for questions about:
Why rear-engine cars (Porsche 911)? Great for acceleration (weight on drive wheels), but tricky handling (oversteer tendency)
All-wheel steering (Honda Prelude, some new cars) - how does it help?
Active aerodynamics (wings, spoilers) - create downforce → increase normal load → more grip!
Torque vectoring — differential that can send different torque to each wheel (manages understeer/oversteer)
Stopping distance awareness: Emphasize safe following distances (2-second rule minimum)
Road conditions: Show dramatic difference in friction (dry vs wet vs ice) affects ALL dynamics
SUV rollover risk: Explain why electronic stability control is mandatory (saves lives)
Performance driving: Track vs street - know limits, don't test on public roads

## Slide 30: ✅ Session Success Criteria
Students leave able to:
✓ Identify all forces and moments acting on vehicle during acceleration, braking, cornering
✓ Calculate longitudinal acceleration performance using tractive force
✓ Analyze load transfer during acceleration (front/rear distribution)
✓ Analyze load transfer during braking (front/rear distribution)
✓ Calculate lateral load transfer during cornering
✓ Explain relationship between weight distribution and handling characteristics
Most importantly: Students apply Sessions 1-3 physics foundation to real vehicle dynamics, can predict vehicle behavior mathematically, and understand the physics underlying all chassis control systems (braking, steering, suspension, ESC).

## Slide 31: 📝 ADDITIONAL NOTES
Mathematical Rigor:
Session 1 (Forces): All resistance forces (rolling, drag) still apply, now added to dynamic analysis
Session 2 (Friction): Friction equation F = μN is basis for all traction limits
Session 3 (Power): Acceleration performance determined by force (today) AND power available (Session 3)
Sessions 4-8 (Powertrain): Engine/transmission deliver force/torque to wheels → creates acceleration we calculated today
Throughout session, preview upcoming topics:
"We calculated 70% weight on front during braking → Session 10 shows how brake system handles this
"Rear wheels prone to lockup → Session 10 explains ABS
"Body roll during cornering → Session 12 shows how suspension and anti-roll bars manage it
"Ackermann geometry mentioned → Session 11 explains steering geometry in detail
Low sports cars: Minimize h → reduce load transfer → improve all dynamics
Wide stance (track): Increase t → reduce lateral load transfer → reduce rollover risk
Long wheelbase luxury cars: Increase L → reduce longitudinal load transfer → smoother ride
F1 cars: Extreme downforce → increase N → increase friction limit (not dependent on weight!)
This session is intentionally math-heavy like Sessions 1-3. Students should:
Work through derivations (builds understanding)
Practice calculations (builds confidence)
Apply to real scenarios (builds relevance)
Maintain high technical standards - these are future automotive engineers who will design safety-critical control systems.

## Slide 32
End of Session 9 Framework