## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 10: Braking Systems'

## Slide 2: Braking Systems
Session 10 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 10. Today we design the systems that safely stop a 1,300 kg vehicle traveling at 100 km/h in just 40-50 meters. This is one of the most critical safety systems in any vehicle.

## Slide 4: Connection to Session 9 - Applying Load Transfer Knowledge
In Session 9, we calculated the physics of braking:
For Honda Civic at maximum braking (μ = 0.85): — Deceleration: a_brake = 8.34 m/s² (0.85g)
Load transfer: ΔW = 2,208 N
Front axle load: 9,303 N (73% of total weight!)
Rear axle load: 3,463 N (only 27%)
Today's question: How do we design a brake system that:
Generates 8.34 m/s² deceleration reliably
Handles 73% of braking force at front wheels
Prevents rear wheels from locking (dangerous!)
Works consistently (hot, cold, wet, repeated stops)
Requires manageable pedal force from driver
Today you'll learn: Complete brake system design from pedal to pad.

## Slide 5: The Braking Challenge - Safety Critical
Why braking systems matter for safety:
Statistics (India): — ~30-40% of accidents involve inadequate braking
Rear-end collisions often due to misjudged stopping distance
ABS reduces accidents by ~18-20% (wet conditions)
Stopping Distance Reality: — 100 km/h on dry road: ~45 m braking distance (+ 40 m reaction = 85 m total)
100 km/h on wet road: ~65 m braking distance (+ 40 m reaction = 105 m total)
100 km/h on ice: ~200+ m braking distance!
Driver often underestimates: Most people think \"I can stop in 20-30 m at 100 km/h\" → WRONG!
Engineering responsibility: Design systems that maximize braking force within friction limits, maintain steering control, and work reliably under all conditions.

## Slide 6: Why This Matters for Electronics Engineers
Modern braking is heavily electronic:
ABS (Anti-lock Braking System): — Sensors: Wheel speed sensors at each wheel (4 sensors)
Actuator: Hydraulic pump + solenoid valves (modulate pressure 5-15 times/second!)
ECU: Processes wheel speed, detects slip, controls valves
Algorithm: Threshold-based or slip-ratio control
EBD (Electronic Brake Distribution): — Uses ABS hardware
Actively adjusts front/rear brake balance based on deceleration and load
ESC (Electronic Stability Control): — Individual wheel braking for yaw control
Integrated with ABS (uses same hardware)
Brake-by-Wire (Future): — No hydraulic connection pedal → wheels
Fully electronic actuation (like EVs)
You'll program these systems → Must understand the hydraulics and mechanics you're controlling!

## Slide 7: Real-World Scenario - Emergency Braking
Design Challenge:
Vehicle: Mid-size sedan (similar to Honda Accord)
Mass: 1,500 kg
Wheelbase: 2.8 m, CG height: 0.58 m
Static weight distribution: 57% front, 43% rear
Tire-road friction: μ = 0.85 (dry), 0.6 (wet)
Wheel/tire radius: 0.32 m
Performance Requirements:
Stopping distance: From 100 km/h, stop in ≤ 45 m (dry road)
Pedal force: Maximum 500 N from driver (manageable for average person)
Reliability: Work consistently for 100,000 km, 200+ emergency stops
Safety: No wheel lockup on wet roads (steering control maintained)
Regulation: Meet BS (Bharat Stage) braking standards
Design Questions: — What brake force needed at each axle?
What hydraulic pressure required?
What disc size and caliper design?
How to prevent rear wheel lockup?
Do we need ABS? (Yes, mandatory in India post-2019!)
By end of session: Complete brake system design!

## Slide 8: How Brakes Work - Converting Kinetic Energy to Heat
Braking = Energy Conversion
Vehicle kinetic energy:
KE = (1/2) × m × v²
Example: 1,500 kg at 100 km/h (27.8 m/s)
KE = 0.5 × 1500 × 27.8² = 579,000 J (579 kJ)
Where does this energy go?
→ Friction between brake pad and disc/drum
→ Converts to HEAT
→ Heat dissipates to air (cooling)
Energy dissipation rate (Power):
Pbrake = Fbrake × v
At start of braking (27.8 m/s, assuming 8 m/s² decel):
F_brake = m × a = 1500 × 8 = 12,000 N
P_brake = 12,000 × 27.8 = 334 kW!
That's like 450 horsepower of heating! (All goes into brakes)
This is why: — Brake discs get red-hot (400-700°C) during hard braking
Brake fade occurs if heat can't dissipate fast enough
Ventilated discs critical for repeated braking (mountain descents, racing)

## Slide 9: Brake Force Calculation Using Friction
At the tire-road interface (from Session 2):
Maximum friction force:
F_brake,max = μ × N
Where:
μ = coefficient of friction (tire-road)
N = Normal load on wheel
From Session 9, during braking: — Front: Nf = Wf,static + ΔW (increases!)
Rear: Nr = Wr,static - ΔW (decreases!)
Maximum braking forces: — Fbrake,f,max = μ × Nf = μ × (Wf,static + ΔW) — Fbrake,r,max = μ × Nr = μ × (Wr,static - ΔW)
Key insight: Front wheels can handle MORE braking force during hard braking (due to load transfer!). Rear wheels prone to lockup if braked too hard.
At the brake disc (inside wheel): — Brake pad presses against disc with force F_clamp
Friction generates braking torque: τbrake = μbrake × Fclamp × reff
This torque resists wheel rotation
Creates reaction force at tire contact patch
Two friction interfaces:
Pad-disc friction (μ_brake ~ 0.35-0.45)
Tire-road friction (μ_road ~ 0.8-0.9 dry)
Limiting factor: Usually tire-road friction (lower μ when wet/icy)

## Slide 10: Complete Braking Force Calculation Example
Example: Honda Accord (m = 1,500 kg, L = 2.8 m, h = 0.58 m, μ = 0.85)
Step 1: Calculate static loads
Assume 57% front / 43% rear (given)
W_f,static = 0.57 × 1500 × 9.81 = 8,388 N
W_r,static = 0.43 × 1500 × 9.81 = 6,328 N
Step 2: Calculate maximum deceleration
a_max = μ × g = 0.85 × 9.81 = 8.34 m/s²
Step 3: Calculate load transfer
ΔW = (m × a × h) / L = (1500 × 8.34 × 0.58) / 2.8 = 2,586 N
Step 4: Calculate dynamic loads
N_f = 8,388 + 2,586 = 10,974 N (74.7% of total!)
N_r = 6,328 - 2,586 = 3,742 N (25.3% of total)
Step 5: Calculate maximum brake forces
Fbrake,f,max = 0.85 × 10,974 = 9,328 N — Fbrake,r,max = 0.85 × 3,742 = 3,181 N — F_brake,total = 9,328 + 3,181 = 12,509 N ✓ (matches m × a = 12,510 N)
Step 6: Calculate required brake torque (at wheel)
τbrake,f = Fbrake,f × rwheel = 9,328 × 0.32 = 2,985 Nm — τbrake,r = Fbrake,r × rwheel = 3,181 × 0.32 = 1,018 Nm
Result: Front brakes must handle ~75% of total braking force!

## Slide 11: Brake Fade - The Temperature Problem
BRAKE FADE = Loss of braking effectiveness due to overheating
What happens: — Repeated hard braking → Disc temperature rises (can reach 600-800°C!)
Pad material changes: — Organic pads: Fade above ~250-300°C (coefficient drops from 0.40 to 0.20!)
Semi-metallic: Fade above ~400°C
Ceramic: Fade above ~600°C (racing pads)
Result: Same pedal pressure produces LESS braking force → Longer stopping distance!
Why it's dangerous: — Driver presses harder → Pedal goes to floor → Still insufficient braking
Commonly occurs: Mountain descents (engine braking critical!)
Solutions:
Ventilated discs: Internal vanes pump air through disc → Better cooling
Larger discs: More mass → More heat capacity, larger surface → More cooling
Better pad material: Higher temperature tolerance (trade-off: noisier, more dust)
Engine braking: Don't rely only on brakes (downshift on long descents)
Modern cars: Ventilated discs standard on front, often solid discs rear (less heat)

## Slide 12
#### Part 2: Hydraulic Brake Systems (Slides 12-17, ~20 minutes)

## Slide 13: Pascal's Principle - Pressure Multiplication
Why hydraulic brakes? Force multiplication!
Pascal's Principle:
Pressure applied to confined fluid transmits equally in all directions.
P = F / A (Pressure = Force / Area)
Since pressure is equal throughout:
Pmaster = Pslave
Fmaster / Amaster = Fslave / Aslave
Rearranging:
Fslave = Fmaster × (Aslave / Amaster)
Example: — Master cylinder: Diameter 25 mm → Area = π × (12.5)² = 491 mm²
Brake caliper piston: Diameter 50 mm → Area = π × (25)² = 1,963 mm²
Force multiplication: 1,963 / 491 = 4:1 — If driver applies 500 N to master → 500 × 4 = 2,000 N at caliper!
But: Slave piston moves 1/4 the distance (conservation of energy)
Additional multiplication: Brake Pedal Lever — Typical pedal ratio: 4:1 to 6:1
Driver foot force 100 N × 5 (pedal ratio) = 500 N at master cylinder
Total system: 100 N (foot) → 500 N (master) → 2,000 N (caliper) = 20x multiplication!

## Slide 14: Master Cylinder - The Heart of Hydraulic System
MASTER CYLINDER converts pedal force to hydraulic pressure
Components: — Piston: Pushed by brake pedal (via pushrod)
Primary seal: Prevents fluid leakage
Return spring: Returns piston when pedal released
Reservoir: Stores brake fluid (DOT 3, DOT 4, or DOT 5.1)
Compensating port: Allows fluid expansion with temperature
Modern design: Tandem Master Cylinder (dual circuit) — Two pistons in series (primary and secondary)
Split circuit: Typically diagonal split (LF+RR, RF+LR) or front/rear split
Safety: If one circuit fails, other still provides 50% braking
Regulation: Dual circuit mandatory (prevents complete brake failure)
Operation:
Pedal pressed → Pushrod moves primary piston → Pressure builds in primary chamber
Primary pressure pushes secondary piston → Pressure builds in secondary chamber
Both circuits pressurize → Brake fluid flows to calipers
Pedal released → Springs return pistons → Fluid returns from calipers
Typical master cylinder: Bore diameter 20-30 mm, stroke 40-60 mm

## Slide 15: Brake Booster - Power Assist
BRAKE BOOSTER reduces pedal effort required
Why needed? — Without booster: Need ~500-700 N foot force for emergency stop (very hard!)
With booster: Only ~100-200 N needed (manageable)
Vacuum Brake Booster (Most common):
Components: — Diaphragm: Large surface area (200-250 cm²)
Vacuum chamber: Connected to engine intake manifold (~0.7-0.8 bar vacuum)
Atmospheric chamber: Can be connected to atmosphere
Control valve: Opens/closes atmospheric connection based on pedal position
Operation:
Pedal released: — Valve closes atmospheric chamber
Both sides of diaphragm at vacuum → No force difference
Pedal pressed: — Valve opens atmospheric chamber to air
Vacuum on one side, atmospheric pressure on other
Pressure difference: ~1 bar × 200 cm² = 2,000 N force! — This force assists driver's foot force
Force multiplication: — Driver: 150 N
Booster: +2,000 N
Total: 2,150 N to master cylinder!
With pedal leverage (5:1): Equivalent to 10,750 N foot force!
Modern trend: Electric Brake Booster (Hybrid/EV) — No engine vacuum in EVs/hybrids
Electric motor-driven pump creates vacuum
Or fully electric actuator (brake-by-wire)

## Slide 16: Brake Calipers and Disc Brakes
DISC BRAKE SYSTEM (Front brakes, increasingly rear too)
Components:
1. Brake Disc (Rotor): — Cast iron or carbon-ceramic (racing/high-end)
Diameter: 280-350 mm (passenger cars), 380-400 mm (performance)
Ventilated design: Two friction surfaces with vanes between (cooling channels)
Thickness: 20-30 mm
Bolted to wheel hub → Rotates with wheel
2. Brake Caliper: — Fixed caliper: Pistons on both sides (2, 4, 6, or 8 pistons total)
Both pads pushed simultaneously
Better performance, more expensive
Floating caliper: Piston(s) on one side only (1 or 2 pistons)
Piston pushes inner pad → Pressure pushes outer pad via caliper sliding
Cheaper, most common on passenger cars
3. Brake Pads: — Friction material bonded to metal backing plate
Materials: Organic (quiet, less dust), Semi-metallic (better heat), Ceramic (best performance)
Typical thickness: 10-12 mm new, replace at 2-3 mm
Coefficient of friction: 0.35-0.45
Operation:
Hydraulic pressure enters caliper
Piston(s) move outward
Pad contacts disc on both sides
Friction creates braking torque
Heat dissipates through ventilated disc
Clamping force calculation: — Caliper pressure: 80 bar (8 MPa)
Piston area: 20 cm² (50 mm diameter)
F_clamp = P × A = 8 × 10⁶ Pa × 20 × 10⁻⁴ m² = 16,000 N! — With two pistons: 32,000 N total clamping force

## Slide 17: Drum Brakes - Traditional Rear Brake Design
DRUM BRAKE SYSTEM (Still used on rear of economy cars)
Components:
1. Brake Drum: — Cylinder attached to wheel hub (rotates with wheel)
Diameter: 200-280 mm
Cast iron
2. Brake Shoes: — Curved metal with friction lining on outer surface
Two shoes per wheel: Leading and trailing (or two leading for performance)
Pivot at bottom (anchor pin)
3. Wheel Cylinder: — Hydraulic actuator with two pistons
Pushes shoes outward against drum
4. Return Springs: — Pull shoes back when brake released
Operation:
Hydraulic pressure pushes wheel cylinder pistons outward
Pistons push brake shoes outward
Shoes contact drum inner surface
Friction creates braking torque
Self-Energizing Effect: — Drum rotation tends to drag leading shoe into further contact
Increases friction force for same hydraulic pressure
\"Servo action\" - mechanical force multiplication
Advantages:
✓ Lower cost (fewer parts)
✓ Parking brake easier to integrate (mechanical cable locks shoes)
✓ Less exposed to water/dirt (enclosed)
Disadvantages:
✗ Poor heat dissipation (enclosed design)
✗ Fade more easily
✗ More complex (more parts that can wear)
✗ Harder to service (pads vs shoes)
Modern trend: Disc brakes even for rear (better performance, easier maintenance)

## Slide 18: Disc vs Drum Comparison
Comprehensive Comparison:
| Aspect | Disc Brakes | Drum Brakes |
|--------|------------|-------------|
| Heat Dissipation | Excellent (exposed) | Poor (enclosed) |
| Fade Resistance | Better | Worse |
| Wet Performance | Good (water flung off by rotation) | Fair (water trapped inside) |
| Maintenance | Easy (pads accessible) | Harder (must remove drum) |
| Cost | Higher | Lower |
| Weight | Lighter | Heavier |
| Parking Brake | Needs separate mechanism | Easy to integrate |
| Self-Energizing | No | Yes (servo action) |
| Performance | Better (consistent) | Adequate for rear/economy |
Modern Application: — Front brakes: ALWAYS disc (handles 70-75% of braking, needs best performance)
Rear brakes: — Economy cars: Drum (cost savings, adequate for 25-30% of braking)
Mid/Premium cars: Disc (better performance, easier service)
Performance cars: Large ventilated disc (maximum performance)
Future: All disc (even economy), possibly electric calipers (brake-by-wire)

## Slide 19
#### Part 3: Brake Force Distribution (Slides 18-20, ~12 minutes)

## Slide 20: The Distribution Problem
Challenge: Load transfer changes front/rear weight distribution during braking, but hydraulic lines have fixed pressure!
The Problem:
Light braking (a = 2 m/s²):
Small load transfer (ΔW small)
Weight distribution closer to static (say 60:40)
Ideal brake distribution: ~60% front, ~40% rear
Hard braking (a = 8 m/s²):
Large load transfer (ΔW large)
Weight shifts forward dramatically (say 75:25)
Ideal brake distribution: ~75% front, ~25% rear
But if we use fixed distribution:
Option A: 75:25 (optimized for hard braking) — At light braking: Front gets too much (could lock), rear too little (inefficient)
At hard braking: Perfect
Option B: 60:40 (optimized for light braking) — At light braking: Perfect
At hard braking: Rear gets too much → LOCKS! (dangerous - loss of stability)
Compromise (typical): ~70:30 distribution
Not optimal at either extreme
Rear slightly under-braked at all times (for safety)
Better solution: Proportioning valve or EBD

## Slide 21: Proportioning Valve - Mechanical Solution
PROPORTIONING VALVE limits rear brake pressure above threshold
Design: — Installed in hydraulic line to rear brakes
Spring-loaded piston and valve
Operation:
Below threshold (light braking): — Pressure < ~40 bar
Valve fully open
Rear pressure = Front pressure (1:1)
Above threshold (hard braking): — Pressure > ~40 bar
Spring compresses, valve partially closes
Rear pressure increases SLOWER than front
Slope change: Rear pressure = k × Front pressure (k ~ 0.4-0.6)
Example: — Front pressure: 80 bar
Without proportioning: Rear = 80 bar → Rear locks!
With proportioning: Rear = 40 + 0.5 × (80-40) = 60 bar → Safer
Graph: Front pressure (X-axis) vs Rear pressure (Y-axis)
Linear 1:1 up to knee point (~40 bar)
Then slope ~0.4-0.6
Still not perfect (can't adapt to load changes like passengers, cargo)
Load-Sensitive Valve (trucks): — Linked to suspension height
When truck loaded → Rear compressed → Valve allows more rear pressure
When truck empty → Valve limits rear pressure more
Adaptive to load!

## Slide 22: Brake Balance and Lockup Analysis
Engineering analysis: When do wheels lock?
Wheel locks when:
Brake force > Friction force
F_brake > μ × N
At front:
Fbrake,f > μ × Nf
At rear:
Fbrake,r > μ × Nr
Since Nf and Nr change with deceleration (load transfer): — As you brake harder, front can handle more force
Rear can handle less force
Ideal brake force ratio:
Ff / Fr = Nf / Nr (changes with deceleration!)
Brake Balance Diagram: — X-axis: Front brake force
Y-axis: Rear brake force
Lockup curves: Show when front or rear locks for different μ values
Brake line: Actual front/rear distribution of brake system
Good design: — Brake line between lockup curves
Front locks slightly before rear (safer - maintains steering)
Never rear locks first (loss of stability, spin-out risk)
This is why: Slight rear under-braking acceptable (proportioning valve ensures this)

## Slide 23
#### Part 4: Anti-Lock Braking System (ABS) (Slides 21-25, ~18 minutes)

## Slide 24: The Locked Wheel Problem
Why wheel lockup is dangerous:
Locked wheel (skidding): — Coefficient of friction DROPS: μkinetic ≈ 0.6-0.7 (vs μstatic = 0.8-0.9)
Longer stopping distance (~20-30% longer!)
Loss of steering control: Locked wheel can't generate lateral force
Flat-spotted tire: Permanent damage from skidding
Rolling wheel with optimal slip: — Maintains higher friction (near μ_static)
Shorter stopping distance — Steering maintained: Can steer around obstacle while braking!
Wheel Slip Ratio Definition:
λ = (vvehicle - vwheel) / v_vehicle × 100%
Where:
v_vehicle = vehicle speed
v_wheel = tangential speed of wheel = ω × r
Slip values: — λ = 0%: Free rolling (no braking)
λ = 10-20%: Optimal braking (maximum friction force!)
λ = 100%: Wheel locked (v_wheel = 0)
Key insight: Maximum friction occurs at ~10-20% slip, NOT at lockup!
ABS goal: Maintain slip in optimal range (10-20%)

## Slide 25: ABS Components and System Architecture
ABS SYSTEM COMPONENTS:
1. Wheel Speed Sensors (4): — One at each wheel
Types: Magnetic reluctance (older) or Hall-effect (modern)
Measures wheel rotational speed (ω)
Output: Pulse train, frequency proportional to wheel speed
Accuracy: ~1-2% (sufficient for slip detection)
2. ABS Electronic Control Unit (ECU): — Processes wheel speed signals (typically 100-200 Hz sample rate)
Calculates vehicle speed (average of non-slipping wheels, or from dedicated sensor)
Calculates slip ratio for each wheel
Control algorithm: Determines pressure increase/hold/decrease
Outputs commands to hydraulic modulator
Processing time: ~10-20 ms (fast enough for stable control)
3. Hydraulic Modulator (HCU - Hydraulic Control Unit): — Solenoid valves: 2 per wheel (inlet and outlet) = 8 valves total
Pump: Re-pressurizes system during ABS cycling
Accumulator: Stores brake fluid during pressure decrease
Valve positions: — Pressure Increase: Inlet open, outlet closed (fluid from master → caliper)
Pressure Hold: Both closed (maintain current pressure)
Pressure Decrease: Inlet closed, outlet open (fluid from caliper → accumulator)
4. Warning Lamp: — Indicates ABS fault (system defaults to normal braking)
System Architecture: — Individual wheel control: 4-channel ABS (best, most cars today)
Select-low: Controls axle based on wheel with most slip (older, 3-channel)
Power supply: ~12V, peak current ~20-30A during ABS cycling

## Slide 26: ABS Control Algorithm
ABS CONTROL ALGORITHM (Simplified)
INPUT: Wheel speeds (ω₁, ω₂, ω₃, ω₄)
PROCESSING:
Step 1: Calculate vehicle reference speed — Use highest wheel speed or average of non-slipping wheels
v_ref = max(ω₁, ω₂, ω₃, ω₄) × r (conservative estimate)
Step 2: Calculate slip ratio for each wheel — λᵢ = (vref - ωᵢ × r) / vref × 100%
Step 3: Determine control action for each wheel
IF λ < 10% (under-braking):
Action: INCREASE PRESSURE (open inlet valve)
Allows more braking force
ELSE IF 10% ≤ λ ≤ 20% (optimal):
Action: HOLD PRESSURE (both valves closed)
Maintain current braking force
ELSE IF λ > 20% (over-braking, approaching lockup):
Action: DECREASE PRESSURE (open outlet valve)
Reduce braking force → Wheel speeds up → Slip decreases
Step 4: Repeat at 10-20 Hz (50-100 ms cycle time)
Result: Brake pressure modulates 5-15 times per second
Driver feels pulsation in pedal (normal!)
System maintains slip in optimal range
Maximum braking force without lockup
Advanced algorithms: — PID control: Smooth modulation (less pulsation)
Fuzzy logic: Handles complex scenarios
Model-based: Predicts vehicle behavior

## Slide 27: ABS Operation Example
ABS Cycle Example: Emergency braking on wet road (μ = 0.6)
Timeline:
t = 0s: Driver stomps brake pedal
All wheels: 100% speed (no slip yet)
Pressure ramping up quickly
t = 0.1s: Pressure reaches high level
Rear wheels start slipping (less load due to weight transfer!)
Slip ratio rear: 25% (exceeds threshold)
ABS activates: DECREASE pressure to rear wheels
t = 0.15s: Rear pressure reduced
Rear wheels speed up
Slip decreases to 15%
ABS action: HOLD pressure
t = 0.20s: Rear wheels stable at 15% slip
Within optimal range
Pressure held constant
t = 0.25s: Road patch with lower friction
Slip increases again to 22%
ABS action: DECREASE pressure again
Pattern continues: Pressure cycles 10-15 times until vehicle stops
Front wheels: May not need ABS intervention (higher load → less prone to lock)
Result: — Stopping distance: ~65m (close to theoretical limit for μ = 0.6)
Without ABS: ~80m+ (locked wheels, μ_kinetic = 0.5)
~15-20% improvement + steering maintained!
Driver experience: — Pedal pulsation (normal - don't release!)
Grinding/buzzing sound (pump and valves)
Vehicle stops straight (no skid)

## Slide 28: Key Takeaways Summary
Let's consolidate today's learning:
FRICTION BRAKING FUNDAMENTALS:
✓ Braking converts kinetic energy to heat (KE = ½mv²)
✓ Brake force: F = μ × N (Session 2 friction!)
✓ Load transfer shifts weight forward (Session 9!) → Front handles ~75% of braking
✓ Brake fade due to heat (pad friction coefficient drops with temperature)
HYDRAULIC BRAKE SYSTEMS:
✓ Pascal's principle: P = F/A, enables force multiplication
✓ Master cylinder: Converts pedal force to hydraulic pressure
✓ Brake booster: Vacuum-assist reduces pedal effort (2,000+ N assist)
✓ Disc brakes: Better heat dissipation, used on front (always) and increasingly rear
✓ Drum brakes: Still used on rear of economy cars (cost savings)
✓ Typical hydraulic pressure: 40-100 bar during braking
BRAKE FORCE DISTRIBUTION:
✓ Ideal distribution changes with deceleration (due to load transfer)
✓ Proportioning valve: Mechanical solution, limits rear pressure above threshold
✓ Load-sensitive valve: Adapts to vehicle load (trucks)
✓ Design goal: Front locks slightly before rear (safer)
ANTI-LOCK BRAKING SYSTEM (ABS):
✓ Optimal slip: 10-20% (maximum friction, NOT at lockup!)
✓ Components: Wheel speed sensors (4), ECU, hydraulic modulator (8 valves + pump)
✓ Control: Modulate pressure 10-20 Hz to maintain optimal slip
✓ Benefits: Shorter stopping distance + steering maintained
✓ EBD: Electronic brake distribution using ABS hardware (adapts to load/conditions)
You can now design complete brake systems from first principles!

## Slide 29: Connection to Next Sessions
Today: Controlled longitudinal motion (braking). Next: Control lateral motion (steering) and vertical motion (suspension).
Session 11: Steering Systems — How to control direction while maintaining vehicle dynamics
Ackermann geometry (prevent tire scrub during turns)
Steering ratio calculations
Power steering (hydraulic and EPAS - Electric Power Assisted Steering)
Steering feel and feedback (why it matters)
Session 12: Suspension Systems — How to manage load transfer we calculated today and Session 9
Spring-mass-damper physics (ride comfort vs handling trade-off)
Suspension types (McPherson, double wishbone, multi-link)
Anti-roll bars: Reduce lateral load transfer during cornering!
Electronic adaptive suspension (real-time damping adjustment)
Integration: — Braking (today) + Steering (Session 11) + Suspension (Session 12) = Complete chassis control — All managed by chassis ECUs in modern vehicles
Session 19 (later): Electronic Stability Control (ESC) - integrates braking, steering, powertrain for stability
Building toward: Complete understanding of vehicle dynamics and control systems!

## Slide 30: Assignment & Q&A
Assignment (Due before Session 11):
Problem 1: Design a hydraulic brake system:
Given vehicle: — Mass: 1,800 kg (SUV)
Wheelbase: 3.0 m, CG height: 0.75 m (higher than car!)
Static distribution: 52% front, 48% rear
Wheel radius: 0.35 m
Tire-road μ = 0.80 (dry), 0.55 (wet)
Calculate:
a) Maximum deceleration (dry road)
b) Load transfer and dynamic weight distribution
c) Braking force required at each axle (assume ideal 75:25 distribution)
d) Brake torque required at each wheel
e) If front disc effective radius is 140 mm and pad μ = 0.38, calculate required clamping force
f) If caliper has 4 pistons of 40 mm diameter each, calculate required hydraulic pressure
g) Design master cylinder (bore diameter) if driver can apply 600 N with brake booster assistance
Problem 2: ABS Analysis:
For the same vehicle, during emergency braking at 80 km/h on wet road (μ = 0.55):
a) Calculate stopping distance WITH perfect ABS (maintains optimal 15% slip)
b) Calculate stopping distance WITHOUT ABS (rear wheels lock, μ_kinetic = 0.45 for locked wheels)
c) Calculate percentage improvement in stopping distance
d) At what vehicle speed does ABS activate if rear wheel slip exceeds 20%?
Problem 3: Proportioning Valve Design:
Design a proportioning valve for the SUV that:
Allows 1:1 distribution up to 50 bar (knee point)
Above 50 bar, rear pressure increases at 50% rate of front pressure
a) Calculate rear pressure when front pressure is 90 bar
b) Plot front vs rear pressure graph (0-100 bar range)
c) Explain why this prevents rear lockup during hard braking
Discussion Questions for Q&A: — Why do performance cars have larger front brakes than rear? (load transfer → front handles most braking)
Can ABS reduce stopping distance on gravel or loose surfaces? (Sometimes NO - locked wheels \"dig in\" can be better!)
Why does brake fluid need to be changed every 2 years? (absorbs moisture → lower boiling point → vapor lock risk)
What is brake-by-wire and why is it used in EVs? (no engine vacuum for booster, electric actuation, regen braking integration)
How does regenerative braking in hybrids/EVs integrate with hydraulic brakes? (blended braking - ECU coordinates)
30 minutes for your questions.

## Slide 31: Real-World Brake System Integration
Final thought: Modern braking is a complex integrated system:
Electronics Integration: — ABS ECU: Wheel slip control
ESC ECU: Stability control (Session 19) - uses individual wheel braking
Regen braking controller (Hybrids/EVs): Coordinates electric motor braking with hydraulic
ADAS systems: Autonomous Emergency Braking (AEB) - applies brakes automatically
Hill Hold Assist: Maintains brake pressure on slopes
CAN Bus Communication: — ABS broadcasts wheel speeds to other ECUs
ESC commands brake actuators
Engine ECU receives braking status (cut fuel during braking)
Instrument cluster displays warnings
Future: — Brake-by-wire: Fully electronic (no hydraulic connection pedal → wheels)
Redundant systems: Dual actuators for fail-safe operation
Predictive braking: Uses sensors to anticipate need for braking
As automotive electronics engineers, you'll: — Program ABS/ESC algorithms
Integrate multiple brake control systems
Develop fail-safe strategies
Tune control parameters for optimal performance
Understanding the mechanics and hydraulics (today) is ESSENTIAL for designing the electronics!
See you in Session 11 for Steering Systems!

## Slide 32: 📊 PPT DESIGN GUIDANCE
Visual Elements to Include:
Consistency: Maintain professional engineering template from Sessions 1-9
System-focused: Clear hydraulic system diagrams, component cutaways
Calculations prominent: Show worked examples with clear step-by-step math
Color coding: — Blue for hydraulic fluid flow paths
Red for brake force/pressure (high values)
Green for ABS sensor signals
Orange for heat/temperature warnings
Purple for electronic control signals
Slide 3: Stopping distance reality – Establishes safety criticality
Slide 10: Complete braking force calculation – Applies Sessions 2 & 9
Slide 12: Pascal's principle – Foundation of hydraulic systems
Slide 15: Disc brake caliper cutaway – Most common system
Slide 17: Disc vs drum comparison – Engineering trade-offs
Slide 23: ABS control algorithm – Core electronic control logic
Slide 26: Complete system design – Integration of all concepts
Slide 27: Summary formulas – Comprehensive reference
Slide 12: Animated hydraulic pressure transmission (master → slave cylinder)
Slide 13: Master cylinder operation (piston movement, fluid flow)
Slide 15: Caliper actuation (piston pushing pad against disc)
Slide 19: Proportioning valve operation (knee point, slope change)
Slide 21: Wheel slip visualization (rolling vs locked wheel)
Slide 23: ABS cycle animation (pressure modulation over time)
Slide 24: Time-series graphs with animated markers showing ABS intervention points
Component photos: Real brake discs, calipers, master cylinder, ABS modulator
Cutaway diagrams: Professional engineering cutaways (disc brake assembly, drum brake, master cylinder)
Hydraulic schematics: Flow diagrams showing fluid paths through complete system
Graphs: Brake balance diagram, friction vs temperature, slip ratio vs friction coefficient
Comparison tables: Disc vs drum, with ABS vs without
Calculation worksheets: Complete worked examples with highlighting

## Slide 33: 🎯 INSTRUCTOR NOTES
Safety/Ethics Notes:
Build on previous sessions: Session 2 (friction), Session 9 (load transfer) applied throughout
System approach: Show how components integrate into complete functional system
Safety emphasis: Highlight life-saving importance of proper brake system design
Electronics integration: Connect mechanical/hydraulic to electronic control (ABS, EBD)
Real-world grounding: Use actual brake specifications, real accident statistics
Challenge 1: "Why is ABS better if optimal slip is 10-20%, not 0%?"
How to address: Show friction vs slip curve - peak friction occurs at ~10-20% slip, then drops off toward lockup (100%). Static friction (0% slip) is high, but once wheel starts slipping, peak is at moderate slip, not at full lockup. Kinetic friction (sliding) is always lower than peak static/slip friction.
Challenge 2: "How does proportioning valve 'know' when pressure is too high for rear?"
How to address: It doesn't "know" braking force - it's purely pressure-sensitive. Spring is calibrated to start compressing at specific pressure threshold (e.g., 40 bar). Above that, mechanical valve design creates slope change. Not adaptive to conditions - that's why EBD is better (uses wheel speed sensors to detect actual slip).
Challenge 3: "If ABS cycles 10-20 times per second, doesn't that make stopping distance longer (pressure not constant)?"
How to address: Without ABS, locked wheel has LOWER friction (μkinetic < μstatic). ABS keeps slip near optimal, which has HIGHER friction than locked. Even though pressure cycles, average braking force is higher because friction coefficient is higher. Show data: With ABS ~0.85μ average, without ABS ~0.65μ (locked) → 30% more friction with ABS!
Challenge 4: "Why do we need brake booster? Can't we just make pedal lever ratio higher?"
How to address: Pedal travel would be excessive! If pedal ratio is 10:1 to get enough force, pedal would need to move 10× master cylinder stroke → maybe 40-60 cm pedal travel! Driver's leg can't reach. Booster adds force WITHOUT increasing pedal travel. Show trade-off: force multiplication vs travel multiplication.
If running short: — Condense drum brake details (Slide 16) - just mention they exist, focus on disc
Reduce proportioning valve details (Slide 19) - show concept, skip detailed analysis
Combine ABS components and algorithm (Slides 22-23) into overview
Move complete design example (Slide 26) to assignment
If running long: — Move disc vs drum comparison (Slide 17) to assignment reading
Skip brake balance diagram details (Slide 20) - just mention concept
Reduce EBD explanation (Slide 25) - briefly mention it uses ABS hardware
Core content (must cover): — Slides 8-10 (Friction braking fundamentals and force calculations)
Slide 12-13 (Hydraulic principles and master cylinder)
Slide 15 (Disc brake operation - most common)
Slides 21-23 (ABS operation and control - critical for electronics engineers)
Slide 26 (Complete system integration)
Slide 3: Share personal story or local accident statistics - make it real and relevant
Slide 11: If possible, show video of brake disc glowing red during repeated braking (racing footage)
Slide 12: Demonstrate Pascal's principle with syringes if available (small syringe pushing large syringe)
Slide 15: Show real brake caliper and disc if available - students can see component
Slide 21: Demonstrate on wheeled chair - lock wheels (can't steer), vs rolling with brakes (can steer)
Slide 24: Play sound of ABS activating (grinding/buzzing) - many students have heard but didn't know what it was
Q&A: Be ready for questions about:
Carbon-ceramic brakes: Why so expensive? (Exotic materials, better fade resistance, lighter, but brittle)
Brake cooling ducts (performance cars): Force air to brakes for cooling
Electronic parking brake (EPB): Electric motor instead of cable, integrates with hill hold
Autonomous emergency braking (AEB): Uses radar/camera to detect collision, applies brakes automatically
Brake fluid types: DOT 3/4/5/5.1 differences (boiling point, hygroscopic properties)
Critical safety system: Any brake system failure can be fatal - emphasize design rigor
Maintenance importance: Brake fluid changes, pad replacement critical - neglect is dangerous
ABS and ESC mandatory: Regulations save lives (show accident reduction statistics)
Don't modify brake systems: Aftermarket "upgrades" can make things worse if not engineered properly
Professional responsibility: As engineers, you design systems people trust with their lives

## Slide 34: ✅ Session Success Criteria
Students leave able to:
✓ Apply friction principles to calculate braking force using tire-road friction and normal load
✓ Calculate braking deceleration and stopping distance for given conditions
✓ Describe hydraulic brake system components and operation (master cylinder, booster, calipers)
✓ Compare disc and drum brakes with performance analysis
✓ Explain ABS operation and wheel slip control principle
✓ Describe brake force distribution and proportioning valve role
Most importantly: Students understand complete brake system design from first principles (friction, load transfer, hydraulics), can apply Sessions 2 and 9 knowledge to real systems, and understand the electronic control systems (ABS, EBD) they'll program as automotive electronics engineers.

## Slide 35: 📝 ADDITIONAL NOTES
Electronics Deep Dive:
Session 2 (Friction): F = μN is basis for all braking force calculations
Session 9 (Dynamics): Load transfer during braking directly determines front/rear force distribution
Sessions 1-3 (Foundation): Energy calculations (KE to heat), force-deceleration relationships
Preview steering throughout:
"ABS maintains steering during braking → Session 11 shows how steering actually works
"Load transfer affects tire grip → Session 11 explains how this impacts steering geometry
"Optimal slip for braking is ~15% → Session 11 will show lateral slip for cornering
Regulatory requirements: ECE R13 (international), FMVSS 105/135 (US), BS (India) - minimum deceleration, fade test, ABS mandatory
Testing: Track testing, brake dynamometer, thermal testing, durability testing
Failure modes: Loss of fluid, vapor lock, pad glazing, disc warping - engineers must anticipate
Cost considerations: Disc vs drum choice often driven by cost (~$50-100 difference per axle)
For electronics students, emphasize:
CAN bus integration: ABS broadcasts wheel speeds (50-100 Hz), receives brake requests from ADAS
Sensor signal processing: Hall-effect sensor outputs pulse train → ECU calculates frequency → wheel speed
PWM valve control: Solenoid valves use PWM for precise pressure control (not just on/off)
Diagnostic codes: OBD-II fault codes for ABS (C-codes), read via scan tool
Calibration: ABS control parameters tuned for specific vehicle (thresholds, PID gains)

## Slide 36
End of Session 10 Framework