## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 11: Steering Systems'

## Slide 2: Steering Systems
Session 11 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title Slide
Instructor Narration:
Welcome to Session 11: Steering Systems. Today, we're going to solve one of the most elegant geometric problems in automotive engineering—how to make a vehicle turn smoothly when all four wheels are traveling in different circles.

## Slide 4: The Fundamental Steering Challenge
Instructor Narration:
Let me show you the problem we need to solve.
When a car turns, imagine looking at it from above. The inside front wheel is traveling in the smallest circle. The outside front wheel is traveling in a larger circle. The rear wheels are on even larger circles.
The Problem: If all wheels pointed in exactly the same direction during a turn, what would happen?
[PAUSE for student thinking]
The tires would scrub against the road surface. They'd be fighting each other. This creates:
Tire wear
Increased steering effort
Reduced grip (bad for cornering!)
Poor handling feel
So we need a geometric solution where each wheel points in exactly the right direction for its particular circular path.
KEY INSIGHT BOX:
STEERING CHALLENGE: Each wheel must follow its own unique circular path Inner wheels → smaller radius → sharper angle Outer wheels → larger radius → gentler angle Solution: Ackermann Steering Geometry

## Slide 5: Ackermann Steering Geometry - The Principle
Vehicle wheelbase (L)
Track width (t)
Inner wheel angle (δᵢ)
Outer wheel angle (δₒ)
Instantaneous center of rotation (ICR)
Extension lines from both front wheels meeting at ICR
Instructor Narration:
The solution was discovered in 1817 by a German carriage designer named Georg Lankensperger, but patented by his agent Rudolph Ackermann in England. So we call it Ackermann steering geometry.
The principle is beautifully simple:
All wheels must rotate about the same instantaneous center.
Look at this diagram. When we extend imaginary lines through both front wheels, they must meet at a single point—the instantaneous center of rotation (ICR). The rear axle centerline also passes through this point.
This geometric constraint gives us a relationship between the inner and outer wheel angles.
EQUATION DISPLAY:
ACKERMANN PRINCIPLE: cot(δₒ) - cot(δᵢ) = t/L Where: δᵢ = Inner wheel steering angle (deg) δₒ = Outer wheel steering angle (deg) t = Track width (wheel center to wheel center) (m) L = Wheelbase (front axle to rear axle) (m)
Instructor Narration (continued):
This equation tells us: for any given inner wheel angle δᵢ, there is one correct outer wheel angle δₒ that satisfies pure rolling without slip.
The outer wheel always turns at a smaller angle than the inner wheel. Why? Because it's traveling in a larger circle.

## Slide 6: Simplified Ackermann Approximation
Instructor Narration:
For small steering angles—typical of normal driving, not tight parking maneuvers—we can use a simpler approximation:
Simplified Ackermann (for small angles):
δₒ ≈ δᵢ × [1 - (t/L)]
But for precise calculations and larger angles (parking, U-turns), we use the full cotangent relationship.
Let me show you how to use this in practice.

## Slide 7: Turning Radius Calculation
Instructor Narration:
Once we know the steering angles, we can calculate the vehicle's turning radius.
The turning radius R is measured from the instantaneous center to the center of the rear axle (not the front axle, notice!).
From basic geometry:
For the inner wheel:
R = L / tan(δᵢ)
For the outer wheel:
R = L / tan(δₒ)
But these give slightly different values unless we have perfect Ackermann. In practice, we use the average front wheel angle:
δ_avg = (δᵢ + δₒ) / 2 R ≈ L / tan(δ_avg)
Or if you only know the steering wheel angle θ_SW, you need to account for the steering ratio:
δ_avg = θ_SW / (Steering Ratio) R = L / tan(δ_avg)
Instructor Narration (continued):
Smaller wheelbase L → smaller turning radius → more maneuverable vehicle. That's why city cars have short wheelbases!
Larger steering angle δ → smaller turning radius → tighter turns.
KEY FORMULA BOX:
TURNING RADIUS: R = L / tan(δ_avg) Where: R = Turning radius (m) [measured at rear axle center] L = Wheelbase (m) δ_avg = Average front wheel steering angle (deg or rad) Small angle approximation (δ in radians): R ≈ L / δ_avg

## Slide 8: Worked Example - Ackermann Calculation
Instructor Narration:
Let's work through a complete example using our Honda Civic.
GIVEN DATA: — Wheelbase L = 2.7 m
Track width t = 1.52 m
Inner wheel angle δᵢ = 35° (tight turn, parking scenario)
Find: Outer wheel angle δₒ and turning radius R
SOLUTION:
Step 1: Convert angles to radians for calculation
δᵢ = 35° × (π/180) = 0.6109 rad
Step 2: Apply Ackermann equation
cot(δₒ) - cot(δᵢ) = t/L cot(δₒ) = cot(δᵢ) + (t/L) cot(δᵢ) = 1/tan(0.6109) = 1/0.7002 = 1.4282 cot(δₒ) = 1.4282 + (1.52/2.7) = 1.4282 + 0.5630 = 1.9912 δₒ = arccot(1.9912) = arctan(1/1.9912) = arctan(0.5022) = 0.4665 rad = 26.7°
Step 3: Calculate average steering angle
δ_avg = (35° + 26.7°) / 2 = 30.85° = 0.5387 rad
Step 4: Calculate turning radius
R = L / tan(δ_avg) = 2.7 / tan(0.5387) = 2.7 / 0.5960 = 4.53 m
RESULTS: — Outer wheel angle: 26.7° (8.3° less than inner wheel)
Turning radius: 4.53 m (measured at rear axle center)
Turning circle diameter: ~9 m (for complete U-turn)
Instructor Narration (continued):
Notice the outer wheel turns 8.3 degrees less than the inner wheel. This is the Ackermann effect preventing tire scrub.
A 4.53-meter turning radius gives this Civic excellent maneuverability for city driving and parking.

## Slide 9: Practice Problem 1 - Turning Radius Calculation
PRACTICE PROBLEM:
A large SUV has the following specifications: - Wheelbase L = 3.0 m - Maximum front wheel steering angle δ_max = 40° Calculate: (a) Minimum turning radius (b) Turning circle diameter (for complete 180° turn) (c) Compare with the Honda Civic (R = 4.53 m)
SOLUTION (for instructor reference, reveal after student attempt):
(a) Minimum turning radius:
R_min = L / tan(δ_max) = 3.0 / tan(40°) = 3.0 / 0.8391 = 3.58 m
(b) Turning circle diameter:
Turning circle = 2 × R_min = 2 × 3.58 = 7.16 m
(c) Comparison: — SUV: R_min = 3.58 m (but remember: longer wheelbase = less maneuverable)
Civic: R_min = 4.53 m at δ = 30.85°
Wait—the SUV has a smaller turning radius? Actually, NO. This calculation used a 40° maximum angle. Let's recalculate at the same 30.85° angle:
R_SUV @ 30.85° = 3.0 / tan(30.85°) = 3.0 / 0.5960 = 5.03 m
Now we see the truth: longer wheelbase = larger turning radius = harder to maneuver.

## Slide 10: Real-World Ackermann Implementation
Instructor Narration:
How do we actually achieve Ackermann geometry mechanically?
The secret is in the steering linkage geometry. Look at this real steering system. The steering arms are not parallel—they're angled inward at the base.
When the linkage pushes the inner wheel to turn, the geometry naturally creates a larger angle on the inner wheel compared to the outer wheel.
MECHANICAL IMPLEMENTATION:
Steering arms are angled inward (typically 10-15° from vertical axis)
Tie rods connect left and right wheels via a track rod
As the rack moves (we'll discuss rack-and-pinion soon), the geometry creates the Ackermann effect
The angle of the steering arms determines how much Ackermann effect you get
100% Ackermann vs Parallel Steering: — 100% Ackermann: Perfect geometry, no tire scrub (ideal for low-speed maneuvers)
Parallel steering: Both wheels turn equal amounts (used in some race cars for high-speed stability)
Most road cars: 60-80% Ackermann (compromise between low-speed maneuverability and high-speed stability)

## Slide 11: Transition - Beyond Pure Geometry
Instructor Narration:
We've solved the fundamental geometry problem—how to make all four wheels turn about the same center.
But there's more to steering than just horizontal angles.
When you look at a car from the front or side, you'll see the wheels aren't perfectly vertical or aligned. There are several invisible angles built into every steering system:
Caster (front-to-back tilt)
Camber (side-to-side tilt)
Toe (slight inward/outward pointing)
Kingpin inclination (steering axis angle)
These angles seem small, but they have enormous effects on handling, tire wear, and steering feel.
Let's explore why these angles exist and what they do.

## Slide 12: PART 2: TRIGGER - "Steering Alignment Parameters

## Slide 13: The Four Alignment Angles
Instructor Narration:
Every wheel has four critical alignment angles. These are the 'DNA' of your steering system.
Let me introduce them:
1. CASTER (Side View) — Tilt of the steering axis front-to-back
Measured in degrees
Typical value: +2° to +7° (positive caster)
2. CAMBER (Front View) — Tilt of the wheel top-to-bottom
Measured in degrees
Typical value: -0.5° to +1° (slightly negative for modern cars)
3. TOE (Top View) — Slight inward or outward pointing
Measured in mm or degrees
Typical value: 0-3 mm toe-in (front wheels)
4. KINGPIN INCLINATION (Front View) — Tilt of the steering axis inward at the top
Measured in degrees
Typical value: 5° to 15°
These four angles work together to create:
Self-centering steering
Straight-line stability
Proper tire contact patch
Minimal steering effort
Even tire wear

## Slide 14: Caster Angle - Straight-Line Stability
Instructor Narration:
Caster is the front-to-back tilt of the steering axis.
Look at this side view. The steering axis (the imaginary line through the ball joints or strut mounts) is tilted backward at the top. This is positive caster.
Why do we want positive caster?
It creates a self-centering effect, just like a shopping cart wheel!
The Physics:
When the steering axis is tilted back, the tire contact patch is behind the point where the steering axis intersects the road. This creates a mechanical trail (also called caster trail).
Mechanical Trail = Caster Angle × (Tire Radius) Typical values: 20-40 mm
When you're driving straight and hit a bump that disturbs the wheel, the mechanical trail creates a restoring torque that pulls the wheel back to center.
Effects of Caster:
✅ Positive Caster (typical): — Self-centering steering (hands-off stability)
Increased straight-line stability
Slightly heavier steering effort (more trail = more torque needed)
Better feedback to driver
❌ Negative Caster (rare, avoided): — No self-centering
Wandering steering
Unstable at speed
Real-World Values: — Economy cars: +2° to +4° (lighter steering, adequate stability)
Sports cars: +5° to +7° (strong self-centering, better feel, heavier steering)
Trucks/SUVs: +3° to +5° (balance of stability and effort)
Instructor Narration (continued):
Have you noticed that when you let go of the steering wheel after a turn, it automatically returns to center? That's positive caster at work. Race cars use very high caster (8-10°) for maximum feedback, but your arms would get tired in daily driving!

## Slide 15: Camber Angle - Tire Contact Optimization
Instructor Narration:
Camber is the inward or outward tilt of the wheel when viewed from the front.
Negative Camber: Top of wheel tilts inward (toward the vehicle center)
Positive Camber: Top of wheel tilts outward (away from vehicle center)
Why do we use camber?
It's all about maintaining optimal tire contact during cornering.
The Physics:
When a car corners, the body rolls outward (we calculated this roll motion in Session 9's lateral load transfer!). This body roll would cause the outside tire to lean outward, reducing contact patch area.
By starting with slight negative camber at rest, when the car corners and rolls, the tire straightens up and maintains full contact with the road.
Effects of Camber:
✅ Slight Negative Camber (-0.5° to -2°): — Better cornering grip (tire stays flat during body roll)
More even tire wear (if set correctly)
Common in modern sports cars
⚖️ Zero Camber (0°): — Maximum straight-line contact patch
Simple, no special effects
Common in trucks and economy cars
❌ Excessive Negative Camber (-3° or more): — Inner tire edge wears rapidly
Reduced straight-line grip
Used only in racing (extreme cornering grip prioritized)
❌ Positive Camber (+1° or more): — Outer tire edge wears rapidly
Generally avoided in modern cars
Was used in old vehicles with solid axles
Real-World Values: — Economy cars: -0.5° to 0° (prioritize tire wear and comfort)
Sports cars: -1° to -2° (prioritize cornering)
Race cars: -3° to -5° (maximum cornering, tire wear ignored)
Instructor Narration (continued):
If you've ever seen those cars with extremely tilted wheels (stance culture), they're running -10° to -15° camber. This is purely aesthetic—it destroys tires and handling. Don't do it on your personal car!

## Slide 16: Toe Angle - Straight-Line Tracking
Instructor Narration:
Toe is the slight inward or outward pointing of the wheels when viewed from above.
Toe-In: Front edges of wheels closer together than rear edges
Toe-Out: Front edges of wheels farther apart than rear edges
Toe is measured in millimeters (distance difference between front and rear of tires) or degrees.
Toe-In: Front wheels point slightly inward [ /\ ] Toe-Out: Front wheels point slightly outward [ \/ ]
Why do we use toe?
It compensates for suspension compliance and road forces.
The Physics:
When you're driving, road forces push and pull on the wheels. On a FWD car, the driving force tends to push the front wheels outward. On a RWD car, resistance tends to push them inward.
By pre-setting a small toe angle, the wheels align themselves perfectly when driving forces are applied.
Effects of Toe:
✅ Slight Toe-In (0-3 mm): — Improved straight-line stability
Slight inward pull counteracts road forces
Common on RWD cars and rear axles
✅ Slight Toe-Out (0-2 mm): — Quicker steering response (wheels already pointed outward for turn initiation)
Less straight-line stability
Sometimes used on FWD front axles
❌ Excessive Toe (>5 mm either direction): — Rapid tire wear (tires are constantly scrubbing)
"Feathering" wear pattern on tire edges
Reduced fuel economy (tires fighting each other)
❌ Zero Toe: — Can work if suspension is very stiff
May cause wandering on rough roads
Tires may wear unevenly
Real-World Values: — Front axle (FWD): 0-2 mm toe-out
Front axle (RWD): 1-3 mm toe-in
Rear axle (most cars): 1-3 mm toe-in (for stability)
Instructor Narration (continued):
Toe is the most critical alignment for tire wear. If your toe is off by even 5 mm, your tires will develop a 'feathered' edge pattern and wear out in 10,000 km instead of 50,000 km. Always check toe when you replace suspension components!

## Slide 17: Kingpin Inclination (KPI) - Steering Geometry
Instructor Narration:
The fourth angle is Kingpin Inclination (KPI)—also called Steering Axis Inclination (SAI).
This is the inward tilt of the steering axis when viewed from the front.
The Steering Axis is the imaginary line connecting:
Top ball joint (or strut mount) to
Lower ball joint
This axis is tilted inward at the top, typically 5° to 15°.
Why tilt the steering axis?
Two reasons: self-centering and reduced scrub radius.
Effect 1: Self-Centering (Vertical Lift)
When you turn the steering wheel, the tilted steering axis tries to lift the front of the car. The weight of the car resists this lift, creating a torque that wants to return the wheel to center.
Try this experiment: Jack up your car's front wheel. Turn the steering—it's easy! Now lower the car and try turning—much harder. That's KPI creating self-centering force.
Effect 2: Scrub Radius
The scrub radius is the horizontal distance between:
Where the steering axis intersects the road, and
The center of the tire contact patch
Positive Scrub Radius: Steering axis inside contact patch Zero Scrub Radius: Steering axis at contact patch center Negative Scrub Radius: Steering axis outside contact patch
Modern cars use slightly negative scrub radius because:
Better straight-line stability during braking (especially if one brake fails)
Reduced steering kickback over bumps
Improved feel and feedback
Real-World Values: — KPI: 5° to 15° (not adjustable, built into suspension geometry)
Scrub Radius: —5 mm to +15 mm (varies by design)
Instructor Narration (continued):
KPI is not adjustable—it's designed into the suspension geometry. If your KPI is wrong, it means suspension components are bent or damaged (usually from a serious impact). This requires replacement, not adjustment.
KEY TAKEAWAY BOX:
FOUR ALIGNMENT ANGLES SUMMARY: 1. CASTER: Self-centering (shopping cart effect) 2. CAMBER: Tire contact during cornering 3. TOE: Straight-line tracking and tire wear 4. KPI: Self-centering and scrub radius control Only Camber and Toe are regularly adjusted during wheel alignment. Caster is sometimes adjustable (with special bolts). KPI is never adjustable (designed into suspension).

## Slide 18: PART 3: RISING ACTION - "Converting Rotation to Translation

## Slide 19: The Steering Mechanism Challenge
Instructor Narration:
We've mastered the geometry (Ackermann) and the alignment angles (caster, camber, toe, KPI).
Now we need to solve a mechanical problem:
How do we convert the driver's rotational input at the steering wheel into linear motion at the wheels?
The steering wheel rotates (angular motion). But the wheels need to pivot left and right (linear motion of the tie rods pushing/pulling the steering arms).
We need a mechanical converter—a mechanism that transforms rotation into translation.
There are two main types:
Rack-and-Pinion (most common in modern cars)
Recirculating Ball (used in trucks, older cars, some SUVs)
Let's explore both.

## Slide 20: Rack-and-Pinion Steering
Instructor Narration:
Rack-and-pinion steering is the most common system in modern passenger cars.
The Mechanism:
The steering column has a small gear called the pinion (typically 8-12 teeth)
The pinion meshes with a rack (a flat bar with teeth cut into it)
When you turn the steering wheel, the pinion rotates
The rotating pinion pushes the rack left or right
The rack is connected to the tie rods, which push/pull the steering arms
The wheels pivot
Advantages:
✅ Simple design (fewer parts, less weight)
✅ Direct feel (immediate feedback from road to driver)
✅ Compact (fits transversely in front-wheel-drive cars)
✅ Efficient (less friction = less energy loss)
✅ Precise (little mechanical play)
Disadvantages:
❌ Transmits road shocks to steering wheel (you feel every bump—some call this feedback, others call it harshness)
❌ Limited travel (rack length limits maximum steering angle)
❌ Can be harder to package in some vehicle layouts
Where It's Used: — Most passenger cars (sedans, hatchbacks, coupes)
Sports cars (valued for direct feel)
Modern SUVs and crossovers
Front-wheel-drive vehicles (compact packaging advantage)
Instructor Narration (continued):
The beauty of rack-and-pinion is its simplicity. Fewer parts mean less that can go wrong. That's why 90% of new cars use this design.

## Slide 21: Recirculating Ball Steering
Instructor Narration:
Recirculating ball steering is an older design that's still used in heavy-duty applications.
The Mechanism:
The steering column connects to a worm gear (threaded shaft)
A ball nut (with internal threads) sits on the worm gear
Tiny ball bearings recirculate through channels between the worm and nut, reducing friction
The ball nut has teeth that mesh with a sector shaft
The sector shaft rotates and moves the pitman arm
The pitman arm pushes/pulls the center link and tie rods
The wheels pivot
Advantages:
✅ Handles high loads (strong, suitable for trucks and heavy vehicles)
✅ Isolates driver from road shocks (smoother feel, less kickback)
✅ Durable (long service life with proper lubrication)
✅ Variable ratio possible (sector shaft geometry can vary the steering ratio through the turn)
Disadvantages:
❌ Complex (more parts, higher weight)
❌ Less direct feel (mechanical isolation = less feedback)
❌ Mechanical play (slight dead zone at center, especially when worn)
❌ Larger package (harder to fit in compact cars)
❌ Requires lubrication (sealed gearbox with gear oil)
Where It's Used: — Heavy-duty trucks (Ford F-250/F-350, Ram 2500/3500)
Older SUVs (pre-2000s design)
Some body-on-frame SUVs (for durability)
Classic cars (standard technology from 1950s-1990s)
Instructor Narration (continued):
Recirculating ball is overbuilt and bombproof. If you're towing 5,000 kg with your truck, you want recirculating ball steering. But for normal passenger cars, it's overkill—rack-and-pinion is lighter, cheaper, and more responsive.

## Slide 22: Steering Ratio - Amplification vs Response
Instructor Narration:
Here's a critical parameter: Steering Ratio.
Definition:
Steering Ratio = (Steering Wheel Rotation) / (Front Wheel Rotation)
For example, a 15:1 ratio means:
Turn the steering wheel 15 degrees →
Front wheels turn 1 degree
Lower Ratio (e.g., 12:1 - 14:1): — Quicker steering response (small steering input → large wheel movement)
More sensitive (easier to oversteer with small corrections)
Heavier steering effort (less mechanical advantage)
Used in: Sports cars, performance vehicles
Higher Ratio (e.g., 18:1 - 24:1): — Slower steering response (large steering input → small wheel movement)
More stable (easier to control, less twitchy)
Lighter steering effort (more mechanical advantage)
Used in: Trucks, SUVs, older cars without power steering
Typical Values: — Sports cars: 12:1 to 14:1 (quick, responsive)
Passenger cars: 14:1 to 16:1 (balanced)
Trucks/SUVs: 17:1 to 24:1 (stable, easy to turn large wheel)
Race cars: 10:1 to 12:1 (maximum responsiveness)
Calculating Steering Ratio:
For rack-and-pinion:
Steering Ratio = (Pinion Pitch Diameter × 360°) / (Rack Travel per Wheel Revolution) Simplified: Steering Ratio = 360° / (Rack Movement per Degree of Pinion Rotation × Steering Arm Length)
For recirculating ball:
Steering Ratio = Worm Gear Turns / Sector Shaft Rotation
Instructor Narration (continued):
Here's the trade-off: Quick steering (low ratio) is fun for spirited driving, but exhausting for parking. Slow steering (high ratio) is easy for maneuvering, but unresponsive on the highway.
Modern cars solve this with variable-ratio steering or speed-sensitive power steering (we'll cover this soon).

## Slide 23: Steering Ratio Calculation Example
WORKED EXAMPLE:
GIVEN: — Rack-and-pinion system
Pinion diameter: 40 mm (radius = 20 mm)
Steering arm length: 150 mm
Rack travel for full lock: ±100 mm (200 mm total travel)
Front wheel total steering range: ±40° (80° total range)
FIND: Steering ratio
SOLUTION:
Step 1: Calculate rack travel per degree of wheel rotation
Rack travel per degree = Total rack travel / Total wheel rotation = 200 mm / 80° = 2.5 mm/°
Step 2: Calculate pinion rotation needed for this rack travel
When the pinion rotates, the rack moves by:
Rack movement = Pinion rotation (in radians) × Pinion radius Rack movement per degree of pinion = (π/180) × 20 mm = 0.349 mm/° of pinion rotation
Step 3: Calculate steering ratio
To move rack by 2.5 mm (to turn wheel by 1°): Pinion must rotate: 2.5 mm / 0.349 mm/° = 7.16° But this doesn't account for steering arm geometry. The actual ratio includes the lever arm effect: Steering Ratio ≈ 7.16 × 2 (typical mechanical advantage factor) ≈ 14.3:1
RESULT:
This vehicle has a 14.3:1 steering ratio—typical for a modern passenger car. This means turning the steering wheel 14.3° will turn the front wheels 1°.
QUICK CHECK: — Lock-to-lock steering wheel rotation = 40° × 14.3 = 572° ≈ 1.6 turns
This is typical for modern cars (1.5 to 2.5 turns lock-to-lock)
Instructor Narration:
Sports cars often have 2-2.5 turns lock-to-lock (quick steering). Older cars and trucks have 3-5 turns lock-to-lock (slow, easy steering). Modern cars are converging on 2.5-3 turns as the sweet spot with power steering assist.

## Slide 24: PART 4: CLIMAX - "The Power Assist Revolution

## Slide 25: The Need for Power Steering
Instructor Narration:
Imagine you're parking a 1950s car without power steering. The front wheels weigh 300 kg each, the tires are 200 mm wide, and you have an 18:1 steering ratio.
The steering effort required: 30-40 kg of force at the steering wheel rim. Your arms would be exhausted after parallel parking!
The Problem: — Heavier vehicles (especially front-wheel-drive with engine weight over front axle)
Wider tires (more contact patch = more friction to overcome when turning stationary)
Lower steering ratios desired (for quicker response)
All these factors increase steering effort.
The Solution: Add a power assist system that amplifies the driver's input.
Two types:
Hydraulic Power Steering (HPS) — Traditional, used since 1950s
Electric Power Assisted Steering (EPAS) — Modern, increasingly common
Let's explore both systems.

## Slide 26: Hydraulic Power Steering (HPS)
Instructor Narration:
Hydraulic Power Steering has been the standard for 70 years.
System Components:
Hydraulic Pump (belt-driven by engine)
Generates high-pressure hydraulic fluid (70-150 bar / 1000-2200 psi)
Runs continuously whenever engine is running
Typically a vane pump or gear pump
Fluid Reservoir — Holds power steering fluid (special hydraulic oil)
Usually integrated with pump
Rotary Valve (inside steering gear housing)
Senses steering torque applied by driver
Directs high-pressure fluid to appropriate side of piston/rack
Power Cylinder — Rack-and-pinion: fluid acts directly on rack
Recirculating ball: fluid acts on ball nut or external cylinder
Pressure/Return Lines — High-pressure hose from pump to gear
Low-pressure hose back to reservoir
How It Works:
At Rest (Driving Straight): — Pump runs continuously, but fluid circulates back to reservoir
No pressure buildup (fluid flows through open center of rotary valve)
No steering assist (driver effort is minimal for small corrections)
During Turn:
Driver applies torque to steering wheel
Torsion bar inside rotary valve twists slightly
Valve ports open, directing high-pressure fluid to one side of the power cylinder
Hydraulic pressure pushes the rack (or ball nut), assisting the turn
The harder you turn, the more the torsion bar twists, the more assist is provided
When you stop turning, the valve centers and pressure drops
Instructor Narration (continued):
The genius of hydraulic power steering is that it's proportional. Light touch = light assist. Heavy effort = heavy assist. The torsion bar acts as a force sensor, and the rotary valve acts as the control element.
KEY ADVANTAGE:
✅ Strong, consistent assist (can handle very heavy vehicles)
✅ Proven, reliable technology (70+ years of refinement)
✅ Good road feel (hydraulic fluid transmits feedback)
DISADVANTAGES:
❌ Energy waste (pump runs continuously, even when not steering)
❌ Fuel economy penalty (parasitic loss of 2-4 hp)
❌ Maintenance (fluid changes, hose/seal leaks)
❌ Fixed assist (same assist at all speeds—too light at highway speeds)

## Slide 27: Electric Power Assisted Steering (EPAS)
Instructor Narration:
Electric Power Assisted Steering (EPAS) is the future—and increasingly, the present.
Instead of a hydraulic pump, we use an electric motor to provide steering assist.
System Components:
Electric Motor (brushless DC motor, typically 400-1000W)
Column-assist: motor on steering column
Pinion-assist: motor on pinion gear
Rack-assist: motor directly on rack (most common in modern cars)
Torque Sensor (measures driver's steering effort)
Typically uses strain gauges or magnetoresistive sensors
Detects torsion bar twist angle (just like hydraulic system)
ECU (Electronic Control Unit) — Calculates required assist based on:
Driver torque input
Vehicle speed
Steering angle
Steering angle rate (how fast you're turning)
Vehicle yaw rate (from stability control system)
Commands motor to provide exact assist needed
Position Sensors — Steering angle sensor
Motor position sensor (for control feedback)
Power Supply — 12V electrical system (12V motor for small/medium cars)
48V electrical system (for larger vehicles, better efficiency)
How It Works:
Driver turns steering wheel
Torque sensor measures applied force
ECU reads:
Torque input
Vehicle speed (from CAN bus)
Current steering angle
ECU calculates required assist:
Low speed (parking): Maximum assist — Medium speed (city): Moderate assist — High speed (highway): Minimum assist (for stability and feel)
Motor applies calculated torque to column/pinion/rack
Driver feels reduced effort
Instructor Narration (continued):
The magic of EPAS is speed-sensitive assist. At 5 km/h in a parking lot, you can turn the wheel with one finger. At 120 km/h on the highway, the steering is heavier and more stable. The ECU adjusts the assist in real-time.
KEY ADVANTAGES:
✅ Energy efficient (motor only runs when steering, saves 0.2-0.4 L/100km fuel)
✅ Speed-sensitive (variable assist based on driving conditions)
✅ No maintenance (no fluid, no hoses, no leaks)
✅ Flexible tuning (engineers can program any assist curve via software)
✅ Enables advanced features: — Lane keeping assist (ADAS)
Self-parking
Autonomous driving
DISADVANTAGES:
❌ Early systems had poor feel (1990s-2000s EPAS felt numb)
❌ Complex electronics (ECU failure = total steering loss in some designs)
❌ Limited assist for very heavy vehicles (electric motors have power limits)
Modern Status: — ~80% of new passenger cars use EPAS
Hybrid and electric vehicles: 100% EPAS (no engine to drive hydraulic pump)
Heavy trucks: Still mostly hydraulic (need very high assist forces)

## Slide 28: EPAS Assist Curve - Speed-Sensitive Control
Instructor Narration:
Let me show you how EPAS creates that speed-sensitive assist magic.
This graph shows a typical EPAS assist curve:
X-axis: Vehicle speed (0 to 150 km/h)
Y-axis: Assist torque multiplier (0% to 100%)
At Low Speed (0-30 km/h): — 100% assist (maximum motor torque)
Why? You're parking, maneuvering in tight spaces
Need effortless steering
Stability is not critical (you're going slow)
At Medium Speed (30-80 km/h): — 60-80% assist (moderate motor torque)
Why? City and suburban driving
Balance between effort and feel
Gentle assist reduction maintains stability
At High Speed (80-150 km/h): — 20-40% assist (minimum motor torque)
Why? Highway cruising, high-speed corners
Need weighted steering feel for stability
Want to feel road feedback
Prevent oversteering with small inputs
Driver Torque Sensitivity:
The ECU also considers how hard you're turning:
Light correction (lane change): Minimal assist
Moderate turn (corner): Standard assist
Hard turn (emergency maneuver): Maximum assist (even at high speed)
Tuning Philosophies: — Comfort-oriented (Toyota, Lexus): Very light at all speeds, isolation from road
Sport-oriented (BMW, Porsche): Heavier steering, more feedback, less assist at high speed
Balanced (Honda, Mazda): Progressive curve, natural feel
Instructor Narration (continued):
This is where EPAS shines. Hydraulic systems can achieve speed-sensitive assist too (with speed-sensitive valves), but it's mechanical and fixed. EPAS is infinitely tunable through software. Engineers can create different 'modes' (Comfort, Sport, etc.) that change this curve instantly.

## Slide 29: Comparison - Hydraulic vs EPAS
Instructor Narration:
Let's directly compare the two technologies:
| Feature | Hydraulic Power Steering (HPS) | Electric Power Assisted Steering (EPAS) |
|-------------|------------------------------------|--------------------------------------------|
| Energy Source | Engine-driven hydraulic pump | Electric motor (battery/alternator) |
| Energy Efficiency | ❌ Poor (pump runs continuously) | ✅ Excellent (motor only runs when steering) |
| Fuel Economy Impact | -2% to -4% (parasitic loss) | -0.5% to -1% (minimal impact) |
| Assist Tuning | ⚠️ Mechanical (fixed or speed valve) | ✅ Software (infinitely adjustable) |
| Speed Sensitivity | ⚠️ Possible (with speed-sensitive valve) | ✅ Built-in (ECU-controlled) |
| Road Feel | ✅ Good (hydraulic feedback) | ⚠️ Variable (early systems poor, modern good) |
| Maintenance | ❌ Fluid changes, leak checks | ✅ None (sealed system) |
| Reliability | ✅ Proven (70+ years) | ✅ Modern systems reliable |
| Weight | ❌ Heavier (pump, lines, fluid) | ✅ Lighter (motor + ECU only) |
| Complexity | ⚠️ Moderate (mechanical) | ⚠️ Moderate (electronic) |
| Cost | ⚠️ Moderate | ⚠️ Moderate (decreasing) |
| ADAS Integration | ❌ Difficult | ✅ Easy (already ECU-controlled) |
| Failure Mode | ⚠️ Graceful (manual steering still works) | ⚠️ Depends on design (some fail to locked, others to manual) |
| Maximum Assist | ✅ Very high (suitable for heavy trucks) | ⚠️ Limited by motor power |
| Typical Applications | Heavy trucks, older cars, some SUVs | Modern passenger cars, hybrids, EVs |
Instructor Narration (continued):
The trend is clear: EPAS is taking over. It's more efficient, more flexible, and essential for autonomous driving features. But hydraulic steering isn't dead—it's still the best choice for heavy-duty applications where extreme assist forces are needed.
SAFETY NOTE:
Both systems are designed with fail-safe behavior:
If power steering fails, you revert to manual steering (heavy, but functional)
Modern EPAS systems have redundant sensors and fail-operational modes
Critical safety systems (ESC, ABS) are independent of steering assist

## Slide 30: Advanced EPAS Features - Beyond Basic Assist
Instructor Narration:
EPAS opens the door to advanced features that were impossible with hydraulic systems.
1. LANE KEEPING ASSIST (LKA) — Camera detects lane markings
If vehicle drifts toward line (without turn signal), EPAS gently steers back — Applies small corrective torque (driver can easily override)
Uses the same motor that provides steering assist
2. LANE CENTERING ASSIST — More active than LKA
Continuously adjusts steering to keep vehicle centered in lane
Common in adaptive cruise control systems
Driver must keep hands on wheel (monitors steering torque)
3. ACTIVE RETURN TO CENTER — After a turn, EPAS actively returns steering to center (not just passive caster effect)
Faster, more controlled return
Adjustable based on driving mode
4. SELF-PARKING (PARK ASSIST) — Driver shifts to reverse, system takes over steering
Ultrasonic sensors detect parking space
EPAS steers automatically while driver controls throttle/brake
Parallel, perpendicular, and angle parking modes
5. TRAFFIC JAM ASSIST / HIGHWAY PILOT — Combines adaptive cruise control + lane centering
EPAS maintains lane position
Hands-on system (Level 2 autonomy)
6. EVASIVE STEERING ASSIST — Detects imminent collision (radar/camera)
If driver steers to avoid, EPAS amplifies steering input — Helps execute emergency lane change faster
7. TORQUE VECTORING SIMULATION — EPAS can apply slight steering corrections during cornering
Mimics the effect of torque vectoring
Improves cornering stability
Instructor Narration (continued):
All of these features are only possible because EPAS is bidirectional:
Driver → Motor: Power assist (traditional function)
Motor → Steering: Active steering (ADAS functions)
Hydraulic systems can only do the first one. This is why every autonomous vehicle development program uses EPAS.
FUTURE TRENDS: — Steer-by-wire (no mechanical connection, full drive-by-wire)
Variable ratio steering (change steering ratio electronically)
Individual wheel steering (four-wheel steering with EPAS on rear axle too)

## Slide 31: PART 5: RESOLUTION - "Steering Feel & Integration

## Slide 32: Steering Feedback - The Art of "Feel"
Instructor Narration:
We've covered the mechanics and the power assist. But there's one more critical element: steering feel.
What is Steering Feel?
It's the information transmitted from the road, through the tires and steering system, to your hands.
Good steering feel tells you:
How much grip the tires have
What the road surface is like (smooth, rough, wet, icy)
Whether the car is understeering or oversteering
How much load is on the front tires
The Feedback Path:
Tire Contact Patch experiences forces (lateral force, self-aligning torque, road irregularities)
Steering Linkage transmits these forces as mechanical vibrations and torques
Steering Column delivers the torque to the steering wheel
Driver's Hands feel the torque, vibration, resistance
Driver's Brain processes this information (consciously and subconsciously)
Driver Adjusts steering input based on feedback
Key Feedback Mechanism: Self-Aligning Torque (SAT)
When a tire generates a lateral force (cornering), it creates a self-aligning torque that tries to straighten the wheel. This torque is transmitted to the steering wheel.
SAT ∝ Lateral Force × Pneumatic Trail Where: - Pneumatic Trail: Distance between tire center and lateral force application point - Typical value: 20-40 mm
As you approach the tire's grip limit: — SAT decreases (pneumatic trail reduces)
Steering feel becomes "light" or "vague
Experienced drivers sense this and know they're near the limit
Instructor Narration (continued):
This is why race car drivers can feel exactly when they're at the limit of grip. The steering goes light right before the tire starts sliding. Hydraulic power steering preserves this feedback reasonably well. Early EPAS systems filtered it out (made steering feel numb). Modern EPAS tries to recreate it electronically.

## Slide 33: Steering Feel - Hydraulic vs EPAS Challenges
Instructor Narration:
Hydraulic Power Steering:
✅ Natural feedback — Forces are transmitted mechanically through hydraulic fluid
✅ Self-aligning torque reaches driver's hands directly
✅ Road texture vibrations come through (some like this, some don't)
❌ Can't be tuned — Feedback is what it is (mechanical reality)
EPAS Challenges:
❌ Electric motor isolates mechanical feedback (motor acts as a damper)
❌ Early EPAS (1990s-2000s) felt completely numb (no feedback at all)
✅ Modern EPAS solution: Artificial feedback simulation
How Modern EPAS Creates Feedback:
Torque Sensor measures forces at steering column
ECU calculates expected self-aligning torque based on:
Steering angle
Lateral acceleration (from ESC sensors)
Vehicle speed
Tire model (programmed into ECU)
Motor applies simulated feedback torque
Driver feels recreated road feedback
Is it as good as hydraulic? — 2000s EPAS: No (too artificial, too filtered)
2010s EPAS: Getting close (better algorithms, faster processors)
2020s EPAS: Very close (machine learning, real-time adaptation)
Some manufacturers do it better than others: — Porsche, BMW: Excellent EPAS feel (heavy investment in tuning)
Mazda: Praised for natural EPAS feel (careful mechanical design + software)
Budget brands: Still somewhat numb (cost constraints on tuning)
Instructor Narration (continued):
Steering feel is part science (mechanical forces, control algorithms) and part art (subjective tuning, driver preference). Some drivers prefer isolated, smooth steering. Others want every pebble transmitted to their hands. Engineers must choose a philosophy and tune accordingly.

## Slide 34: Complete Steering System Integration
Instructor Narration:
Let's put everything together. Here's a complete modern EPAS rack-and-pinion steering system.
COMPONENT BREAKDOWN:
1. Steering Wheel — Diameter: 350-400 mm (sports cars smaller, trucks larger)
Airbag integrated
Multi-function controls (audio, cruise control, phone)
2. Steering Column — Collapsible design (safety feature for frontal impact)
Tilt and telescoping adjustment (driver comfort)
Torque sensor (measures driver input) ← Critical for EPAS
Steering angle sensor (for ESC, ADAS)
Universal joints (allow angle change between column and pinion)
3. EPAS Motor & ECU — Motor location options: — Column-assist (on column) - compact cars
Pinion-assist (on pinion) - mid-size cars
Rack-assist (on rack) - most common in modern cars
ECU (Electronic Control Unit):
Inputs: Torque sensor, angle sensor, vehicle speed, yaw rate
Outputs: Motor current (PWM control)
Runs at 100-200 Hz update rate
4. Steering Rack — Rack housing (aluminum or magnesium for light weight)
Rack bar with machined teeth
Pinion gear meshing with rack
Tie rod ends (ball joints for articulation)
Steering boots (protect from dirt and moisture)
5. Steering Arms & Tie Rods — Tie rods (adjustable length for toe alignment)
Steering arms (angled for Ackermann geometry)
Ball joints (allow vertical wheel movement + steering rotation)
6. Steering Knuckle — Connects steering system to suspension
Wheel hub mounted to knuckle
Ball joints (upper and lower, or strut mount + lower ball joint)
Brake caliper mounts to knuckle
Integration with Other Systems:
→ Electronic Stability Control (ESC): — Steering angle sensor provides input to ESC
ESC can detect oversteer/understeer
ESC may request EPAS to provide feedback torque (alert driver)
→ ABS: — Steering angle helps ABS optimize brake distribution
Prevents steering during hard braking (stability)
→ ADAS (Advanced Driver Assistance): — Lane keeping assist uses EPAS motor
Adaptive cruise with lane centering
Self-parking systems
→ Four-Wheel Steering (if equipped): — Front EPAS coordinates with rear steering actuators
Low speed: rear wheels steer opposite (tighter turning)
High speed: rear wheels steer same direction (stability)
Instructor Narration (continued):
Modern steering is not a standalone system—it's integrated with the entire vehicle dynamics control network. The steering angle sensor feeds data to 5-10 different ECUs. The EPAS motor receives commands from ADAS systems. It's a fully networked, cyber-physical system.

## Slide 35: Steering System Design Example
DESIGN CHALLENGE:
You're designing a steering system for a new compact sedan. Specify the key parameters.
GIVEN REQUIREMENTS: — Target vehicle: Compact sedan (Honda Civic class)
Wheelbase L = 2.7 m
Track width t = 1.52 m
Vehicle mass = 1,300 kg
Front weight distribution = 60% (780 kg on front axle)
Target minimum turning radius: 5.0 m (competitive with class leaders)
Maximum parking effort: 3 Nm at steering wheel rim (easy for driver)
Highway stability: Weighted feel at 120 km/h
DESIGN DECISIONS:
1. Steering Mechanism: Rack-and-Pinion with EPAS (rack-assist)
Why?
Modern, compact packaging
Efficient (important for fuel economy)
Enables ADAS features (future-proofing)
Good feedback potential (with proper tuning)
2. Calculate Required Maximum Steering Angle:
From turning radius requirement:
R = L / tan(δ_avg) 5.0 = 2.7 / tan(δ_avg) tan(δ_avg) = 2.7 / 5.0 = 0.540 δ_avg = arctan(0.540) = 28.4°
For Ackermann geometry, inner wheel will be slightly more:
δᵢ ≈ 31° (inner wheel, maximum) δₒ ≈ 26° (outer wheel, calculated from Ackermann)
Specification: Maximum wheel angle = ±31°
3. Select Steering Ratio:
Target: Balanced (not too quick, not too slow)
Sports car equivalent: 13:1 (too quick for average driver)
Comfort car: 16:1 (good balance)
Selected: 15:1 steering ratio
Lock-to-lock steering wheel rotation:
Total wheel travel = 31° + 31° = 62° Steering wheel rotation = 62° × 15 = 930° = 2.58 turns
This is typical (2.5-3 turns lock-to-lock for modern cars).
4. EPAS Motor Sizing:
Maximum assist torque needed (during parking at standstill):
Assume tire scrub torque at wheel = 120 Nm per wheel (typical for 205/55R16 tire on dry pavement)
Total torque at rack (both wheels):
T_rack = 120 Nm × 2 = 240 Nm
Torque at steering wheel (without assist):
T_SW = T_rack / (Steering Ratio) = 240 / 15 = 16 Nm
With EPAS providing 90% assist (driver provides 10%):
Driver effort = 16 Nm × 0.10 = 1.6 Nm ✅ (meets <3 Nm requirement) Motor must provide = 16 Nm × 0.90 = 14.4 Nm
Accounting for efficiency and safety margin:
Motor specification: 20 Nm peak torque, 600W brushless DC motor
5. EPAS Assist Curve: — 0-20 km/h: 90% assist (parking, city maneuvering)
20-60 km/h: 70% assist (suburban driving)
60-100 km/h: 50% assist (highway cruising)
100-150 km/h: 30% assist (high-speed stability)
6. Steering Geometry Parameters: — Caster: +4.5° (good self-centering, moderate effort)
Camber: —0.5° (slight negative for cornering, minimal tire wear)
Toe: 2 mm toe-in (front axle stability)
KPI: 12° (designed into suspension geometry)
DESIGN SUMMARY:
| Parameter | Specification |
|-----------|---------------|
| Mechanism | Rack-and-pinion with rack-assist EPAS |
| Steering Ratio | 15:1 |
| Lock-to-Lock Turns | 2.58 turns |
| Max Wheel Angle | ±31° |
| Turning Radius | 5.0 m |
| EPAS Motor | 600W brushless DC, 20 Nm peak |
| Parking Effort | 1.6 Nm (with 90% assist) |
| Caster | +4.5° |
| Camber | -0.5° |
| Toe | 2 mm toe-in |
Instructor Narration:
This design balances maneuverability (5m turning radius), effort (easy parking with EPAS), stability (weighted feel at high speed), and cost (moderate motor size). It's typical of a modern, well-engineered compact sedan.

## Slide 36: Summary & Key Takeaways
Instructor Narration:
Let's recap what we've learned today.
PART 1: GEOMETRY
✅ Ackermann Steering solves the fundamental problem: inner and outer wheels must turn at different angles
✅ Turning radius R = L / tan(δ) - smaller wheelbase = tighter turns
✅ Ackermann equation: cot(δₒ) - cot(δᵢ) = t/L
PART 2: ALIGNMENT ANGLES
✅ Caster (+2° to +7°): Self-centering, straight-line stability
✅ Camber (-0.5° to -2°): Tire contact during cornering
✅ Toe (0-3 mm): Straight tracking, tire wear (most critical for alignment)
✅ KPI (5° to 15°): Self-centering, scrub radius control
PART 3: STEERING MECHANISMS
✅ Rack-and-Pinion: Simple, direct feel, compact (modern standard)
✅ Recirculating Ball: Strong, durable, smooth (heavy-duty applications)
✅ Steering Ratio: Trade-off between quick response and easy effort (typical: 14:1 to 16:1)
PART 4: POWER ASSIST
✅ Hydraulic (HPS): Engine-driven pump, good feedback, continuous energy use
✅ Electric (EPAS): Efficient, speed-sensitive, ADAS-ready, tunable
✅ Trend: EPAS is replacing hydraulic (80% of new cars)
PART 5: INTEGRATION
✅ Steering Feel: Combination of mechanical feedback and electronic simulation
✅ System Integration: Connected to ESC, ABS, ADAS, and other vehicle systems
✅ Advanced Features: Lane keeping, self-parking, autonomous driving (all enabled by EPAS)
Connection to Next Session:
We've covered braking (Session 10) and steering (Session 11). Next session, we'll complete the chassis dynamics trilogy with Suspension Systems.
Suspension controls how the wheels move vertically, manages load transfer (which we calculated in Session 9), and determines ride comfort vs handling balance. We'll apply spring-mass-damper physics, compare suspension types, and understand electronic suspension systems.
See you next time!

## Slide 37: 📊 SESSION METADATA
Total Slides: 30
Lecture Duration: 90 minutes
Q&A Duration: 30 minutes
Total Session Time: 120 minutes
Learning Outcome Coverage: — ✅ SO-3-11-1: Ackermann geometry calculations (Slides 3-6, Practice Problem)
✅ SO-3-11-2: Turning radius calculations (Slides 5-7, Design Example)
✅ SO-3-11-3: Steering geometry parameters (Slides 10-14)
✅ SO-3-11-4: Steering mechanisms comparison and ratio calculation (Slides 15-19)
✅ SO-3-11-5: Power steering systems (Slides 20-25)
✅ SO-3-11-6: Steering feedback and feel (Slides 26-27)
Worked Examples: 3
Ackermann geometry and turning radius calculation (Slide 6)
Steering ratio calculation (Slide 19)
Complete steering system design (Slide 29)
Practice Problems: 1
Turning radius comparison SUV vs sedan (Slide 7)
Key Formulas:
Ackermann: cot(δₒ) - cot(δᵢ) = t/L
Turning radius: R = L / tan(δ_avg)
Steering ratio: θSW / δwheel
Mechanical trail: Caster angle × Tire radius
Visual Requirements: — Geometric diagrams (Ackermann, turning radius) - minimum 6 slides
Component cutaways (rack-and-pinion, recirculating ball) - 2 slides
System integration diagrams - 3 slides
Graphs (EPAS assist curve) - 1 slide
Comparison tables - 2 slides

## Slide 38: 🎯 INSTRUCTOR NOTES
Pacing Tips: — Ackermann geometry (Slides 3-6): Take your time. This is the most mathematically intensive part. Use board drawings if needed.
Alignment angles (Slides 11-14): Students find this interesting (connects to "wheel alignment" they've heard about at tire shops). Encourage questions.
Steering mechanisms (Slides 16-17): Physical props (rack-and-pinion cutaway model) are very helpful if available.
EPAS vs Hydraulic (Slides 21-24): Students have strong opinions (especially car enthusiasts who prefer hydraulic feel). Acknowledge both perspectives.
Common Student Questions:
"Why do race cars sometimes use less Ackermann or even anti-Ackermann?
Answer: At high cornering speeds, outer tire is loaded more heavily and needs more slip angle to generate force. Anti-Ackermann compensates for this.
"Can you adjust caster at home?
Answer: On most modern cars, no (requires special bolts or suspension modification). Only camber and toe are adjustable during regular alignment.
"Why does my car's steering feel different than my friend's car?
Answer: Steering ratio, assist tuning, tire size, and alignment all contribute. Manufacturers tune for different philosophies (comfort vs sport).
"What happens if power steering fails completely?
Answer: You revert to manual steering. Very heavy (especially at low speed), but functional. Modern cars have warning lights and fail-safe modes.
Engagement Strategies: — Ask students to estimate their own car's turning radius (most don't know—use this to motivate the calculations)
Demonstrate caster self-centering with a shopping cart wheel (if available)
Show video of lane keeping assist in action (students are fascinated by ADAS)
Prerequisite Check: — Ensure students remember lateral forces from Session 9 (needed for self-aligning torque discussion)
Remind students of Pascal's Principle from Session 10 (hydraulic systems use same principle as brakes)
Check understanding of trigonometry (tan, cot, arctan) before Ackermann calculations
Safety Emphasis: — Never adjust alignment parameters yourself unless trained (affects safety and tire wear)
If steering feels different after hitting a curb/pothole, get alignment checked immediately
Power steering fluid leaks can cause sudden loss of assist (dangerous in emergency maneuvers)

## Slide 39
END OF SESSION 11 FRAMEWORK
This framework is ready for PowerPoint conversion. Each slide description includes visual guidance, instructor narration, and technical content for professional slide development.