## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 14: Vehicle Control Systems'

## Slide 2: Vehicle Control Systems
Session 14 | Automotive Vehicles (AEL ZC441)

## Slide 3: Automotive Sensors - Classification
Instructor Narration:
An ECU is useless without information. Sensors are the ECU's eyes and ears—they measure the physical world and convert it to electrical signals.
SENSOR CLASSIFICATION:
By Measurement Type:
1. TEMPERATURE SENSORS — Measure: °C or °F
Examples: Engine coolant temp, intake air temp, exhaust gas temp, cabin temp
2. PRESSURE SENSORS — Measure: kPa, bar, psi
Examples: Manifold absolute pressure (MAP), tire pressure (TPMS), fuel pressure, brake pressure
3. POSITION SENSORS — Measure: Angle or linear position (degrees, mm)
Examples: Throttle position, camshaft position, crankshaft position, pedal position
4. SPEED SENSORS — Measure: RPM or km/h
Examples: Wheel speed (ABS), vehicle speed, engine speed (tachometer)
5. FLOW SENSORS — Measure: kg/s or L/min
Examples: Mass airflow (MAF), fuel flow
6. COMPOSITION SENSORS — Measure: Chemical composition (%)
Examples: Oxygen sensor (lambda), NOx sensor
By Signal Type:
ANALOG SENSORS: — Output: Continuous voltage (0-5V typical) or resistance
Example: Coolant temperature sensor (resistance decreases with temperature)
ECU reads via analog-to-digital converter (ADC)
DIGITAL SENSORS: — Output: On/off signal or pulse train
Example: Crankshaft position sensor (digital pulses)
ECU counts pulses directly
SMART SENSORS: — Output: Digital data over serial communication (CAN, LIN)
Example: Tire pressure monitoring sensor (transmits pressure + temperature + ID)
Most advanced, least susceptible to noise
Let's explore each major sensor type in detail.

## Slide 4: Temperature Sensors - Thermistors (NTC)
Instructor Narration:
Temperature is fundamental—engines, transmissions, everything has optimal operating temperature.
NTC THERMISTOR (Negative Temperature Coefficient)
Technology: — Semiconductor material (metal oxide ceramic)
Resistance decreases as temperature increases — Non-linear relationship
Typical Characteristics:
At 25°C: 2,500 Ω (2.5 kΩ)
At 80°C: 300 Ω
At 100°C: 180 Ω
How ECU Measures:
Circuit:
ECU supplies 5V reference voltage
Voltage divider: 5V → Fixed Resistor (2.5 kΩ) → Thermistor → Ground
ECU measures voltage at junction
Voltage changes as thermistor resistance changes
Calculation:
V_sensor = 5V × (R_thermistor / (R_fixed + R_thermistor))
Example: — Engine cold (20°C): R_thermistor = 3,000 Ω
V_sensor = 5V × (3,000 / 5,500) = 2.73V
ECU interprets: 20°C — Engine hot (90°C): R_thermistor = 250 Ω
V_sensor = 5V × (250 / 2,750) = 0.45V
ECU interprets: 90°C
Applications:
1. Engine Coolant Temperature (ECT) — Location: Thermostat housing or cylinder head
Purpose:
Cold start enrichment (add fuel when cold)
Cooling fan control (turn on at 95°C)
Fuel trim adjustment (density changes with temperature)
2. Intake Air Temperature (IAT) — Location: Intake manifold or air filter housing
Purpose:
Air density calculation (cold air denser = more oxygen)
Fuel adjustment (more air = need more fuel)
Knock protection (hot air more prone to detonation)
3. Transmission Fluid Temperature (TFT) — Location: Transmission oil pan
Purpose:
Shift strategy adjustment (firm shifts when hot)
Overheating protection (lock torque converter, reduce load)
Advantages:
✅ Simple, cheap ($5-15)
✅ No external power needed
✅ Very reliable (no moving parts)
Disadvantages:
❌ Non-linear (requires lookup table in ECU)
❌ Slow response (thermal mass takes time to heat/cool)
Instructor Narration (continued):
'When your engine runs cold for too long (stuck-open thermostat), the ECU sees low coolant temperature and enriches the fuel mixture. Result: poor fuel economy, high emissions, rough running. The ECU is responding correctly to bad sensor data—the problem is the thermostat, not the ECU!'

## Slide 5: Slide 10-15: Other Sensor Types (Summarized)
[These slides would cover:
Slide 10: Pressure sensors (piezo-resistive, capacitive) - MAP sensor
Slide 11: Position sensors (potentiometer, Hall effect) - TPS, pedal position
Slide 12: Speed sensors (inductive, Hall effect) - Crankshaft, camshaft, wheel speed
Slide 13: Mass airflow sensor (hot-wire, hot-film) - Critical for fuel calculation
Slide 14: Oxygen sensor (lambda sensor) - Zirconia, wide-band vs narrow-band
Slide 15: Sensor summary table comparing all types]

## Slide 6: PART 3: RISING ACTION - "Acting on the World

## Slide 7: Automotive Actuators - Classification
Instructor Narration:
Sensors measure the world; actuators change it. These are the ECU's muscles.
ACTUATOR CLASSIFICATION:
By Type:
1. SOLENOIDS (Electromagnetic Actuators) — Convert electrical current → linear or rotary motion
Examples: Fuel injectors, transmission shift solenoids, VVT solenoids, purge valve
2. ELECTRIC MOTORS — Convert electrical power → rotary motion
Examples: Throttle valve motor, EPAS motor, cooling fan, fuel pump
3. STEPPER MOTORS — Precise rotary positioning
Examples: Idle air control valve, cruise control throttle
4. RELAYS — Electrically controlled switches (we covered in Session 13)
Examples: Fuel pump relay, cooling fan relay, A/C compressor clutch
By Control Method:
ON/OFF (Bang-Bang Control) — Actuator is either fully on or fully off
Example: Cooling fan relay (on when temp > 95°C, off when < 90°C)
PWM (Pulse Width Modulation) — Vary average power by rapidly switching on/off
Example: Fuel injector (pulse width determines fuel quantity)
ANALOG (Continuous Control) — Smoothly variable output
Example: Throttle motor position (precise angle control)
Let's explore key actuators.

## Slide 8: Fuel Injectors - PWM Control
Instructor Narration:
The fuel injector is the most critical actuator for engine control.
FUEL INJECTOR DESIGN:
Components:
1. Solenoid Coil — Electromagnetic coil (many turns of fine wire)
Typical: 2-5 Ω resistance, 12V supply
When energized: Creates magnetic field
2. Plunger (Armature) — Movable iron core
Held closed by spring
Pulled open by magnetic field
3. Nozzle & Spray Pattern — Precision-machined orifice
Creates fine fuel mist (atomization)
Spray pattern optimized for combustion chamber shape
4. Fuel Supply — Constant pressure fuel rail (typically 300-400 kPa / 43-58 psi)
Fuel always present, ready to inject

## Slide 9
HOW IT WORKS:
Injector Closed (De-energized): — No current through coil
Spring holds plunger closed
Fuel blocked (no flow)
Injector Open (Energized):
ECU sends current pulse to solenoid (12V)
Magnetic field pulls plunger open
Fuel sprays through nozzle (pressure differential)
Atomized fuel mixes with air
Injector Closes:
ECU cuts current
Magnetic field collapses
Spring forces plunger closed
Fuel flow stops
Response Time: 1-2 milliseconds (open/close cycle)

## Slide 10
PWM CONTROL - PULSE WIDTH MODULATION:
Concept: Control fuel quantity by varying how long injector stays open
Key Parameters:
Pulse Width (Injection Duration): — Measured in milliseconds (ms)
Typical range: 1-15 ms
Longer pulse = more fuel
Fuel Quantity Formula:
Fuel Mass = Fuel Pressure × Injector Flow Rate × Pulse Width Or simplified: Fuel (mg) ≈ K × Pulse Width (ms) Where K = injector flow coefficient (depends on pressure, nozzle size)
Example: — Injector flow rate: 200 cc/min @ 300 kPa
Pulse width: 3 ms
Fuel delivered: ~10 mg per pulse
Operating Conditions:
Idle: — Low air mass → need low fuel
Pulse width: 2-3 ms
Frequency: ~25 pulses/sec (engine at 750 RPM, 4-cylinder, 4-stroke)
Full Load (Wide Open Throttle): — High air mass → need high fuel
Pulse width: 10-15 ms
Frequency: ~100 pulses/sec (engine at 6,000 RPM)
Cold Start: — Cold engine → poor fuel vaporization
Need extra fuel (enrichment)
Pulse width: +50-100% longer than normal

## Slide 11
MULTI-POINT FUEL INJECTION (MPFI) vs DIRECT INJECTION (GDI):
Port Injection (MPFI): — Injector sprays into intake port (before intake valve)
Fuel mixes with air in port
Enters cylinder already mixed
Pressure: 300-400 kPa
Direct Injection (GDI): — Injector sprays directly into combustion chamber — Much higher pressure: 10,000-35,000 kPa (100-350 bar)
More precise control (inject during compression stroke)
Better efficiency, more power
Instructor Narration (continued):
'PWM control is everywhere in automotive systems—not just fuel injectors. Variable valve timing solenoids, transmission shift solenoids, EVAP purge valve—all use PWM. The ECU rapidly switches them on/off, and the average (duty cycle) determines the effect. It's digital control of analog systems.'

## Slide 12: Slide 18-21: Other Actuator Types (Summarized)
[These slides would cover:
Slide 18: Electronic throttle (drive-by-wire) - DC motor, position feedback
Slide 19: VVT solenoid (variable valve timing) - Oil pressure control
Slide 20: EGR valve (exhaust gas recirculation) - Stepper motor control
Slide 21: Transmission shift solenoids - Hydraulic pressure PWM control]

## Slide 13: PART 4: CLIMAX - "Closed-Loop Control

## Slide 14: Open-Loop vs Closed-Loop Control
Instructor Narration:
We've seen sensors (measurement) and actuators (control). Now let's see how they work together in control loops.
OPEN-LOOP CONTROL (No Feedback)
Definition: ECU commands actuator based on pre-programmed map, without measuring the result.
Example: Cold Start Fuel Enrichment (Simplified)
Process:
ECU reads coolant temperature sensor: 5°C
ECU looks up fuel enrichment table:
At 5°C → enrich by +40%
ECU increases injector pulse width by 40%
No measurement of actual air-fuel ratio
Diagram:
[Coolant Temp Sensor] → [ECU] → [Fuel Injector] ↑ [Lookup Table]
Advantages:
✅ Simple (no feedback sensor needed)
✅ Fast (no time delay for feedback)
Disadvantages:
❌ Inaccurate (assumes table is correct for all conditions)
❌ No error correction (if actual AFR is wrong, ECU doesn't know)
❌ Cannot adapt (altitude, fuel quality, aging components affect result)

## Slide 15
CLOSED-LOOP CONTROL (With Feedback)
Definition: ECU commands actuator, measures the result, compares to target, and corrects errors.
Example: Lambda Control (Air-Fuel Ratio Control)
Process:
ECU calculates target AFR: 14.7:1 (stoichiometric)
ECU calculates required fuel based on air mass (from MAF sensor)
ECU commands fuel injector
Oxygen sensor measures actual AFR in exhaust
ECU compares: Actual vs Target
If actual ≠ target: ECU adjusts fuel injection
Repeat continuously (closed loop)
Diagram:
[Target AFR] → [ECU] → [Fuel Injector] → [Engine] → [Exhaust] ↑ ↓ ←──────── [Oxygen Sensor] ←────────────── (Feedback)
Advantages:
✅ Accurate (measures actual result, corrects errors)
✅ Adaptive (compensates for altitude, fuel quality, aging)
✅ Self-correcting (if something drifts, feedback compensates)
Disadvantages:
❌ Requires feedback sensor (cost)
❌ Slower (feedback delay)
❌ Can oscillate if tuned incorrectly

## Slide 16
WHEN TO USE EACH:
Open-Loop: — Cold start (before oxygen sensor warms up)
Transient conditions (rapid throttle changes—feedback too slow)
Fail-safe mode (if feedback sensor fails)
Closed-Loop: — Normal operation (cruising, steady-state)
Emissions-critical operation (catalyst requires precise AFR)
Long-term adaptation (learn fuel system aging)
Instructor Narration (continued):
'Modern engine management uses both. During cold start, open-loop enriches fuel (no O2 sensor yet). After 30-60 seconds, oxygen sensor warms up, ECU switches to closed-loop, measures actual AFR, and trims fuel precisely to 14.7:1. This is why emissions are high for the first minute after starting—no closed-loop yet.'

## Slide 17: Lambda Control - The Perfect Air-Fuel Ratio
Instructor Narration:
Let's dive deep into the most important closed-loop control in engine management: Lambda Control (air-fuel ratio control).
THE GOAL: STOICHIOMETRIC COMBUSTION
Chemistry:
Gasoline (C8H18) + Air (21% O2, 79% N2) → CO2 + H2O + Heat Stoichiometric Ratio: 14.7 kg of air : 1 kg of fuel (mass ratio) Lambda (λ) = Actual AFR / Stoichiometric AFR λ = 1.0 → Perfect mixture (14.7:1) λ > 1.0 → Lean (excess air, AFR > 14.7:1) λ < 1.0 → Rich (excess fuel, AFR < 14.7:1)
Why λ = 1.0 Matters:
Three-Way Catalytic Converter REQUIRES λ = 1.0 ± 0.01
At λ = 1.0:
✅ CO oxidized to CO2 (requires oxygen)
✅ HC oxidized to CO2 + H2O (requires oxygen)
✅ NOx reduced to N2 (requires reducing agent—excess fuel)
Catalyst Efficiency: — λ = 1.00: 95-99% conversion (excellent)
λ = 0.95: 60% NOx conversion (too rich)
λ = 1.05: 40% CO conversion (too lean)
Emissions regulations (BS6, Euro 6) demand λ = 1.00 ± 0.01 —--
LAMBDA CONTROL SYSTEM:
Components:
1. Mass Airflow Sensor (MAF) — Measures: kg/s of air entering engine
Technology: Hot-wire sensor (air cools wire, resistance changes)
Output: 0-5V analog (proportional to airflow)
Example: — At idle: 3 g/s (0.003 kg/s)
At full load: 150 g/s (0.150 kg/s)
2. Engine Control ECU — Calculates required fuel mass:
Fuel Mass = Air Mass / 14.7
Calculates injector pulse width:
Pulse Width = Fuel Mass / Injector Flow Rate
3. Fuel Injector — Delivers calculated fuel mass
Response time: 1-2 ms
4. Oxygen Sensor (Lambda Sensor) — Measures: Oxygen content in exhaust gas
Technology: Zirconia ceramic (generates voltage based on O2 concentration)
Output: 0-1V (0.45V = lean, 0.55V = rich, 0.5V = stoich)
Two Types:
Narrow-Band Oxygen Sensor (Switch Type): — Output: Sharp transition at λ = 1.0
Range: Can only detect λ = 0.95-1.05 (narrow window)
Cannot measure HOW rich or lean, only "rich" or "lean
Cheap ($30-80)
Wide-Band Oxygen Sensor (Linear Type): — Output: Linear voltage proportional to λ
Range: λ = 0.65-1.3 (wide range)
CAN measure exact AFR (12:1, 14.7:1, 16:1, etc.)
Expensive ($150-400)
Used in performance applications, diesel engines

## Slide 18
CLOSED-LOOP OPERATION:
Step 1: Open-Loop Calculation
Given: — MAF sensor: 10 g/s airflow
Target: λ = 1.0 (AFR = 14.7:1)
Calculate fuel needed:
Fuel = Air / AFR = 10 g/s / 14.7 = 0.68 g/s
Convert to injector pulse width:
Injector flow rate: 200 cc/min = 160 mg/stroke @ 300 kPa Pulse width = (0.68 g/s / 4 cylinders) / (160 mg/stroke) × 1000 = ~4.25 ms per injection
Step 2: ECU Commands Injector — Pulse width: 4.25 ms
Fuel sprays, combustion occurs
Step 3: Oxygen Sensor Measures — Exhaust reaches O2 sensor (~500 ms delay)
O2 sensor voltage: 0.52V
Interpretation: — 0.52V > 0.50V → Slightly rich (too much fuel)
Actual λ ≈ 0.98 (slightly rich)
Step 4: ECU Corrects — ECU reduces pulse width: 4.25 ms → 4.20 ms (-1.2%)
Less fuel injected
Step 5: Repeat — O2 sensor measures again (after 500 ms)
Voltage: 0.48V → Slightly lean — ECU increases pulse width: 4.20 ms → 4.23 ms
Repeat continuously (oscillates around λ = 1.0)

## Slide 19
CONTROL FREQUENCY:
Update Rate: — ECU recalculates every 10-50 ms — O2 sensor feedback delay: 200-500 ms (exhaust travel time)
System oscillates ± 2% around λ = 1.0
Average λ = 1.00 over time
Result: — Catalyst sees average λ = 1.00
95-99% emissions conversion — Meets BS6/Euro 6 standards
Instructor Narration (continued):
'This is why catalytic converters fail if you have persistent misfires or run too rich/lean for extended periods. The catalyst is designed for λ = 1.0. If you run at λ = 0.8 (very rich—maybe due to bad MAF sensor), the catalyst sees excess fuel, overheats, and the ceramic substrate melts. A $50 sensor failure leads to a $1,500 catalyst replacement!'

## Slide 20: Slide 24-26: PID Control & Other Examples
[These slides would cover:
Slide 24: PID control basics (Proportional-Integral-Derivative)
Slide 25: Idle speed control example (closed-loop)
Slide 26: Knock control example (closed-loop timing adjustment)]

## Slide 21: PART 5: RESOLUTION - "Complete System Integration

## Slide 22: Engine Management ECU - Complete System
Instructor Narration:
Let's integrate everything: sensors, actuators, and control loops into a complete Engine Management System.
ENGINE CONTROL ECU (ECM/PCM)
INPUTS (Sensors):
Air System: — Mass Airflow Sensor (MAF): Air mass (kg/s)
Intake Air Temperature (IAT): Air density correction
Manifold Absolute Pressure (MAP): Load indication (some systems use MAP instead of MAF)
Throttle Position Sensor (TPS): Driver demand
Fuel System: — Oxygen Sensor (O2/Lambda): Exhaust gas O2 (closed-loop feedback)
Fuel Pressure Sensor: Rail pressure monitoring
Fuel Temperature Sensor: Density correction
Ignition System: — Crankshaft Position Sensor (CKP): Engine speed, TDC position
Camshaft Position Sensor (CMP): Cylinder identification, valve timing
Knock Sensor: Detonation detection (piezoelectric accelerometer)
Cooling System: — Engine Coolant Temperature (ECT): Cold start, fan control, fuel trim
Driver Inputs: — Accelerator Pedal Position: Driver torque request
Brake Switch: Decel fuel cut, idle control
Cruise Control Switches: Target speed
Other: — Vehicle Speed Sensor (VSS): Transmission control, cruise control
Battery Voltage: Charging system status
A/C Request: Load compensation (increase idle speed)

## Slide 23
OUTPUTS (Actuators):
Fuel System: — Fuel Injectors (4-12 depending on cylinders): Precise fuel metering (PWM, 1-15 ms pulse)
Fuel Pump Relay: Prime fuel system, maintain pressure
Ignition System: — Ignition Coils (one per cylinder): Spark timing (0-40° BTDC typically)
Ignition timing advance/retard based on load, speed, knock
Air System: — Electronic Throttle Valve (Drive-by-wire): Throttle opening (0-90°)
Idle Air Control Valve: Idle speed regulation (bypass air)
VVT Solenoids: Variable valve timing (intake/exhaust cam phasing)
Emissions: — EGR Valve: Exhaust gas recirculation (reduce NOx)
Purge Valve: Evaporative emissions control (EVAP system)
Secondary Air Pump: Catalyst warm-up (cold start)
Other: — Cooling Fan Relay: Engine temperature control
Check Engine Light (MIL): Fault indication
Tachometer Signal: RPM display

## Slide 24
CONTROL STRATEGIES:
1. Base Fuel Calculation (Open-Loop):
Base Fuel = MAF (kg/s) / 14.7 (AFR) / Engine Speed (rev/s) / Cylinders
2. Fuel Trims (Closed-Loop):
Final Fuel = Base Fuel × Short-Term Trim × Long-Term Trim Short-Term Trim: Immediate correction based on O2 sensor (±25%) Long-Term Trim: Learned compensation (±15-25%, stored in ECU memory)
3. Ignition Timing:
Base Timing = Lookup Table [Engine Speed, Load] Final Timing = Base Timing - Knock Retard + Coolant Compensation
4. Idle Speed Control:
Target Idle = 700 RPM (warm), 1,200 RPM (cold) Idle Air Valve Opening = PID(Target RPM - Actual RPM)
All These Run Simultaneously: — Fuel calculation: Every 5-10 ms
Ignition timing: Every cylinder firing (every 10-20 ms @ 3,000 RPM)
Idle control: Every 50-100 ms
Lambda control: Every 200-500 ms
Fault detection: Continuous
ECU Processing: — Processor: 32-bit, 100-200 MHz
Memory: 512 KB - 4 MB Flash, 128 KB RAM
I/O: 50-100 inputs/outputs
Power: 5-10W
Instructor Narration (continued):
'The engine ECU is one of the most complex computers in the vehicle. It's executing thousands of calculations per second, managing 50+ sensors and actuators, all while ensuring emissions compliance, driveability, and reliability. And it must work flawlessly for 200,000+ km in extreme conditions—from -40°C to +125°C, vibration, humidity, everything. It's an engineering marvel.'

## Slide 25: Transmission Control Unit (TCU) - Shift Strategy
Instructor Narration:
Let's look at another major ECU: the Transmission Control Unit (TCU or TCM).
TCU FUNCTION:
Control automatic transmission shifting to optimize:
Performance (fast shifts when driver demands)
Fuel economy (early upshifts for cruising)
Smoothness (gentle shifts for comfort)
INPUTS:
From Sensors: — Vehicle Speed Sensor (VSS): km/h
Turbine Speed Sensor: Transmission input speed (RPM)
Output Shaft Speed Sensor: Transmission output speed (RPM)
Throttle Position Sensor (TPS): Driver demand (% throttle)
Accelerator Pedal Position: Driver intent
Brake Switch: Deceleration indication
Transmission Fluid Temperature (TFT): Fluid condition
Gear Position Sensor: Current gear (P/R/N/D/S/L)
From Engine ECU (via CAN bus): — Engine RPM — Engine Torque — Engine Load
From Driver: — Transmission Mode Selection: Drive, Sport, Manual, Eco

## Slide 26
OUTPUTS:
Shift Solenoids (Hydraulic Valves): — Solenoid A, B, C, D, E: Control hydraulic circuits
Each gear = unique solenoid combination
Example (4-speed auto):
1st gear: A=ON, B=OFF, C=OFF
2nd gear: A=ON, B=ON, C=OFF
3rd gear: A=OFF, B=ON, C=ON
4th gear: A=OFF, B=OFF, C=ON
Pressure Control Solenoids: — Line Pressure Control: Overall hydraulic pressure (PWM control)
Clutch Pressure Control: Individual clutch engagement force (smooth shifts)
Torque Converter Lock-Up Clutch: — Lock solenoid: Engage/disengage lock-up (eliminate slip, improve efficiency)
Other: — Gear Position Indicator: Display current gear (dashboard)
Shift Lock Solenoid: Prevent shifting out of Park without brake

## Slide 27
SHIFT STRATEGY (Example: 2→3 Upshift):
Shift Decision:
Inputs: — Vehicle speed: 60 km/h
Throttle position: 30% (light acceleration)
Engine RPM: 2,500 RPM (in 2nd gear)
Transmission mode: Drive (D)
TCU Logic:
Step 1: Lookup Shift Map
Shift Map [Throttle Position, Vehicle Speed] At 30% throttle, 60 km/h → Shift point = 2→3 upshift
Step 2: Check Conditions — Transmission fluid temp: 80°C ✅ (OK, not too cold)
Engine torque: Normal ✅ (no wide-open throttle)
Brake not applied ✅
Step 3: Execute Shift
Pre-shift (100 ms before):
TCU requests engine ECU: "Reduce torque by 20%
Engine ECU retards ignition timing → torque reduction
Result: Smooth shift (no jerk)
During shift (300-500 ms):
De-energize 2nd gear solenoid
Energize 3rd gear solenoid (overlap for smoothness)
Modulate clutch pressure (PWM control):
Gradual release of 2nd gear clutch
Gradual engagement of 3rd gear clutch
Clutch slip controlled to 50-200 RPM during transition
Post-shift:
TCU signals engine ECU: "Restore full torque
Engine ECU returns to normal ignition timing
RPM drops from 2,500 to 1,800 RPM (typical gear ratio change)
Shift complete
Shift Quality Metrics: — Shift time: 300-500 ms (smooth), 100-200 ms (sport mode)
Clutch slip during shift: 50-200 RPM (controlled)
Torque reduction: 10-30% (minimizes jerk)

## Slide 28
ADAPTIVE LEARNING:
Modern TCUs learn over time:
Clutch Wear Compensation: — As clutches wear, apply pressure slightly earlier
Maintain consistent shift quality over 200,000 km
Driver Style Recognition: — Aggressive driver (frequent WOT) → hold gears longer, firmer shifts
Gentle driver (light throttle) → early upshifts, softer shifts
Temperature Compensation: — Cold fluid (-10°C) → delay shifts (fluid viscosity high)
Hot fluid (110°C) → firmer shifts, lock torque converter early (protect transmission)
Instructor Narration (continued):
'This is why transmission 'relearning' is a thing. If you disconnect the battery, the TCU loses its adaptive parameters. For the first 100-200 km after reconnecting, shifts may feel slightly different while the TCU relearns. Also, if you sell your car to someone with a different driving style, the transmission will adapt to the new driver over a week or two—automatic customization!'

## Slide 29: Slide 29-30: Summary & Preview
[Slides 29-30 would cover:
Slide 29: Complete integration—how engine ECU, TCU, ABS ECU all work together (preview of networks in Session 15)
Slide 30: Summary of Session 14, preview of Session 15 (CAN bus, OBD-II, network architecture)]

## Slide 30: 📊 SESSION METADATA
Total Slides: 28-30
Lecture Duration: 90 minutes
Q&A Duration: 30 minutes
Learning Outcome Coverage: — ✅ SO-4-14-1: ECU role and types (Slides 1-7)
✅ SO-4-14-2: Engine management ECU functions (Slide 27)
✅ SO-4-14-3: Sensor classification and operation (Slides 8-15)
✅ SO-4-14-4: Actuator classification and control (Slides 16-21)
✅ SO-4-14-5: Closed-loop control principle (Slides 22-26)
✅ SO-4-14-6: TCU operation and shift strategies (Slide 28)
Key Concepts:
Sensors (NTC thermistor, MAF, O2 sensor) convert physical → electrical
Actuators (injectors, throttle, solenoids) convert electrical → physical
ECUs implement control algorithms (open/closed loop)
Closed-loop control uses feedback for accuracy (lambda control example)
Modern vehicles have 30-100 ECUs working together

## Slide 31
END OF SESSION 14 FRAMEWORK
This framework is ready for PowerPoint conversion.