## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 15: Vehicle Communication Networks'

## Slide 2: Vehicle Communication Networks
Session 15 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title Slide
Instructor Narration:
Welcome to Session 15: Vehicle Communication Networks. Today we complete Module 4 by exploring the 'digital nervous system' that allows 30-100 ECUs to work together seamlessly.

## Slide 4: The Point-to-Point Wiring Problem
Instructor Narration:
Imagine designing a 1990 vehicle with 20 ECUs using point-to-point wiring.
Example System: — Engine ECU
Transmission ECU
ABS ECU
Instrument Cluster
Body Control Module
Climate Control ECU
Airbag ECU
Cruise Control ECU
Lighting Control ECU
Security ECU
Information Sharing Needed:
Engine ECU needs to send: — RPM → Instrument cluster (tachometer)
Coolant temp → Instrument cluster (temp gauge)
VSS (speed) → Cruise control
Throttle position → Transmission ECU
Engine torque → Transmission ECU, ABS ECU
That's 5 output connections from just ONE ECU!
Total wiring requirement: — If each connection = 2 wires (signal + ground)
10 ECUs with average 5 connections each = 50 wires
Plus all sensor/actuator wiring = 100-200+ wires
Weight: 10-15 kg just for inter-ECU communication
Cost: $100-200 in copper and connectors
Failure rate: High (each connection = potential failure point)

## Slide 5
THE GROWTH PROBLEM:
1990: 10-15 ECUs → 100 wires → Manageable
2000: 30-40 ECUs → 400 wires → Difficult
2010: 50-70 ECUs → 1,000 wires → Nearly impossible
2025: 80-100 ECUs → 3,000 wires → Completely impractical
The Breaking Point:
Around 2000, automotive engineers realized: Point-to-point wiring cannot scale. —--

## Slide 6: The Network Solution - Multiplexing
Instructor Narration:
The solution came from telecommunications: Multiplexing (sharing one communication channel among many users).
NETWORK ARCHITECTURE:
Physical Setup: — One communication bus (2-wire twisted pair)
All ECUs connect to this bus (parallel connection)
Messages broadcast to all ECUs
Each ECU listens for messages it needs
How It Works:
Traditional (Point-to-Point):
Engine ECU → Dedicated wire → Instrument Cluster (RPM signal) Engine ECU → Dedicated wire → Transmission ECU (Torque signal) Engine ECU → Dedicated wire → Cruise Control (Speed signal) Total: 6 wires (3 signals × 2 wires each)
Networked (Multiplexed):
Engine ECU broadcasts on bus: Message 1: "RPM = 2,500 Message 2: "Torque = 150 Nm Message 3: "Speed = 80 km/h All ECUs connected to bus receive all messages - Instrument Cluster listens for RPM - Transmission ECU listens for Torque - Cruise Control listens for Speed Total: 2 wires (one bus, shared by all)
Savings: — Weight: 20-30 kg reduction in wiring harness
Cost: $200-500 savings per vehicle
Complexity: 90% reduction in inter-ECU wiring
Reliability: Fewer connectors = fewer failure points
The Standard: CAN Bus
CAN = Controller Area Network — Developed by Bosch (1983)
Standardized (ISO 11898)
Dominant in automotive (99% of vehicles since 2008)

## Slide 7: Slide 4-6: Multiplexing Concepts & Network Benefits
[Slides 4-6 would cover:
Slide 4: Message-based communication (broadcast vs point-to-point)
Slide 5: Benefits quantified (weight, cost, reliability data)
Slide 6: Transition to CAN bus technical details]

## Slide 8: PART 2: TRIGGER - "CAN Bus Fundamentals

## Slide 9: CAN Bus Overview
Instructor Narration:
Let's explore CAN bus (Controller Area Network) in detail.
PHYSICAL LAYER:
Wiring: — 2 wires: CAN-High (CAN-H) and CAN-Low (CAN-L)
Twisted pair (reduces electromagnetic interference)
120 Ω termination resistors at both ends of bus
Voltage Levels:
Recessive (Logical 1): — CAN-H: 2.5V
CAN-L: 2.5V
Differential voltage: 0V
Dominant (Logical 0): — CAN-H: 3.5V
CAN-L: 1.5V
Differential voltage: 2V
Why Differential Signaling? — Noise immunity: External interference affects both wires equally
Differential voltage unaffected by noise
Example: +0.5V noise on both wires
CAN-H: 3.5V + 0.5V = 4.0V
CAN-L: 1.5V + 0.5V = 2.0V
Differential: Still 2V (noise cancelled!)
Bus Speed (Bit Rate): — High-Speed CAN: 125 kbps to 1 Mbps (typical: 500 kbps)
Low-Speed CAN: 10-125 kbps (older, fault-tolerant variant)
Typical Speeds: — Powertrain CAN: 500 kbps (engine, transmission—fast response needed)
Body CAN: 125 kbps (lights, windows—slower acceptable)
Diagnostic CAN: 500 kbps (OBD-II access)
Instructor Narration (continued):
'CAN bus is like a party phone line from the old days—everyone shares one line, you can hear everyone talking, but there are rules about when you can speak. Except CAN is incredibly sophisticated about managing who talks when.'

## Slide 10: CAN Message Frame Structure
Instructor Narration:
CAN communication happens via messages (called frames). Let's decode the structure.
CAN DATA FRAME (Standard Format):
Total Length: 44-108 bits (depends on data length)
FIELD-BY-FIELD:
1. START OF FRAME (SOF) - 1 bit — Value: Dominant (0)
Purpose: Synchronize all ECUs (start of new message)
2. IDENTIFIER (ID) - 11 bits (Standard CAN) — Range: 0x000 to 0x7FF (0-2047 decimal)
Purpose: — Message identification (what information is this?)
Priority (lower ID = higher priority)
Example IDs: — 0x100: Engine RPM
0x200: Vehicle speed
0x300: Brake pressure
Extended CAN: 29-bit ID (supports 536 million unique IDs—used in some modern systems)
3. REMOTE TRANSMISSION REQUEST (RTR) - 1 bit — 0: Data frame (contains data)
1: Remote frame (request data from another ECU)
Rarely used in modern systems
4. CONTROL FIELD - 6 bits — IDE (Identifier Extension) - 1 bit: Standard (11-bit) vs Extended (29-bit) ID
r0 (Reserved) - 1 bit: Future use
DLC (Data Length Code) - 4 bits: Number of data bytes (0-8)
5. DATA FIELD - 0 to 64 bits (0-8 bytes) — Actual message content — Examples: — Engine RPM: 2 bytes (0-6,500 RPM)
Coolant temp: 1 byte (-40 to +215°C)
VIN request: 8 bytes
6. CRC (Cyclic Redundancy Check) - 15 bits + 1 delimiter — Purpose: Error detection
Calculation: Polynomial checksum of frame content
Receiver: Recalculates CRC, compares to transmitted CRC
If mismatch: Error detected → message rejected
7. ACK (Acknowledgment) - 2 bits — ACK slot: Transmitter sends recessive (1)
Any ECU that receives correctly: Overrides with dominant (0)
If no ACK: Message not received by anyone → error
8. END OF FRAME (EOF) - 7 bits — Value: 7 recessive bits (1111111)
Purpose: Mark end of frame
9. INTERMISSION - 3 bits — Value: 3 recessive bits
Purpose: Minimum gap before next frame

## Slide 11
EXAMPLE MESSAGE: Engine RPM
ID: 0x100 (Engine RPM message)
DLC: 2 (two data bytes)
Data: 0x09C4 (2500 decimal = 2,500 RPM)
Binary Frame (Simplified):
SOF: 0 ID: 00100000000 (0x100) RTR: 0 IDE: 0 r0: 0 DLC: 0010 (2 bytes) Data: 00001001 11000100 (0x09C4 = 2,500) CRC: [15-bit checksum] ACK: 0 (acknowledged) EOF: 1111111
Total frame length: 44 + 16 (data) = 60 bits
At 500 kbps: Transmission time = 60 bits / 500,000 bps = 0.12 ms = 120 microseconds
Instructor Narration (continued):
'CAN messages are incredibly compact. In 120 microseconds, you transmit engine RPM to every ECU in the vehicle. For comparison, this sentence takes about 2 seconds to speak—in that time, CAN transmits over 8,000 messages!'

## Slide 12: Slide 9-15: CAN Protocol Details
[Slides 9-15 would cover:
Slide 9: Message types (Data, Remote, Error, Overload)
Slide 10: Bit stuffing (prevent long strings of identical bits)
Slide 11-12: Arbitration (how ECUs resolve simultaneous transmission)
Slide 13: Error detection mechanisms (5 types)
Slide 14: Fault confinement (error counters, node states)
Slide 15: CAN bus load calculation example]

## Slide 13: PART 3: RISING ACTION - "CAN Operation & Reliability

## Slide 14: CAN Arbitration - Non-Destructive Bus Access
Instructor Narration:
Here's the clever part: CAN allows multiple ECUs to start transmitting simultaneously without collision.
THE SCENARIO:
Timing: — Time = 0 μs: Bus is idle (all recessive)
Three ECUs want to transmit: — ECU-A: Message ID = 0x100 (00100000000)
ECU-B: Message ID = 0x150 (00101010000)
ECU-C: Message ID = 0x200 (01000000000)
Arbitration Process (Bit-by-Bit):
Bit 0 (SOF): — All three ECUs transmit: Dominant (0) — All see dominant on bus
Continue transmitting
Bit 1 (ID bit 10 - MSB): — ECU-A transmits: 0 (dominant)
ECU-B transmits: 0 (dominant)
ECU-C transmits: 0 (dominant)
Bus state: Dominant
All continue
Bit 2 (ID bit 9): — ECU-A transmits: 0 (dominant)
ECU-B transmits: 0 (dominant)
ECU-C transmits: 1 (recessive)
Bus state: Dominant (dominant wins over recessive)
ECU-C: "I transmitted 1 but see 0 on bus → someone else has priority → I stop transmitting and listen
ECU-A and ECU-B continue
Bit 3 (ID bit 8): — ECU-A transmits: 1 (recessive)
ECU-B transmits: 1 (recessive)
Bus state: Recessive
Both continue
Bit 4 (ID bit 7): — ECU-A transmits: 0 (dominant)
ECU-B transmits: 0 (dominant)
Both continue
Bit 5 (ID bit 6): — ECU-A transmits: 0 (dominant)
ECU-B transmits: 1 (recessive)
Bus state: Dominant
ECU-B: "I transmitted 1 but see 0 → ECU-A has priority → I stop
ECU-A wins arbitration, continues transmitting entire message —--
KEY PRINCIPLE:
Wired-AND Logic: — If ANY ECU transmits dominant (0), bus is dominant
All ECUs read bus state
If ECU transmits recessive (1) but reads dominant (0) → Lost arbitration, stop immediately
Result: — Lower ID = Higher Priority (more zeros early in ID = win arbitration)
Non-Destructive: No data lost (losing ECUs retry after winner finishes)
Deterministic: Highest-priority message always wins
Priority Assignment:
Critical Messages (Low ID, High Priority): — 0x000-0x0FF: Safety-critical (ABS, airbag, ESC)
0x100-0x1FF: Powertrain (engine, transmission)
0x200-0x3FF: Chassis (steering, suspension)
Non-Critical Messages (High ID, Low Priority): — 0x400-0x5FF: Body (lights, windows, mirrors)
0x600-0x7FF: Comfort (climate, seats, entertainment)
Example: — ABS urgent message (ID=0x050) vs Climate control (ID=0x650)
Both transmit simultaneously
ABS wins (lower ID)
Climate control waits ~200 μs, retries
Safety always prioritized automatically
Instructor Narration (continued):
'This arbitration is genius. No central controller, no scheduling, no collisions. Pure distributed intelligence. If an airbag needs to broadcast deployment command, it gets bus access within microseconds, even if 20 other ECUs are trying to talk.'

## Slide 15: Slide 17-21: Error Detection and Fault Tolerance
[Slides 17-21 would cover:
Slide 17: Five error detection mechanisms (Bit monitoring, Bit stuffing check, Frame check, ACK check, CRC check)
Slide 18: Error counters and node states (Error-Active, Error-Passive, Bus-Off)
Slide 19: Fault confinement (preventing one faulty ECU from disrupting entire bus)
Slide 20: Real-world reliability (automotive CAN achieves <10^-9 bit error rate)
Slide 21: CAN bus load calculation and bandwidth management]

## Slide 16: PART 4: CLIMAX - "Complete Network Architecture

## Slide 17: Multi-Bus Architecture
Instructor Narration:
Real vehicles use multiple CAN buses with different speeds.
TYPICAL ARCHITECTURE:
1. POWERTRAIN CAN (High-Speed: 500 kbps) — ECUs: Engine, Transmission, ABS/ESC, EPAS
Why fast? Real-time control (engine-transmission coordination needs <10 ms response)
Message volume: 500-1,000 messages/second
2. BODY CAN (Medium-Speed: 125 kbps) — ECUs: Body Control Module, Lighting, Windows, Mirrors, Seats, Climate
Why slower? Not time-critical (0.5s delay to turn on light is acceptable)
Message volume: 200-500 messages/second
3. INFOTAINMENT CAN (Medium-Speed: 125 kbps) — ECUs: Radio, Navigation, Display, Phone, Voice control
Why separate? Isolate non-critical systems from safety systems
Message volume: 100-300 messages/second
4. DIAGNOSTIC CAN (High-Speed: 500 kbps) — Purpose: OBD-II connector (external scan tool access)
Connects to: All buses via gateway
Why? Technician needs access to ALL ECUs for fault diagnosis
5. LIN BUSES (Low-Speed: 19.2 kbps) — Purpose: Simple devices (window switches, mirror motors, seat controls)
Why LIN? Much cheaper than CAN for low-bandwidth applications
Typical: 5-10 LIN buses controlled by Body Control Module

## Slide 18
GATEWAY ECU:
Function: Bridge between different buses
Example: — Instrument cluster on Body CAN needs engine RPM (on Powertrain CAN)
Gateway receives RPM message on Powertrain CAN (ID=0x100)
Gateway retransmits same data on Body CAN (ID=0x500)
Instrument cluster displays RPM
Security: — Gateway filters messages (only forwards necessary data)
Prevents: Infotainment CAN from sending commands to engine
Protects: Critical systems from non-critical system faults
Typical Gateway Traffic: — Powertrain → Body: RPM, Speed, Coolant temp, Fuel level
Body → Powertrain: Driver inputs (brake pedal, cruise control)
Any → Diagnostic: All faults and diagnostic data

## Slide 19: LIN Bus - Low-Cost Alternative
Instructor Narration:
LIN (Local Interconnect Network) is CAN's simpler, cheaper cousin.
COMPARISON: CAN vs LIN
| Feature | CAN Bus | LIN Bus |
|---------|---------|---------|
| Speed | 125 kbps - 1 Mbps | 1-20 kbps (typical: 19.2 kbps) |
| Topology | Multi-master (any ECU can transmit) | Single-master (one controller, multiple slaves) |
| Wiring | 2-wire (CAN-H, CAN-L) | 1-wire + ground |
| Cost per node | $3-5 | $0.50-1.00 |
| Max nodes | 64-110 | 16 |
| Use case | Real-time control | Simple switches, motors |
LIN APPLICATIONS:
Master ECU (Body Control Module): — Sends commands to slaves
Schedules all communication (slaves cannot initiate)
Slave Devices: — Window motors: Up/down commands
Mirror motors: Position control
Seat motors: Adjust commands
Door lock actuators: Lock/unlock
Interior lights: On/off/dim
Rain sensor: Wiper speed request
Example: Power Window Control
Hardware: — LIN bus (1 wire + ground)
Body Control Module (LIN master)
4 window motor modules (LIN slaves, one per door)
Operation:
Driver presses window switch
Switch signal → Body Control Module
BCM sends LIN message: "Left-Front Window, Down, 50% speed
Left-front window module receives, activates motor
Window moves down
BCM periodically polls: "Window position?
Module responds: "80% down
Process repeats until fully down
Why LIN for Windows? — Cost: $1 per motor controller vs $5 for CAN
Speed sufficient: 19.2 kbps plenty for window control (not safety-critical)
4 windows × $4 savings = $16 saved per vehicle
Multiply by 10 million vehicles → $160 million savings!
Instructor Narration (continued):
'LIN is automotive engineering at its finest: Identify that you don't need CAN's sophistication for simple tasks, develop simpler protocol, save billions across the industry. Every penny counts when you manufacture millions of units.'

## Slide 20: Slide 24-27: Network Topology and Design
[Slides 24-27 would cover:
Slide 24: Network topology types (line, star, hybrid)
Slide 25: Bus load calculation (bandwidth utilization)
Slide 26: Message scheduling and timing analysis
Slide 27: Network design example problem]

## Slide 21: PART 5: RESOLUTION - "Diagnostics & Future

## Slide 22: OBD-II - On-Board Diagnostics
Instructor Narration:
OBD-II (On-Board Diagnostics, Second Generation) is the standardized access point to vehicle networks.
WHAT IS OBD-II?
Legal Requirement: — Mandated in USA (1996+), Europe (2001+), India (BS4: 2010+, BS6: 2020+)
Purpose: Monitor emissions-related systems, store fault codes, enable repairs
Physical Interface: — 16-pin connector (standardized location: under dashboard, driver side)
Pin Assignment: — Pin 4, 5: Ground
Pin 16: +12V (battery power)
Pin 6, 14: CAN-High, CAN-Low (500 kbps, ISO 15765)
Other pins: Older protocols (ISO 9141, J1850—rarely used post-2008)
OBD-II FUNCTIONS:
1. Malfunction Indicator Lamp (MIL) - Check Engine Light — Illuminates when emission-related fault detected
Rules: — Misfire that could damage catalyst → Light on immediately
Sensor drift → Light on after 2-3 drive cycles (confirms persistent fault)
2. Diagnostic Trouble Codes (DTCs) — 5-character code: Format: P0XXX
P: Powertrain (B=Body, C=Chassis, U=Network)
0: Generic (standardized, same for all manufacturers)
1: Manufacturer-specific
XXX: Specific fault
Common DTCs: — P0300: Random misfire detected
P0171: System too lean (Bank 1)
P0420: Catalyst efficiency below threshold
P0335: Crankshaft position sensor malfunction
3. Freeze Frame Data — When fault occurs, ECU captures:
RPM, vehicle speed, coolant temp, load, fuel trim, etc.
Helps diagnosis: "What was vehicle doing when fault occurred?
4. Emission Monitors (Readiness) — Tests: Catalyst, O2 sensors, EVAP system, EGR, etc.
Status: Complete/Incomplete
Purpose: Verify all emission systems checked since last fault code clear
Example: — Clear codes, drive 50 km
Some monitors still "Incomplete" (haven't run yet)
Vehicle won't pass emissions test until all "Complete
5. Live Data Stream — Scan tool can read real-time data:
RPM, MAF, Coolant temp, Fuel trim, O2 sensor voltage, etc.
Used for: Diagnosis, performance monitoring

## Slide 23
USING OBD-II:
Equipment: — Scan tool: $50-5,000 (consumer to professional)
Smartphone app + Bluetooth adapter: $20-100 (basic)
Process:
Connect scan tool to OBD-II port
Turn ignition ON (engine can be off)
Scan tool powers up via pin 16 (+12V)
Tool sends diagnostic request on CAN bus (pin 6,14)
Gateway ECU routes request to appropriate ECU (engine, ABS, etc.)
ECU responds with data
Tool displays fault codes, data
Example Diagnostic Session:
Symptom: Check engine light on
Steps:
Connect scan tool
Read codes: P0171 (System Too Lean - Bank 1)
Check freeze frame: RPM=2,500, MAF=8 g/s, Fuel trim=+25%
Interpretation: Engine adding 25% extra fuel to compensate
Likely cause: Vacuum leak (unmeasured air entering engine)
Action: Inspect intake manifold for leaks
Instructor Narration (continued):
'OBD-II democratized vehicle repair. Before 1996, you needed manufacturer-specific (expensive) scan tools. After OBD-II, any generic tool works on any car. This enabled independent repair shops to compete with dealerships—saving consumers billions.'

## Slide 24: Automotive Ethernet & Future Trends
Instructor Narration:
CAN bus has served well for 40 years. But new demands are pushing beyond CAN's limits.
CAN LIMITATIONS:
Bandwidth: — Max: 1 Mbps
Sufficient for: Engine control, sensors, actuators
Insufficient for: Cameras (10-100 Mbps per camera), Radar (5-50 Mbps), High-res displays
Example: — ADAS system with 5 cameras
Each camera: 720p @ 30 fps = ~20 Mbps
Total: 100 Mbps
CAN cannot handle this —--
AUTOMOTIVE ETHERNET (100/1000 Mbps):
Technology: — Based on standard Ethernet (like home/office networks)
Modified for automotive (EMI resistance, temperature range)
Speed: 100 Mbps (Fast Ethernet) to 1 Gbps (Gigabit)
Applications: — ADAS: Camera, radar, lidar data
Infotainment: High-res displays, video streaming
OTA updates: Over-the-air software updates (download 1 GB update in 10-20 seconds)
Diagnostics: Fast ECU reprogramming
Adoption: — 2015: First premium vehicles (BMW 7-series, Mercedes S-class)
2025: Standard in most new vehicles
CAN still present (legacy systems, low-bandwidth control)

## Slide 25
FUTURE: ZONAL ARCHITECTURE
Current: Domain-based (Powertrain CAN, Body CAN, etc.)
Future: Zone-based (Front zone, Rear zone, Left zone, Right zone)
Concept: — Zone controller in each vehicle area
Connects all local devices (sensors, actuators)
Central computer coordinates zones via high-speed Ethernet backbone
Benefits: — Shorter wiring (devices connect to nearest zone controller)
Faster: Ethernet backbone (1-10 Gbps)
Flexible: Software-defined functionality (OTA updates change features)
Timeline: — 2020s: Early adopters (Tesla, startups)
2030s: Industry standard
Instructor Narration (continued):
'The transition from CAN to Ethernet is like upgrading from dial-up internet to fiber optic. CAN (1 Mbps) = dial-up. Automotive Ethernet (1 Gbps) = fiber. Same function (communicate data), but 1,000× faster. Necessary for autonomous driving, where vehicles process gigabytes of sensor data per second.'

## Slide 26: Summary & Module 4 Complete
Instructor Narration:
Let's recap Module 4: Electrical & Control Systems.
SESSION 13: Electrical Architecture
✅ Power generation & storage (battery, alternator)
✅ Power distribution (wiring, fuses, relays)
✅ Grounding (chassis as common negative)
✅ Lighting technologies (halogen → HID → LED)
SESSION 14: Vehicle Control Systems
✅ ECUs (30-100 per vehicle, distributed intelligence)
✅ Sensors (thermistors, MAF, O2 sensor, etc.)
✅ Actuators (injectors, throttle, solenoids)
✅ Closed-loop control (lambda control example)
SESSION 15: Communication Networks (Today)
✅ CAN bus (500 kbps, multi-master, arbitration)
✅ LIN bus (19.2 kbps, low-cost, master-slave)
✅ OBD-II (diagnostic access, standardized)
✅ Network architecture (multi-bus, gateways)
✅ Future (Automotive Ethernet, zonal architecture)
THE BIG PICTURE:
Modern vehicles are mobile computers with:
Electrical power system (Session 13)
Distributed computing (30-100 ECUs, Session 14)
High-speed data networks (Session 15)
Everything we studied in Modules 1-3 (mechanical systems) is now controlled electronically:
Engine (ECU, injectors, throttle—Session 14)
Transmission (TCU, solenoids—Session 14)
Brakes (ABS ECU—Session 10)
Steering (EPAS ECU—Session 11)
Suspension (Adaptive ECU—Session 12)
All communicate via CAN bus (Session 15) using electrical power (Session 13).
NEXT MODULE: Module 5 - Vehicle Architecture & Comfort — Session 16: Chassis & Body Architecture
Session 17: HVAC Systems
Session 18: Passive Safety Systems
We'll integrate mechanical, electrical, and control systems into complete vehicle packages.
See you in Session 16!

## Slide 27: 📊 SESSION METADATA
Total Slides: 30
Lecture Duration: 90 minutes
Q&A Duration: 30 minutes
Learning Outcome Coverage: — ✅ SO-4-15-1: Need for networks, point-to-point vs networked (Slides 2-6)
✅ SO-4-15-2: CAN architecture, protocol, message frame (Slides 7-15)
✅ SO-4-15-3: CAN arbitration, error detection, fault confinement (Slides 16-21)
✅ SO-4-15-4: LIN bus operation and applications (Slide 23)
✅ SO-4-15-5: OBD-II standards and DTCs (Slide 28)
✅ SO-4-15-6: Network topology and bus load calculation (Slides 24-27)
Worked Examples: 2
CAN arbitration (Slide 16)
Bus load calculation (Slide 26 placeholder)
Key Formulas:
Message transmission time: Bits / Bit_rate
Bus load: (Totalbits/sec) / (Busspeed) × 100%
Network efficiency calculation

## Slide 28
END OF SESSION 15 FRAMEWORK
END OF MODULE 4 (ELECTRICAL & CONTROL SYSTEMS)
This framework is ready for PowerPoint conversion.