## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 16: Chassis & Body Architecture'

## Slide 2: Chassis & Body Architecture
Session 16 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title Slide
Instructor Narration:
Welcome to Session 16: Chassis & Body Architecture. Today we step back and look at the vehicle as a complete system—how do you integrate all the components we've studied into a safe, efficient, manufacturable structure?

## Slide 4: Vehicle Classification by Design
Instructor Narration:
Before we discuss architecture, let's classify vehicles by design type.
PASSENGER VEHICLES:
1. SEDAN (Saloon) — Definition: 4-door, separate trunk (boot)
Characteristics: — Three-box design (engine compartment, passenger cabin, trunk—visually distinct)
Fixed roof, four doors
Typically seats 5 (2 front, 3 rear)
Examples: Honda Accord, Toyota Camry, BMW 3-Series
Advantages: Aerodynamic, quiet (trunk isolates cabin from road noise), formal appearance
Disadvantages: Limited cargo flexibility (trunk separate from cabin)
2. HATCHBACK — Definition: 2-door or 4-door with rear liftgate, integrated cargo area
Characteristics: — Two-box design (engine, passenger/cargo combined)
Fold-down rear seats (expand cargo volume)
Typically compact (3.5-4.5m length)
Examples: Honda Civic Hatchback, VW Golf, Maruti Swift
Advantages: Versatile cargo (seats fold), compact (easy parking), efficient packaging
Disadvantages: Less aerodynamic than sedan, cargo area shares cabin (noise, odors)
3. SUV (Sport Utility Vehicle) — Definition: High ground clearance, rugged appearance, optional AWD/4WD
Characteristics: — High seating position (H-point 600-700mm vs 400-500mm sedan)
Body-on-frame OR unibody construction
Typically seats 5-7
Examples: Toyota Fortuner, Honda CR-V, Mahindra XUV700
Advantages: High visibility, perceived safety, cargo capacity, off-road capability (if 4WD)
Disadvantages: Higher fuel consumption, less aerodynamic, higher center of gravity (rollover risk)
4. CROSSOVER (CUV - Crossover Utility Vehicle) — Definition: SUV-like appearance, unibody construction (car-based platform)
Characteristics: — Built on passenger car chassis (not truck chassis)
Car-like handling, better fuel economy than traditional SUV
FWD or AWD (rarely RWD)
Examples: Honda CR-V, Hyundai Creta, Tata Nexon
Note: Most "SUVs" sold today are actually crossovers
5. COUPE — Definition: 2-door, sporty appearance, sloping roofline
Characteristics: — Emphasis on style and performance over practicality
Typically seats 2+2 (tight rear seats)
Examples: Ford Mustang, BMW 4-Series
6. WAGON (Estate) — Definition: Extended roofline to rear, large cargo area, sedan-based
Characteristics: — Like sedan but with extended roof and cargo area
More cargo than sedan, better aerodynamics than SUV
Examples: Volvo V90, Audi A6 Avant (rare in India)
7. MPV/MINIVAN (Multi-Purpose Vehicle) — Definition: Tall roof, 6-9 seats, focus on passenger space
Characteristics: — Boxy design (maximize interior volume)
Sliding rear doors (common)
Three rows of seating
Examples: Toyota Innova, Maruti Ertiga
COMMERCIAL VEHICLES:
8. PICKUP TRUCK — Definition: Open cargo bed, separate cab
Characteristics: — Body-on-frame construction
Rear axle designed for heavy loads
2-door or 4-door cab
Examples: Toyota Hilux, Ford Ranger, Tata Xenon
Instructor Narration (continued):
'Each design prioritizes different attributes. Sedan = efficiency + comfort. SUV = versatility + capability. Hatchback = urban maneuverability. The architecture underneath reflects these priorities.'

## Slide 5: Slide 3-6: Classification by Application and Fuel
[Slides 3-6 would cover:
Slide 3: Application-based classification (city car, family car, executive, sports, luxury)
Slide 4: Fuel type classification (gasoline, diesel, hybrid, EV, CNG)
Slide 5: Segment classification (A, B, C, D, E segments)
Slide 6: Transition to structural architecture]

## Slide 6: PART 2: TRIGGER - "Chassis Types

## Slide 7: Chassis Types Overview
Instructor Narration:
The chassis is the vehicle's structural foundation. Everything else—engine, suspension, body panels—mounts to the chassis.
THREE FUNDAMENTAL APPROACHES:
1. MONOCOQUE (Unibody) — Concept: Body and chassis are one integrated structure
Load path: Distributed throughout body shell
Used in: 90%+ of modern passenger cars
2. LADDER FRAME (Body-on-Frame) — Concept: Separate chassis frame + body mounted on top
Load path: Frame carries all loads, body is just a shell
Used in: Heavy trucks, off-road SUVs, some pickups
3. SPACE FRAME — Concept: Tubular metal framework, lightweight panels
Load path: Tubes carry loads in tension/compression
Used in: Race cars, exotic sports cars (Lotus, some Audis)
Let's explore each in detail.

## Slide 8: Monocoque (Unibody) Construction
Instructor Narration:
Monocoque means 'single shell' (from French: mono = one, coque = shell).
CONCEPT: — Body panels (floor, roof, pillars, doors) are structural members — Welded together into rigid cage
No separate chassis frame
CONSTRUCTION:
Key Structural Elements:
1. Floor Pan — Stamped steel sheet (1.5-2.5mm thick)
Forms passenger compartment floor
Contains transmission tunnel (raised section for driveshaft/exhaust)
Multiple layers welded together for strength
2. Pillars (A, B, C, D) — A-pillar: Front, beside windshield
B-pillar: Middle, between front/rear doors
C-pillar: Rear, beside rear window
D-pillar: (if present) rear-most, wagons/SUVs
Tubular or box-section steel
Critical for roof strength (rollover protection)
3. Rocker Panels (Sills) — Run along bottom of doors (left and right sides)
Box-section steel
Connect front and rear structures
Major load path during side impact
4. Firewall (Bulkhead) — Vertical panel separating engine compartment from cabin
Multiple layers (structure + sound/heat insulation)
Mounting point for pedals, steering column, HVAC
5. Roof Panel — Stamped steel (thinner: 0.7-1.0mm)
Welded to pillars and side rails
Forms protective cage (roll strength)
6. Front & Rear Structures — Front: Engine cradle, radiator support, fender aprons
Rear: Rear floor pan, wheel arches, trunk floor
Bolted or welded to main cabin structure

## Slide 9
LOAD DISTRIBUTION:
Multi-Path Structure: — Loads spread throughout body shell
Example: Side impact force
Enters at door
Distributes through rocker panel, B-pillar, floor, roof rail
Opposite side absorbs energy
No single "frame" member—entire shell acts as structure
Advantages:
✅ Lightweight (30-40% lighter than equivalent body-on-frame)
✅ Stiff (integrated structure, high torsional rigidity)
✅ Space-efficient (no frame rails underneath = more cabin space)
✅ Safer (energy absorption distributed, controlled crush)
✅ Quiet (fewer mechanical joints = less squeaks/rattles)
✅ Manufacturing (suitable for mass production, automated welding)
Disadvantages:
❌ Expensive tooling (complex stamping dies, welding fixtures)
❌ Crash damage costly (structural repair requires specialized equipment)
❌ Lower load capacity (not ideal for heavy towing, off-road abuse)
❌ Harder to modify (can't easily lengthen/shorten wheelbase)
Manufacturing Process:
Body-in-White (BIW) Assembly:
Stamping: Steel sheets stamped into panels (floor, roof, doors, fenders)
Welding: 3,000-5,000 spot welds join panels into body shell
Robot assembly: Automated welding (180-300 robots in modern plant)
Corrosion protection: E-coat (electrodeposition coating—dipped in primer bath)
Paint: Multiple layers (primer, base coat, clear coat)
Final assembly: Install powertrain, interior, glass, electrical
Result: Completed monocoque body
Used In: — All modern passenger cars (sedans, hatchbacks, crossovers)
Most modern SUVs (unibody construction)
Minivans, MPVs
Instructor Narration (continued):
'Monocoque revolutionized automotive design in the 1930s-1950s. Before this, all cars used body-on-frame. Citroën Traction Avant (1934) and Fiat 600 (1955) proved monocoque could be mass-produced. By 1980, body-on-frame passenger cars essentially disappeared—monocoque won due to weight, safety, and packaging advantages.'

## Slide 10: Ladder Frame (Body-on-Frame) Construction
Instructor Narration:
Ladder Frame (also called body-on-frame) is the original automotive chassis design—and still the best for heavy-duty applications.
CONCEPT: — Separate chassis frame (looks like a ladder—two parallel rails with cross members)
Body mounted on top via rubber bushings (body is non-structural)
All loads carried by frame, not body
CONSTRUCTION:
Frame Components:
1. Side Rails (Frame Rails) — Two parallel C-channel or box-section steel beams
Run full length of vehicle (front to rear)
Typical dimensions: 150-250mm tall, 80-120mm wide, 3-6mm thick
Carry bending and torsional loads
2. Cross Members — Perpendicular beams connecting left and right rails
Typically 5-8 cross members
Locations: Front (radiator support), middle (transmission/transfer case), rear (axle mounting)
Provide torsional stiffness (prevent frame twist)
3. Body Mounts — Rubber or polyurethane bushings (isolate body from frame vibration)
Typically 6-12 mounting points
Body bolted to frame (not welded—allows body removal)
4. Suspension Mounts — Brackets welded to frame rails
Mount suspension control arms, springs, shocks
5. Powertrain Mounts — Engine and transmission mount directly to frame
Heavy-duty brackets (engine produces significant torque/vibration)

## Slide 11
LOAD PATHS:
Simple, Direct Loads: — Vertical load (vehicle weight + cargo) → suspension → frame → wheels
Longitudinal load (acceleration, braking) → frame rails
Torsional load (one wheel over bump) → cross members resist twist
Analogy: Like a bridge—two main beams (frame rails) + cross bracing (cross members)
Advantages:
✅ Very strong (can handle heavy loads: 1,000-3,000 kg payload)
✅ Durable (withstands off-road abuse, twisting, impacts)
✅ Easy to repair (body damage doesn't affect frame—replace body panel easily)
✅ Versatile (same frame can support different bodies: pickup, SUV, van)
✅ High ground clearance (frame sits above axles, allows large wheels/tires)
✅ Excellent for towing (frame distributes trailer tongue weight)
Disadvantages:
❌ Heavy (frame alone: 200-400 kg for truck)
❌ Poor fuel economy (weight penalty + aerodynamic compromises)
❌ Less safe (body-on-frame has less controlled crash energy absorption)
❌ Higher floor (frame sits between wheels and cabin—raised seating position)
❌ Less rigid (frame can flex/twist more than monocoque)
❌ NVH (Noise/Vibration/Harshness): Body and frame can vibrate/squeak relative to each other
Modern Improvements:
Hydroformed Rails: — Liquid pressure forms tubes into complex shapes
Variable cross-section (thick where needed, thin where not)
25-30% weight reduction vs stamped C-channel
Boxed Rails: — Fully enclosed box section (instead of open C-channel)
50-60% increase in torsional rigidity
Integrated Front Structure: — Front frame extends forward with controlled crush zones
Modern body-on-frame SUVs have better crash performance than 1990s designs
Used In: — Heavy-duty pickups (Ford F-250/350, Ram 2500/3500, Tata 407)
Body-on-frame SUVs (Toyota Land Cruiser, Mahindra Thar, Jeep Wrangler)
Commercial vehicles (buses, heavy trucks)
Off-road vehicles (require chassis flex for wheel articulation)
Instructor Narration (continued):
'If you're towing a 3,500 kg trailer or driving through a boulder field, you want body-on-frame. If you're commuting 50 km/day on smooth roads, monocoque is better (lighter, more efficient, safer). Engineering is about choosing the right tool for the job.'

## Slide 12: Slide 10-13: Space Frame and Chassis Comparison
[Slides 10-13 would cover:
Slide 10: Space frame construction (tubular design, exotic applications—Lotus, Audi A8)
Slide 11: Comparison table (monocoque vs ladder vs space frame)
Slide 12: Hybrid approaches (Jeep Wrangler, Mercedes G-Class—integrated frames)
Slide 13: Transition to materials]

## Slide 13: PART 3: RISING ACTION - "Materials & Manufacturing

## Slide 14: Materials Selection - The Steel vs Aluminum Trade-off
Instructor Narration:
Chassis material choice involves fundamental engineering trade-offs.
THE CHALLENGE: — Strong materials are usually heavy
Light materials are usually expensive
Cheap materials are usually heavy or weak
MATERIAL OPTIONS:
1. MILD STEEL (Low-Carbon Steel)
Properties: — Yield strength: 200-250 MPa
Density: 7,850 kg/m³
Cost: ₹50-60/kg ($0.60-0.70/kg)
Advantages:
✅ Very cheap (lowest cost structural material)
✅ Easy to form (stamping, bending, welding)
✅ Good weldability (spot welding, arc welding)
✅ Crash energy absorption (plastic deformation in controlled crush zones)
Disadvantages:
❌ Heavy (high density)
❌ Low strength (thick sections required)
❌ Corrosion (rusts without protection)
Used in: Non-structural body panels, inner structures

## Slide 15
2. HIGH-STRENGTH STEEL (HSS)
Properties: — Yield strength: 300-550 MPa (2-3× mild steel)
Density: 7,850 kg/m³ (same as mild steel)
Cost: ₹60-80/kg (slightly more expensive)
Advantages:
✅ 2-3× stronger than mild steel
✅ Thinner sections (same strength, less weight)
✅ Same density as mild steel (no density penalty)
✅ Good weldability (similar to mild steel)
Disadvantages:
❌ Less formable (harder to stamp complex shapes)
❌ Springback (wants to return to original shape after forming)
Used in: B-pillars, rocker panels, door intrusion beams

## Slide 16
3. ULTRA-HIGH-STRENGTH STEEL (UHSS) & ADVANCED HIGH-STRENGTH STEEL (AHSS)
Types: — Dual-Phase (DP) Steel
TRIP (Transformation-Induced Plasticity) Steel
Martensitic Steel
Boron Steel (press-hardened)
Properties: — Yield strength: 600-1,500 MPa (up to 7× mild steel!)
Density: 7,850 kg/m³
Cost: ₹100-200/kg
Boron Steel (Press-Hardened Steel - PHS): — Process: Heat to 900°C, stamp while hot, quench in die (rapid cooling)
Result: Martensite structure (extremely hard: 1,300-1,500 MPa)
Advantage: Can create very thin, very strong parts
Advantages:
✅ Extremely strong (thin sections with high strength)
✅ Weight savings (30-40% vs mild steel for same strength)
✅ Excellent crash performance (controlled deformation)
Disadvantages:
❌ Expensive (special processing, limited formability)
❌ Difficult to weld (special techniques required)
❌ Requires special tooling (press-hardening furnaces)
Used in: A-pillars, B-pillars, roof rails, door intrusion beams (safety cage)

## Slide 17
4. ALUMINUM ALLOYS
Common Alloys: — 5000-series (Al-Mg): Good formability, corrosion resistance
6000-series (Al-Mg-Si): Heat-treatable, moderate strength
Properties: — Yield strength: 100-300 MPa (varies by alloy and heat treatment)
Density: 2,700 kg/m³ (65% lighter than steel!)
Cost: ₹200-300/kg (3-5× steel)
Advantages:
✅ Lightweight (2/3 lighter than steel—major fuel economy benefit)
✅ Corrosion resistant (natural oxide layer)
✅ Recyclable (90% energy savings vs virgin aluminum)
Disadvantages:
❌ Expensive (3-5× cost of steel)
❌ Lower strength (for same thickness—must use thicker sections)
❌ Difficult welding (requires specialized techniques: MIG, TIG, rivet bonding)
❌ Expensive tooling (softer material, different forming processes)
Weight Comparison: — Steel body: 300 kg
Aluminum body: 200 kg (33% weight savings)
Fuel economy benefit: ~5-10% improvement
Cost Impact: — Aluminum body adds ₹50,000-100,000 to vehicle cost
Premium/luxury brands absorb this (Audi A8, Jaguar XE, Ford F-150 aluminum body)
Used in: Hood, trunk lid, doors (outer panels); complete bodies (luxury vehicles)

## Slide 18
5. COMPOSITES (Carbon Fiber, Fiberglass)
Carbon Fiber Reinforced Polymer (CFRP): — Strength: 600-1,000 MPa (in fiber direction)
Density: 1,600 kg/m³ (50% of aluminum, 20% of steel!)
Cost: ₹2,000-5,000/kg (insanely expensive!)
Advantages:
✅ Extremely light (lightest structural material)
✅ Very strong (in fiber direction)
✅ Corrosion-proof (polymer matrix)
Disadvantages:
❌ Prohibitively expensive (50-100× steel cost)
❌ Labor-intensive (hand layup, autoclave curing)
❌ Poor crash energy absorption (brittle fracture)
❌ Difficult to recycle
Used in: Supercars (McLaren, Lamborghini), F1 race cars, exotic applications
Fiberglass (GFRP - Glass Fiber Reinforced Polymer): — Cheaper than carbon fiber (₹200-500/kg)
Lower strength (200-400 MPa)
Used in: Body panels (Corvette), non-structural parts
Instructor Narration (continued):
'Material selection is economic engineering. Steel is cheap but heavy. Aluminum is light but expensive. Carbon fiber is lightest but unaffordable for mass production. Most modern vehicles use mixed materials: steel for most of structure (cheap), AHSS for safety cage (strong), aluminum for hood/doors (light), and maybe carbon fiber for spoilers (low-volume, high-value). This is called multi-material design.'

## Slide 19: Slide 15-19: Manufacturing and Material Trends
[Slides 15-19 would cover:
Slide 15: Steel types summary and material selection criteria
Slide 16: Manufacturing processes (stamping, welding, riveting, adhesive bonding)
Slide 17: Multi-material design example (BMW 7-Series uses 15+ materials)
Slide 18: Future trends (increased aluminum, CFRP for electric vehicles—weight critical)
Slide 19: Transition to weight distribution]

## Slide 20: PART 4: CLIMAX - "Weight Distribution & Crash Safety

## Slide 21: Weight Distribution - Impact on Performance
Instructor Narration:
Now let's connect architecture to performance—a topic from Session 9 (Vehicle Dynamics).
WEIGHT DISTRIBUTION:
Percentage of total vehicle weight on each axle.
Typical Distribution:
| Vehicle Type | Front % | Rear % | Reason |
|--------------|---------|--------|--------|
| FWD sedan | 60-65% | 35-40% | Engine/transmission over front axle |
| RWD sports car | 50-52% | 48-50% | Engine front, transmission rear (better balance) |
| Mid-engine sports car | 40-45% | 55-60% | Engine behind driver (Ferrari, Lamborghini) |
| Rear-engine (Porsche 911) | 38-40% | 60-62% | Engine over rear axle |
| Pickup truck (unloaded) | 55-60% | 40-45% | Front-heavy when empty |
| Pickup truck (loaded) | 40-45% | 55-60% | Rear-heavy when cargo loaded |
IDEAL: 50/50 Front/Rear
Why?
From Session 9, we learned:
Maximum lateral acceleration (cornering): a_lat,max = μ × g × (Weight on loaded tires / Total weight) 50/50 distribution → Both axles equally loaded → Maximum total grip
Impact on Handling:
Front-Heavy (60/40): — Front tires more loaded → More front grip potential
But: Front tires must handle steering AND acceleration (FWD) or braking
Result: Understeer tendency (front loses grip first)
Good for: Safety (predictable), easy for average drivers
Rear-Heavy (40/60): — Rear tires more loaded → More rear grip potential
Result: Oversteer tendency (rear loses grip first)
Dangerous for: Untrained drivers (car can spin)
Preferred by: Enthusiasts (adjustable with throttle)
50/50 (Balanced): — Front and rear equally loaded
Neutral handling (neither under nor oversteer bias)
Best for: Performance, control, fun
Achieved by: Careful component placement (engine, transmission, fuel tank, battery)

## Slide 22
CALCULATING WEIGHT DISTRIBUTION:
Simple Model (2D, Front/Rear):
Given: — Vehicle mass: m = 1,500 kg
Wheelbase: L = 2.7 m
Distance from front axle to center of gravity (CG): a = 1.2 m
Distance from rear axle to CG: b = 1.5 m
Front Axle Load:
W_f = m × g × (b / L) = 1,500 × 9.81 × (1.5 / 2.7) = 1,500 × 9.81 × 0.556 = 8,185 N
Rear Axle Load:
W_r = m × g × (a / L) = 1,500 × 9.81 × (1.2 / 2.7) = 1,500 × 9.81 × 0.444 = 6,535 N
Distribution:
Front %: 8,185 / (8,185 + 6,535) × 100% = 55.6% Rear %: 6,535 / (8,185 + 6,535) × 100% = 44.4% Distribution: 56/44 (front-biased, typical FWD)
Instructor Narration (continued):
'Architects can manipulate weight distribution by relocating components. BMW moved the battery to the trunk (rear weight transfer). Corvette uses a transaxle (transmission at rear axle). Porsche 911 keeps engine in rear (unique handling). Every placement decision affects distribution and handling.'

## Slide 23: Slide 21-26: Crash Safety Architecture
[Slides 21-26 would cover:
Slide 21: Crash safety principles (energy absorption, occupant deceleration limits)
Slide 22: Crumple zones (front and rear—controlled deformation)
Slide 23: Safety cage (rigid passenger compartment—A/B/C pillars, roof rails)
Slide 24: Load paths during frontal impact (forces distributed through frame rails, firewall, floor)
Slide 25: Side impact protection (door intrusion beams, B-pillar reinforcement)
Slide 26: Crash testing standards (NCAP, Euro NCAP, IIHS ratings)]

## Slide 24: PART 5: RESOLUTION - "Complete Integration

## Slide 25: Complete Vehicle Architecture - Subsystem Integration
Instructor Narration:
Let's integrate everything we've studied into a complete vehicle architecture.
FRONT SECTION:
Powertrain Compartment: — Engine: Longitudinal (RWD) or transverse (FWD) mounting
Transmission: Attached to engine (integrated or separate)
Radiator: Front mounting (airflow from grille)
Battery: Typically front right (some luxury cars: trunk-mounted)
Air intake system: Feeds from front grille or fender
Exhaust manifold: Connects to catalytic converter, muffler (runs underneath)
Front Structure: — Crumple zones: Designed to collapse in controlled manner (60-80 cm deformation in severe crash)
Frame rails / Unibody structure: Absorb crash energy
Subframe: Bolt-on structure for engine/transmission mounting (allows easy assembly/disassembly)

## Slide 26
MIDDLE SECTION (Passenger Compartment):
Safety Cage: — A-pillar: UHSS or boron steel (1,500 MPa), ~3mm thick
B-pillar: Reinforced with door intrusion beam
Rocker panels: Box-section, carries side impact loads
Floor pan: Multiple layers, transmission tunnel reinforced
Roof rails: Connect pillars, provide rollover protection
Interior Packaging: — Front seats: Adjustable (fore/aft, recline, height)
Steering column: Telescoping, collapsible (safety—deforms in crash)
Dashboard: Airbag housing, instrument cluster, HVAC vents
Center console: Transmission selector, storage, armrest
Rear seats: Bench (3-passenger) or buckets (2-passenger), fold-down for cargo
Underbody: — Fuel tank: Typically under rear seats or rear axle area (protected location)
Exhaust system: Runs along underbody from engine to rear
Brake/fuel lines: Run along frame rails or floor (protected from road debris)
Electrical harness: Runs under carpet, through firewall

## Slide 27
REAR SECTION:
Rear Structure: — Crumple zone: Rear-end collision protection (less deformation than front—typically 40-60 cm)
Trunk floor / Cargo area: Steel or composite panel
Spare tire well: (if equipped—many modern cars use tire repair kit instead)
Rear Suspension: — Independent: McPherson/multi-link (sedans, crossovers)
Solid axle: Beam or live axle (trucks, some SUVs)
Rear Systems: — Fuel filler: Connects to fuel tank via hose
Exhaust outlet: Muffler and tailpipe exit
Rear lights: Tail lights, brake lights, reverse lights, turn signals
License plate mounting —--
ROOF & SIDES:
Roof: — Structural panel: Stamped steel, welded to pillars
Optional sunroof: Requires reinforcement around opening
Headliner: Interior trim (fabric/vinyl + foam sound absorption)
Doors: — Outer panel: Aluminum or steel (dent-resistant)
Inner structure: Steel with intrusion beam
Window regulator: Motor-driven or manual
Door latch mechanism: Connects to body-mounted striker
Side impact airbags: Mounted in door or seat
Fenders: — Front: Typically bolted on (easy replacement after minor crash)
Rear: Integrated into body (welded) or bolted

## Slide 28
COMPLETE MASS BREAKDOWN (Typical 1,500 kg Sedan):
| Component | Mass (kg) | % of Total |
|-----------|-----------|------------|
| Body-in-White (BIW) | 300-350 | 20-23% |
| Powertrain (engine + transmission) | 250-350 | 17-23% |
| Chassis (suspension, brakes, wheels, tires) | 200-250 | 13-17% |
| Interior (seats, dashboard, carpet, insulation) | 100-150 | 7-10% |
| Electrical/Electronics | 80-120 | 5-8% |
| Fluids (fuel, oil, coolant) | 60-80 | 4-5% |
| Glass (windows, windshield) | 40-60 | 3-4% |
| Exterior trim (bumpers, mirrors, grille) | 30-50 | 2-3% |
| HVAC system | 20-30 | 1-2% |
| Exhaust system | 20-30 | 1-2% |
| Fuel system (tank, pump, lines) | 15-25 | 1-2% |
| Miscellaneous | 50-100 | 3-7% |
| TOTAL | ~1,500 kg | 100% |
Weight Reduction Targets (Modern Design):
Typical 2025 targets vs 2010 baseline:
Body: 10-15% lighter (AHSS, aluminum, optimized design)
Powertrain: 5-10% lighter (aluminum blocks, smaller displacement + turbo)
Chassis: 5-10% lighter (aluminum suspension arms, lighter wheels)
Total: 8-12% vehicle weight reduction → 5-8% fuel economy improvement
Instructor Narration (continued):
'Every kilogram saved improves fuel economy, reduces emissions, and improves performance (acceleration, braking, handling). This is why engineers obsess over weight—it's the gift that keeps giving. Remove 100 kg, and you improve everything.'

## Slide 29: Slide 28-30: Summary and Integration
[Slides 28-30 would cover:
Slide 28: Design trade-offs summary (cost vs weight vs performance vs safety)
Slide 29: Modern trends (lightweighting, electrification impact on architecture, skateboard platforms for EVs)
Slide 30: Complete session summary and preview of Session 17 (HVAC)]

## Slide 30: 📊 SESSION METADATA
Total Slides: 30
Lecture Duration: 90 minutes
Q&A Duration: 30 minutes
Learning Outcome Coverage: — ✅ SO-5-16-1: Vehicle classification (Slides 2-6)
✅ SO-5-16-2: Chassis types comparison (Slides 7-13)
✅ SO-5-16-3: Materials and construction (Slides 14-19)
✅ SO-5-16-4: Weight distribution calculation (Slide 20)
✅ SO-5-16-5: Crash structures and crumple zones (Slides 21-26)
✅ SO-5-16-6: Complete architecture integration (Slide 27)
Worked Example: 1
Weight distribution calculation (Slide 20)
Key Concepts:
Monocoque (unibody) vs ladder frame vs space frame
Material trade-offs (steel cheap/heavy, aluminum light/expensive, AHSS strong)
Weight distribution affects handling (50/50 ideal, front-heavy = understeer)
Crash safety requires crumple zones + rigid safety cage
Complete vehicle is integrated system of subsystems

## Slide 31
END OF SESSION 16 FRAMEWORK
This framework is ready for PowerPoint conversion.