## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 3: Traditional vs Model-Based Systems Engineering'

## Slide 2: Traditional vs Model-Based Systems Engineering
Session 3 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 3. Last week, we learned the frameworks that guide systems engineering: ISO/IEC 15288, the V-Model, systems thinking principles. Today, we answer a practical question that every systems engineer faces: How do we actually DO this work?

## Slide 4: Recap - The Frameworks We Learned
Quick recap. Session 2 gave us:
ISO/IEC 15288: The standard technical processes - requirements, architecture, design, verification, validation
The V-Model: Decompose requirements, implement, integrate, verify
Life cycle stages: Concept to retirement
Stakeholder engagement: The foundation of all requirements
These are our WHAT. Today, we tackle the HOW.
Here's the reality: You can have the best framework in the world, but if you implement it poorly, you still fail. The question is: What tools and approaches give us the best chance of success?

## Slide 5: The Real-World Problem
Let me paint a picture. It's 2005. You're a systems engineer on a complex automotive platform. Your job is to manage:
3,000+ system requirements (in Word documents)
500+ subsystem specifications (in Excel spreadsheets)
1,200+ interface definitions (in PowerPoint presentations)
800+ test cases (in various templates)
Hundreds of stakeholders across 50+ suppliers
Now answer this: How do you know if requirement R-1247 is properly verified by test case TC-0892? How do you track the impact when a stakeholder changes a critical requirement? How do you ensure architectural consistency?
You spend 60% of your time managing documents, not engineering the system.
This is the traditional approach. It works, but it's painful. There has to be a better way.

## Slide 6: The Evolution Story
Systems engineering has evolved through three major eras:
Era 1: Document-Centric SE (1960s-1990s) — Requirements in text documents
Designs in drawings and specs
Manual traceability matrices
Works, but doesn't scale
Era 2: Digital Documents (1990s-2010s) — Word processors and spreadsheets
Requirements management tools
Better than paper, but still document-focused
Traceability is manual or fragile
Era 3: Model-Based SE (2000s-present) — Requirements as model elements
Designs as executable models
Automated traceability
Simulation and analysis built-in
We're living through this transition right now. Some industries (aerospace, defense) are heavily MBSE. Others (automotive) are in the middle. Understanding both approaches is critical.

## Slide 7: Traditional Systems Engineering - The Document Paradigm
Traditional systems engineering is fundamentally document-centric. What does that mean?
Every engineering artifact is captured in a document:
Requirements → Requirements Document
Architecture → Architecture Specification
Design → Design Document
Interfaces → Interface Control Documents
Tests → Test Plans and Procedures
These documents are the single source of truth. Engineers create them, review them, approve them, baseline them, and maintain them throughout the system life cycle.
Let me walk you through how this works in practice.

## Slide 8: Traditional SE Workflow Example
Imagine we're developing a brake-by-wire system. Here's the traditional workflow:
Phase 1: Requirements Definition — Systems engineer interviews stakeholders
Writes 'System Requirements Specification' (SRS) document
Contains functional requirements: 'The system shall reduce vehicle speed at rate proportional to pedal force'
Contains performance requirements: 'Braking force shall achieve 1.0g deceleration'
Document goes through review and approval process
Baseline version stored in document management system
Phase 2: Architecture Design — Architect reads SRS
Creates 'System Architecture Document' (SAD)
Defines subsystems: Pedal sensor, ECU, hydraulic actuator
Allocates requirements to subsystems
Creates interface specifications (separate documents)
Review, approve, baseline
Phase 3: Detailed Design — Component engineers receive allocated requirements
Create detailed design documents for each component
More reviews, approvals, baselines
Phase 4: Verification — Test engineers read requirements documents
Write test procedures (new documents)
Execute tests, record results (test reports - more documents)
Notice what's happening? Information flows through documents. Changes propagate through document revisions.

## Slide 9: Traditional SE - Strengths
Before we criticize this approach, let's acknowledge its strengths. Traditional document-based SE has served us well for decades:
Strengths:
Familiar and Accessible — Everyone knows Word, Excel, PowerPoint
Low training barrier
No special software licenses required
Human-Readable — Natural language is flexible
Easy to communicate with non-technical stakeholders
Can express complex ideas clearly
Regulatory Acceptance — Regulations often require specific document deliverables
Established audit trails
Proven in certification processes (ISO 26262, DO-178C, etc.)
Works for Simple Systems — Effective for systems with 100-500 requirements
Good for stable, well-understood domains
Proven track record
Flexibility — Can capture any type of information
Easy to add context, rationale, diagrams
Not constrained by tool limitations
This approach has delivered spacecraft, aircraft, automobiles, medical devices successfully. It's not broken - it's just challenged by modern complexity.

## Slide 10: What is Model-Based Systems Engineering?
Model-Based Systems Engineering (MBSE) represents a fundamental paradigm shift:
Traditional SE: Information captured in documents
MBSE: Information captured in models
INCOSE defines MBSE as:
'The formalized application of modeling to support system requirements, design, analysis, verification and validation activities beginning in the conceptual design phase and continuing throughout development and later life cycle phases.'
Let me break this down:
Formalized modeling: Not just drawings - structured, machine-readable models
Support all activities: Requirements, design, analysis, V&V all in the model
Entire life cycle: From concept to retirement
The key difference: — Documents are for humans to read
Models are for humans AND machines to process
A model is a structured, executable representation of the system. Not just a picture - it's a database of system information with rules, relationships, and semantics.

## Slide 11: The MBSE Paradigm Shift
Let me show you the paradigm shift with our brake-by-wire example:
Traditional Approach: — Requirement text: 'The system shall reduce vehicle speed at rate proportional to pedal force'
Exists as natural language in Word document
Must manually trace to design
Must manually create test case
MBSE Approach: — Requirement exists as model element with:
Unique ID (automatically assigned)
Requirement text (structured field)
Verification method (linked attribute)
Allocated architecture element (automatic relationship)
Verification test case (automatic trace)
All relationships are machine-readable — Changes automatically propagate
Impact analysis is automatic query
The magic: The model maintains relationships automatically. Change a requirement, and you instantly see:
Which architecture elements are affected
Which test cases need updating
Which subsystems must be re-verified
This is the power of MBSE.

## Slide 12: Core Principles of MBSE
MBSE rests on four core principles:
Principle 1: Single Source of Truth — One authoritative model, not scattered documents
All stakeholders work from the same model
No synchronization problems
Principle 2: Formalized Semantics — Model elements have precise meanings
Relationships have defined rules
Machine can reason about the model
Principle 3: Automated Traceability — Requirements trace to architecture automatically
Architecture traces to tests automatically
Impact analysis is querying, not detective work
Principle 4: Model Continuity — Same model used across life cycle stages
Requirements model → Architecture model → Design model → Test model
Continuous thread from stakeholder needs to validation
Example in automotive: — Stakeholder says: 'I need emergency braking'
This becomes a requirement element in the model
System architect allocates it to 'Autonomous Emergency Braking' system element — That system is decomposed into subsystem elements: sensor fusion, decision logic, brake actuation
Each subsystem has interface elements defined
Test engineer links test case elements to requirements
When stakeholder changes the requirement, all these relationships update automatically
This is model continuity and traceability in action.

## Slide 13: The MBSE Workflow
Here's how MBSE works in practice:
Step 1: Stakeholder Needs Modeling — Capture stakeholder needs as model elements
Define use cases and scenarios
Model operational context
Step 2: Requirements Modeling — Transform needs into formal requirements
Structure requirements hierarchically
Define verification methods in model
Step 3: Functional/Logical Architecture — Model system functions (what the system does)
Define functional interfaces
Allocate requirements to functions
Step 4: Physical Architecture — Define physical components (hardware, software)
Map functions to components
Define physical interfaces
Step 5: Behavior Modeling — Model system dynamics
Simulate behavior
Analyze performance
Step 6: Verification & Validation Modeling — Define test architecture
Link tests to requirements
Capture V&V results in model
Key difference from traditional: All of this exists in ONE integrated model, not separate documents. Changes ripple through automatically.

## Slide 14: MBSE Benefits - Why Make the Shift?
Why adopt MBSE? Let me give you concrete benefits, backed by industry data:
Benefit 1: Improved Quality — Early error detection: Model consistency checks catch errors in requirements phase
Reduced rework: NASA reports 40-60% reduction in late-stage rework with MBSE
Better completeness: Automated checks find missing requirements and interfaces
Benefit 2: Better Communication — Visual models: Easier to understand than 500-page documents
Common language: All stakeholders work from same model
Reduced ambiguity: Formalized semantics eliminate interpretation errors
Benefit 3: Automated Traceability — Real-time impact analysis: Know instantly what changes affect
Audit readiness: Traceability reports generated automatically
Compliance: Easier to demonstrate regulatory compliance
Benefit 4: Reuse — Model libraries: Reuse proven system patterns
Product lines: Model variants more easily
Reduced development time: Lockheed Martin reports 25% reduction in development time
Benefit 5: Integration with Simulation — Early validation: Simulate system behavior before building hardware
What-if analysis: Test design alternatives quickly
Performance prediction: Verify performance requirements in model
Benefit 6: Scalability — Handles 10,000+ requirements effectively
Manages complex multi-level architectures
Supports large distributed teams
Industry data: — JPL (NASA): 30% reduction in integration issues
Lockheed Martin: 50% improvement in requirements quality
Boeing: 25% faster time to market for complex systems
The ROI is real, but there's a catch...

## Slide 15
#### Part 2: MBSE Challenges and Realities (Slides 15-17, ~8 minutes)

## Slide 16: MBSE Challenges - The Honest Assessment
MBSE isn't a silver bullet. Let me give you the honest challenges:
Challenge 1: Steep Learning Curve — Learning SysML, Cameo, Rhapsody, etc. takes months
Different mindset than document-based work
Engineers resist change ('I know Word, why learn this?')
Training costs: $2,000-5,000 per engineer
Challenge 2: Expensive Tools — Enterprise MBSE tools: $5,000-15,000 per license per year
Infrastructure costs: servers, IT support, tool integration
Small companies struggle with upfront investment
Challenge 3: Organizational Change — Requires process changes
New roles (model managers, librarians)
Cultural resistance: 'We've always done it with documents'
Takes 2-3 years to fully transition
Challenge 4: Tooling Immaturity — MBSE tools still evolving
Interoperability issues between tools
Not all domains have mature model libraries
Challenge 5: Over-Engineering Risk — Easy to build overly complex models
'Modeling for modeling's sake' - adding no value
Need discipline to model at right level of abstraction
Challenge 6: Doesn't Replace Engineering Judgment — Models don't design systems - engineers do
Garbage in, garbage out
Still need skilled systems engineers
Challenge 7: Regulatory Uncertainty — Some regulations still require specific documents
Auditors may not accept models (yet)
May need to generate documents FROM models anyway
Bottom line: MBSE has significant adoption barriers. Success requires commitment, training, and cultural change.

## Slide 17: The Adoption Reality - Industry Snapshot
Let's look at reality. MBSE adoption varies dramatically by industry:
High Adoption (60-80%): — Aerospace & Defense: NASA, Lockheed Martin, Northrop Grumman - heavily invested
Satellite systems: Complex, long life cycles, benefit from MBSE
Military systems: Mandated by U.S. DoD in some contracts
Medium Adoption (30-50%): — Commercial aerospace: Boeing 787 used MBSE partially
Medical devices: Complex regulated devices (pacemakers, surgical robots)
Rail systems: High-speed trains, signaling systems
Growing Adoption (10-30%): — Automotive: Varies by OEM - premium brands leading (Mercedes, BMW)
Industrial automation: Factory systems, robotics
Low Adoption (<10%): — Consumer electronics: Fast cycles, less benefit
Small companies: Cost barriers
Simple mechanical systems: Overkill for the complexity
Automotive-specific: — Tier 1 suppliers: Bosch, Continental experimenting with MBSE
OEMs: Using MBSE for specific systems (ADAS, powertrains) but not enterprise-wide
Trend: Growing adoption driven by electrification, autonomy, software complexity
We're in a transition period. You'll likely encounter both approaches in your career.

## Slide 18: Hybrid Approaches - The Pragmatic Path
Here's the practical reality: Most organizations don't do pure MBSE or pure traditional SE. They do hybrid:
Common Hybrid Pattern: — High-level architecture: Model-based (SysML)
Detailed requirements: Traditional documents (managed in DOORS, Jira)
Mechanical design: CAD tools (not MBSE)
Software design: Simulink models (behavioral MBSE)
Electrical design: Traditional schematics
Testing: Mix of model-based test generation and manual test procedures
Why hybrid? — Leverage MBSE where it adds most value
Keep familiar approaches where they work
Gradual transition minimizes disruption
Lower cost and risk than full MBSE adoption
Example: Automotive powertrain development — System requirements: Traditional document (stakeholder comfort)
Control algorithm design: Simulink models (enables simulation)
Software architecture: AUTOSAR models (industry standard)
Calibration data: Excel spreadsheets (engineer preference)
Test cases: Model-based test generation from Simulink
This pragmatic approach is common and often sensible. Use the right tool for each job.

## Slide 19
#### Part 3: MBSE Tools and Languages (Slides 18-21, ~15 minutes)

## Slide 20: The MBSE Tool Landscape
MBSE isn't one tool - it's an ecosystem. Let me map it out:
Category 1: Systems Modeling Tools — Purpose: Create system architecture, requirements, behavioral models
Tools: Cameo Systems Modeler, IBM Rhapsody, Vitech GENESYS, PTC Windchill Modeler
Language: Typically SysML (Systems Modeling Language)
Category 2: Behavioral/Simulation Tools — Purpose: Model dynamic behavior, simulate system performance
Tools: MATLAB/Simulink, Modelica/Dymola, ANSYS
Use case: Control systems, physical systems, multi-domain simulation
Category 3: Requirements Management Tools — Purpose: Manage requirements traceability
Tools: IBM DOORS, Jama Connect, Polarion
Can integrate with: SysML tools, Simulink
Category 4: Architecture Tools — Purpose: Define system structure, allocations
Tools: Enterprise Architect, MagicDraw, Capella
Category 5: Automotive-Specific — AUTOSAR: Software architecture standard for automotive
EAST-ADL: Architecture description language for automotive
The challenge: These tools must integrate. You don't use just one - you use a toolchain.

## Slide 21: SysML - The Language of MBSE
Let's focus on SysML - Systems Modeling Language. This is the lingua franca of MBSE.
What is SysML? — A graphical modeling language for systems engineering
Based on UML (Unified Modeling Language from software)
Standardized by OMG (Object Management Group)
Supported by most MBSE tools
SysML has 9 diagram types organized in 4 categories:
1. Structure Diagrams (What is the system made of?)
Block Definition Diagram (bdd): Shows system hierarchy, components, relationships
Internal Block Diagram (ibd): Shows internal structure, interfaces, flows
Package Diagram: Organizes model elements into packages
2. Behavior Diagrams (What does the system do?)
Activity Diagram: Shows functional flows and control logic
Sequence Diagram: Shows interactions between components over time
State Machine Diagram: Shows system states and transitions
Use Case Diagram: Shows system interactions with external actors
3. Requirement Diagrams (What must the system satisfy?)
Requirement Diagram: Shows requirements and relationships (derive, satisfy, verify, refine)
4. Parametric Diagrams (What are the system constraints?)
Parametric Diagram: Shows mathematical relationships and constraints
Example: Brake-by-wire system in SysML — Block Definition Diagram: Shows BrakeSystem block composed of PedalSensor, BrakeECU, HydraulicActuator
Internal Block Diagram: Shows how these blocks connect (signal flows, power flows)
Activity Diagram: Shows 'Apply Braking' activity flow
Requirement Diagram: Shows 'Deceleration Requirement' satisfied by 'BrakeSystem'
Parametric Diagram: Shows equation: BrakingForce = f(PedalPosition, VehicleSpeed)
SysML enables you to capture the ENTIRE system in one coherent model.

## Slide 22: Simulink & MATLAB - Behavioral MBSE
Now let's talk about Simulink and MATLAB - the workhorses of behavioral modeling in automotive.
What is Simulink? — A block diagram environment for modeling dynamic systems
Developed by MathWorks
Used extensively in automotive for control systems design
Enables model-based design (requirements → model → simulation → code generation)
Key capabilities:
1. Behavioral Modeling — Model control algorithms, signal processing, state machines
Represents continuous (physics) and discrete (logic) systems
2. Simulation — Execute the model to predict system behavior
Test 'what-if' scenarios
Verify performance requirements before hardware exists
3. Automatic Code Generation — Generate production C/C++ code directly from model
Eliminates hand-coding errors
Used in safety-critical automotive systems
4. Integration with Requirements — Link Simulink blocks to requirements (via Simulink Requirements)
Automated test case generation
Coverage analysis
MATLAB Integration: — MATLAB provides the computation engine
Analyze data, optimize parameters, run Monte Carlo simulations
Pre-processing and post-processing of simulation results
Automotive example: ABS (Anti-lock Braking System) — Model vehicle dynamics: Tire slip, braking force, vehicle deceleration
Model ABS control algorithm: Slip detection, pressure modulation
Simulate scenario: Emergency braking on wet road
Verify requirement: 'System shall prevent wheel lock-up' - verified via simulation
Generate code: ABS ECU software generated from validated model
Why this matters: — Traditional approach: Write control algorithm spec (document), hand-code in C, debug on hardware
Simulink approach: Model algorithm, simulate extensively, auto-generate verified code
Result: 50-70% reduction in development time for complex control systems
This is MBSE for the behavioral domain.

## Slide 23: Toolchain Integration - Making It Work Together
Here's the hard truth: No single tool does everything. Real MBSE requires toolchain integration.
Typical automotive MBSE toolchain:
1. Requirements Management — Tool: IBM DOORS or Jama Connect
Purpose: Capture and manage text requirements
Interfaces with: SysML tools, Simulink
2. System Architecture — Tool: Cameo Systems Modeler (SysML)
Purpose: Define system structure, allocations, interfaces
Interfaces with: Requirements tool, Simulink, CAD
3. Behavioral Modeling — Tool: MATLAB/Simulink
Purpose: Model and simulate control systems, dynamics
Interfaces with: Requirements tool, SysML, code generators
4. Software Architecture — Tool: AUTOSAR tooling (e.g., Vector DaVinci)
Purpose: Define automotive software architecture
Interfaces with: Simulink (code generation), requirements
5. Mechanical Design — Tool: CAD (CATIA, NX, SolidWorks)
Purpose: Design physical components
Interfaces with: SysML (for geometry allocation), simulation tools
6. Test Management — Tool: Vector CANoe, dSPACE, or custom test automation
Purpose: Execute tests, capture results
Interfaces with: Requirements tool (for traceability)
Integration challenges: — Different data formats
Synchronization issues
Licensing costs multiply
Need integration expertise
Solution patterns: — API integration: Tools communicate via APIs
Common data formats: ReqIF (requirements), OSLC (lifecycle), FMI (simulation)
Model exchange: Export/import models between tools
Traceability backbone: Central traceability database that all tools update
Real example: Mercedes-Benz MBSE toolchain — Requirements: DOORS
Architecture: Enterprise Architect (SysML)
Controls: Simulink
Software: AUTOSAR tooling
Integration: Custom integration layer
Result: End-to-end traceability from customer needs to test cases
Building and maintaining this toolchain is a significant investment. But for complex systems, the benefits outweigh the costs.

## Slide 24
#### Part 4: Digital Twins - The Next Frontier (Slides 22-23, ~7 minutes)

## Slide 25: What is a Digital Twin?
Now let me introduce you to the next evolution in MBSE: Digital Twins.
Definition:
A digital twin is a virtual representation of a physical system that:
Mirrors the physical system in real-time
Is updated with sensor data from the physical system
Enables simulation, prediction, and optimization
Spans the entire life cycle from design to operation to retirement
Key difference from traditional MBSE models: — Traditional MBSE: Model used during development, then archived
Digital Twin: Model continues to evolve and is used throughout operation
The concept: — Create a high-fidelity model during development (MBSE approach)
Deploy system with sensors and connectivity
Physical system sends operational data to digital twin
Digital twin updates to reflect actual system state
Use digital twin for:
Performance monitoring: Is the system operating within parameters?
Predictive maintenance: Will a component fail soon?
Optimization: How can we tune system for better performance?
What-if analysis: What happens if we change this parameter?
Example: Automotive digital twin — During development: Create Simulink model of electric powertrain
In production vehicle: Embed sensors (battery state, motor temperature, energy consumption)
During operation: Vehicle streams data to cloud digital twin
Digital twin simulates battery degradation, predicts remaining range
Optimizes charging strategy based on real usage patterns
Predicts maintenance needs before failure
This closes the loop from design to operation.

## Slide 26: When to Use Traditional SE vs MBSE
Now for the critical question: When should you use traditional document-based SE, and when should you use MBSE?
There's no universal answer, but here's a decision framework:
Use Traditional (Document-Based) SE when:
1. Simple Systems — Fewer than 500 requirements
Well-understood domain
Low interdependency between components
Example: Simple mechanical assembly, consumer appliance
2. Stable Requirements — Requirements won't change frequently
Long time between design and deployment
Example: Infrastructure projects (bridges, buildings)
3. Limited Resources — Small team (< 10 people)
Budget constraints (can't afford MBSE tools)
No time for training investment
4. Regulatory Constraints — Regulations mandate specific document deliverables
Auditors unfamiliar with MBSE
Example: Some medical device certifications
5. Short Life Cycle — System will be obsolete quickly (< 2 years)
Not worth investment in comprehensive model
Example: Marketing prototypes, short-term projects
Use MBSE when:
1. Complex Systems — 1,000+ requirements
High interdependency (aerospace, automotive platforms)
Multiple subsystems and interfaces
Example: Modern vehicles, aircraft, satellites
2. Evolving Requirements — Expect significant changes during development
Agile development approach
Need to manage change impact efficiently
3. Long Life Cycle — System will be in service 10+ years
Need to maintain and evolve over time
Return on MBSE investment is high
Example: Commercial aircraft, power plants
4. Reuse Requirements — Product line engineering (multiple variants)
Platform-based development
Model reuse saves significant time
Example: Automotive platforms (VW MQB, Toyota TNGA)
5. Simulation-Intensive — Need to verify performance before hardware exists
Safety-critical systems requiring extensive analysis
Example: Flight control systems, autonomous vehicles
6. Large Distributed Teams — 50+ engineers across multiple sites
Need consistent communication and collaboration
MBSE provides common language
7. High Consequence of Failure — Safety-critical or mission-critical systems
Need rigorous traceability and verification
Regulatory compliance requirements
Example: Medical implants, aircraft, defense systems
The hybrid approach: Use MBSE for complex subsystems, traditional for simple ones.

## Slide 27: Migration Path - How to Transition to MBSE
If you decide MBSE makes sense, how do you get there? Here's a pragmatic migration path:
Phase 1: Foundation (6-12 months) — Action: Select tools, train core team (5-10 people)
Pilot: Pick ONE subsystem for MBSE pilot project
Deliverable: Lessons learned, tool configuration, process definition
Risk: Low - limited scope
Phase 2: Expansion (12-18 months) — Action: Roll out to additional projects, train more engineers (20-30)
Integration: Connect MBSE tools to existing requirements management
Deliverable: Proven MBSE process, expanded model library
Risk: Medium - change management challenges
Phase 3: Enterprise Adoption (18-36 months) — Action: Make MBSE the standard approach for new complex systems
Infrastructure: Enterprise model repositories, governance processes
Deliverable: Organizational competency in MBSE
Risk: High - requires cultural change, sustained executive support
Phase 4: Optimization (Ongoing) — Action: Integrate digital twin concepts, advanced simulation, AI
Deliverable: Mature MBSE practice, continuous improvement
Critical success factors: — Executive sponsorship and sustained funding
Don't try to MBSE everything - focus on high-value systems
Invest in training (20-40 hours per engineer)
Start with architecture modeling, add behavioral modeling later
Measure benefits (defect reduction, time savings) to justify investment
Common pitfalls: — Trying to model everything to excessive detail
Insufficient training - engineers revert to documents
Tool selection without process definition
No integration with existing toolchain
Underestimating cultural resistance
Realistic timeline: 3-5 years for full organizational transformation.

## Slide 28: The Future - Where SE is Heading
Before we wrap up, let me give you a glimpse of where systems engineering is heading:
Trend 1: MBSE Becomes Default for Complex Systems — 5-10 years: MBSE will be standard practice in automotive, aerospace
Universities will teach SysML alongside CAD
Traditional SE will persist for simple systems only
Trend 2: Digital Twins Everywhere — Every connected product will have a digital twin
Twins will enable new business models (performance-as-a-service)
Regulation may require twins for safety-critical systems
Trend 3: AI-Assisted Systems Engineering — AI will help design optimal architectures
Automated requirement generation from natural language
Intelligent test case generation
Anomaly detection in complex models
Trend 4: Continuous Engineering — Blurring line between development and operation
OTA updates mean systems never 'finish' development
DevOps for systems engineering
Trend 5: Democratization of MBSE — Lower-cost tools (cloud-based, subscription models)
Easier-to-use interfaces (less UML/SysML expertise required)
Open-source MBSE tools emerging
Trend 6: Lifecycle Digital Thread — Unbroken digital thread from stakeholder needs → design → manufacturing → operation → support
All data in connected models
Complete traceability across entire value chain
What this means for you: — Invest in learning MBSE tools and languages
Understand data science and simulation
Develop software engineering skills (models ARE software)
Think across the entire system life cycle
Be comfortable with continuous learning (tools evolve rapidly)
The future systems engineer is part traditional engineer, part data scientist, part software engineer.

## Slide 29: Connecting the Sessions - Your Journey So Far
Let's see where we've been and where we're going:
Session 1: Introduction to Systems Engineering — WHY systems engineering matters
Failure case studies: Therac-25, Mars Climate Orbiter, Toyota
The cost of poor SE
Session 2: Systems Engineering Fundamentals — WHAT is systems engineering
INCOSE definition, systems thinking
ISO/IEC 15288 processes
V-Model execution framework
Session 3: Traditional vs MBSE (Today)
HOW we practice systems engineering
Document-based vs model-based approaches
Tools: SysML, Simulink, MATLAB
Digital twins
Decision framework
You now have: — The motivation (Session 1)
The framework (Session 2)
The implementation approaches (Session 3)
Where we go next:
Session 4: Requirements Engineering — Deep dive into requirements definition
How to write good requirements
Requirements management (traditional AND MBSE approaches)
Traceability in practice
Sessions 5-8: Design, Analysis, Integration, V&V — Working through the V-Model in detail
Architecture development
Functional and operational analysis
Verification and validation strategies
Future sessions: We'll see MBSE concepts integrated throughout - requirements in models, architecture in SysML, simulation for V&V.

## Slide 30: Key Takeaways - What You Must Remember
Here are your key takeaways from Session 3:
1. Two Paradigms — Traditional SE: Document-centric, manual traceability, works for simple systems
MBSE: Model-centric, automated traceability, scales for complex systems
2. MBSE Principles — Single source of truth (one integrated model)
Formalized semantics (machine-readable)
Automated traceability (relationships maintained automatically)
Model continuity (same model across life cycle)
3. Tools and Languages — SysML: Language for system architecture and requirements
Simulink/MATLAB: Behavioral modeling and simulation
Integration: Real MBSE requires toolchain integration
4. Digital Twins — Virtual representations updated with real-world data
Enable predictive maintenance, optimization, continuous validation
The next evolution of MBSE
5. Decision Framework — Use Traditional SE for: Simple systems, stable requirements, limited resources
Use MBSE for: Complex systems, evolving requirements, long life cycles, high stakes
Hybrid is often most pragmatic
6. Migration Reality — MBSE adoption takes 3-5 years
Requires training, tools, process changes, cultural shift
Start with pilots, expand gradually
7. Both Implement Same Framework — ISO/IEC 15288 processes apply to both
V-Model works with both
It's the IMPLEMENTATION that differs, not the principles
The meta-lesson: As a systems engineer, you must choose appropriate methods for your context. There's no one-size-fits-all answer.

## Slide 31: Preparation for Next Session & Questions
Assignment for next session:
1. Reading: — INCOSE Systems Engineering Handbook, Chapter 3 (Requirements Engineering)
Provided article: 'Introduction to SysML' (5 pages)
2. Practical Exercise: — Choose a system you're familiar with (automotive or otherwise)
Identify 10 system requirements
Sketch how you would capture these:
Traditional approach (what documents?)
MBSE approach (what model elements? what relationships?)
Submit 2-page comparison
3. Tool Exploration (Optional): — Explore Papyrus (open-source SysML tool) or Simulink (if you have access)
Try creating a simple model
No submission required - just familiarization
Reflection Questions: — When would you choose MBSE over traditional SE for an automotive system?
What are the biggest barriers to MBSE adoption in your organization?
How could digital twins change automotive maintenance and operation?
Next Session Preview:
Session 4 goes deep into Requirements Engineering — the most critical technical process. We'll learn:
How to identify stakeholders systematically
How to distinguish needs from requirements
Functional vs non-functional vs constraint requirements
How to write verifiable, traceable, clear requirements
Requirements management in both traditional and MBSE contexts
Common pitfalls and how to avoid them
Requirements are the foundation of everything else. If you get requirements wrong, everything built on top is wrong. That's why we dedicate an entire session to this.
Now, let's open it up for questions. 30 minutes for discussion.
Questions to prompt discussion:
Has anyone used SysML or Simulink? What was your experience?
What systems in your organization might benefit from MBSE?
What concerns do you have about transitioning to MBSE?
Where do you see digital twins making the biggest impact in automotive?

## Slide 32: 📊 PPT DESIGN GUIDANCE
Diagrams to Include:
Comparative visuals: Side-by-side comparisons of traditional vs MBSE throughout
Tool screenshots: Show actual SysML diagrams, Simulink models (not just clipart)
Process flows: Clear workflow diagrams showing document flow vs model flow
Decision matrices: Use structured decision frameworks (2x2 matrices, decision trees)
Color coding: Consistent colors - Blue for traditional, Green for MBSE, Purple for hybrid
Slide 3 (The Real-World Problem) - Make the pain vivid
Slide 11 (MBSE Paradigm Shift) - The core difference
Slide 19 (SysML Overview) - Show actual diagram examples
Slide 20 (Simulink) - Show real automotive control model
Slide 22-23 (Digital Twins) - Visually compelling use cases
Slide 24 (Decision Framework) - Practical decision support
Slide 26 (Synthesis) - Integration of all concepts
Slide 7: Build traditional workflow step-by-step
Slide 11: Side-by-side build showing traditional vs MBSE workflow
Slide 19: Reveal each SysML diagram type with example
Slide 21: Animate toolchain integration connections
Slide 25: Progressive disclosure of migration phases
SysML diagrams: Block definition diagram, internal block diagram, requirement diagram from automotive system
Simulink model: ABS or cruise control model screenshot
Digital twin architecture: Real automotive digital twin architecture (Tesla, BMW, etc.)
Tool screenshots: Actual Cameo, DOORS, Simulink interfaces (use with permission or sanitize)
Industry data: Charts showing MBSE adoption rates, ROI data
Define acronyms on first use: MBSE, SysML, DOORS, AUTOSAR
Use consistent terminology: "model elements" not "objects," "requirements" not "specs
Include vendor-neutral language when discussing tools
Provide specific examples for abstract concepts
Use quotes from industry practitioners if available
Document-centric workflow (Slide 7)
Model-based workflow (Slide 13)
SysML 9 diagram types overview (Slide 19)
MBSE toolchain integration architecture (Slide 21)
Digital twin data flow (Slide 22)
Decision matrix: Traditional vs MBSE (Slide 24)
Migration roadmap timeline (Slide 25)

## Slide 33: 🎯 INSTRUCTOR NOTES
Optional Advanced Topics (If Time Permits):
Comparative approach: Constantly compare traditional vs MBSE to build understanding
Practical focus: Emphasize real-world application, not theoretical perfection
Tool demonstration: If possible, show live tool demos (5-minute SysML demo, Simulink demo)
Balanced perspective: Don't oversell MBSE - acknowledge challenges honestly
Decision support: Give students frameworks to make their own informed choices
Tool overwhelm: Students get lost in tool features
Solution: Focus on concepts first, tools second. Emphasize that tools change, principles don't.
MBSE skepticism: "Why not just use documents? We've always done it that way.
Solution: Use concrete data on error reduction, time savings. Acknowledge transition pain.
SysML complexity: SysML seems abstract and complex
Solution: Use simple, relatable automotive examples. Show one complete SysML example end-to-end.
Confusion on when to use MBSE: "Should I always use MBSE?
Solution: Emphasize decision framework (Slide 24). No universal answer.
MBSE Benefits and Challenges (Slides 14-17): Critical section - allocate full 20 minutes
Students need honest assessment of both pros and cons
Tools section (Slides 18-21): Can compress to 12 minutes if time tight
Focus on SysML and Simulink; skim toolchain integration
Digital Twins (Slides 22-23): Don't skip - this is highly engaging and future-looking
Decision Framework (Slide 24): Essential - give students practical takeaway
Slide 3: Ask students: "How would YOU manage 3,000 requirements in Word documents?
Slide 9: Pair discussion: "What's the biggest pain point with document-based work in your experience?
Slide 15: Reality check: "Raise your hand if you'd be excited to learn a new modeling language" (acknowledge resistance)
Slide 24: Interactive exercise: "Given this system [describe one], traditional or MBSE? Why?
Slide 30: Open discussion on MBSE adoption challenges in their organizations
5-minute SysML demo: Create a simple block definition diagram for automotive system
5-minute Simulink demo: Show control system simulation
Tool comparison: Show same requirement captured in Word vs in MBSE tool
Traceability query: Show automatic impact analysis in MBSE tool vs manual search in documents
SysML specification or cheat sheet (1-page diagram type overview)
List of MBSE tools with comparison matrix
Case studies: Organizations that adopted MBSE (NASA, Lockheed Martin, automotive OEMs)
Digital twin architecture examples
Quick check (Slide 12): Can students articulate the 4 core MBSE principles?
Application (Slide 19): Given a system, which SysML diagrams would you create?
Evaluation (Slide 24): Given system characteristics, should you use traditional or MBSE?
Assignment: Compare traditional vs MBSE for a chosen system (tests synthesis)
SysML v2 (next-generation SysML language)
OSLC (Open Services for Lifecycle Collaboration) for tool integration
Formal verification methods for models
Model-based requirements engineering (Cameo Requirements, Simulink Requirements)

## Slide 34: ✅ Session Success Criteria
Students leave able to:
✓ Explain the fundamental difference between document-centric and model-centric SE
✓ Articulate 4 core MBSE principles (single source of truth, formalized semantics, automated traceability, model continuity)
✓ Name key MBSE tools and their purposes (SysML for architecture, Simulink for behavior)
✓ Describe what a digital twin is and give 2 automotive applications
✓ Apply decision framework to choose traditional vs MBSE for a given system
✓ List 3 benefits and 3 challenges of MBSE adoption
✓ Understand that MBSE implements the same SE principles (ISO/IEC 15288, V-Model) but with different artifacts
Critical outcome: Students understand that traditional and model-based SE are alternative implementations of the same fundamental systems engineering framework. They can make informed decisions about which approach to use based on system characteristics and organizational context.

## Slide 35: 📚 Instructor Preparation Checklist
Before class: — [ ] Review SysML specification and prepare simple diagrams
[ ] Prepare Simulink example (ABS or cruise control)
[ ] Research latest MBSE adoption statistics for automotive industry
[ ] Identify digital twin case studies (Tesla, BMW, Waymo)
[ ] Prepare tool comparison matrix
[ ] Test any tool demonstrations in classroom environment
[ ] Review INCOSE MBSE resources
Materials to provide: — [ ] SysML diagram types cheat sheet (1-page reference)
[ ] MBSE tool comparison matrix
[ ] Case study: Successful MBSE adoption (e.g., JPL, Lockheed Martin)
[ ] Reading: "Introduction to SysML" article
[ ] Assignment handout with rubric
[ ] List of open-source MBSE tools for student exploration (Papyrus, Modelio)
Optional materials: — [ ] Trial access to MBSE tool (Cameo, Rhapsody) if available through university
[ ] Video: MBSE tool demonstration (if live demo not possible)
[ ] Industry practitioner guest speaker (if available)
Post-class: — [ ] Share slides via eLearn
[ ] Post assignment with detailed rubric
[ ] Post discussion forum: "Traditional vs MBSE in your context
[ ] Share tool exploration resources (tutorials, trial versions)
[ ] Prepare Session 4 connection: Requirements in both traditional and MBSE contexts

## Slide 36: 🔗 Connections to Other Sessions
Builds on: — Session 1: Motivation (failures) → Need for better implementation
Session 2: Framework (ISO/IEC 15288, V-Model) → How to implement the framework
Leads to: — Session 4: Requirements Engineering → How to capture requirements in both traditional and MBSE approaches
Session 5: System Design and Architecture → SysML architecture modeling in depth
Session 7: Operational and Functional Analysis → Behavioral modeling with activity diagrams, sequence diagrams
Session 8: Integration, V&V → Model-based testing, simulation-based verification
Session 16: Emerging Trends → Advanced MBSE, digital engineering, AI in SE
Key concept thread: — Session 1: WHY systems engineering?
Session 2: WHAT is systems engineering?
Session 3: HOW do we practice it (implementation methods)?
Session 4: Requirements — first detailed application
Sessions 5-8: Execution — working through the V-Model
Sessions 9-16: Management and specialization
MBSE integration throughout course:
From this point forward, instructors should reference both traditional and MBSE approaches when teaching technical processes:
Requirements management (Session 4): Word documents vs. SysML requirement diagrams
Architecture (Session 5): Architecture documents vs. SysML block diagrams
Behavioral analysis (Session 7): Functional specs vs. SysML activity/sequence diagrams
V&V (Session 8): Manual test procedures vs. model-based test generation

## Slide 37: 🌟 Additional Teaching Tips
Future-Proofing:
Students often struggle with abstract MBSE concepts. Use these techniques:
1. Start with familiar system: — Use a simple system everyone knows (bicycle brake, door lock, coffee maker)
Show how to model it in SysML
Then scale to automotive complexity
2. Side-by-side comparison: — Same requirement expressed in Word document
Same requirement as SysML requirement element
Show the difference in traceability, impact analysis
3. Tell the human story: — Interview with systems engineer who transitioned to MBSE
"Day in the life" comparison: document-based vs. model-based engineer
Change impact scenario: "Requirement changed, now what?" in both paradigms
Some students (especially experienced engineers) resist MBSE:
Acknowledge concerns: — "I hear you - learning new tools is frustrating
"You're right that documents work for many systems
"The transition is painful; organizations underestimate it
Provide choice: — "Use the decision framework - not every system needs MBSE
"Hybrid approaches are valid and common
"Your job is to choose the right tool for the job
Show data: — Industry adoption curves
Error reduction statistics
Time savings data
ROI case studies
Constantly reinforce that MBSE is an implementation, not a replacement:
ISO/IEC 15288 technical processes: Same in both approaches
Traditional: Captured in documents
MBSE: Captured in models
V-Model: Works with both approaches
Traditional: Requirements doc → Design doc → Test doc
MBSE: Requirements model → Design model → Test model
Better traceability in MBSE via automatic relationships
Prepare students for evolving landscape:
Tools will change (SysML v2 is coming)
Concepts remain stable (systems thinking, traceability, V-Model)
Emphasize learning to learn
Point to resources for staying current (INCOSE conferences, webinars, journals)

## Slide 38
End of Framework
Next Session: Session 4 - Requirements Engineering (Deep dive into requirements definition, attributes, management, and traceability in both traditional and MBSE contexts)