## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 4: Requirements Engineering'

## Slide 2: Requirements Engineering
Session 4 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 4. Today we tackle what many consider the MOST critical process in systems engineering: Requirements Engineering.
Get requirements wrong, and everything that follows is built on a faulty foundation. Get them right, and you've set yourself up for success.

## Slide 4: Connection to Previous Sessions
Let's connect the journey we've been on:
Session 1: We learned WHY systems engineering matters through failure cases. Poor requirements were at the root of many disasters.
Session 2: We learned the SE framework - ISO/IEC 15288 technical processes. The FIRST technical process? Stakeholder needs and requirements definition.
Session 3: We explored Traditional vs MBSE approaches. Both start with the same thing: defining requirements.
Today's focus: How do we actually DO requirements engineering in practice?

## Slide 5: Why Requirements Engineering Is Critical
Let me show you some sobering data from the Standish Group's CHAOS Report:
Top causes of project failure: — 37% - Incomplete requirements
28% - Lack of user involvement (stakeholder engagement)
19% - Lack of resources
16% - Unrealistic expectations (poor requirements management)
Over 65% of failures trace back to requirements issues.
In automotive systems: — Average cost to fix a requirements defect found in design: $1,000
Average cost if found in testing: $10,000
Average cost if found after production: $100,000+
Recalls due to requirements failures: Millions of dollars
This is why we spend today mastering this discipline.

## Slide 6: Real-World Example - The Mars Climate Orbiter
Remember this from Session 1? The $327 million Mars Climate Orbiter lost because one team used metric units, another used imperial.
Requirements failure analysis: — Root cause: Interface requirement didn't specify units
What was missing: 'The navigation software shall output thrust values in Newtons (N)'
What was assumed: Teams made different assumptions
A single missing word - the UNIT of measurement - destroyed the mission.
This is the power and precision requirements engineering demands.

## Slide 7: A Deceptively Simple Task
Let me give you a challenge. Your manager says:
'Design a cruise control system for our new vehicle.'
Sounds simple, right? Let me show you what happens when you skip requirements engineering.
Scenario 1 - Engineering student approach:
'Okay, cruise control maintains constant speed. I'll write code that keeps throttle position constant.'
Result: Vehicle slows down on hills, speeds up downhill. FAILED.
Scenario 2 - Better attempt:
'Cruise control maintains speed using feedback control. I'll adjust throttle based on speed sensor.'
Result: Works on flat roads. But what about:
Driver hits brake? (Should cruise disengage)
Steep downhill? (Should engine brake be used?)
Speed limit changes? (Should there be limits?)
Sudden obstacle? (How does it interact with collision avoidance?)
Clutch pressed? (Manual transmission considerations)
Suddenly, 'simple' cruise control has dozens of requirements across multiple systems.

## Slide 8: Who Are the Stakeholders?
First principle: A system serves stakeholders. We must know who they are and what they need.
For our cruise control system, who are the stakeholders?
[Pause - let students think]
Here's the complete list:
Primary Stakeholders: — Drivers: Want convenient speed control, ease of use, safety
Vehicle OEM: Wants reliability, cost-effectiveness, regulatory compliance
Safety engineers: Want fail-safe operation, no unintended acceleration
Secondary Stakeholders: — Service technicians: Want diagnosability, easy calibration
Regulators: Want compliance with FMVSS, ISO 26262 (functional safety)
Other ECU teams: Integration with powertrain, brakes, ADAS
Testing team: Want verifiable, testable requirements
Marketing: Want competitive features (adaptive cruise, traffic assist)
Tertiary Stakeholders: — Insurance companies: Want proven safety record
Fleet operators: Want fuel efficiency data
End-of-life recyclers: Want material identification
Notice: It's not just 'the customer.' Each group has DIFFERENT needs.

## Slide 9: Stakeholder Analysis Matrix
We analyze stakeholders systematically using this matrix:
| Stakeholder | Interest | Influence | Priority | Engagement Strategy |
|-------------|----------|-----------|----------|---------------------|
| Driver | High | Medium | Critical | User studies, focus groups |
| Safety Engineer | High | High | Critical | Requirements reviews, FMEA |
| Regulator | Medium | High | High | Standards compliance verification |
| Service Tech | Medium | Low | Medium | Service manual, diagnostics |
Interest: How much does the system affect them?
Influence: How much power do they have over the system?
Priority: How important are they to success?
Engagement: How do we gather their input?
Automotive example - Real case:
Tesla initially ignored service technician stakeholders when designing Model S battery packs. Result: Battery replacement required lifting entire vehicle, 6+ hour procedure. Later redesigned after technician feedback.
Lesson: Identify ALL stakeholders early.

## Slide 10: Eliciting Stakeholder Needs
How do we extract what stakeholders actually need? Six proven techniques:
1. Interviews (One-on-one or small groups)
Best for: Deep understanding, clarification
Example: Interview experienced drivers about cruise control usage patterns
2. Surveys (Questionnaires)
Best for: Quantitative data from many stakeholders
Example: 'How often do you use cruise control?' (Daily/Weekly/Rarely/Never)
3. Observation (Watch users in context)
Best for: Understanding actual behavior vs stated preferences
Example: Observe drivers on highway to see when they engage/disengage cruise
4. Workshops (Facilitated group sessions)
Best for: Resolving conflicts, building consensus
Example: Joint session with powertrain, brakes, and safety teams to define interfaces
5. Prototyping (Show early concepts)
Best for: Getting concrete feedback
Example: Simulator with cruise control to test driver reactions
6. Document Analysis (Review existing systems, standards)
Best for: Baseline requirements, regulatory compliance
Example: Analyze FMVSS 126 (Electronic Stability Control) for related requirements
Best practice: Use MULTIPLE techniques. Different stakeholders respond to different approaches.

## Slide 11: From Stakeholder Needs to Requirements
Stakeholders express NEEDS in their language. We must transform these into REQUIREMENTS.
Example transformation:
Driver need (in their words):
'I want cruise control that doesn't freak out when I'm going downhill and makes me speed.'
Translation process: — Implied need: System should not allow speed to exceed set speed significantly
Technical requirement: 'The cruise control system shall maintain vehicle speed within ±3 km/h of the set speed under grade conditions from -10% to +10%.'
Another example:
Safety engineer need:
'The system must be safe even if sensors fail.'
Requirements (multiple): — REQ-CC-001: 'The system shall detect wheel speed sensor failures within 100ms.'
REQ-CC-002: 'Upon detection of sensor failure, the system shall transition to fail-safe state (cruise disabled) within 200ms.'
REQ-CC-003: 'The system shall alert the driver of cruise control unavailability via dashboard indicator.'
Key insight: One stakeholder need often generates MULTIPLE technical requirements.
This translation is the art and science of requirements engineering.

## Slide 12
#### Part 2: Needs vs Requirements - The Critical Distinction (Slides 12-14, ~8 minutes)

## Slide 13: Understanding the Difference
This is foundational: Needs and requirements are NOT the same thing.
NEEDS: — Stakeholder desires and goals
Expressed in stakeholder language
Often vague, subjective, negotiable
Answer: 'What problem are we solving?'
Example: 'I need a comfortable driving experience on long trips'
REQUIREMENTS: — Specific, measurable system capabilities
Expressed in engineering language
Precise, objective, verifiable
Answer: 'What must the system do?'
Example: 'The cruise control system shall maintain speed with maximum throttle variation of ±5% when operating on grades ≤8%'
The V-Model connection (from Session 2):
Left side top: Stakeholder NEEDS → System REQUIREMENTS
Right side top: Validation tests verify we met NEEDS
Right side lower: Verification tests verify we met REQUIREMENTS
Needs define SUCCESS. Requirements define IMPLEMENTATION.

## Slide 14: The Requirements Hierarchy
Requirements exist at multiple levels. Understanding this hierarchy is critical:
Level 1 - Stakeholder Requirements (SR) — High-level capabilities from stakeholder perspective
Example: 'SR-001: The vehicle shall provide driver-assisted speed control on highways'
Level 2 - System Requirements (SysR) — System-level functional and performance requirements
Example: 'SysR-CC-015: The cruise control system shall maintain set speed within ±2 km/h in steady-state conditions'
Level 3 - Subsystem Requirements (SSR) — Allocated to specific subsystems/components
Example: 'SSR-CC-ECU-042: The cruise control ECU shall read wheel speed sensor data at minimum 50 Hz'
Level 4 - Component Requirements (CR) — Detailed design requirements for components
Example: 'CR-CC-SW-128: The speed calculation algorithm shall use floating-point arithmetic with minimum 32-bit precision'
Traceability flows DOWN (allocation): SR → SysR → SSR → CR
Verification flows UP: Component test → Subsystem test → System test → Validation
This is the left side of the V-Model in practice.

## Slide 15: Automotive Industry Standard - Requirements Layers
In automotive, we follow additional structure from ISO 26262 (Functional Safety):
Customer Requirements (Market)
↓
Vehicle Level Requirements (Vehicle attributes)
↓
System Requirements (e.g., Cruise Control System)
↓
Hardware/Software Requirements (ECU, sensors, actuators)
↓
Component Requirements (Microcontroller, algorithms)
Real example - Adaptive Cruise Control (ACC): — Customer: 'I want hands-free highway driving'
Vehicle: 'Vehicle shall provide Level 2 autonomous capability per SAE J3016'
System: 'ACC system shall maintain time gap of 1.0-2.5 seconds to lead vehicle'
HW/SW: 'Radar sensor shall detect vehicles up to 150m with ±0.5m range accuracy'
Component: 'Radar processing FPGA shall execute object tracking algorithm at 20 Hz'
Each level adds specificity and enables different teams to work in parallel.

## Slide 16
#### Part 3: Types of Requirements (Slides 15-18, ~12 minutes)

## Slide 17: The Three Categories
All requirements fall into three categories. Master these and you'll capture complete system behavior.
1. Functional Requirements (FR) — WHAT the system shall do
Describes behavior, inputs, outputs, operations
Example: 'The system shall activate cruise control when driver presses SET button'
2. Non-Functional Requirements (NFR) — HOW WELL the system shall perform
Quality attributes, performance, reliability, usability
Example: 'The system shall respond to SET button within 200ms'
3. Constraints (CON) — Design restrictions and boundaries
Technology, standards, regulations, interfaces
Example: 'The system shall comply with ISO 26262 ASIL-B requirements'
Common mistake: Forgetting non-functional requirements. A system that does everything functionally but is too slow, unreliable, or unusable is still a failure.
Let me show you detailed examples from automotive cruise control.

## Slide 18: Functional Requirements Examples
Functional Requirements define system behavior. Here are real examples:
Basic Control Functions: — FR-CC-001: 'The system shall engage cruise control when driver presses SET button while vehicle speed is between 30-180 km/h'
FR-CC-002: 'The system shall set target speed to current vehicle speed when SET button is pressed'
FR-CC-003: 'The system shall increase target speed by 1 km/h for each RES+ button press'
FR-CC-004: 'The system shall decrease target speed by 1 km/h for each SET- button press'
Deactivation Functions: — FR-CC-010: 'The system shall disengage cruise control when driver presses CANCEL button'
FR-CC-011: 'The system shall disengage cruise control when brake pedal is depressed >10%'
FR-CC-012: 'The system shall disengage cruise control when clutch pedal is depressed (manual transmission)'
Speed Maintenance: — FR-CC-020: 'The system shall modulate throttle position to maintain target speed'
FR-CC-021: 'The system shall request engine torque reduction when speed exceeds target by >5 km/h on descents'
Notice the structure: Each requirement specifies a clear input condition and system response. No ambiguity.

## Slide 19: Non-Functional Requirements Examples
Non-Functional Requirements define quality attributes. These are often forgotten but equally critical.
Performance: — NFR-CC-001: 'The system shall achieve steady-state speed accuracy within ±2 km/h within 5 seconds of engagement'
NFR-CC-002: 'The control loop shall execute at minimum 20 Hz update rate'
Reliability: — NFR-CC-010: 'The system shall achieve ASIL-B rating per ISO 26262'
NFR-CC-011: 'The system shall have failure rate <10 FIT (Failures In Time per billion hours)'
Usability: — NFR-CC-020: 'Driver shall be able to engage cruise control with single button press (no menu navigation)'
NFR-CC-021: 'System status shall be visible on instrument cluster within driver's primary field of view'
Maintainability: — NFR-CC-030: 'The system shall log fault codes per SAE J1979 OBD-II standard'
NFR-CC-031: 'Calibration parameters shall be modifiable via diagnostic tool without ECU replacement'
Safety: — NFR-CC-040: 'The system shall transition to safe state within 200ms upon detection of critical sensor failure'
Environmental: — NFR-CC-050: 'The ECU shall operate in temperature range -40°C to +85°C'
These are often harder to specify but critical to user satisfaction and system success.

## Slide 20: Constraints Examples
Constraints limit design freedom. They come from regulations, standards, existing architecture, and business decisions.
Regulatory Constraints: — CON-CC-001: 'The system shall comply with FMVSS 126 (Electronic Stability Control)'
CON-CC-002: 'The system shall meet Euro NCAP 5-star safety assessment requirements'
Standards Constraints: — CON-CC-010: 'The system shall implement ISO 26262 safety life cycle processes'
CON-CC-011: 'Communication shall use CAN 2.0B protocol per ISO 11898'
Interface Constraints: — CON-CC-020: 'The system shall interface with existing vehicle CAN bus (500 kbps)'
CON-CC-021: 'The system shall use existing steering wheel switch inputs (resistive ladder, 0-5V)'
Technology Constraints: — CON-CC-030: 'The ECU shall use existing platform microcontroller (Infineon AURIX TC39x)'
CON-CC-031: 'Software shall be written in MISRA C:2012 compliant code'
Business Constraints: — CON-CC-040: 'ECU unit cost shall not exceed $45 at 100k volume'
CON-CC-041: 'Development shall reuse existing powertrain control algorithms (≥70% reuse)'
Constraints often drive architecture decisions. You design AROUND constraints; you design TO requirements.

## Slide 21
#### Part 4: Requirements Attributes - What Makes a Good Requirement? (Slides 19-21, ~10 minutes)

## Slide 22: The Quality Framework
A requirement can be technically correct but still be useless. Why? Because it lacks critical quality attributes.
A GOOD requirement is:
Clear — Unambiguous, single interpretation
Concise — Succinct, no unnecessary words
Verifiable — Can be tested/proven
Feasible — Technically and economically achievable
Traceable — Linked to source (needs) and destination (tests)
Necessary — Actually needed (not nice-to-have masquerading as requirement)
Complete — Includes all needed information
Consistent — Doesn't contradict other requirements
Unambiguous — Only ONE possible interpretation
Let me show you good vs bad examples for each attribute.

## Slide 23: Good vs Bad Requirements Examples
Let's analyze requirements through these quality attributes:
BAD: Ambiguous
❌ 'The cruise control system shall be fast'
What is 'fast'? Response time? Processing speed? Acceleration?
GOOD: Clear and Verifiable
✓ 'The cruise control system shall engage within 500ms of SET button press'
Specific metric, testable, no ambiguity

## Slide 24
BAD: Not Verifiable
❌ 'The system shall be user-friendly'
How do you test 'user-friendly'? Subjective.
GOOD: Verifiable
✓ 'The system shall enable driver to set target speed with maximum 3 button presses'
Countable actions, testable, objective

## Slide 25
BAD: Contains Design (Should Be Requirement)
❌ 'The system shall use PID controller with Kp=0.5, Ki=0.1, Kd=0.05 to maintain speed'
This is design solution, not requirement
GOOD: Design-Free
✓ 'The system shall maintain speed within ±2 km/h with settling time ≤5 seconds'
Specifies WHAT, not HOW. Allows engineers to choose best controller.

## Slide 26
BAD: Incomplete
❌ 'The system shall disengage when driver brakes'
Missing: How much brake pressure? What's the timing?
GOOD: Complete
✓ 'The system shall disengage cruise control within 100ms when brake pedal is depressed >10% of travel'
Includes threshold and timing

## Slide 27
BAD: Multiple Requirements
❌ 'The system shall maintain speed and disengage on brake press and display status'
Three requirements in one (violates 'atomic' principle)
GOOD: Atomic (Single Requirement)
✓ Split into three:
'The system shall maintain target speed within ±2 km/h'
'The system shall disengage when brake pedal is depressed >10%'
'The system shall display engagement status on instrument cluster'
Each can be verified independently.

## Slide 28: Requirements Writing Best Practices
Professional requirements follow standard structure. Here's the template:
Standard Structure:
'[System] shall [action] [object] [qualifier] [condition]'
Examples: — 'The cruise control system shall maintain vehicle speed within ±2 km/h when operating on grades ≤8%'
System: cruise control system
Action: maintain
Object: vehicle speed
Qualifier: within ±2 km/h
Condition: when operating on grades ≤8%
Key writing rules:
Use 'shall' for requirements — 'shall' = mandatory requirement
'should' = guidance/goal (not a requirement)
'will' = statement of fact
'may' = permission/option
Avoid weak words: 'adequate', 'sufficient', 'good', 'user-friendly', 'fast', 'reliable'
Replace with specific, measurable criteria
Be specific about conditions: Don't say 'when appropriate' or 'as needed'
Specify exact conditions: 'when vehicle speed exceeds 30 km/h'
Quantify everything possible:
Not: 'quickly' → 'within 500ms'
Not: 'accurately' → 'with ±2% error'
Not: 'most of the time' → '99.9% of operational time'
One requirement per statement (atomic)
If you can split it with 'and', it's probably multiple requirements
Automotive standard reference: Many companies use IEEE 29148 (Requirements Engineering) or EARS (Easy Approach to Requirements Syntax).

## Slide 29
#### Part 5: Requirements Traceability (Slides 22-23, ~8 minutes)

## Slide 30: Why Traceability Matters
Traceability is the ability to follow a requirement through the entire life cycle.
Why it's critical:
Impact Analysis: If a stakeholder need changes, what requirements are affected? What components? What tests?
Verification Coverage: Are all requirements tested? Are there orphan tests (tests with no requirement)?
Regulatory Compliance: ISO 26262, ASPICE, DO-178C all REQUIRE traceability
Change Management: Understanding ripple effects of changes
Project Visibility: What's implemented? What's tested? What's validated?
Traceability links:
Forward traceability (downstream):
Stakeholder Need → System Requirement → Subsystem Requirement → Design Element → Code Module → Test Case
Backward traceability (upstream):
Test Result → Test Case → Requirement → Stakeholder Need
Bi-directional traceability: Ability to navigate both directions
Let me show you how we implement this.

## Slide 31: Requirements Traceability Matrix (RTM)
The primary tool is the Requirements Traceability Matrix (RTM).
Example RTM for Cruise Control:
| Stakeholder Need | System Req | Subsystem Req | Design | Implementation | Test Case | Status |
|------------------|------------|---------------|--------|----------------|-----------|--------|
| SN-001: Driver wants hands-free highway speed control | SR-CC-001 | SSR-CC-ECU-010, SSR-CC-SW-005 | DD-CC-SpeedControl | SW-Module-CC-001 | TC-CC-045 | Verified |
| SN-002: System must be safe even with sensor failures | SR-CC-020 | SSR-CC-ECU-025, SSR-CC-Diag-003 | DD-CC-FailSafe | SW-Module-CC-FailSafe | TC-CC-078, TC-CC-079 | Verified |
What this shows: — Every stakeholder need maps to one or more system requirements
System requirements decompose to subsystem requirements
Design elements implement requirements
Test cases verify requirements
Status tracking: Not Started / In Progress / Implemented / Verified / Validated
Red flags the RTM catches: — Orphan requirements: Requirement with no test case (Can't verify!)
Orphan tests: Test with no requirement (Testing what?)
Uncovered needs: Stakeholder need with no requirements (Gap!)
Unimplemented requirements: Requirement with no design element (Missed!)
Tool support: IBM DOORS, Jama, PTC Integrity, Siemens Polarion, or even Excel for small projects.
Automotive reality: On a complete vehicle program, RTMs have 10,000+ rows. Tool support is essential.

## Slide 32
#### Part 6: Requirements Management Tools and Processes (Slides 24, ~4 minutes)

## Slide 33: The Seven Deadly Sins of Requirements
Let me show you the most common requirements engineering failures. Learn to recognize these anti-patterns.
Sin #1: Ambiguity
❌ Example: 'The system shall provide adequate performance'
What's 'adequate'? Different stakeholders have different interpretations
Fix: 'The system shall accelerate from 50-100 km/h in ≤8 seconds'
Sin #2: Gold Plating (Unnecessary Features)
❌ Example: 'The cruise control shall display average fuel economy'
Nice feature, but is it NEEDED for cruise control? (Instrument cluster does this)
Impact: Adds cost, complexity, testing burden
Fix: Challenge every requirement - trace to stakeholder need
Sin #3: Scope Creep — Requirements continuously added without formal change process
Example: Mid-development: 'Oh, let's also add traffic sign recognition'
Impact: Schedule delays, budget overruns, quality issues
Fix: Formal change control board, impact analysis before accepting changes
Sin #4: Implementation Bias
❌ Example: 'The system shall use a Kalman filter to estimate vehicle speed'
This specifies HOW (Kalman filter) not WHAT (accurate speed estimation)
Fix: 'The system shall estimate vehicle speed with ±1 km/h accuracy'
Let designers choose the best algorithm (might be Kalman, might not)
Sin #5: Missing Non-Functionals — Specifying all functional behavior but forgetting performance, safety, reliability
Example: Having 100 functional requirements but zero reliability requirements
Impact: System works but is unusable (too slow, unreliable, unsafe)
Fix: Systematically review NFR categories (performance, reliability, safety, usability, maintainability, security)
Sin #6: Inconsistency
❌ Example:
REQ-001: 'System shall operate in -20°C to +70°C'
REQ-045: 'Display shall use LCD screen' (LCDs typically fail below -10°C)
Fix: Requirements review, consistency checking (tools help)
Sin #7: Weak Traceability — Can't answer: 'Which test verifies REQ-CC-042?'
Can't answer: 'If we change this need, what's impacted?'
Impact: Requirements not verified, changes cause unintended consequences
Fix: Maintain RTM religiously, use tools
Every project I've seen fail had at least 3 of these sins.

## Slide 34: Real Automotive Example - Unintended Acceleration
Let's apply what we've learned to a real disaster: Toyota unintended acceleration (2009-2011).
Background:
89 deaths, millions of vehicles recalled
$1.2B settlement
Root cause: Software failures in Electronic Throttle Control System (ETCS)
Requirements Engineering Failures:
1. Incomplete Safety Requirements — Missing requirement: 'System shall prevent simultaneous conflicting commands (accelerator + brake)'
Missing requirement: 'System shall default to brake priority in conflict scenarios'
2. Inadequate Failure Mode Requirements — Didn't specify behavior for all sensor failure combinations
Didn't require testing of bit-flip errors in memory
3. Poor Traceability — NASA analysis found: Many safety requirements were NOT traced to test cases
Orphan code: Functions that weren't tied to any requirement
4. Ambiguous Requirements — Example found in investigation: 'Throttle shall respond appropriately to pedal input'
What's 'appropriately'? Different interpretations led to unsafe behavior
5. Missing Non-Functional Requirements — No requirement for maximum task blocking time in RTOS
No requirement for stack overflow detection
Result: Software tasks could block critical safety functions
What proper requirements engineering would have prevented:
Functional Requirements (missing): — FR-ETCS-SAFE-001: 'If brake pedal is depressed >20% while accelerator is >50%, system shall reduce throttle to idle within 100ms'
Non-Functional Requirements (missing): — NFR-ETCS-SAFE-010: 'Maximum task blocking time shall not exceed 10ms'
NFR-ETCS-SAFE-011: 'System shall detect and respond to stack overflow within one task cycle'
Constraints (missing): — CON-ETCS-SAFE-020: 'Software shall comply with MISRA C safety guidelines'
Lessons learned: — Safety requirements need extra rigor
Traceability to tests is non-negotiable
Non-functional requirements are NOT optional
External review of requirements catches gaps
This cost 89 lives and $1.2B. Requirements engineering is not bureaucracy - it's life-saving discipline.

## Slide 35: Key Takeaways
Let's consolidate what you've learned today:
1. Stakeholder-Driven Process — Systems serve stakeholders - identify them ALL
Elicit needs systematically (interviews, observation, workshops)
Transform needs into requirements
2. Needs ≠ Requirements — Needs: Stakeholder desires (why)
Requirements: System capabilities (what)
Design: Implementation solution (how)
3. Three Requirement Types — Functional: What system does
Non-functional: How well it performs
Constraints: Design limitations
4. Quality Attributes — Clear, concise, verifiable, traceable, complete, consistent
Use 'shall' structure with quantification
Avoid ambiguity and design bias
5. Traceability is Essential — Needs → Requirements → Design → Implementation → Tests
Use RTM and tools (DOORS, Jama, etc.)
Ensures nothing falls through cracks
6. Common Pitfalls to Avoid — Ambiguity, gold plating, scope creep, implementation bias
Missing non-functionals, inconsistency, weak traceability
Remember: Poor requirements are the #1 cause of project failure. Master this, and you're already ahead of most engineers.

## Slide 36: Connection to V-Model and Next Sessions
Let's place today's learning in the bigger systems engineering context.
Today (Session 4): We're at the TOP LEFT of the V-Model
Stakeholder needs and requirements definition
This is the FOUNDATION of everything else
What comes next:
Session 5 - System Design and Architecture:
How do we transform requirements into architecture?
How do we allocate requirements to subsystems?
How do we define interfaces?
Moving down the left side of the V
Session 7 - Operational and Functional Analysis:
How do we analyze operational scenarios?
How do we allocate requirements to functions?
Functional flow block diagrams
Session 8 - Integration, Verification & Validation:
Right side of the V-Model
How do we verify requirements? (Did we build it right?)
How do we validate against needs? (Did we build the right thing?)
Requirements traceability to tests
The thread: — Session 4: Define requirements
Session 5: Architect the solution
Session 7: Analyze functions and operations
Session 8: Verify requirements are met
Key connection: The requirements you write today MUST be verifiable in Session 8. Always write requirements with testing in mind.
In Session 3, we learned MBSE. In MBSE tools (SysML), requirements are embedded directly in models, enabling automatic traceability and consistency checking. Same principles, different representation.

## Slide 37: 📊 PPT DESIGN GUIDANCE
Real Examples to Include:
Practical Exercise (Due before Session 5):
You are the systems engineer for an Automatic Emergency Braking (AEB) system for a passenger vehicle.
Part 1: Stakeholder Analysis (30%)
Identify at least 6 stakeholder groups
Create stakeholder analysis matrix (Interest, Influence, Priority, Engagement Strategy)
List 2-3 needs per stakeholder
Part 2: Requirements Development (50%)
Write at least 15 system-level requirements:
Minimum 8 functional requirements
Minimum 4 non-functional requirements (including performance, safety, usability)
Minimum 3 constraints (regulatory, interface, technology)
Each requirement must:
Follow 'shall' structure
Be clear, verifiable, and complete
Include unique identifier (REQ-AEB-XXX)
Be traceable to a stakeholder need
Part 3: Traceability Matrix (20%)
Create RTM mapping stakeholder needs → requirements
Identify at least one test approach for each requirement
Grading Criteria: — Completeness of stakeholder identification
Quality of requirements (clear, verifiable, unambiguous)
Proper categorization (FR/NFR/CON)
Traceability
Professional formatting
Submission: 1-page stakeholder analysis + 2-page requirements list + 1-page RTM (4 pages total)
Tips: — Research real AEB systems (Euro NCAP requirements, SAE standards)
Think about failure modes and safety
Consider regulatory requirements (UN R152, FMVSS)
Don't specify implementation (no 'use radar' - instead specify detection requirements)
Discussion Questions: — How would requirements differ for AEB in a passenger car vs a heavy truck?
What are the ethical requirements for AEB? (e.g., prioritizing pedestrians vs occupants)
How do you handle conflicting stakeholder needs?
30 minutes for your questions. —--
Professional engineering aesthetic: Clean, technical, data-driven
Color coding:
Blue for Functional Requirements
Green for Non-Functional Requirements
Orange for Constraints
Red for anti-patterns and warnings
Use real automotive examples: Photos of actual cruise control systems, driver interfaces
Diagrams: Professional process flows, RTM tables, stakeholder networks
Slide 3 (Why Requirements Engineering Is Critical) - Statistics that grab attention
Slide 11 (Needs → Requirements transformation) - Core concept
Slide 15 (Three requirement types) - Fundamental categorization
Slide 20 (Good vs Bad requirements) - Practical examples students will reference
Slide 23 (RTM) - Industry-standard tool
Slide 26 (Toyota case study) - Real-world consequences
Slide 28 (Summary) - Students will photograph this
Slide 7: Animate system context diagram connections appearing one by one
Slide 11: Animate transformation from need → requirement with visual flow
Slide 13: Build requirements hierarchy pyramid from bottom to top
Slide 23: Highlight RTM traceability links with animated arrows
Slide 26: Timeline animation showing Toyota unintended acceleration investigation
Slide 9: Stakeholder analysis matrix (use real cruise control example)
Slide 20: Good vs bad requirements comparison table
Slide 23: Full RTM example (6-8 rows minimum for clarity)
Slide 24: Tool comparison matrix with features
Use actual automotive requirements from public sources (SAE standards, Euro NCAP, FMVSS)
Screenshots of DOORS or Jama (if licensing permits, otherwise mockups)
Real cruise control system diagrams from service manuals
Actual requirements statements from ISO 26262 examples

## Slide 38: 🎯 INSTRUCTOR NOTES
Assessment Opportunities:
Start concrete (cruise control), expand abstract (principles), return concrete (exercise) — Use real failure case (Toyota) to drive home consequences — Emphasize practical skills: Students should be able to write requirements after today
Industry-standard terminology: Use same terms as INCOSE, IEEE, ISO
Tool exposure: Show actual tools, not just theory
Challenge 1: "Why can't we just say 'make it work well'?"
How to address: Show Slide 4 (Mars Climate Orbiter) - ambiguity costs $327M. Show Slide 20 - translate vague statement to verifiable requirement. Emphasize: If you can't test it, it's not a requirement.
Challenge 2: "Non-functional requirements seem less important than functional"
How to address: Use examples: A car that drives (functional) but catches fire (reliability NFR failure) is useless. A system that works but takes 5 minutes to respond (performance NFR failure) won't be used. NFRs define QUALITY.
Challenge 3: "This seems like a lot of bureaucracy"
How to address: Show Slide 3 statistics - 65% of projects fail due to requirements issues. Show Slide 26 - Toyota's $1.2B lesson. Ask: "Is traceability bureaucracy or insurance?" Frame requirements engineering as RISK REDUCTION.
Challenge 4: "How do I know when I have enough requirements?"
How to address: Coverage criteria:
Every stakeholder need has ≥1 requirement
Every operational scenario is covered
All interfaces defined
All failure modes addressed
All regulatory requirements mapped
Every requirement is verifiable
Use reviews and checklists (Slide 27)
Challenge 5: "What if stakeholders want contradictory things?"
How to address: This is NORMAL. Systems engineering is about trade-offs. Example: Marketing wants 200 km/h top speed, Safety wants governor at 180 km/h. Solution: Negotiate, analyze risk, escalate to decision authority. Document rationale. This leads to Session 10 (Decision Management).
If running short: — Condense Slide 10 (elicitation techniques) - brief overview, details in reading
Reduce Slide 24 (tools) to 2-3 tools only
Move some good/bad examples from Slide 20 to backup slides
If running long: — Extend Slide 26 (Toyota case) with more forensic details
Add interactive exercise: Give students a vague requirement, have them improve it
Show live demo of DOORS or Jama tool
Core content (must cover - non-negotiable): — Slides 8-11 (stakeholders and needs)
Slides 12-14 (needs vs requirements)
Slides 15-18 (requirement types)
Slides 19-21 (quality attributes and writing)
Slides 22-23 (traceability and RTM)
Slide 26 (Toyota case study)
Slide 28 (summary)
Slide 6: Interactive - pause after showing cruise control challenge. Ask: "What could go wrong if we don't specify requirements?" Let students call out scenarios.
Slide 11: Work through transformation together - show a raw stakeholder quote, have students help translate to requirement.
Slide 20: For each bad requirement, ask students: "What's wrong with this?" before revealing the answer.
Slide 23: Walk through RTM together - trace one requirement from need to test.
Slide 26: This should be a mini-case study discussion. Ask: "What specific requirement would have prevented this?
Quick Poll (Slide 3): "How many have worked on projects that failed due to unclear requirements?" (Show of hands - normalizes the problem)
Pair Exercise (Slide 21): Give pairs 3 minutes to write one requirement for "vehicle shall have good fuel economy." Then critique together using quality attributes.
Case Analysis (Slide 26): Small groups discuss: "If you were the requirements engineer, what would you have done differently?
Before class: — [ ] Real RTM example (anonymized from industry project if possible)
[ ] Screenshots or demo of DOORS/Jama
[ ] Printed requirement quality checklist (1-page handout)
[ ] Case study materials for Toyota unintended acceleration
[ ] Exercise assignment handout with rubric
Handouts: — [ ] Requirements writing template (Slide 21 format)
[ ] Quality attributes checklist
[ ] Stakeholder analysis matrix template
[ ] RTM template (Excel)
[ ] List of automotive standards (ISO 26262, ASPICE, FMVSS, Euro NCAP)
Post-class: — [ ] Share slides
[ ] Post exercise assignment with due date
[ ] Post requirements writing template and examples
[ ] Post links to IEEE 29148, INCOSE requirements guide
[ ] Create discussion forum: "Share a bad requirement you've encountered and how to fix it
During lecture: — Quick quiz (Slide 14): "What's the difference between a need and a requirement?
Quick quiz (Slide 18): "Classify this requirement: FR, NFR, or CON?
Exercise assessment criteria: — Stakeholder completeness (Did they identify non-obvious stakeholders?)
Requirement quality (Verifiable? Clear? Properly structured?)
Traceability (Is RTM complete and consistent?)
Professional formatting (Industry-standard presentation?)
Common student mistakes to watch for: — Writing implementation as requirements
Forgetting non-functional requirements
Ambiguous language
Missing traceability
Copy-pasting requirements from internet without understanding

## Slide 39: ✅ Session Success Criteria
Students leave able to:
✓ Identify stakeholders systematically for automotive systems
✓ Distinguish between stakeholder needs and system requirements
✓ Categorize requirements as functional, non-functional, or constraints
✓ Write clear, verifiable, traceable requirements using standard structure
✓ Recognize good vs bad requirements using quality attributes
✓ Create and interpret requirements traceability matrices
✓ Identify common requirements engineering pitfalls
✓ Understand tool landscape for requirements management
Critical outcome: Students can write professional-quality requirements for an automotive system and understand that requirements engineering is a systematic discipline with proven methods, not ad-hoc documentation.
Evidence of success: — Student can take a vague stakeholder statement and convert it to a verifiable requirement
Student can critique a requirement using quality attributes framework
Student understands traceability chain from need to test
Student can explain why Toyota unintended acceleration was a requirements failure

## Slide 40: 📚 Additional Resources for Students
Standards and Guidelines: — IEEE 29148-2018: Systems and Software Engineering - Life Cycle Processes - Requirements Engineering
ISO/IEC/IEEE 15288:2015: Systems and Software Engineering - System Life Cycle Processes
INCOSE Systems Engineering Handbook, Chapter 4: Requirements Analysis
EARS (Easy Approach to Requirements Syntax) - Rolls-Royce method
Automotive-Specific: — ISO 26262-8:2018: Road Vehicles - Functional Safety - Part 8: Supporting Processes (Requirements specification)
Automotive SPICE (ASPICE) v3.1: SYS.3 System Requirements Analysis
SAE J3061: Cybersecurity Guidebook for Cyber-Physical Vehicle Systems
Books: — "Requirements Engineering Fundamentals" by Klaus Pohl & Chris Rupp
"Writing Effective Use Cases" by Alistair Cockburn (for scenario-based requirements)
"Software Requirements" by Karl Wiegers (applicable to systems too)
Online Tools and Templates: — Jama Software: Free requirements training modules
IBM DOORS tutorials (YouTube)
ReqIF format specification (for tool interoperability)

## Slide 41: 🔗 Connections to Other Sessions
Builds on: — Session 1: Failures often traced to requirements issues
Session 2: Requirements definition is first technical process in ISO/IEC 15288
Session 3: MBSE embeds requirements in models (SysML requirements diagrams)
Leads to: — Session 5: How do we transform requirements into architecture and design?
Session 7: How do we allocate requirements to functions using operational analysis?
Session 8: How do we verify requirements? (Right side of V-Model - testing)
Session 9: How do we manage requirements changes? (Change control, configuration management)
Session 12: How do we specify safety requirements? (ISO 26262 safety requirements)
Key concept thread: — Session 2: WHAT is systems engineering? (Framework)
Session 3: HOW do we implement it? (Traditional vs MBSE)
Session 4: HOW do we capture requirements? (This session)
Session 5: HOW do we design solutions? (Architecture)
Session 8: HOW do we verify we met requirements? (V&V)
Requirements traceability appears in: — Session 8 (test traceability)
Session 9 (configuration management)
Session 12 (safety requirements traceability per ISO 26262)
Session 15 (measurement and traceability metrics)

## Slide 42: 🎬 Opening and Closing Strategies
Closing (Last 2 minutes):
Start with the Mars Climate Orbiter image on screen as students enter. Begin:
Before we start, I want you to look at this image. This is a $327 million spacecraft that was destroyed because of a single missing word in a requirement. One. Word.
Today, we're going to learn how to write requirements so precisely, so carefully, that this never happens on your projects. Because in automotive, instead of losing a spacecraft, we could lose lives.
Welcome to Session 4: Requirements Engineering - the most critical skill in systems engineering.
Return to the opening image:
We started with a $327 million failure caused by poor requirements. You now have the knowledge to prevent this:
You can identify stakeholders systematically
You can write clear, verifiable requirements
You can build traceability from needs to tests
You know the pitfalls and how to avoid them
The exercise I've given you is your chance to practice these skills. Treat it seriously - imagine you're the requirements engineer and 89 lives depend on your work. Because someday, they might.
See you in Session 5, where we'll transform these requirements into system architecture.

## Slide 43: 📈 Learning Objectives Mapping to Assessment
| Session Objective | Assessment Method | Success Criteria |
|-------------------|-------------------|------------------|
| Distinguish needs from requirements | Exercise Part 2 | Correctly categorizes stakeholder statements as needs; derives requirements from them |
| Identify and analyze stakeholders | Exercise Part 1 | Identifies ≥6 diverse stakeholder groups; complete analysis matrix |
| Classify requirement types | Exercise Part 2 | Correctly labels ≥8 FR, ≥4 NFR, ≥3 CON |
| Apply quality attributes | Exercise Part 2 | All requirements follow 'shall' structure, are verifiable, clear |
| Create traceability matrix | Exercise Part 3 | Complete RTM with needs→reqs→tests mappings |
| Recognize pitfalls | In-class discussion + exercise quality | Avoids ambiguity, design bias, missing NFRs |
| Select tools | Knowledge check (Q&A) | Can name 2-3 tools and their use cases |

## Slide 44
End of Session 4 Framework
Next: Session 5 (System Design and Architecture)