## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 5: System Design and Architecture'

## Slide 2: System Design and Architecture
Session 5 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 5: System Design and Architecture. Today marks a critical transition point in our systems engineering journey.
In Session 4, we mastered requirements engineering - defining WHAT the system must do. Today, we answer the next question: HOW will we design the system to meet those requirements?
This is where engineering creativity meets engineering discipline. This is where we architect solutions.

## Slide 4: The Journey So Far - Connection to Previous Sessions
Let's connect our journey:
Session 1: We learned WHY systems engineering matters. Poor design decisions amplify requirements errors.
Session 2: We learned the SE framework - ISO/IEC 15288 technical processes. After 'Requirements Definition' comes 'Architecture Definition.'
Session 3: We explored MBSE. SysML has specific diagrams for architecture - Block Definition Diagrams, Internal Block Diagrams.
Session 4: We defined requirements systematically. Now we must satisfy those requirements through architecture.
Today's critical link: Requirements drive design. But design must not be embedded IN requirements. We separate WHAT (requirements) from HOW (architecture).
This separation enables innovation, allows multiple solutions, and facilitates trade studies.

## Slide 5: Requirements Drive Architecture
Architecture is the bridge between requirements and implementation.
The relationship:
Requirements say WHAT: — 'The vehicle shall detect obstacles within 150m with ±0.5m accuracy'
'The system shall respond to driver inputs within 200ms'
'The system shall operate in temperatures from -40°C to +85°C'
Architecture says HOW (conceptually): — 'Use radar sensor subsystem for long-range detection, camera subsystem for classification'
'Implement distributed architecture with sensor ECUs, fusion ECU, and actuation ECU'
'Partition functions: sensing, perception, decision, control, actuation'
Design says HOW (specifically): — 'Use 77 GHz FMCW radar with antenna array configuration...'
'ECU network topology: star configuration with gateway...'
'Algorithms: Kalman filter for sensor fusion, PID for control...'
Today we focus on ARCHITECTURE - the high-level structural decisions that shape the entire system.
Every major automotive system failure involves architecture decisions:
Toyota unintended acceleration? Throttle control architecture
Boeing 737 MAX MCAS? Sensor architecture and redundancy
Tesla Autopilot incidents? Sensor fusion architecture
Architecture is where we make or break system success.

## Slide 6: What IS System Architecture?
Let me give you the formal definition from INCOSE and ISO/IEC 42010:
System Architecture:
'The fundamental organization of a system, embodied in its components, their relationships to each other and the environment, and the principles governing its design and evolution.'
Breaking this down:
1. Fundamental organization — High-level structure, not detailed design
2. Components — Major subsystems, elements, modules
For vehicle: Powertrain, chassis, body, electrical, ADAS, infotainment
For ADAS: Sensors, perception, planning, control, actuation
3. Relationships — How components interact
Interfaces: CAN bus, Ethernet, mechanical connections
Data flows: Sensor data → perception → decisions → commands
Dependencies: Control ECU depends on sensor data quality
4. Environment — Context and boundaries
What's inside the system? What's outside?
External interfaces: Driver, road, regulations, other vehicles
5. Design principles — Governing rules
Modularity, redundancy, fail-safe behavior, maintainability
'All safety-critical functions shall have dual redundancy'
'Sensing and actuation shall be physically separated'
Architecture exists at multiple levels: — Enterprise: Entire vehicle architecture
System: ADAS architecture, powertrain architecture
Subsystem: Radar sensor architecture, brake system architecture
Today we focus on SYSTEM-level architecture for automotive systems.

## Slide 7: Architecture in the V-Model
Where does architecture fit in the systems engineering V-Model?
Left side (Design):
Stakeholder Requirements (Session 4) - What stakeholders need
System Requirements (Session 4) - What system must do
→ SYSTEM ARCHITECTURE ← (Today) — How system is organized
Subsystem Requirements - Requirements allocated to subsystems
Detailed Design - Component-level implementation
Right side (Verification):
We verify architecture through integration testing - does the architecture work as designed?
Critical insight from V-Model:
Architecture decisions made TODAY determine:
Integration strategy (how we assemble the system)
Interface verification (how subsystems communicate)
System-level testing approach (how we verify behavior)
The architecture must be: — Traceable to requirements — Every requirement allocated to architectural element
Verifiable — Can we build and test this architecture?
Implementable — Can subsystems be developed in parallel?
Poor architecture = expensive integration problems downstream.
Good architecture = smooth integration, modular testing, parallel development.

## Slide 8: A Deceptively Complex System
Let's use Adaptive Cruise Control (ACC) as our running example. You might think:
Initial thought: 'ACC maintains speed and keeps distance from lead vehicle. Just need a radar and throttle control. Simple!'
Reality check - What's involved in ACC architecture?
Sensing layer: — Long-range radar (150m detection)
Camera (lane detection, sign recognition)
Wheel speed sensors (own vehicle speed)
Yaw rate sensor (vehicle dynamics)
GPS (map context)
Processing layer: — Sensor fusion (combine radar + camera data)
Object tracking (maintain continuity of detected vehicles)
Threat assessment (is lead vehicle decelerating?)
Path planning (longitudinal trajectory)
Control algorithms (speed and spacing control)
Actuation layer: — Throttle control (acceleration requests to powertrain ECU)
Brake control (deceleration requests to brake ECU)
Transmission control (gear selection optimization)
Interface layer: — Driver interface (buttons, displays, alerts)
Other vehicle systems (ESC, ABS, lane keeping, collision avoidance)
Diagnostic systems (fault detection and logging)
OTA update capability (software updates)
Suddenly, we have 10+ subsystems, 20+ interfaces, 50+ requirements to allocate!
This is why we need systematic architecture development.

## Slide 9: What is CONOPS?
Before we architect the system, we must understand HOW it will be used. This is the Concept of Operations (CONOPS).
CONOPS Definition:
'A verbal and graphic statement, in user-oriented terminology, describing how a system will be operated, who will operate it, and under what conditions it will be used to achieve mission objectives.'
CONOPS answers critical questions: — Who are the users? (Driver, passengers, service technicians, fleet managers)
What will they do with the system? (Engage ACC, set speed, monitor, disengage)
When will they use it? (Highway driving, traffic jams, long trips)
Where will it operate? (Geographic regions, road types, weather conditions)
Why do they need it? (Reduce fatigue, improve fuel economy, enhance safety)
How will they interact? (Steering wheel buttons, displays, voice commands)
CONOPS is NOT: — ❌ Detailed design (not HOW the system works internally)
❌ System requirements (not WHAT the system must do)
❌ User manual (not step-by-step instructions)
CONOPS IS: — ✓ Operational vision (HOW users will employ the system)
✓ Context for architecture (shapes design decisions)
✓ Communication tool (aligns stakeholders on operational concept)
In automotive: — CONOPS developed early (concept phase)
Drives requirements (what capabilities enable operations?)
Shapes architecture (what structure supports operations?)
Guides testing (validate against operational scenarios)

## Slide 10: ACC CONOPS Example - Operational Scenarios
Let's develop CONOPS for our ACC system through operational scenarios.
Scenario 1: Highway Cruising (Normal Operation)
Context: — Driver: Experienced, highway driving, light traffic
Environment: Clear weather, dry road, daylight
Vehicle speed: 120 km/h
Operational sequence:
Driver accelerates to desired speed (120 km/h)
Driver presses SET button on steering wheel
System activates ACC, displays status on cluster ('ACC Active, 120 km/h')
System maintains speed automatically
No lead vehicle ahead → system maintains set speed
Driver monitors traffic, keeps hands on wheel
Driver can adjust speed with +/- buttons (±1 km/h per press)
Expected system behavior: — Smooth speed maintenance (±2 km/h tolerance)
Fuel-efficient throttle modulation
Display shows status continuously

## Slide 11
Scenario 2: Following Vehicle (Adaptive Behavior)
Context: — ACC engaged at 120 km/h
Lead vehicle appears ahead, traveling at 100 km/h
Set following distance: 2.0 seconds time gap
Operational sequence:
Radar detects lead vehicle at 100m distance
System assesses: 'Lead vehicle slower, closing speed 20 km/h'
System decelerates smoothly (gentle braking, 0.2g max)
System achieves 2.0 sec following distance (55m at 100 km/h)
System matches lead vehicle speed (100 km/h)
Display shows: 'ACC Active, Following, 100 km/h, Distance: 2.0s'
Driver can adjust following distance (1.0s, 1.5s, 2.0s, 2.5s settings)
Expected system behavior: — Comfortable deceleration (not jerky)
Maintain safe following distance
Respond to lead vehicle speed changes

## Slide 12
Scenario 3: Lead Vehicle Cuts In (Dynamic Response)
Context: — ACC following at 100 km/h, 2.0s gap
Vehicle from adjacent lane cuts in front suddenly
New lead vehicle now only 20m ahead (0.7s gap - too close!)
Operational sequence:
Radar detects new target suddenly closer
System identifies: 'Critical - following distance below threshold'
System applies moderate braking (0.3g) immediately
Display alerts driver: 'Take Over' warning (visual + audible)
System increases following distance to 2.0s
If driver doesn't respond and gap keeps decreasing → system applies stronger braking
Expected system behavior: — Rapid but safe response to cut-ins
Clear driver alerts
Maintain safety (don't cause rear-end collision)

## Slide 13
Scenario 4: Driver Override and Deactivation
Context: — ACC engaged
Driver needs to take control
Deactivation triggers:
Driver presses brake pedal → ACC disengages immediately, driver controls braking
Driver presses CANCEL button → ACC disengages, returns to manual throttle
Driver presses accelerator >50% → ACC suspends, driver controls speed temporarily
System detects sensor failure → ACC disengages, alerts driver ('ACC Unavailable')
Vehicle speed drops below 30 km/h → ACC disengages (designed for highway use)
Expected system behavior: — Instant response to driver inputs (driver always has authority)
Clear status indication (driver knows ACC state)
Safe transitions (no sudden changes)
These scenarios drive architecture requirements: — Need rapid sensor processing (detect cut-ins quickly)
Need smooth actuation (comfort during speed changes)
Need clear HMI (driver must understand system state)
Need fail-safe behavior (handle sensor failures)

## Slide 14: From CONOPS to Architecture Implications
CONOPS directly shapes architecture. Let's trace the connections:
Operational Need → Architectural Implication
1. 'Detect lead vehicle at 150m in all weather'
→ Architecture must include:
Long-range sensing capability (77 GHz radar, not just camera)
Weather-robust sensor (radar works in fog/rain, camera doesn't)
Sensor positioning (front bumper, unobstructed field of view)
2. 'Respond to sudden cut-ins within 0.5 seconds'
→ Architecture must include:
High-frequency sensor sampling (20+ Hz)
Low-latency processing (sensor → decision → actuation <500ms)
High-priority CAN messaging (ACC messages preempt lower priority)
Fast actuator response (electronic throttle, brake-by-wire)
3. 'Driver can override instantly by pressing brake'
→ Architecture must include:
Brake pedal monitoring (direct input to ACC ECU or via CAN)
Preemptive arbitration (brake command overrides ACC commands)
Fail-safe logic (on any fault, release control to driver)
4. 'System operates in -40°C to +50°C ambient'
→ Architecture must include:
Industrial-grade ECUs (automotive temperature range)
Sensor heating (radar lens heating, camera lens defogging)
Cold-start calibration (sensors may need warm-up time)
5. 'Maintain operation even if one sensor fails'
→ Architecture must include:
Sensor redundancy (radar + camera, not single sensor)
Fault detection and isolation (FDI algorithms)
Degraded mode operation (fall back to reduced functionality)
6. 'Driver must understand system state at all times'
→ Architecture must include:
Dedicated HMI subsystem (instrument cluster integration)
Multiple indication methods (visual icon, text, color, sound)
State machine visibility (engaged, standby, following, error)
CONOPS forces us to think OPERATIONALLY, not just FUNCTIONALLY.
Many architecture failures come from designing the system in isolation, ignoring how it's actually used.

## Slide 15
#### Part 2: System Context and Boundaries (Slides 12-14, ~10 minutes)

## Slide 16: Defining System Boundaries
Critical architecture step: Define what's IN the system and what's OUT.
Why boundaries matter: — Scope control: What are we responsible for designing?
Interface identification: What do we interface with but don't control?
Responsibility allocation: Where does our system end and others begin?
For ACC system, let's define boundaries:
INSIDE the ACC System (Our Responsibility): — ACC ECU (processing unit)
ACC software (algorithms, control logic)
Radar sensor (if dedicated to ACC)
ACC-specific HMI elements (dashboard icon, settings menu)
ACC wiring harness
OUTSIDE the ACC System (External Interfaces): — Driver: User, operator
Interface: Steering wheel buttons (input), instrument cluster (output)
Powertrain ECU: Controls engine/motor torque
Interface: CAN messages (ACC sends torque requests)
Brake ECU: Controls brake actuation
Interface: CAN messages (ACC sends deceleration requests)
ESC (Electronic Stability Control): Vehicle dynamics control
Interface: CAN messages (wheel speeds, yaw rate data)
Transmission ECU: Gear selection
Interface: CAN messages (optimal gear for ACC operation)
Instrument Cluster: Driver displays
Interface: CAN messages (status, warnings, icons)
Body Control Module: Vehicle state information
Interface: CAN messages (door status, ignition state)
Gateway ECU: Network management
Interface: CAN bus connection, network routing
Diagnostic System: Service and fault logging
Interface: OBD-II / UDS protocols
Infrastructure: Road, traffic, weather
Interface: Radar/camera perception (one-way, sensing only)
Other Vehicles: Lead vehicle, surrounding traffic
Interface: Radar/camera perception (one-way, sensing only)
Regulations: FMVSS, Euro NCAP, UN R79
Interface: Compliance requirements (constraints)
Boundary decisions drive: — Development responsibility (who develops what?)
Integration testing (where are interface test points?)
Fault isolation (if something fails, whose problem is it?)
Cost allocation (budget and resources)
Common mistake: Vague boundaries
Example: Is the camera 'inside' ACC or 'shared' with lane keeping?
If shared: Need coordination, joint calibration, arbitration
If dedicated: ACC team owns it fully
Decision impacts architecture significantly
SysML representation: Context diagrams, Block Definition Diagrams (BDD) with boundary boxes

## Slide 17: External Interface Identification
Once boundaries are clear, we catalog ALL external interfaces.
Interface Identification Matrix - ACC System:
| External Entity | Interface Type | Protocol/Physical | Data Flow | Criticality |
|----------------|----------------|-------------------|-----------|-------------|
| Driver | Human-Machine Interface | Steering wheel switches (resistive, 0-5V) | Bidirectional (commands in, status out) | High |
| Powertrain ECU | Electronic | CAN 2.0B, 500 kbps | Bidirectional (torque request out, engine status in) | Critical |
| Brake ECU | Electronic | CAN 2.0B, 500 kbps | Bidirectional (decel request out, brake status in) | Critical |
| ESC ECU | Electronic | CAN 2.0B, 500 kbps | Input only (wheel speeds, yaw rate) | Critical |
| Instrument Cluster | Electronic | CAN 2.0B, 500 kbps | Output only (status, warnings) | Medium |
| Radar Sensor | Electronic | CAN FD, 2 Mbps (or Ethernet) | Input only (object list, targets) | Critical |
| Camera Sensor | Electronic | Automotive Ethernet, 100 Mbps | Input only (video stream, lane data) | High |
| Gateway ECU | Electronic | CAN 2.0B, 500 kbps | Bidirectional (diagnostics, updates) | Medium |
| Road/Environment | Physical | Electromagnetic (radar, optical) | Input only (sensing) | N/A |
For each interface, specify:
1. Interface Control Document (ICD) Required — Physical layer: Connectors, pinouts, voltages, timing
Protocol layer: Message IDs, data formats, update rates
Behavioral layer: Sequence diagrams, state machines
Error handling: Fault detection, timeout behavior, defaults
Example - Powertrain Interface ICD:
Message: ACC_TorqueRequest CAN ID: 0x245 DLC: 8 bytes Byte 0-1: Requested torque (Nm, scaled 0.1 Nm/bit, offset -500 Nm) Byte 2: Torque rate limit (Nm/s) Byte 3: Torque control mode (0=None, 1=Speed, 2=Torque) Byte 4-7: Reserved Update rate: 20 ms (50 Hz) Timeout: If no message for 100ms, powertrain reverts to driver control
2. Interface Verification Plan — How will we test this interface?
Unit test (ECU bench), integration test (vehicle), validation
3. Interface Change Management — Who can change interface definition?
Approval process (both sides must agree)
Version control
Architecture implication:
Every interface is a RISK. — Communication failures
Timing issues
Mismatched interpretations
Architecture principle:
Minimize interfaces. Simplify interfaces. Document interfaces rigorously.
80% of integration problems come from interface issues.

## Slide 18: System Context Diagram
Let's visualize the complete system context.
ACC System Context Diagram:
[Visual shows ACC ECU in center, surrounded by external entities with labeled arrows]
Key elements:
Center: ACC System (boundary box)
External entities (outside boundary):
Driver (top)
Road/Environment (bottom)
Vehicle systems ECUs (left and right)
Diagnostic/service (bottom right)
Interface flows (arrows with labels):
Driver → ACC: Button presses (SET, RES, CANCEL, +/-), time gap selection
ACC → Driver: Status displays, warnings, alerts
Radar/Camera → ACC: Detected objects, distances, velocities
ACC → Powertrain: Torque requests, acceleration demands
ACC → Brake: Deceleration requests, braking intensity
ESC → ACC: Vehicle speed, yaw rate, wheel speeds
ACC ↔ Cluster: Status, mode, set speed, following distance
ACC ↔ Gateway: Diagnostics, fault codes, software updates
This diagram answers critical questions: — What flows INTO our system? (Inputs we must handle)
What flows OUT? (Outputs we must generate)
What don't we control? (External dependencies)
Architecture decisions from context: — High sensor bandwidth (radar/camera) → Need fast network (Ethernet or CAN FD)
Critical safety interfaces (brake, powertrain) → Need redundancy, fault detection
Human interaction (driver) → Need clear, unambiguous feedback
Multiple ECU interfaces → Need network architecture design
This context diagram becomes: — Foundation for detailed architecture
Basis for interface testing
Communication tool with stakeholders
Input to trade studies (where to partition functionality?)
SysML equivalent: BDD (Block Definition Diagram) with system context

## Slide 19
#### Part 3: Design Principles and Architecture Patterns (Slides 15-18, ~12 minutes)

## Slide 20: High-Level Design Principles
Good architecture follows proven design principles. These are timeless guidelines that lead to robust systems.
Fundamental Design Principles for Automotive Systems:
1. MODULARITY - Decompose into Cohesive Modules
Definition: System divided into independent, interchangeable modules with well-defined interfaces
Benefits:
Parallel development (teams work independently)
Easier testing (test modules separately, then integrate)
Maintainability (replace/upgrade modules without touching others)
Reusability (use proven modules in multiple systems)
ACC Example:
Sensing module (radar, camera)
Perception module (object detection, tracking)
Planning module (trajectory, spacing control)
Actuation module (throttle/brake commands)
HMI module (driver interface)
Each module has defined inputs/outputs, can be developed separately.

## Slide 21
2. HIERARCHY - Organize in Levels of Abstraction
Definition: System organized in layers, each level abstracts complexity of levels below
ACC Architecture Hierarchy:
Level 0: Complete ACC system
Level 1: Subsystems (Sensing, Processing, Actuation, HMI)
Level 2: Components (Radar ECU, Fusion Algorithm, Brake Interface, Display Driver)
Level 3: Modules/Functions (Target Selection, Distance Control, PID Controller)
Benefits:
Manage complexity (understand one level at a time)
Clear responsibility (each level has defined role)
Verification strategy (test bottom-up: components → subsystems → system)

## Slide 22
3. ABSTRACTION - Hide Implementation Details
Definition: Interface defines WHAT, not HOW
Example:
Bad: 'Radar ECU outputs raw ADC samples at 1 MHz'
Good: 'Sensor subsystem provides list of detected objects with position, velocity, confidence'
Abstraction allows changing implementation without affecting users of the interface.

## Slide 23
4. SEPARATION OF CONCERNS - Isolate Responsibilities
Definition: Different aspects handled by different elements
ACC Example:
Sensing concerns: Separated into dedicated sensor ECUs
Safety concerns: Separated into monitoring function
Diagnostic concerns: Separated into diagnostic manager
Don't mix safety-critical and non-critical in same module.

## Slide 24
5. INFORMATION HIDING - Encapsulation
Definition: Internal details not visible to external users
Example:
Other ECUs don't need to know ACC's internal state machine
They interact via defined CAN messages only
ACC can change internal algorithms without affecting others

## Slide 25
6. INTERFACE STANDARDIZATION - Use Common Patterns
Definition: Reuse interface patterns across system
Example:
All actuator commands use same CAN message structure
All status messages use same format
Reduces learning curve, testing burden

## Slide 26
7. REDUNDANCY - Critical Functions Have Backups
Definition: Duplicate critical capabilities
ACC Safety Architecture:
Dual sensors (radar + camera, independent failures)
Plausibility checking (cross-check sensor data)
Safe fallback (if sensors fail, disable gracefully)
Trade-off: Redundancy adds cost and complexity but improves safety and availability.

## Slide 27
8. FAIL-SAFE DESIGN - Fail to Safe State
Definition: On any fault, system transitions to safe configuration
ACC Fail-Safe:
Sensor failure → Disable ACC, alert driver (don't guess)
Communication loss → Disable ACC (don't act on stale data)
ECU crash → Watchdog resets ECU, ACC stays off until next ignition cycle
Critical for automotive: Never fail in a way that causes accident.
These principles guide every architecture decision we make.

## Slide 28: Common Architecture Patterns
Beyond principles, we use proven architecture patterns - recurring solutions to common problems.
Pattern 1: LAYERED ARCHITECTURE
Structure: System organized in horizontal layers, each layer uses services of layer below
Automotive Example - ADAS Architecture:
┌─────────────────────────────────────────┐ │ Layer 4: Application │ (ACC, LKA, AEB functions) ├─────────────────────────────────────────┤ │ Layer 3: Planning & Decision │ (Trajectory planning, arbitration) ├─────────────────────────────────────────┤ │ Layer 2: Perception & Fusion │ (Object detection, tracking, fusion) ├─────────────────────────────────────────┤ │ Layer 1: Sensing & Actuation │ (Radar, camera, throttle, brake) └─────────────────────────────────────────┘
Rules:
Layer N can only call Layer N-1 (downward)
Layer N provides services to Layer N+1 (upward)
No skipping layers (Layer 4 can't directly access Layer 1)
Benefits:
Clear separation of concerns
Easy to replace a layer (if interface maintained)
Testable (test layers independently)
Drawback:
Can introduce latency (must pass through layers)
Rigid structure
When to use: Complex systems with clear functional hierarchy

## Slide 29
Pattern 2: PIPE-AND-FILTER (Data Flow Architecture)
Structure: Data flows through sequence of processing stages (filters), connected by data channels (pipes)
Automotive Example - Sensor Processing Pipeline:
Raw Radar → Filtering → Detection → Tracking → Fusion → Object List Signals (Filter) (Filter) (Filter) (Filter) (Output)
Benefits:
Intuitive for data processing tasks
Easy to add/remove stages
Parallel processing (stages can run concurrently)
Reusable filters
Drawback:
Not suitable for interactive systems
Assumes unidirectional flow
When to use: Sensor processing, signal chains, data transformations

## Slide 30
Pattern 3: DISTRIBUTED (NETWORKED) ARCHITECTURE
Structure: Multiple ECUs connected via network, each handles subset of functions
Automotive Example - Modern Vehicle Architecture:
┌─────────┐ ┌─────────┐ ┌─────────┐ │Radar ECU│ │ACC ECU │ │Brake ECU│ └────┬────┘ └────┬────┘ └────┬────┘ │ │ │ ─────┴───────────────────┴───────────────────┴───── CAN Bus │ │ │ ┌────┴────┐ ┌────┴────┐ ┌────┴────┐ │Camera │ │Gateway │ │Cluster │ │ECU │ │ECU │ │ECU │ └─────────┘ └─────────┘ └─────────┘
Benefits:
Scalability (add ECUs as needed)
Fault isolation (one ECU failure doesn't crash system)
Supplier independence (different suppliers for different ECUs)
Drawback:
Network complexity (timing, bandwidth, reliability)
Integration challenges
Network is single point of failure
When to use: Complex vehicles with many functions (standard for automotive)

## Slide 31
Pattern 4: CENTRALIZED (DOMAIN CONTROLLER) ARCHITECTURE
Structure: Powerful central ECU handles multiple functions, reduces distributed ECUs
Automotive Example - Tesla/Future Architecture:
┌──────────────────────────────────┐ │ Central ADAS Computer │ │ (ACC + LKA + AEB + Parking...) │ │ (Multi-core, high performance) │ └────────┬─────────────────┬───────┘ │ │ Ethernet Ethernet │ │ ┌────────┴──┐ ┌────┴─────────┐ │Sensor Hub │ │Actuator Hub │ │(Cameras, │ │(Throttle, │ │ Radar) │ │ Brake, Steer)│ └───────────┘ └──────────────┘
Benefits:
Reduced ECU count (cost savings, weight reduction)
Easier software updates (one central computer)
Higher performance (powerful processor)
Simplified integration
Drawback:
Single point of failure (need redundancy for safety)
High complexity in one unit
Expensive central computer
When to use: Future vehicles, EVs, high-performance ADAS
Trend: Automotive moving from distributed → centralized (domain controllers)

## Slide 32: Designing for Quality Attributes
Architecture must satisfy not just functional requirements but QUALITY attributes (Non-Functional Requirements from Session 4).
Quality Attribute: SAFETY
Architectural strategies: — Redundancy: Dual sensors, dual processing paths
Monitoring: Watchdog timers, plausibility checks
Fail-safe defaults: On fault, disable function safely
Isolation: Safety-critical functions physically separated
ACC Example:
Radar + Camera (redundant perception)
Watchdog monitors ACC ECU heartbeat
Sensor disagreement > threshold → disable ACC
Safety monitor runs on separate core

## Slide 33
Quality Attribute: RELIABILITY
Architectural strategies: — Fault detection: Self-diagnostics, health monitoring
Graceful degradation: Reduced functionality vs complete failure
Robust communication: Error detection (CRC), retransmission
ACC Example:
If camera fails but radar OK → Continue with reduced confidence
CAN messages have CRC checksums
ECU logs faults to non-volatile memory

## Slide 34
Quality Attribute: PERFORMANCE (Timing)
Architectural strategies: — Parallel processing: Distribute load across multiple cores/ECUs
Priority scheduling: Critical tasks run first
Efficient communication: High-bandwidth networks (Ethernet)
ACC Example:
Sensor processing on dedicated cores (parallel)
Control loop runs at 20 Hz (highest priority task)
Object list transmitted on CAN FD (faster than CAN 2.0)

## Slide 35
Quality Attribute: MAINTAINABILITY
Architectural strategies: — Modularity: Replace modules independently
Standardized interfaces: Common connector types, protocols
Diagnostics: Extensive fault logging, diagnostic protocols
ACC Example:
Radar sensor is plug-and-play module (calibrated at factory)
OBD-II/UDS diagnostics expose fault codes
Software updatable via OTA or service tool

## Slide 36
Quality Attribute: TESTABILITY
Architectural strategies: — Test points: Accessible interfaces for measurement
Simulation interfaces: Inject test signals
Observability: Log internal states
ACC Example:
CAN bus accessible via OBD port (can monitor all messages)
Radar can be fed simulated targets (test mode)
ECU exposes internal state via diagnostic service ($22)

## Slide 37
Quality Attribute: EVOLVABILITY (Future-Proofing)
Architectural strategies: — Abstraction: Define stable interfaces
Modularity: Swap components without redesign
Extensibility: Design for future additions
ACC Example:
Sensor interface abstracted (can add lidar without changing ACC logic)
Over-the-air (OTA) update capability designed in
Spare CAN bandwidth reserved (30% margin for future features)
Architecture insight:
You can't add quality attributes AFTER architecture is fixed.
They must be designed in from the start.

## Slide 38: Architecture Trade-offs
Architecture is about TRADE-OFFS. You can't optimize everything simultaneously.
Common Trade-offs in Automotive Architecture:
1. Safety vs Cost — High safety: Dual redundancy, expensive sensors, extra monitoring
Low cost: Minimum redundancy, cheaper components
Decision: Depends on ASIL level (ISO 26262)
ASIL D (highest) → Must have redundancy, cost secondary
ASIL A (lowest) → Single sensor acceptable, cost matters
ACC: Typically ASIL B or C → Partial redundancy (radar + camera)

## Slide 39
2. Performance vs Power Consumption — High performance: Powerful processors, fast networks, continuous operation
Low power: Lower clock speeds, sleep modes, minimal communication
Decision: Mission profile dependent
ADAS systems: Performance critical (safety), power secondary
Comfort systems: Power savings important (battery drain)
ACC: Performance dominates (can't compromise safety for power savings)

## Slide 40
3. Flexibility vs Complexity — High flexibility: Configurable, many options, extensible
Low complexity: Fixed design, simple, easy to validate
Decision: Product strategy
Platform architecture: High flexibility (reuse across models)
Single-vehicle architecture: Simplicity (faster development)
ACC: Moderate flexibility (configurable time gap, speed limits, but core algorithm fixed)

## Slide 41
4. Centralized vs Distributed — Centralized: Fewer ECUs, easier integration, single point of failure
Distributed: Fault isolation, supplier flexibility, network complexity
Decision: Technology maturity and safety requirements
Current vehicles: Distributed (proven, fail-safe)
Future vehicles: Centralized domain controllers (cost, performance)
ACC: Distributed (current), moving toward centralized (next generation)

## Slide 42
5. COTS (Commercial Off-The-Shelf) vs Custom — COTS: Faster development, proven components, less control
Custom: Optimized for application, higher development cost
Decision: Criticality and differentiation
Commodity functions: COTS (cost-effective)
Differentiating features: Custom (competitive advantage)
ACC: Hybrid (COTS radar sensors, custom fusion algorithms)
How to make trade-off decisions?
→ Trade Studies (we'll cover in Part 6)
Document:
Alternatives considered
Evaluation criteria
Rationale for decision
Risks accepted
Architecture trade-offs define the system. Choose deliberately.

## Slide 43
#### Part 4: Architecture Development Process (Slides 19-21, ~10 minutes)

## Slide 44: Functional Decomposition
How do we go from requirements to architecture? Step 1: Functional Decomposition.
Functional Decomposition Process:
1. Identify top-level functions (from requirements and CONOPS)
ACC Top-Level Functions: — Monitor driver inputs
Sense environment
Detect and track objects
Determine desired speed and spacing
Control vehicle longitudinal motion
Provide driver feedback
Perform self-diagnostics
2. Decompose each function into sub-functions
Example: 'Sense Environment' decomposes to: — Emit radar signals
Receive radar reflections
Process radar returns → range, velocity
Capture camera images
Process images → lane markings, objects
Fuse sensor data → unified world model
Example: 'Control Vehicle Longitudinal Motion' decomposes to: — Calculate required acceleration/deceleration
Determine actuator commands (throttle or brake)
Send commands to powertrain/brake ECUs
Monitor command execution
Detect actuator failures
3. Continue decomposition until functions are implementable
Example: 'Calculate Required Acceleration' decomposes to: — Determine speed error (target speed - current speed)
Determine spacing error (desired gap - actual gap)
Apply speed control algorithm (PID, MPC, etc.)
Apply spacing control algorithm
Arbitrate between speed and spacing control
Limit acceleration (comfort and safety bounds)
4. Create Functional Flow Block Diagram (FFBD)
[Visual shows FFBD with functions and logic flow]
5. Allocate requirements to functions
Example Allocation: — REQ-ACC-015: 'System shall detect vehicles up to 150m'
→ Allocated to 'Process Radar Returns' function
REQ-ACC-042: 'System shall respond to driver button within 200ms'
→ Allocated to 'Monitor Driver Inputs' function
Traceability: — Every requirement allocated to at least one function
Every function traces to at least one requirement
Functional decomposition outcomes: — Clear understanding of system behavior
Basis for architecture (functions → components)
Enables parallel development (different teams, different functions)
Verification planning (test each function)
Session 7 goes deeper: Operational and Functional Analysis

## Slide 45: Requirements Allocation to Subsystems
After functional decomposition, we allocate requirements to architectural elements (subsystems, components).
Allocation Process:
1. Define architectural elements (physical subsystems)
ACC Architecture Elements: — Radar Sensor ECU
Camera Sensor ECU
ACC Control ECU
HMI Module (part of Instrument Cluster)
Powertrain Interface
Brake Interface
CAN Communication Network
2. Map functions to architectural elements
Function → Element Mapping: — 'Emit/Receive Radar Signals' → Radar Sensor ECU
'Process Radar Returns' → Radar Sensor ECU
'Process Camera Images' → Camera Sensor ECU
'Fuse Sensor Data' → ACC Control ECU
'Calculate Acceleration' → ACC Control ECU
'Send Actuator Commands' → ACC Control ECU
'Display Status' → HMI Module
3. Allocate requirements to elements
Requirements Allocation Matrix - Example:
| Requirement | Allocated To | Derived Requirements |
|-------------|--------------|---------------------|
| REQ-ACC-010: Detect vehicles at 150m | Radar Sensor ECU | REQ-Radar-001: Range ≥150m<br>REQ-Radar-002: Update rate ≥20 Hz |
| REQ-ACC-020: Respond within 200ms | ACC Control ECU | REQ-ACC-ECU-015: Processing latency ≤100ms<br>REQ-CAN-005: Message latency ≤50ms |
| REQ-ACC-035: Maintain speed ±2 km/h | ACC Control ECU | REQ-ACC-ECU-025: Speed control accuracy ±1.5 km/h<br>REQ-Actuator-010: Throttle response ≤0.5 km/h |
4. Derive subsystem requirements from system requirements
Example Derivation:
System Requirement:
REQ-ACC-100: 'System shall operate in -40°C to +85°C'
Derived Subsystem Requirements:
REQ-Radar-ECU-050: 'Radar ECU shall operate in -40°C to +85°C'
REQ-Camera-ECU-050: 'Camera ECU shall operate in -40°C to +85°C'
REQ-ACC-ECU-050: 'ACC ECU shall operate in -40°C to +85°C'
REQ-Radar-Lens-010: 'Radar lens shall include heating element for operation <0°C'
5. Ensure complete coverage
Verification: — Every system requirement allocated? (100% coverage)
Every allocated requirement verifiable at subsystem level?
Any conflicts between allocations? (requirements pulling in opposite directions)
Allocation challenges:
Challenge 1: Shared requirements — REQ-ACC-200: 'Total system cost <$800'
Can't allocate to one subsystem - it's a system-level constraint
Solution: Derive cost budgets for each subsystem
Radar ECU: $300, Camera ECU: $200, ACC ECU: $150, Other: $150
Challenge 2: Interface requirements — REQ-ACC-250: 'CAN latency <50ms'
Affects multiple elements (sender, network, receiver)
Solution: Allocate to interface definition, specify responsibilities
Challenge 3: Emergent requirements — Some system behaviors emerge from interactions
Example: 'System stability' depends on control algorithm + actuator response + sensor noise
Solution: Allocate to integration-level verification
Outcome: Subsystem Requirements Specifications (SRS) — Each subsystem gets its own requirements document
Traceable to system requirements
Basis for subsystem design and verification

## Slide 46: Interface Definition
After allocating requirements, we define interfaces between architectural elements.
Interface Definition Process:
1. Identify all interfaces from architecture
ACC Internal Interfaces: — Radar ECU ↔ ACC Control ECU
Camera ECU ↔ ACC Control ECU
ACC Control ECU ↔ Powertrain ECU
ACC Control ECU ↔ Brake ECU
ACC Control ECU ↔ HMI Module
ACC Control ECU ↔ Diagnostic Module
All ECUs ↔ CAN Network
2. Define interface characteristics
For each interface, specify:
A. Physical Interface — Connector type (e.g., HDSCS 16-pin connector)
Pin assignment
Electrical characteristics (voltage levels, current capacity)
Environmental protection (IP6K9K for exterior sensors)
B. Communication Protocol — Network type (CAN 2.0B, CAN FD, Ethernet)
Baud rate (500 kbps, 2 Mbps, 100 Mbps)
Addressing scheme
Error handling (CRC, acknowledgment, retransmission)
C. Data Interface — Message catalog (all CAN messages defined)
Data structures (byte layouts, scaling, offsets)
Update rates (how often data refreshes)
Timing constraints (max latency, synchronization)
D. Behavioral Interface — Initialization sequence (power-up, calibration)
Normal operation (steady-state message exchange)
Fault handling (timeouts, error responses)
Shutdown sequence (graceful deactivation)
Example Interface Definition: ACC ECU → Powertrain ECU
Interface ID: IF-ACC-PWR-001
Physical:
Connection: Via CAN bus, no direct physical connection
CAN transceiver: ISO 11898 compliant
Protocol:
Network: CAN 2.0B
Baud rate: 500 kbps
Bus: Powertrain CAN
Data Messages:
Message 1: ACC_TorqueRequest — CAN ID: 0x245
DLC: 8 bytes
Sender: ACC ECU
Receiver: Powertrain ECU
Rate: 20 ms (50 Hz)
Data:
Byte 0-1: Requested torque (Nm, signed, scale 0.1, offset -500, range -500 to 500 Nm)
Byte 2: Torque rate limit (Nm/s, unsigned, scale 1, range 0-255 Nm/s)
Byte 3: Control mode (0=Inactive, 1=Active, 2=Standby)
Byte 4-6: Reserved (0x00)
Byte 7: CRC-8 checksum
Message 2: Powertrain_Status — CAN ID: 0x312
Sender: Powertrain ECU
Receiver: ACC ECU (+ others)
Rate: 10 ms (100 Hz)
Data:
Engine torque actual (Nm)
Throttle position (%)
Powertrain ready flag
Fault status
Behavioral:
Normal: ACC sends torque request, Powertrain responds with status
Timeout: If ACC doesn't receive Powertrain_Status for >100ms → Disable ACC, alert driver
Error: If Powertrain_Status shows fault → ACC disengages
3. Create Interface Control Documents (ICDs)
ICD is a formal specification: — Agreed upon by both sides (ACC team and Powertrain team)
Version controlled
Changes require approval from both parties
Basis for interface testing
4. Define interface verification strategy
How to test interface? — Unit level: Simulate Powertrain ECU, verify ACC ECU sends correct messages
Integration level: Connect actual ECUs, verify end-to-end communication
Fault injection: Timeout scenarios, corrupted messages, unexpected values
Interface risks: — 80% of integration problems are interface issues
Misunderstood specifications
Timing violations
Error handling gaps
Best practice: — Define interfaces EARLY
Review interfaces thoroughly
Test interfaces separately before system integration
SysML representation: Internal Block Diagrams (IBD) with ports and connectors

## Slide 47
#### Part 5: Architecture Frameworks and Views (Slides 22-23, ~8 minutes)

## Slide 48: Multiple Architecture Views
Complex systems need multiple views to fully describe architecture. No single diagram captures everything.
Kruchten's 4+1 Architectural View Model (adapted for automotive):
1. LOGICAL VIEW - Functional Decomposition
Purpose: Show system functionality and behavior
Diagrams:
Functional block diagrams
State machines (system behavior)
Data flow diagrams
ACC Logical View Example:
┌──────────────┐ ┌──────────────┐ ┌──────────────┐ │ Environment │───>│ Perception │───>│ Planning │ │ Sensing │ │ & Fusion │ │ & Control │ └──────────────┘ └──────────────┘ └──────────────┘ │ V ┌──────────────┐ │ Actuation │ └──────────────┘
Stakeholders: Systems engineers, software architects, algorithm developers

## Slide 49
2. PHYSICAL VIEW - Hardware Architecture
Purpose: Show physical components and their deployment
Diagrams:
Component diagrams (ECUs, sensors, actuators)
Deployment diagrams (where software runs)
Network topology
ACC Physical View Example:
[Radar Sensor]───────CAN FD─────┐ │ │ [Radar ECU] │ │ V └─────CAN 2.0B────────>[ACC ECU]────CAN──>[Powertrain ECU] │ [Camera Sensor]──Ethernet───────┤ │ │ [Camera ECU]────CAN FD──────────┘ │ CAN Bus │ [Instrument Cluster]
Stakeholders: Hardware engineers, integration team, manufacturing

## Slide 50
3. DEVELOPMENT VIEW - Software Architecture
Purpose: Show software organization, modules, layers
Diagrams:
Package diagrams (software modules)
Layer diagrams (AUTOSAR layers)
Component diagrams (software components)
ACC Software View (AUTOSAR Layers):
┌─────────────────────────────────────┐ │ Application Layer │ ACC_SpeedControl, ACC_DistanceControl ├─────────────────────────────────────┤ │ Runtime Environment (RTE) │ Inter-component communication ├─────────────────────────────────────┤ │ Basic Software (BSW) │ CAN drivers, diagnostics, OS ├─────────────────────────────────────┤ │ Microcontroller Abstraction │ Hardware drivers └─────────────────────────────────────┘
Stakeholders: Software developers, software architects, testing team

## Slide 51
4. PROCESS VIEW - Runtime Behavior
Purpose: Show dynamic behavior, concurrency, timing
Diagrams:
Sequence diagrams (message exchanges)
Timing diagrams (real-time constraints)
Task/thread diagrams (concurrency)
ACC Process View Example - Message Sequence:
Time │ Radar ECU ACC ECU Powertrain ECU │ │ │ │ ├──────>│ Object List │ │ (20ms cycle) │ │────────────────>│ │ │ │ │ Compute Control │ │ │ │ ─────────────> │ │ │ │ Torque Request │ │ │ │─────────────────>│ │ │ │ │ Actuate │ │ │<────Status───────│
Stakeholders: Real-time engineers, integration team, verification team

## Slide 52
5. SCENARIO VIEW (+1) - Use Cases
Purpose: Tie views together through operational scenarios
Diagrams:
Use case diagrams
CONOPS scenarios
Operational sequence diagrams
ACC Scenario Example: Lead vehicle cut-in scenario (from Slide 10)
Stakeholders: All stakeholders (validates architecture meets needs)

## Slide 53
Why multiple views? — Different stakeholders need different perspectives
No single view shows everything
Views are CONSISTENT (describe same system from different angles)
Architecture tools (SysML, Enterprise Architect) generate multiple views from single model
Best practice: Document all views, maintain consistency across views

## Slide 54: Automotive Architecture Frameworks
Automotive industry uses standardized architecture frameworks. These provide structure and common language.
Framework 1: AUTOSAR (AUTomotive Open System ARchitecture)
Purpose: Standardize automotive software architecture
Key Concepts:
Layered architecture (Application, RTE, Basic Software, Hardware)
Software Components (SWCs) with defined interfaces
Virtual Function Bus (VFB) abstracts communication
Standardized interfaces for common functions (CAN, diagnostics, OS)
ACC in AUTOSAR:
ACC implemented as Application SWCs
RTE handles communication between SWCs
BSW provides CAN communication, diagnostics, OS
Benefits:
Portability (move software between ECUs)
Reusability (use same SWCs in different vehicles)
Supplier interoperability (common interfaces)
Adoption: Industry standard (most OEMs and suppliers use AUTOSAR)

## Slide 55
Framework 2: ISO 26262 Safety Architecture
Purpose: Structure architecture for functional safety
Key Concepts:
ASIL decomposition (break down safety requirements)
Safety elements (Safety Mechanisms, Safety Monitor)
Freedom from Interference (safety and non-safety isolated)
Fault tolerant architecture patterns
ACC Safety Architecture:
ACC function: ASIL B
Safety monitor: ASIL B (independent check)
Sensor redundancy: Radar (ASIL B) + Camera (ASIL B)
Fail-safe: On fault → safe state (disable, alert driver)
Architectural Requirements from ISO 26262:
Hardware-software interface (HSI) clearly defined
Software partitioning (safety vs non-safety)
Diagnostic coverage (detect faults)

## Slide 56
Framework 3: E/E Architecture Reference Models
Purpose: Standardize electrical/electronic architecture
Common Models:
Distributed Architecture (Current vehicles):
Domain-based: Powertrain, Chassis, Body, Infotainment, ADAS
Each domain has multiple ECUs
Gateway for inter-domain communication
Centralized Architecture (Future vehicles):
Zone controllers (front, rear, left, right zones)
Central compute (high-performance ADAS computer)
Simplified wiring
Service-Oriented Architecture (SOA) (Emerging):
Software services accessible over Ethernet
Dynamic service discovery
Similar to IT architectures (microservices)

## Slide 57
Framework 4: DODAF / Zachman (Enterprise Architecture)
Purpose: Comprehensive enterprise/system architecture
DODAF Views (Department of Defense Architecture Framework):
Operational View (OV): Operational scenarios
System View (SV): System architecture
Technical View (TV): Standards and protocols
Zachman Framework:
Matrix: Perspectives (Planner, Owner, Designer, Builder, Implementer)
× Questions (What, How, Where, Who, When, Why)
Automotive Use:
Not common for vehicle-level (too heavyweight)
Used for enterprise architecture (OEM IT systems, manufacturing)

## Slide 58
Choosing Framework:
For ACC system: — Use AUTOSAR for software architecture (industry standard)
Use ISO 26262 for safety architecture (regulatory requirement)
Use multiple views (logical, physical, process, scenario)
Benefits of frameworks: — Common language across teams and suppliers
Proven patterns (don't reinvent)
Tool support (AUTOSAR tools, SysML tools)
Compliance (ISO 26262 requires architectural documentation)
Trade-off: Frameworks add structure but also complexity. Use appropriately.

## Slide 59
#### Part 6: Trade Studies and Configuration Management (Slides 24, ~10 minutes)

## Slide 60: Design Freeze and Baseline Management
Architecture evolves during development. We must manage this evolution through baselines and design freeze.
Architecture Lifecycle:
Phase 1: Concept (Months 0-6) — Explore multiple architectures
Trade studies (like we just saw)
Preliminary architecture selected
Baseline 1: Concept Architecture (30% confidence)
Phase 2: Preliminary Design (Months 6-12) — Refine architecture
Interface definitions
Subsystem allocation
Baseline 2: Preliminary Architecture (70% confidence)
Phase 3: Detailed Design (Months 12-18) — Finalize architecture
Detailed interface specs (ICDs)
Component specifications
Baseline 3: Critical Design Review (CDR) - DESIGN FREEZE (95% confidence)
Phase 4: Implementation (Months 18-30) — Architecture FROZEN (changes require formal approval)
Components developed to frozen architecture
Integration per frozen interface specs
Baseline 4: As-Built Architecture (100%, production)

## Slide 61
What is Design Freeze?
Definition: Point where architecture is locked; further changes require formal change control process
Why Design Freeze? — Enables parallel development: Teams develop components knowing interfaces won't change
Prevents chaos: Without freeze, constant changes disrupt development
Allows integration: Can't integrate if architecture keeps changing
Supports verification: Tests written against frozen architecture
What gets frozen at Design Freeze?
✓ Subsystem architecture (what components exist)
✓ Interface definitions (ICDs locked)
✓ Requirements allocation (which subsystem satisfies which requirement)
✓ Safety architecture (ASIL decomposition, redundancy)
What can still change after freeze? — Internal implementation details (algorithms, code structure)
Internal component design (if interfaces maintained)
Non-functional optimizations (performance tuning)

## Slide 62
Configuration Management:
What is Configuration Management (CM)?
'Formal process for identifying, controlling, and tracking configuration items (CIs) throughout lifecycle'
Configuration Items for Architecture: — Architecture diagrams (logical, physical views)
Interface Control Documents (ICDs)
Requirements Allocation Matrix
Trade study reports
Design decision logs
CM Activities:
1. Identification — Each architecture artifact has unique ID
Version numbering (v1.0, v1.1, v2.0)
Example: 'ICD-ACC-PWR-v2.3' (Interface between ACC and Powertrain, version 2.3)
2. Change Control — Change Request (CR) process
Impact analysis (what does this change affect?)
Change Review Board (CRB) approves/rejects
Only approved changes implemented
3. Status Accounting — Track status of all CIs (draft, reviewed, approved, released, obsolete)
Know which version is current
4. Auditing — Physical Configuration Audit (PCA): Does as-built match design?
Functional Configuration Audit (FCA): Does it meet requirements?

## Slide 63
Change Control Process (Post-Freeze):
Step 1: Change Request Submitted — Example: 'Need to increase CAN message frequency from 20ms to 10ms'
Rationale: Improved control loop performance
Step 2: Impact Analysis — Which subsystems affected? (ACC ECU software, CAN bus load)
What changes required? (Software timing, CAN bus bandwidth analysis)
What's the risk? (May exceed CAN bandwidth limit)
Cost impact? (+1 week development, $5k testing)
Step 3: Review by Change Control Board (CCB) — Members: Chief Engineer, Systems Engineer, Safety Engineer, Project Manager
Evaluate: Is benefit worth cost and risk?
Decision: Approve / Reject / Defer
Step 4: Implementation (if approved) — Update architecture documentation
Update ICDs
Notify affected teams
Re-verify affected interfaces
Step 5: Verification — Test change (regression testing)
Update test cases
Step 6: New Baseline — Release new version of affected CIs
Update configuration status

## Slide 64
Design Freeze Trade-offs:
Freeze TOO EARLY: — ❌ Architecture not mature (high risk of changes needed)
❌ Expensive late changes (rework)
Freeze TOO LATE: — ❌ Delays implementation start (schedule risk)
❌ Teams waiting (idle resources)
Optimal timing: Freeze when architecture confidence is 90-95%
Some uncertainty remains, but major decisions made
Typical: After Critical Design Review (CDR)
Automotive typical timeline: — Concept freeze: Month 6 (explore → commit to direction)
Architecture freeze: Month 12 (preliminary → detailed)
Design freeze (CDR): Month 18 (start production development)
Start of Production (SOP): Month 36-48
Modern challenge: Agile vs Design Freeze — Agile: Embrace change, iterate quickly
Automotive: Safety-critical, long validation cycles, need stability
Hybrid approach: Freeze safety-critical interfaces, allow agility in non-critical areas
Configuration management is not bureaucracy - it's risk management for complex systems.

## Slide 65: ACC Architecture - Complete Example
Let's synthesize everything we've learned by looking at the complete ACC architecture.
ACC System Architecture - Integrated Views:
1. Context View:
Boundaries: ACC system vs external vehicle systems
External interfaces: 8 major interfaces (driver, sensors, actuators, diagnostics)
2. Logical View (Functional):
Functions: Sensing → Perception → Planning → Control → Actuation → HMI
Functional flow: Continuous loop (20 Hz control cycle)
3. Physical View (Hardware):
Components: Radar ECU, Camera ECU, ACC ECU, Instrument Cluster
Network: CAN 2.0B (500 kbps) + CAN FD (2 Mbps for sensors)
Topology: Star (all ECUs connect to CAN backbone)
4. Process View (Runtime):
Timing: 50 ms end-to-end latency (sensor → decision → actuation)
Tasks: Sensor processing (10 ms), Fusion (20 ms), Control (20 ms), HMI (100 ms)
Priorities: Control (highest), Sensing (high), HMI (medium), Diagnostics (low)
5. Safety Architecture (ISO 26262):
ASIL: ASIL B (moderate safety-critical)
Redundancy: Radar + Camera (independent sensing)
Safety monitor: Plausibility checks, watchdog
Fail-safe: On fault → disable ACC, alert driver, log fault
Key Architecture Decisions Recap:
Decision 1: Distributed architecture (Radar ECU + Camera ECU + ACC ECU)
Rationale: Fault isolation, supplier flexibility, proven approach
Alternative rejected: Centralized (single ECU) - less mature, higher risk
Decision 2: Radar + Camera sensor fusion
Rationale: Trade study showed best cost-performance-safety balance
Alternative rejected: Radar-only (insufficient classification), Lidar (too expensive)
Decision 3: CAN 2.0B for vehicle network, CAN FD for sensor data
Rationale: CAN 2.0B proven, CAN FD needed for high-bandwidth sensor data
Alternative rejected: Full Ethernet (not yet mature in all domains)
Decision 4: AUTOSAR software architecture
Rationale: Industry standard, reusability, portability
Alternative rejected: Custom architecture (reinventing wheel)
Decision 5: Design freeze at Month 12 (after preliminary design)
Rationale: 90% architecture confidence, allows 18 months implementation
Interfaces locked, internal algorithms can still evolve
Requirements Allocation (Sample): — REQ-ACC-010 'Detect vehicles at 150m' → Radar ECU + Fusion Algorithm
REQ-ACC-025 'Maintain ±2 km/h accuracy' → Control Algorithm + Powertrain Interface
REQ-ACC-050 'Respond within 200 ms' → System-level (sensor latency + processing + actuation)
This architecture is:
✓ Traceable: All requirements allocated, all decisions justified
✓ Verifiable: Clear test strategy for each interface and subsystem
✓ Implementable: Subsystems can be developed in parallel
✓ Safe: Redundancy, fail-safe, ISO 26262 compliant
✓ Maintainable: Modular, documented, standardized (AUTOSAR)
From requirements (Session 4) → Architecture (Session 5) → Implementation (design/code)

## Slide 66: Key Takeaways
Let's consolidate today's learning:
1. CONOPS Drives Architecture — Understand HOW the system will be used before designing it
Operational scenarios reveal architectural requirements
CONOPS informs trade studies and design decisions
2. Context and Boundaries Matter — Define what's IN vs OUT explicitly
Catalog all external interfaces
Interfaces are risk - minimize, simplify, document rigorously
3. Apply Design Principles — Modularity, hierarchy, abstraction, separation of concerns
Redundancy and fail-safe for safety-critical systems
Principles are timeless - patterns are proven solutions
4. Architecture Has Multiple Views — Logical (functional), Physical (hardware), Process (runtime), Development (software)
No single view captures everything
Use standard frameworks (AUTOSAR, ISO 26262, SysML)
5. Systematic Architecture Development — Functional decomposition (requirements → functions)
Requirements allocation (functions → subsystems)
Interface definition (subsystems ↔ subsystems)
Use trade studies to evaluate alternatives
6. Configuration Management is Essential — Baseline architecture at key milestones
Design freeze enables parallel development
Change control process post-freeze
Documentation must stay synchronized with implementation
7. Trade Studies Justify Decisions — Identify alternatives, define criteria, evaluate systematically
Document rationale (defensible decisions)
Sensitivity analysis reveals risks
8. Architecture is Where We Make or Break the System — Poor architecture → expensive integration problems, late failures
Good architecture → smooth integration, modular testing, maintainable system
Architecture decisions have long-lasting consequences
Critical connection: — Session 4: Requirements tell us WHAT to build
Session 5 (Today): Architecture tells us HOW to organize the solution
Session 7: Functional analysis tells us HOW to allocate behavior
Session 8: Integration and verification tell us we built it right
Architecture is the bridge from requirements to implementation.

## Slide 67: Connection to V-Model and Next Sessions
Let's place today in the systems engineering journey.
V-Model Left Side (Design):
Session 4 - Requirements Engineering:
Stakeholder needs and system requirements
WHAT the system must do
Output: Requirements Specification
Session 5 - Architecture (Today):
System architecture and design
HOW the system is organized
Output: System Architecture Description, ICDs
↓ Next step: Subsystem design (detailed design)
What comes next:
Session 7 - Operational and Functional Analysis:
Analyze operational scenarios in depth
Functional flow block diagrams (FFBD)
Allocate requirements to functions systematically
Timeline analysis (sequence of operations)
Connection: Session 5 created architecture; Session 7 allocates behavior to that architecture
Session 8 - Integration, Verification & Validation:
Right side of V-Model
Integration strategy (how to assemble system from subsystems)
Verification (did we build architecture correctly?)
Validation (does architecture meet stakeholder needs?)
Connection: Verify architecture through integration testing
Session 9 - Risk Management:
Identify architectural risks (single points of failure, interface complexity)
DFMEA (Design Failure Mode and Effects Analysis)
Mitigate risks in architecture
Session 10 - Decision Management:
Advanced trade study techniques (AHP, multi-attribute utility theory)
Dealing with uncertainty in architecture decisions
Connection: Extends trade studies from today
Session 12 - Safety Engineering (ISO 26262):
Safety architecture requirements
ASIL decomposition
Safety mechanisms
Connection: Today we mentioned safety architecture; Session 12 goes deep
The thread: — Requirements → Architecture → Functional Allocation → Design → Implementation → Verification
Each session builds on previous
Architecture is the pivotal link
Key insight from V-Model:
Architecture decisions made on LEFT side determine integration approach on RIGHT side.
Modular architecture → modular integration and testing.

## Slide 68: 📊 PPT DESIGN GUIDANCE
Real Examples to Include:
Practical Exercise (Due before Session 6):
You are the lead systems architect for a Lane Keeping Assist (LKA) system.
Part 1: CONOPS (20%) — Develop 3 operational scenarios for LKA (normal operation, lane departure, driver override)
Each scenario includes: context, operational sequence, expected system behavior
Part 2: System Context (20%) — Create system context diagram
Identify all external interfaces (minimum 8)
Define system boundary (what's IN vs OUT)
Part 3: Architecture Development (40%) — Develop system architecture with:
Functional decomposition (minimum 6 major functions)
Physical architecture (ECUs, sensors, actuators, network)
Allocate 10 system requirements to architectural elements (use requirements from your Session 4 exercise or create new ones)
Define 3 key interfaces (create simplified ICDs with message definitions)
Part 4: Trade Study (20%) — Conduct trade study for ONE architecture decision:
Camera configuration: Monocular vs Stereo vs Fisheye
OR Actuation: Steering torque overlay vs Steering angle control
OR ECU architecture: Integrated (with ACC) vs Dedicated LKA ECU
Include: alternatives, criteria (minimum 5), weighted scoring, recommendation, rationale
Deliverables: — Part 1: CONOPS document (1-2 pages)
Part 2: Context diagram + interface table (1 page)
Part 3: Architecture diagrams (logical, physical views) + allocation matrix (2-3 pages)
Part 4: Trade study report (1-2 pages)
Total: 5-8 pages
Grading Criteria: — CONOPS quality: Operational scenarios realistic and detailed? (20%)
Context completeness: All interfaces identified? Boundary clear? (20%)
Architecture soundness:
Functional decomposition logical? (10%)
Physical architecture feasible? (10%)
Requirements properly allocated? (10%)
Interfaces well-defined? (10%)
Trade study rigor: Criteria justified? Scoring documented? Sensitivity considered? (20%)
Tips: — Research real LKA systems (Euro NCAP, SAE standards)
Think about safety architecture (ISO 26262 ASIL B typical for LKA)
Consider camera placement (windshield vs side mirrors)
Don't over-design (stay at system architecture level, not detailed design)
Use SysML notation if you know it (not required)
Document rationale for all major decisions
Bonus (Optional): — Create Process View showing message timing (sequence diagram)
Identify potential failure modes and architectural mitigations
Compare your architecture to Tesla Autopilot LKA (publicly available info)
Discussion Questions: — How would LKA architecture differ from ACC architecture? (Similar sensors, different actuation)
What if we combine LKA + ACC into single system? (Integration challenges? Benefits?)
How does camera placement affect architecture? (Windshield vs hood vs mirrors)
Learning objectives: — Practice CONOPS development
Practice architecture decomposition and allocation
Conduct systematic trade study
Document architecture professionally
30 minutes for your questions. —--
Professional engineering aesthetic: Clean, technical, systems-oriented
Color coding:
Blue for functional/logical views
Green for physical/hardware views
Orange for interfaces
Red for safety/critical elements
Purple for trade-offs/decisions
Use real automotive examples: ACC system throughout, LKA references, Tesla/ADAS photos
Diagrams: Block diagrams, ICDs, context diagrams, architecture views (SysML/UML style)
Slide 3 (Requirements Drive Architecture) - Critical connection from Session 4
Slide 8 (Architecture Decisions) - Real decisions students will face
Slide 10 (CONOPS Scenarios) - Operational thinking
Slide 15 (Design Principles) - Timeless guidelines
Slide 16 (Architecture Patterns) - Proven solutions
Slide 22 (Multiple Views) - Comprehensive perspective
Slide 24 (Trade Studies) - Systematic evaluation
Slide 27 (Complete ACC Architecture) - Integration of all concepts
Slide 28 (Takeaways) - Students will photograph this
Slide 3: Animate flow from Requirements → Architecture → Design → Implementation
Slide 8: Build architecture decision tree progressively
Slide 10: Animate CONOPS scenarios as timeline sequences
Slide 13: Highlight interfaces appearing one by one on context diagram
Slide 19: Build functional decomposition tree level by level
Slide 22: Transition between architecture views (logical → physical → process)
Slide 24: Animate trade study scoring calculation step by step
Slide 27: Layer complete architecture views (build up final integrated view)
Slide 12: Context diagram with boundary box
Slide 13: Interface identification matrix
Slide 16: Architecture pattern comparison (4 patterns side-by-side)
Slide 19: Functional hierarchy tree
Slide 20: Requirements allocation matrix
Slide 22: 4+1 view model diagrams
Slide 24: Trade study evaluation matrix with calculations
Slide 26: Configuration management process flow
ACC system (primary example throughout)
Tesla architecture references (publicly available)
AUTOSAR layer diagrams
ISO 26262 safety architecture examples
CAN message definitions (real format)
SysML diagrams (BDD, IBD examples)

## Slide 69: 🎯 INSTRUCTOR NOTES
Assessment Opportunities:
Concrete → Abstract → Concrete: Start with ACC example, teach principles, return to ACC complete architecture
Multiple perspectives: Show that architecture needs multiple views (not just one diagram)
Decisions over perfection: Emphasize trade-offs and justified decisions
Tools and standards: Expose students to industry practices (AUTOSAR, ISO 26262, SysML)
Challenge 1: "Difference between architecture and design?"
How to address: Architecture = high-level structure, interfaces, major components. Design = detailed implementation (algorithms, data structures, code). Use analogy: Architecture = house floor plan; Design = electrical wiring diagram, plumbing details.
Challenge 2: "How much detail in architecture?"
How to address: Goldilocks principle - enough detail to enable parallel development and integration, not so much that you constrain implementation. Interface definitions must be detailed; internal algorithms can remain abstract.
Challenge 3: "Overwhelming number of diagrams/views"
How to address: Each view serves specific stakeholders. You don't create all views for every project - select relevant ones. Small project: Maybe 2-3 views. Large vehicle project: All views needed.
Challenge 4: "When to freeze architecture?"
How to address: Freeze when confidence is 90-95%. Use design reviews as checkpoints. Too early = rework risk. Too late = schedule delays. Show timeline examples from real projects.
Challenge 5: "Trade studies seem subjective"
How to address: They ARE subjective - criteria weights reflect priorities. Key is TRANSPARENCY and DOCUMENTATION. Sensitivity analysis reveals where subjectivity matters most. Even imperfect systematic approach beats gut decisions.
If running short: — Condense Slide 16 (patterns) - focus on 2-3 patterns most relevant
Reduce Slide 22 (views) to 3 views instead of 5
Simplify Slide 24 (trade study) - show process, skip detailed calculation
If running long: — Extend Slide 10 (CONOPS) with additional scenarios and student discussion
Add live demo: Create simple SysML diagram using tool
Extend Slide 24 (trade study) with sensitivity analysis discussion
Show real automotive architecture documentation examples
Core content (must cover - non-negotiable): — Slides 9-11 (CONOPS)
Slides 12-14 (Context and boundaries)
Slides 15-17 (Design principles and patterns)
Slides 19-21 (Architecture development process)
Slide 24 (Trade studies)
Slide 25 (Design freeze and configuration management)
Slide 27 (Complete example)
Slide 28 (Summary)
Slide 7: Interactive - Ask students: "What subsystems would YOU include in ACC?" List on board, compare to complete answer.
Slide 8: Poll - "Which decision do you think is most critical?" Discuss why.
Slide 13: Work through one interface definition together - students suggest what needs to be specified.
Slide 16: Ask students to identify pattern in a system they know (smartphone, home automation).
Slide 24: Live trade study - pick a simple decision, have class suggest criteria and weights.
Quick Poll (Slide 8): "How many have worked on projects where architecture changed late?" (Show of hands - normalizes the integration pain)
Think-Pair-Share (Slide 15): "Pick one design principle. How would you apply it to ACC?" (2 minutes individual, 2 minutes pairs, 3 minutes share)
Small Group Exercise (Slide 24): Break into groups, each evaluates one alternative for trade study, then combine scores.
Before class: — [ ] ACC architecture diagrams (all views)
[ ] Sample ICD (real or realistic)
[ ] Trade study template (spreadsheet)
[ ] SysML tool demo (Enterprise Architect, Cameo, or Papyrus)
[ ] Real automotive architecture examples (from publicly available sources)
[ ] Configuration management process flowchart
Handouts: — [ ] Architecture documentation template
[ ] Trade study template (Excel with formulas)
[ ] Interface Control Document template
[ ] Design principles checklist
[ ] Architecture review checklist
Post-class: — [ ] Share slides
[ ] Post exercise assignment with due date and rubric
[ ] Post architecture templates (SAD template, ICD template, trade study template)
[ ] Share links to AUTOSAR standard, ISO 26262 Part 4 (architecture), SysML tutorials
[ ] Create discussion forum: "Share an architecture decision from your experience and the trade-offs
During lecture: — Quick quiz (Slide 15): "Name three design principles and how they apply to ACC
Quick quiz (Slide 22): "What's the purpose of Physical View vs Logical View?
Exercise assessment criteria: — CONOPS realism (Are scenarios operationally sound?)
Context completeness (All interfaces identified? Boundary clear?)
Architecture feasibility (Could this be built? Does it satisfy requirements?)
Trade study rigor (Systematic evaluation? Documented rationale?)
Professional presentation (Industry-standard diagrams and formatting?)
Common student mistakes to watch for: — Confusing architecture with detailed design (too much detail)
Missing interfaces (incomplete context analysis)
Ignoring non-functional requirements in architecture
No traceability from requirements to architecture
Trade studies with unjustified criteria or weights
Vague interface definitions (not specific enough for implementation)

## Slide 70: ✅ Session Success Criteria
Students leave able to:
✓ Develop CONOPS for automotive systems
✓ Define system context and identify all external interfaces
✓ Apply design principles (modularity, hierarchy, abstraction, redundancy, fail-safe)
✓ Decompose system functionally and allocate requirements to subsystems
✓ Create multiple architecture views (logical, physical, process)
✓ Conduct systematic trade studies for architecture decisions
✓ Understand design freeze and configuration management
✓ Document architecture professionally
Critical outcome: Students understand that architecture is systematic, not ad-hoc, and that architecture decisions have long-term consequences for cost, safety, maintainability, and integration.
Evidence of success: — Student can develop a credible system architecture from requirements
Student can justify architecture decisions through trade studies
Student understands that multiple architecture views are necessary
Student can trace requirements to architectural elements
Student can define interfaces precisely enough for parallel development

## Slide 71: 📚 Additional Resources for Students
Standards and Guidelines: — ISO/IEC/IEEE 42010:2011: Systems and Software Architecture Description
ISO/IEC 15288:2015: System Architecture Definition Process (Section 6.4.4)
INCOSE Systems Engineering Handbook, Chapter 5: System Architecture
IEEE 1471: Architectural Description (predecessor to ISO 42010)
Automotive-Specific: — ISO 26262-4:2018: Road Vehicles - Functional Safety - Part 4: Product Development at System Level
AUTOSAR Architecture Specifications (www.autosar.org)
SAE J3016: Taxonomy of Automated Driving (architecture implications)
EAST-ADL: Electronics Architecture and Software Technology - Architecture Description Language
Books: — "Software Systems Architecture" by Rozanski & Woods (views and perspectives)
"Documenting Software Architectures" by Clements et al. (SEI)
"Automotive Software Engineering" by Schäuffele & Zurawka (automotive-specific architecture)
"Design Patterns" by Gamma et al. (software patterns applicable to systems)
Online Resources: — AUTOSAR tutorials and specifications
SysML tutorials (OMG SysML website)
ISO 26262 architecture examples (public case studies)
SAE standards for automotive systems

## Slide 72: 🔗 Connections to Other Sessions
Builds on: — Session 1: Architecture failures cause system failures (case studies)
Session 2: ISO/IEC 15288 Architecture Definition process
Session 3: MBSE - SysML diagrams for architecture (BDD, IBD)
Session 4: Requirements drive architecture; architecture satisfies requirements
Leads to: — Session 6: Case study applying requirements + architecture
Session 7: Functional analysis allocates behavior to architecture
Session 8: Integration strategy flows from architecture; verification tests architecture
Session 9: Risk management identifies architectural risks; DFMEA on architecture
Session 10: Advanced decision techniques for architecture trade-offs
Session 12: Safety architecture (ISO 26262) - extends today's safety concepts
Session 15: Configuration management and technical planning - extends baseline concepts
Key concept thread: — Session 2: WHAT is the SE process? (ISO/IEC 15288 framework)
Session 3: WHAT are the tools? (MBSE, SysML)
Session 4: WHAT must the system do? (Requirements)
Session 5 (Today): HOW is the system organized? (Architecture)
Session 7: HOW does the system behave? (Functional analysis)
Session 8: HOW do we verify? (Integration and V&V)
Architecture appears in: — Session 7 (functional allocation to architecture)
Session 8 (architecture-driven integration)
Session 9 (architecture risk analysis)
Session 12 (safety architecture)
Session 13 (life cycle cost driven by architecture)

## Slide 73: 🎬 Opening and Closing Strategies
Closing (Last 2 minutes):
Show image of ACC system on screen. Begin:
Look at this image - an Adaptive Cruise Control system. Seems simple, right? Maintain speed, keep distance.
But hidden inside this 'simple' system are 10+ subsystems, 20+ interfaces, decisions about sensors, networks, ECUs, safety mechanisms, fault handling...
The difference between a $327 million failure and a successful system often comes down to architecture.
Today, we learn how to architect automotive systems systematically. We transform requirements into structure.
Welcome to Session 5: System Design and Architecture.
Return to ACC image:
We started with this seemingly simple ACC system. You now understand what's really inside:
CONOPS that drives design decisions
Context boundaries and 20+ interfaces
Functional decomposition into 6 major functions
Physical architecture with distributed ECUs
Design principles: modularity, redundancy, fail-safe
Trade studies that justified sensor choices
Baselines and design freeze that enable development
Architecture is where we make the system real. It's the bridge from WHAT (requirements) to HOW (implementation).
Your exercise: Apply these same principles to Lane Keeping Assist. Make deliberate, justified architecture decisions.
In Session 7, we'll take this architecture and analyze how it operates. We'll allocate behavior through functional flow diagrams.
See you then!

## Slide 74: 📈 Learning Objectives Mapping to Assessment
| Session Objective | Assessment Method | Success Criteria |
|-------------------|-------------------|------------------|
| Explain CONOPS and its role | Exercise Part 1 | 3 realistic operational scenarios developed with context, sequence, behavior |
| Define system context and boundaries | Exercise Part 2 | Context diagram with clear boundary, ≥8 interfaces identified |
| Apply design principles | Exercise Part 3 | Architecture demonstrates modularity, hierarchy, appropriate redundancy |
| Develop system architecture | Exercise Part 3 | Functional decomposition + physical architecture with traceable allocation |
| Compare architecture patterns | Discussion/Q&A | Can explain when to use distributed vs centralized, layered vs pipe-filter |
| Understand design freeze and CM | Knowledge check (Q&A) | Can explain when to freeze, what gets frozen, change control process |
| Perform trade studies | Exercise Part 4 | Complete trade study with alternatives, criteria, scoring, sensitivity, rationale |

## Slide 75
End of Session 5 Framework
Next: Session 6 (Case Study 1) or Session 7 (Operational and Functional Analysis)