## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 8: System Integration, Verification & Validation'

## Slide 2: System Integration, Verification & Validation
Session 8 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 8: System Integration, Verification & Validation. This is where the rubber meets the road in systems engineering.
We've spent 7 sessions learning to define, design, and decompose systems. Today: How do we prove our system actually works?
PPT Content:
SESSION 8: SYSTEM INTEGRATION, VERIFICATION & VALIDATION Testing, Proving, and Delivering Systems That Work Module 2: System Design and Analysis Automotive Systems Engineering (AE ZG517 / AEL ZG517)
Outcomes Addressed: Setting context for LO2, LO4

## Slide 4: Connection to Sessions 1-7 (Mid-Semester Review)
Before we dive in, let's see how everything connects. This is your mid-semester integration point:
Session 1: Learned WHY SE matters - failures like Apollo 13, Therac-25
Session 2: Learned SE fundamentals - ISO/IEC 15288, V-Model, systems thinking
Session 3: Traditional vs MBSE - modern approaches to complexity
Session 4: Requirements Engineering - defining WHAT the system must do
Session 5: Architecture & Design - HOW the system is structured
Session 6: Case Study 1 - Boeing 737 MAX failure analysis
Session 7: Functional Analysis - decomposing system behaviors
Session 8 (Today): Proving the system meets requirements - closing the V-Model
Everything we've learned culminates in V&V. Without verification and validation, we have no proof our system works.
PPT Content:
THE SYSTEMS ENGINEERING JOURNEY SO FAR Sessions 1-3: Foundation • Why SE matters (failures) • SE processes & frameworks • MBSE evolution Sessions 4-5: Requirements & Design • Requirements engineering • System architecture Sessions 6-7: Analysis & Case Study • Real-world failure analysis • Functional decomposition Session 8: Proving It Works ← TODAY • Integration, verification, validation

## Slide 5: The V-Model Right Side
Remember the V-Model from Session 2? We've been working down the left side:
Requirements → High-level design
Architecture → Detailed design
Functions → Implementation
Today we climb back up the right side: — Unit testing → Integration testing
System testing → Acceptance testing
Key insight: Each level on the left has a corresponding verification level on the right.
Requirements defined in Session 4? Validated in acceptance testing.
Architecture designed in Session 5? Verified in integration testing.
Functions from Session 7? Tested in unit and integration tests.
This is called bidirectional traceability.
PPT Content:
THE V-MODEL: CLIMBING BACK UP Left Side (Done): Right Side (Today): Requirements ←————→ Acceptance Testing Architecture ←————→ System Testing Design ←————→ Integration Testing Implementation ←————→ Unit Testing Each decomposition step has a corresponding verification step

## Slide 6: Why Integration and V&V Matter - Real Costs
Let me show you why today's topic is critical:
Industry data on V&V: — 40-50% of project budgets go to testing and V&V
70% of defects found in testing were preventable with better V&V planning
Cost multiplier: 1x (requirements) → 10x (design) → 100x (testing) → 1000x (field)
Automotive examples: — Toyota unintended acceleration (Session 6 case): Inadequate testing of ETCS
Takata airbag recall: $10 billion, inadequate validation of propellant aging
Tesla Autopilot incidents: Insufficient scenario coverage in validation
The paradox: V&V is expensive, but NOT doing it properly is catastrophically more expensive.
PPT Content:
WHY V&V MATTERS: THE COST OF FAILURE Industry Statistics: • 40-50% of project budget goes to V&V • Defect cost multiplier: 1x → 10x → 100x → 1000x • 70% of defects preventable with better V&V planning Automotive Recalls (V&V Failures): • Takata airbags: $10B, 100M vehicles • GM ignition switch: $4.1B, 124 deaths • Toyota ETCS: $1.2B, inadequate software testing **V&V is expensive. Not doing it is catastrophic.**

## Slide 7: The Three Critical Questions
Every V&V strategy must answer three fundamental questions:
Question 1: Did we build the system right? (VERIFICATION)
Does the system meet its specifications?
Are all requirements implemented correctly?
Does the design match the architecture?
Question 2: Did we build the right system? (VALIDATION)
Does the system solve the customer's problem?
Does it meet stakeholder needs?
Will it work in the real operational environment?
Question 3: How do we know? (EVIDENCE)
What tests prove it?
What analysis supports it?
What documentation demonstrates it?
Example: Adaptive Cruise Control (ACC) — Verification: Does ACC maintain the specified 2-second gap? (Specification)
Validation: Does ACC make drivers feel safe and comfortable? (Need)
Evidence: Test reports, data logs, customer feedback
These questions guide everything we do today.
PPT Content:
THREE CRITICAL V&V QUESTIONS 1. Did we build the system RIGHT? → VERIFICATION • Meets specifications • Requirements implemented correctly • Conforms to design 2. Did we build the RIGHT system? → VALIDATION • Solves customer problem • Meets stakeholder needs • Works in real environment 3. How do we KNOW? → EVIDENCE • Test results • Analysis data • Documentation **All three must be answered with traceable evidence**

## Slide 8: The Lane Keep Assist Integration Problem
Let's start with a real challenge. You're the integration lead for a Lane Keep Assist (LKA) system with these components:
8 Components to integrate:
Forward camera (lane detection)
Image processing ECU
Lane detection algorithm
Control ECU
Steering torque actuator
Vehicle CAN bus
HMI warning system
Driver monitoring system
The challenge: How do you integrate these? What's your strategy?
Two extreme approaches:
Approach A - 'Big Bang': Get all 8 components, connect them all at once, power on, hope it works
Approach B - 'Incremental': Integrate components step-by-step, testing each integration point
Which would you choose? Why?
Think about what could go wrong with each approach.
PPT Content:
INTEGRATION CHALLENGE: LANE KEEP ASSIST (LKA) System Components (8): 1. Forward camera 2. Image processing ECU 3. Lane detection algorithm 4. Control ECU 5. Steering actuator 6. CAN bus interface 7. HMI warning display 8. Driver monitoring Question: How do you integrate 8 components with 12+ interfaces? Option A: Big Bang (all at once) Option B: Incremental (step-by-step) **What are the risks and benefits of each?**

## Slide 9: What Usually Happens (The Failure Mode)
Here's what typically happens with big bang integration:
Week 1: Assemble all components, power on system
Result: Doesn't work. Multiple failures.
Week 2: Debug. Is it the camera? The ECU? The algorithm? The CAN bus? All of the above?
Problem: With 8 components and 12 interfaces, you have:
8 × 7 / 2 = 28 possible pairwise interactions
Hundreds of possible fault combinations
No idea where to start debugging
Real example - Tesla Autopilot early integration: — 2015: Integrated camera, radar, ultrasonic, GPS all at once
Result: Sensor conflicts, phantom braking, weeks of debugging
Lesson: Switched to incremental integration with Hardware-in-the-Loop (HIL) testing
This is why integration strategy matters.
We need a systematic approach. That's what we'll learn today.
PPT Content:
BIG BANG INTEGRATION: WHAT GOES WRONG Timeline: Week 1: Integrate all components → System fails Week 2: Debug → Can't isolate root cause Week 3: Still debugging → Multiple interacting faults Week 4: Project delay With 8 components: • 28 pairwise interactions • 100+ fault combinations • Impossible to isolate failures **Real Example: Early Tesla Autopilot** Integrated all sensors at once → sensor conflicts Switched to incremental + HIL testing **Lesson: Integration strategy is critical**

## Slide 10: Defining Verification and Validation
Let's nail down the most important distinction in V&V:
VERIFICATION: 'Are we building the product right?'
Confirms product meets specifications
Objective, measurable criteria
Based on requirements and design documents
Question: Does it match what we specified?
VALIDATION: 'Are we building the right product?'
Confirms product meets user needs
Subjective, user-centered evaluation
Based on stakeholder expectations and operational environment
Question: Does it solve the real problem?
House analogy: — Verification: Does the house match the blueprint? (measurements, materials, code compliance)
Validation: Does the house meet the family's needs? (comfortable, functional, suitable)
You can have perfect verification and still fail validation.
Example: A house built exactly to spec (verified) but family hates the layout (not validated).
PPT Content:
VERIFICATION vs VALIDATION: THE DISTINCTION VERIFICATION: "Building the product RIGHT • Meets specifications • Objective criteria • Based on requirements • Question: Does it match specs? VALIDATION: "Building the RIGHT product • Meets user needs • Subjective evaluation • Based on stakeholder expectations • Question: Does it solve the problem? **House Analogy:** Verification → Matches blueprint? Validation → Family happy with it? **You can verify perfectly but still fail to validate**

## Slide 11: Automotive Example - Verification vs Validation
Let's make this concrete with Automatic Emergency Braking (AEB):
VERIFICATION Activities: — Test: AEB activates when closing speed > 40 km/h and TTC < 1.5s (requirement AEB-FR-012)
Test: Braking deceleration = 6 m/s² ± 0.5 m/s² (requirement AEB-FR-018)
Inspection: CAN message ID 0x234 transmitted every 10ms (requirement AEB-IF-003)
Analysis: Brake response time < 150ms (requirement AEB-NFR-001)
These verify the system meets its specifications.
VALIDATION Activities: — Real-world testing: Does AEB prevent crashes in actual traffic?
User studies: Do drivers trust and accept AEB interventions?
Scenario testing: Works in rain, fog, night conditions?
Field trials: Reduces rear-end collisions in fleet data?
These validate the system solves the safety problem.
Key insight: You can perfectly verify AEB (all specs met) but if drivers disable it because they don't trust it, you've failed validation.
Both are required for success.
PPT Content:
AUTOMOTIVE EXAMPLE: AEB VERIFICATION vs VALIDATION VERIFICATION (Meets Specs): ✓ Activation threshold: TTC < 1.5s, speed > 40 km/h ✓ Brake deceleration: 6 m/s² ± 0.5 m/s² ✓ CAN timing: 10ms message period ✓ Response time: < 150ms VALIDATION (Meets Needs): ✓ Prevents crashes in real traffic? ✓ Drivers trust interventions? ✓ Works in rain/fog/night? ✓ Reduces fleet collision rates? **Success = Verification AND Validation** **Failure mode:** Perfect specs, but users disable feature

## Slide 12: When to Verify vs Validate
When do we do verification vs validation?
VERIFICATION: Throughout development
Requirements phase: Verify requirements are complete, consistent
Design phase: Verify design implements requirements
Implementation: Verify code implements design
Integration: Verify interfaces work correctly
System test: Verify all requirements met
Continuous activity at every stage.
VALIDATION: At key milestones
Concept validation: Does concept meet needs? (Before detailed design)
Design validation: Will design solve problem? (Before implementation)
System validation: Does system work in real environment? (Before production)
Operational validation: Meets needs in service? (After deployment)
Gate-based activity at decision points.
In practice: Verification is more frequent, validation is more expensive and time-consuming.
Automotive standard (ISO 26262): Validation required at phase transitions.
PPT Content:
WHEN TO VERIFY vs VALIDATE VERIFICATION: Throughout Development • Requirements → Design → Code → Integration → Test • Continuous activity • Frequent, incremental • Lower cost per activity VALIDATION: At Key Milestones • Concept → Design → System → Operations • Gate-based activity • Infrequent, comprehensive • Higher cost per activity **ISO 26262 Requirement:** Validation at each phase transition **Practical Rule:** Verify often (daily/weekly) Validate at gates (monthly/quarterly)

## Slide 13: Integration Strategy Options
Now let's address the integration challenge from Slide 7. There are four main integration strategies:
1. Big Bang Integration — Integrate all components at once
Pros: Fast if it works
Cons: Debugging nightmare, high risk
When to use: Simple systems (<5 components), well-tested components
2. Bottom-Up Integration — Start with lowest-level components, build up
Pros: Early hardware testing, realistic performance
Cons: No system-level view until late, requires test drivers
When to use: Hardware-dependent systems
3. Top-Down Integration — Start with high-level control, stub lower components
Pros: Early system-level behavior, validates architecture
Cons: Stubs may not represent real performance
When to use: Software-intensive systems, architecture validation
4. Sandwich/Hybrid Integration — Top-down for control logic, bottom-up for hardware
Pros: Best of both worlds
Cons: More complex to manage
When to use: Complex automotive systems (most cases)
Automotive standard: Most OEMs use sandwich with HIL testing.
PPT Content:
INTEGRATION STRATEGIES: FOUR OPTIONS 1. Big Bang • All at once • Fast but risky 2. Bottom-Up • Start with hardware • Realistic performance 3. Top-Down • Start with control logic • Early system validation 4. Sandwich/Hybrid ← AUTOMOTIVE STANDARD • Combination approach • Best for complex systems **Selection criteria:** System complexity, hardware dependencies, schedule

## Slide 14: Bottom-Up Integration Example (LKA)
Let's see bottom-up integration for our LKA system:
Integration Sequence:
Step 1: Test camera hardware standalone
Verify camera captures images
Verify CAN interface works
Test with known patterns
Step 2: Integrate camera + image processing ECU
Verify image data transfer
Check processing latency
Test with real road images
Step 3: Add lane detection algorithm
Verify lane line detection accuracy
Check processing time < 50ms
Test various lighting conditions
Step 4: Integrate control ECU
Verify control calculations
Test steering torque commands
Validate safety limits
Step 5: Add steering actuator
Verify actual steering response
Measure end-to-end latency
Test force limits
Steps 6-8: Add CAN bus, HMI, driver monitoring
Benefit: At each step, only ONE new component. If something breaks, you know what caused it.
Drawback: Don't see complete system behavior until Step 8.
PPT Content:
BOTTOM-UP INTEGRATION: LKA EXAMPLE Step 1: Camera (standalone) ↓ Step 2: + Image Processing ECU ↓ Step 3: + Lane Detection Algorithm ↓ Step 4: + Control ECU ↓ Step 5: + Steering Actuator ↓ Step 6-8: + CAN, HMI, Driver Monitor At each step: ✓ Test ONE new component ✓ Easy to isolate failures ✗ No system-level view until late **Best for: Hardware-intensive systems**

## Slide 15: Top-Down Integration with Stubs
Top-down integration works differently. We start with the system-level controller and 'stub' the components:
Step 1: Implement main control ECU with ALL components stubbed
Stub camera: Returns simulated lane lines
Stub actuator: Logs steering commands (doesn't move)
Validates overall control logic and state machine
Step 2: Replace camera stub with real camera
Now using real image data
Control logic unchanged
Validates camera integration
Step 3: Replace actuator stub with real actuator
Now producing real steering
Validates safety-critical path
Steps 4-8: Replace remaining stubs one by one
Benefit: See system-level behavior from Day 1. Validates architecture early.
Drawback: Stubs may not capture real timing, performance issues. Can give false confidence.
Automotive use case: Software-in-the-Loop (SIL) testing uses stubbed sensors/actuators extensively.
PPT Content:
TOP-DOWN INTEGRATION: WITH STUBS Step 1: Control ECU + ALL STUBS • Stub camera → simulated data • Stub actuator → log commands • Validate control logic ↓ Step 2: Replace camera stub → REAL camera ↓ Step 3: Replace actuator stub → REAL actuator ↓ Steps 4-8: Replace remaining stubs Benefits: ✓ Early system-level validation ✓ Architecture validation from Day 1 ✗ Stubs may not capture real performance **Best for: Software-intensive systems, early integration**

## Slide 16: Sandwich Integration (Automotive Standard)
In practice, automotive systems use sandwich integration:
Top layer (Top-Down):
System controller
State machine
High-level decision logic
Validated early with SIL (Software-in-the-Loop)
Bottom layer (Bottom-Up):
Sensors (camera, radar, lidar)
Actuators (steering, braking)
CAN communication
Validated early with HIL (Hardware-in-the-Loop)
Middle layer (Last):
Sensor fusion algorithms
Control algorithms
Integrated after top and bottom layers proven
Timeline for LKA:
Weeks 1-4: Top layer SIL + Bottom layer HIL (parallel)
Weeks 5-8: Integrate middle layer algorithms
Weeks 9-12: Full system integration and validation
Why this works:
Reduces integration risk
Parallel development (software + hardware teams)
Early detection of interface issues
Industry standard approach (Tesla, BMW, Toyota all use variations)
This is what you'll use in practice.
PPT Content:
SANDWICH INTEGRATION: AUTOMOTIVE STANDARD TOP LAYER (Top-Down): System controller, state machine Validated: SIL (Software-in-Loop) MIDDLE LAYER (Last): Algorithms, sensor fusion Integrated: After top/bottom proven BOTTOM LAYER (Bottom-Up): Sensors, actuators, CAN Validated: HIL (Hardware-in-Loop) Timeline: Weeks 1-4: Top SIL + Bottom HIL (parallel) Weeks 5-8: Middle layer integration Weeks 9-12: Full system validation **Industry standard for ADAS/autonomous systems**

## Slide 17: The Four Verification Methods
ISO/IEC 15288 and IEEE 15288 define FOUR verification methods. Every requirement must specify which method(s) will be used:
1. TEST (Most common) — Stimulate system with inputs, measure outputs
Pros: High confidence, finds integration issues
Cons: Expensive, time-consuming
Examples: Road testing, HIL testing, EMC testing
Use when: Safety-critical functions, customer-facing features
2. ANALYSIS (Mathematical/simulation) — Mathematical proof, simulation, modeling
Pros: Early feedback, explores parameter space
Cons: Only as good as model assumptions
Examples: Thermal analysis, stress analysis, timing analysis, simulation
Use when: Physical properties, performance prediction
3. INSPECTION (Visual/manual) — Visual examination, code review, document review
Pros: Low cost, simple
Cons: Subjective, may miss issues
Examples: Code review, design review, drawing inspection
Use when: Qualitative requirements, documentation
4. DEMONSTRATION (Show it works) — Demonstrate functionality in realistic scenario
Pros: Convincing, user-focused
Cons: May not cover edge cases
Examples: Customer demo, pilot program, trade show
Use when: User acceptance, stakeholder confidence
Automotive: Typically 70% test, 20% analysis, 8% inspection, 2% demonstration.
PPT Content:
FOUR VERIFICATION METHODS (ISO/IEC 15288) 1. TEST • Stimulate inputs, measure outputs • High confidence, expensive • Example: Road testing, HIL 2. ANALYSIS • Mathematical/simulation • Early feedback, model-dependent • Example: Thermal, timing, stress 3. INSPECTION • Visual/manual examination • Low cost, subjective • Example: Code review, drawing check 4. DEMONSTRATION • Show it works in scenario • Convincing, may miss edge cases • Example: Customer demo **Automotive typical: 70% test, 20% analysis, 8% inspect, 2% demo**

## Slide 18: Verification Method Selection (AEB Example)
Let's see how to select verification methods for AEB requirements:
Requirement AEB-FR-001: 'System shall detect vehicles ahead within 150m range'
Verification method: TEST
Rationale: Safety-critical, must prove in real conditions
Test: Place target vehicle at 140m, 150m, 160m. Verify detection.
Requirement AEB-NFR-002: 'System response time shall be < 150ms from detection to brake command'
Verification method: ANALYSIS + TEST
Rationale: Timing analysis can predict, test confirms
Analysis: WCET analysis of software timing
Test: Measure actual response time with oscilloscope
Requirement AEB-IF-005: 'CAN message format shall comply with J1939 standard'
Verification method: INSPECTION + TEST
Rationale: Standards compliance check + functional test
Inspection: Review CAN database file
Test: CAN bus analyzer capture and decode
Requirement AEB-SAF-010: 'System shall meet ISO 26262 ASIL-B'
Verification method: INSPECTION + DEMONSTRATION
Rationale: Process compliance + assessment
Inspection: Review safety artifacts (FMEA, FTA, safety case)
Demonstration: Present safety case to assessor
Notice: Most requirements use MULTIPLE methods for higher confidence.
PPT Content:
VERIFICATION METHOD SELECTION: AEB EXAMPLE Req ID | Requirement | Method(s) ----------------|--------------------------------|------------------ AEB-FR-001 | Detect vehicles within 150m | TEST AEB-NFR-002 | Response time < 150ms | ANALYSIS + TEST AEB-IF-005 | CAN format per J1939 | INSPECTION + TEST AEB-SAF-010 | Meet ISO 26262 ASIL-B | INSPECTION + DEMO **Key Insight:** Most requirements need MULTIPLE methods **ISO 26262 guidance:** Safety requirements require at minimum: • Analysis (FMEA/FTA) • Test (functional + fault injection) • Inspection (safety case review)

## Slide 19: Verification Traceability Matrix
Every requirement must be traceable to its verification. This is the Requirements Verification Traceability Matrix (RVTM):
RVTM Structure: — Requirement ID
Requirement text
Verification method(s)
Test case ID / Analysis ID / Inspection ID
Verification status
Pass/Fail result
Evidence (test report reference)
Example RVTM for AEB (5 requirements shown):
| Req ID | Requirement | Method | Test ID | Status | Result | Evidence |
|--------|-------------|--------|---------|--------|--------|----------|
| AEB-FR-001 | Detect vehicle 150m | Test | TC-AEB-001 | Complete | Pass | TR-2024-01 |
| AEB-FR-002 | Brake if TTC<1.5s | Test | TC-AEB-002 | Complete | Pass | TR-2024-02 |
| AEB-NFR-001 | Response <150ms | Analysis+Test | AN-001, TC-003 | Complete | Pass | AR-2024-01 |
| AEB-IF-001 | CAN per J1939 | Inspect+Test | IN-001, TC-004 | Complete | Pass | IR-2024-01 |
| AEB-SAF-001 | ASIL-B | Inspect+Demo | IN-002, DM-001 | In Progress | - | Pending |
Key benefits:
Every requirement has verification plan
Traceability from requirement → test → evidence
Status tracking for program management
Compliance evidence for assessors (ISO 26262, Automotive SPICE)
Tools: IBM DOORS, Jama Connect, Polarion, Excel (for small projects)
This matrix is your V&V roadmap.
PPT Content:
REQUIREMENTS VERIFICATION TRACEABILITY MATRIX (RVTM) Columns: • Requirement ID • Requirement Text • Verification Method(s) • Test/Analysis/Inspection ID • Status (Not Started / In Progress / Complete) • Result (Pass / Fail / Pending) • Evidence Reference Benefits: ✓ Every requirement has verification plan ✓ Traceability: Req → Test → Evidence ✓ Status tracking ✓ Compliance documentation **RVTM = Your V&V roadmap and proof of completion** Tools: DOORS, Jama, Polarion, Excel

## Slide 20: The Four Testing Levels
Testing happens at FOUR levels, corresponding to the V-Model:
Level 1: UNIT TESTING (Bottom of V)
Test: Individual software modules, hardware components
Scope: Single function, single file, single component
Who: Developers
Coverage: 80-100% code coverage target
Examples: Test lane detection algorithm function, test CAN driver module
Level 2: INTEGRATION TESTING (Lower-middle of V)
Test: Interfaces between components
Scope: 2-5 components interacting
Who: Integration engineers
Coverage: All interface scenarios
Examples: Camera + image processing, Control ECU + actuator
Level 3: SYSTEM TESTING (Upper-middle of V)
Test: Complete system against requirements
Scope: All components integrated
Who: Test engineers
Coverage: All system requirements
Examples: Full LKA system on test bench, HIL testing
Level 4: ACCEPTANCE TESTING (Top of V)
Test: System in operational environment
Scope: Real-world usage scenarios
Who: Validation engineers + customers
Coverage: User needs and expectations
Examples: Road testing, beta fleet, customer validation
Key: Each level builds on the previous. Don't skip levels.
PPT Content:
FOUR TESTING LEVELS (V-Model Alignment) Level 4: ACCEPTANCE TESTING ← Validates needs Real-world scenarios Who: Validation + Customer Level 3: SYSTEM TESTING ← Verifies requirements Complete system Who: Test engineers Level 2: INTEGRATION TESTING ← Verifies interfaces Component interactions Who: Integration engineers Level 1: UNIT TESTING ← Verifies implementation Individual modules Who: Developers **Test Pyramid:** More unit tests, fewer acceptance tests

## Slide 21: Unit Testing - Software and Hardware
Unit testing for automotive systems includes BOTH software and hardware:
SOFTWARE UNIT TESTING:
Example: Testing `calculateSteeringTorque()` function in LKA controller
Test cases: — TC-UT-001: Lane offset = 0.0m → Torque = 0.0 Nm (centered)
TC-UT-002: Lane offset = 0.3m right → Torque = +2.5 Nm (correct left)
TC-UT-003: Lane offset = 0.3m left → Torque = -2.5 Nm (correct right)
TC-UT-004: Lane offset = 1.0m → Torque clamped to ±8.0 Nm (safety limit)
TC-UT-005: No lane detected → Torque = 0.0 Nm (safe fallback)
Tool: Unit test framework (Google Test, CUnit, VectorCAST)
Coverage: Statement coverage 100%, branch coverage 95%+
HARDWARE UNIT TESTING:
Example: Testing camera module standalone
Test cases: — TC-HW-001: Power supply 12V ± 1V → Camera outputs video
TC-HW-002: CAN bus 500 kbps → Camera sends frame data
TC-HW-003: Temperature -40°C to +85°C → Camera operates
TC-HW-004: Lens obstruction → Camera reports fault code
Tool: Bench test setup, oscilloscope, CAN analyzer
Automotive standard (ASPICE): Unit testing is a MANDATORY practice.
PPT Content:
UNIT TESTING: SOFTWARE + HARDWARE SOFTWARE UNIT TEST: Function: calculateSteeringTorque() Test Cases: • Lane centered → 0 Nm • 0.3m offset → ±2.5 Nm • 1.0m offset → clamp to ±8 Nm • No lane → 0 Nm (safe) Coverage: 100% statement, 95%+ branch HARDWARE UNIT TEST: Component: Camera module Test Cases: • Power 12V±1V → video output • CAN 500kbps → frame data • Temp -40 to +85°C → operates • Lens blocked → fault code **ASPICE Requirement: Unit testing mandatory**

## Slide 22: Integration Testing - Interface Focus
Integration testing focuses on INTERFACES between components. This is where many automotive defects hide.
Integration Test Example: Camera → Image Processing ECU
Test Scenario 1: Data Transfer — TC-IT-001: Camera sends 1280x720 frame at 30 fps
Verify: ECU receives all frames, no data loss
Verify: Frame timestamps correct
Verify: No CAN bus overrun errors
Test Scenario 2: Timing — TC-IT-002: Measure end-to-end latency camera → ECU
Verify: Latency < 50ms (requirement)
Verify: Jitter < 5ms
Test Scenario 3: Error Handling — TC-IT-003: Camera sends corrupted frame
Verify: ECU detects checksum error
Verify: ECU requests retransmission
Verify: ECU continues operation (graceful degradation)
Test Scenario 4: Fault Injection — TC-IT-004: Disconnect camera CAN cable
Verify: ECU detects timeout (within 100ms)
Verify: ECU sets DTC (Diagnostic Trouble Code)
Verify: ECU reports fault to vehicle supervisor
Why integration testing matters: — 40% of automotive defects found at integration level
Interface specifications often ambiguous
Timing issues only appear when components interact
Tool: HIL (Hardware-in-the-Loop) simulators (dSPACE, Vector, National Instruments)
PPT Content:
INTEGRATION TESTING: INTERFACE FOCUS Test: Camera → Image Processing ECU Scenarios: 1. Data Transfer • 1280x720 @ 30fps • Verify: No frame loss, correct timing 2. Latency • Measure end-to-end < 50ms • Jitter < 5ms 3. Error Handling • Corrupted frame → detect & recover 4. Fault Injection • Disconnect → timeout, DTC, report **40% of automotive defects found at integration level** Tools: HIL (dSPACE, Vector, NI)

## Slide 23: System and Acceptance Testing
The top two testing levels validate the complete system:
SYSTEM TESTING (Level 3)
Purpose: Verify ALL system requirements in controlled environment
LKA System Test Examples:
TC-ST-001: Verify LKA keeps vehicle centered in lane on straight road
TC-ST-002: Verify LKA handles curves (radius > 250m)
TC-ST-003: Verify LKA disengages if driver overrides steering
TC-ST-004: Verify HMI warnings display correctly
TC-ST-005: Verify system works 10°C to 40°C
TC-ST-020: Verify emergency scenarios (brake during LKA, sudden lane change)
Environment: Test track, proving ground, HIL simulator
Coverage: 100% of system requirements
Tools: Test vehicles, data logging, automated test scripts
ACCEPTANCE TESTING (Level 4)
Purpose: Validate system meets user needs in REAL operational environment
LKA Acceptance Test Examples:
Field testing: 100,000 km on public roads
Weather conditions: Rain, snow, fog, night
Road types: Highway, city, rural, construction zones
Driver variability: Different driving styles
User feedback: Surveys, interviews, usability studies
Environment: Real roads, real traffic, real customers
Coverage: Operational scenarios and stakeholder needs
Duration: Months (beta fleets, pilot programs)
Acceptance testing answers: 'Does this solve the customer's problem?'
This is validation, not just verification.
PPT Content:
SYSTEM TESTING (Level 3): Verify Requirements Environment: Controlled (test track, HIL) Coverage: 100% system requirements Examples: • LKA keeps centered in lane • Handles curves, disengages on override • HMI warnings correct • Temperature 10-40°C Tools: Test vehicles, data logging, automation ACCEPTANCE TESTING (Level 4): Validate Needs Environment: Real-world (public roads) Coverage: Operational scenarios Examples: • 100,000 km field testing • Rain, snow, fog, night • Highway, city, rural • User feedback surveys Duration: Months (beta fleets) **Acceptance = Does it solve the customer problem?**

## Slide 24: V&V Plan Structure
Every automotive system needs a comprehensive V&V Plan. Here's the standard structure:
Section 1: Introduction — System overview
V&V objectives
Scope and boundaries
References (requirements, standards)
Section 2: V&V Strategy — Verification approach (methods: test, analysis, inspection, demo)
Validation approach (field testing, user studies)
Integration strategy (big bang / bottom-up / top-down / sandwich)
Test levels (unit / integration / system / acceptance)
Section 3: Test Environment — Test facilities (track, lab, HIL)
Test equipment (sensors, data acquisition, CAN tools)
Test vehicles
Environmental conditions
Section 4: Test Cases and Procedures — Requirements Verification Traceability Matrix (RVTM)
Detailed test procedures for each test case
Pass/fail criteria
Expected results
Section 5: Test Schedule — Timeline for each test level
Dependencies and sequencing
Resource allocation
Milestones
Section 6: Roles and Responsibilities — Test manager, test engineers, developers
Approval authorities
Escalation procedures
Section 7: Risks and Mitigation — Test environment unavailability
Schedule delays
Resource constraints
Contingency plans
Section 8: Reporting and Documentation — Test reports format
Defect tracking process
Configuration management
Compliance evidence
Automotive standards: ISO 26262 mandates V&V plan for ASIL B+ systems.
PPT Content:
V&V PLAN STRUCTURE (ISO 26262 Compliant) 1. Introduction (system, objectives, scope) 2. V&V Strategy (methods, levels, integration) 3. Test Environment (facilities, equipment, vehicles) 4. Test Cases & Procedures (RVTM, detailed tests) 5. Test Schedule (timeline, dependencies, milestones) 6. Roles & Responsibilities (team, approvals) 7. Risks & Mitigation (environment, schedule, resources) 8. Reporting & Documentation (reports, defects, evidence) **ISO 26262:** V&V plan mandatory for ASIL B+ **Typical size:** 50-200 pages for ADAS system **Tools:** DOORS, Jama (requirements trace), JIRA (defect tracking)

## Slide 25: Test Coverage - How Much Is Enough?
One of the most common questions: 'How much testing is enough?' Let's look at coverage metrics:
SOFTWARE CODE COVERAGE:
Statement Coverage: Every line of code executed?
Target: 100% for safety-critical (ISO 26262 ASIL C/D)
Target: 80-90% for ASIL A/B
Tool: VectorCAST, LDRA, Cantata
Branch Coverage: Every decision (if/else) tested both ways?
Target: 95%+ for safety-critical
More rigorous than statement coverage
Path Coverage: Every execution path tested?
Target: Infeasible for large systems (combinatorial explosion)
Focus on critical paths
REQUIREMENTS COVERAGE:
Functional Coverage: Every requirement has passing test?
Target: 100% (non-negotiable)
Tracked in RVTM
Scenario Coverage: Operational scenarios tested?
Target: Cover normal, boundary, exceptional cases
Example AEB: 30 km/h, 50 km/h, 80 km/h, 120 km/h (speed range)
Example AEB: Dry, wet, snow, ice (surface conditions)
INTERFACE COVERAGE:
Message Coverage: Every CAN message sent/received?
Target: 100% of defined messages
Tool: CANoe, CANalyzer
Fault Coverage: Error scenarios tested?
Target: All single-point failures
Example: Sensor failures, communication timeouts, invalid data
Automotive Standard (ISO 26262):
ASIL A: 80% statement + branch coverage
ASIL B: 90% statement + branch coverage
ASIL C: 95% statement + branch + MC/DC coverage
ASIL D: 100% statement + branch + MC/DC coverage
Reality: 100% coverage doesn't guarantee zero defects. But it's a necessary baseline.
PPT Content:
TEST COVERAGE: HOW MUCH IS ENOUGH? CODE COVERAGE: • Statement: Every line executed • Branch: Every decision both ways • Path: Every execution path ISO 26262 Targets: ASIL A: 80% | ASIL B: 90% | ASIL C: 95% | ASIL D: 100% REQUIREMENTS COVERAGE: • Functional: Every requirement tested → 100% • Scenario: Normal + boundary + exceptional INTERFACE COVERAGE: • Message: Every CAN message → 100% • Fault: All single-point failures **100% coverage ≠ zero defects, but it's the baseline** Tools: VectorCAST, LDRA, CANoe

## Slide 26: Tesla Model S Autopilot Crash - V&V Failure Analysis
Let's examine a tragic V&V failure: the 2016 Tesla Model S Autopilot crash in Florida.
Incident Overview: — May 7, 2016: Model S in Autopilot mode
White tractor-trailer crossing highway
Autopilot failed to detect trailer
Driver failed to take control
Fatal collision
V&V Failure Analysis:
1. Incomplete Scenario Coverage — What was tested: Standard vehicle detection (cars, trucks on same lane)
What wasn't tested: Perpendicular white vehicles against bright sky
Gap: Cross-traffic scenarios not in test suite
Lesson: Validation must include operational context, not just requirements
2. Sensor Fusion Validation Inadequate — Camera: Detected trailer but classified as overhead sign (white + high)
Radar: Detected metal but classified as overhead structure
Fusion logic: Both sensors agreed 'not a vehicle' → ignored
Gap: No validation of conflicting sensor interpretations
Lesson: Integration testing must stress-test fusion logic with ambiguous inputs
3. Human Factors Validation Missing — System name 'Autopilot' implied full autonomy
Users treated it as self-driving (validation gap)
No adequate driver monitoring
Gap: Validation of human-system interaction inadequate
Lesson: Validate system in realistic usage, not just ideal usage
4. Edge Case Testing Insufficient — White vehicle + bright sky = unusual scenario
But not impossible or unforeseeable
Should have been in acceptance test scenarios
Gap: Edge case identification incomplete
Lesson: Validation must explore 'rare but possible' scenarios
NTSB Findings: — 'Tesla's validation process did not account for driver misuse scenarios'
'System tested primarily in highway scenarios with conventional vehicles'
'Inadequate testing of perception system in unusual lighting conditions'
What should have been tested (but wasn't):
Cross-traffic scenarios
White vehicles in high-contrast lighting
Driver monitoring effectiveness
Realistic driver behavior (not just attentive drivers)
Result: Tesla added cross-traffic detection, improved driver monitoring, clarified Autopilot limitations.
PPT Content:
CASE STUDY: 2016 TESLA MODEL S AUTOPILOT CRASH Incident: Autopilot failed to detect white trailer crossing highway V&V FAILURES IDENTIFIED: 1. Incomplete Scenario Coverage ✗ Cross-traffic not tested Lesson: Validate operational context 2. Sensor Fusion Validation Inadequate ✗ Ambiguous input cases not tested Lesson: Stress-test fusion logic 3. Human Factors Validation Missing ✗ Realistic usage not validated Lesson: Test actual user behavior 4. Edge Case Testing Insufficient ✗ Rare scenarios not covered Lesson: Explore 'possible but unusual' **NTSB: "Validation did not account for real usage scenarios"** Changes: Added cross-traffic detection, driver monitoring

## Slide 27: V&V Best Practices Summary
Let's consolidate the best practices for automotive V&V:
Planning Phase:
✓ Create V&V plan early (during requirements phase)
✓ Select verification methods for each requirement
✓ Build Requirements Verification Traceability Matrix (RVTM)
✓ Define test coverage targets (ISO 26262 compliance)
✓ Plan integration strategy (sandwich recommended)
Execution Phase:
✓ Start testing early (unit tests during development)
✓ Test at all four levels (unit → integration → system → acceptance)
✓ Use multiple verification methods (test + analysis + inspection)
✓ Automate regression testing
✓ Document evidence for every test
Quality Phase:
✓ Achieve code coverage targets (80-100% per ASIL)
✓ Ensure 100% requirements coverage
✓ Test edge cases and fault scenarios
✓ Validate human-system interaction
✓ Conduct real-world field testing
Documentation Phase:
✓ Maintain bidirectional traceability
✓ Generate test reports with pass/fail evidence
✓ Track and close all defects
✓ Create safety case (ISO 26262)
✓ Archive configuration and test data
Continuous Improvement:
✓ Analyze field failures
✓ Update test cases based on field data
✓ Improve V&V process each iteration
✓ Share lessons learned across projects
Follow these practices, and your V&V will be robust.
PPT Content:
V&V BEST PRACTICES CHECKLIST PLANNING: ✓ V&V plan early (requirements phase) ✓ Verification methods per requirement ✓ Build RVTM ✓ Define coverage targets (ISO 26262) ✓ Integration strategy (sandwich) EXECUTION: ✓ Test early (unit tests in development) ✓ All four levels (unit → accept) ✓ Multiple methods (test + analysis) ✓ Automate regression ✓ Document evidence QUALITY: ✓ Code coverage (80-100%) ✓ 100% requirements coverage ✓ Edge cases + faults ✓ Human factors validation ✓ Real-world field testing DOCUMENTATION: ✓ Bidirectional traceability ✓ Test reports ✓ Defect closure ✓ Safety case ✓ Archive data

## Slide 28: Connection to Remaining Sessions and Mid-Semester Review
Session 8 completes our first half. Let's connect everything and preview what's ahead:
Sessions 1-8 Completed:
Module 1: Foundations (Sessions 1-4)
Session 1: Why SE matters (failures)
Session 2: SE fundamentals (ISO/IEC 15288, V-Model)
Session 3: Traditional vs MBSE
Session 4: Requirements Engineering
Module 2: Design & Analysis (Sessions 5-8)
Session 5: System Architecture
Session 6: Case Study 1 (Boeing 737 MAX)
Session 7: Functional Analysis
Session 8: Integration & V&V ← TODAY
You now know:
How to define systems (requirements)
How to design systems (architecture)
How to analyze systems (functional decomposition)
How to verify and validate systems (V&V)
This is the core SE lifecycle.
Sessions 9-16 Ahead:
Module 3: Management (Sessions 9-12)
Session 9: Project & Risk Management
Session 10: Decision & Quality Management
Session 11: Agreement & Infrastructure Management
Session 12: Specialty Engineering (Safety & Security)
Module 4: Lifecycle & Trends (Sessions 13-16)
Session 13: Life Cycle Cost (LCC) & TCO
Session 14: Case Study 2
Session 15: Technical Management & Enabling Processes
Session 16: Emerging Trends in SE
Coming up: Management processes that enable successful SE execution.
Mid-semester exam covers Sessions 1-8. Use this session as your integration point.
PPT Content:
MID-SEMESTER CHECKPOINT: SESSIONS 1-8 COMPLETE MODULE 1: Foundations (Sessions 1-4) ✓ Why SE matters ✓ SE fundamentals ✓ Traditional vs MBSE ✓ Requirements engineering MODULE 2: Design & Analysis (Sessions 5-8) ✓ System architecture ✓ Case study 1 ✓ Functional analysis ✓ Integration & V&V ← TODAY **Core SE Lifecycle Complete** AHEAD: Modules 3-4 (Sessions 9-16) • Management (project, risk, quality) • Lifecycle cost • Emerging trends **Mid-semester exam: Sessions 1-8**

## Slide 29: Key Takeaways and Practice Exercise
Let's lock in the key takeaways from Session 8:
Key Takeaway 1: Verification asks 'Did we build it right?' (meets specs), Validation asks 'Did we build the right thing?' (meets needs). Both required.
Key Takeaway 2: Integration strategy matters. Use sandwich integration (top-down + bottom-up) for automotive systems. Avoid big bang.
Key Takeaway 3: Four verification methods (test, analysis, inspection, demonstration). Use multiple methods for safety-critical requirements.
Key Takeaway 4: Test at four levels (unit, integration, system, acceptance). Each level serves a purpose. Don't skip levels.
Key Takeaway 5: Coverage is necessary but not sufficient. Achieve 100% requirements coverage and ISO 26262 code coverage targets.
Key Takeaway 6: Bidirectional traceability from need → requirement → design → code → test → evidence is your proof.
Key Takeaway 7: Validation must include edge cases, human factors, and real-world scenarios. Simulator alone is insufficient.
PRACTICE EXERCISE: Develop V&V Plan for Adaptive Cruise Control (ACC)
Assignment:
Create a 5-8 page V&V plan for an Adaptive Cruise Control system covering:
V&V Strategy (integration approach, verification methods)
Test Levels (unit, integration, system, acceptance examples)
Requirements Verification Traceability Matrix (RVTM) for 10 ACC requirements
Test Coverage Plan (code, requirements, scenarios)
Test Schedule (timeline for 12-week V&V program)
Deliverables:
V&V Plan document (follow structure from Slide 23)
RVTM with 10 requirements mapped to test cases
Integration test sequence diagram (show order of component integration)
Due: One week before mid-semester exam
Grading:
V&V strategy completeness (30%)
RVTM quality (30%)
Test coverage plan (20%)
Integration sequence (10%)
Professional formatting (10%)
This exercise prepares you for the mid-semester exam and real-world V&V planning.
PPT Content:
SESSION 8 KEY TAKEAWAYS 1. Verification (right) vs Validation (right thing) → Both needed 2. Sandwich integration (top + bottom) for automotive 3. Four verification methods → Use multiple for safety 4. Four test levels (unit → accept) → Don't skip 5. 100% requirements coverage + ISO 26262 targets 6. Bidirectional traceability = proof 7. Validate edge cases + human factors + real-world PRACTICE EXERCISE: ACC V&V Plan Create 5-8 page V&V plan covering: • V&V strategy (integration, methods) • Test levels (examples for each) • RVTM (10 requirements) • Coverage plan (code, req, scenarios) • Test schedule (12-week timeline) Due: 1 week before mid-semester Grading: Strategy 30%, RVTM 30%, Coverage 20% **Prepares you for exam and real-world V&V**

## Slide 30: 📝 INSTRUCTOR NOTES
Additional Resources
Approach: Process-Focused/Technical
This session requires balancing theoretical V&V concepts with practical automotive application. The pedagogy emphasizes:
Clear Distinctions: Verification vs validation is foundational. Use multiple examples to cement this.
Practical Integration: Sandwich integration is industry standard. Show why through LKA example.
Real Consequences: Use Tesla, Toyota cases to show V&V failures have real costs.
Comprehensive Coverage: Four methods × four levels = complete V&V framework.
Traceability Emphasis: This is what separates amateur from professional V&V.
Mid-Semester Integration: This session serves as the capstone for Sessions 1-7. Explicitly connect V&V back to requirements (S4), architecture (S5), and functional analysis (S7).
Challenge 1: "Isn't verification just testing?
Response: No. Testing is ONE verification method. Analysis (simulation, math), inspection (review), and demonstration are equally valid. Show examples where testing is insufficient (timing analysis, thermal analysis).
Challenge 2: "Why is integration so complicated? Just connect everything.
Response: Use the LKA debugging nightmare example (Slide 8). When 8 components have 28 interactions, big bang fails. Show how sandwich systematically reduces debug complexity.
Challenge 3: "100% code coverage means zero bugs, right?
Response: No. Coverage metrics tell you what you tested, not what you didn't test. Therac-25 example: all paths tested, but race condition timing not tested. Coverage is necessary, not sufficient.
Challenge 4: "Validation seems subjective. How do we measure it?
Response: Validation IS more subjective than verification, but still measurable: user surveys, field trial data, incident rates, customer acceptance criteria. Show AEB example: measure actual collision reduction in fleet.
Critical timing considerations:
Part 3 (Verification Methods) can run long if you demo tools. Limit tool demos to 2 minutes each, focus on concepts.
Part 4 (Testing Levels) is the most detailed. Budget full 12 minutes. Students need concrete examples at each level.
Case Study (Slide 26-27) can generate extensive discussion. Set 8-minute timer, defer detailed debate to case study session.
Reserve 5 minutes at end for Q&A on mid-semester exam scope.
If running short on time:
Condensed: Combine Slides 12-15 into high-level integration overview (5 min instead of 12 min)
Skip: Slide 18 (RVTM details) can be assigned as reading
If extra time:
Tool demonstration: Show actual DOORS/Jama traceability or CANoe integration test
V&V plan review: Walk through real automotive V&V plan (if available)
Extended case discussion: Tesla Autopilot regulatory response
Slide 7: Poll students - "Who would choose big bang? Who incremental?" Show of hands before revealing answer.
Slide 10: Interactive question - "Is AEB verification or validation?" Have students argue both sides.
Slide 16: Quick exercise - "For this requirement (provide example), which verification method?" Students vote.
Slide 22: "What scenarios should we test for LKA acceptance?" Brainstorm as group, capture on whiteboard.
Slide 26: "What V&V would have prevented Tesla crash?" Small group discussion (3 minutes).
Before class:
[ ] Load Tesla Autopilot crash video (2-3 minute clip)
[ ] Prepare V-Model diagram animation showing bidirectional flow
[ ] Print sample RVTM for handout reference
[ ] Load CANoe or similar tool for optional integration test demo
[ ] Prepare ACC V&V plan template for exercise
Optional materials:
Real automotive V&V plan (redacted) for show-and-tell
ISO 26262 Part 4 (V&V requirements) excerpt
Test reports from automotive projects (sanitized)
Formative Assessment (During Session):
Quick check after Slide 11: "Give me one verification example and one validation example for your car's ABS
Quick check after Slide 19: "At which test level would you find this defect?" (provide scenario)
Quick check after Slide 25: "If requirement SR-045 changes, what must you update?" (test traceability)
Summative Assessment (Exercise):
ACC V&V Plan development (detailed in Slide 30)
Graded against professional V&V plan standards
Provides mid-semester exam preparation
Mid-Semester Exam Coverage:
Session 8 contributes 15-20% of mid-semester exam questions:
Verification vs validation distinction (definition question)
Integration strategy selection (scenario question)
Verification method selection for requirements (application question)
Test level identification (case-based question)
RVTM interpretation (analysis question)
Students successfully understand Session 8 if they can:
Define verification and validation, giving automotive examples of each
Select appropriate integration strategy for a given system
Choose verification methods for different requirement types
Design test cases at all four test levels
Calculate test coverage and identify gaps
Create traceability matrix linking requirements to tests
Analyze V&V failures in case studies and propose improvements
Backward Links:
Session 2: V-Model right side connects to Session 2's V-Model introduction
Session 4: Requirements from Session 4 must have verification methods
Session 5: Architecture from Session 5 drives integration strategy
Session 7: Functions from Session 7 are verified at unit/integration levels
Forward Links:
Session 9: V&V risks are managed through risk management processes
Session 10: V&V is a key quality management activity
Session 12: Safety V&V (ISO 26262) is covered in specialty engineering
Session 14: Case Study 2 will apply V&V analysis to another failure
Standards:
ISO/IEC/IEEE 15288:2023 (Systems and software engineering - System life cycle processes)
ISO 26262:2018 Part 4 (Product development at the system level - V&V)
Automotive SPICE v3.1 (SWE.4: Software Unit Verification, SWE.5: Software Integration)
Tools:
VectorCAST (code coverage)
IBM DOORS / Jama Connect (requirements traceability)
CANoe / CANalyzer (integration testing)
dSPACE / ETAS (HIL testing)
Further Reading:
"Software Testing" by Ron Patton (Chapter 3: Test Levels)
"Systems Engineering Handbook" INCOSE (Chapter 7: Verification and Validation)
ISO 26262 Part 4 (full standard for automotive safety V&V)

## Slide 31: END OF SESSION 8 FRAMEWORK
Prepared for: Automotive Systems Engineering (AE ZG517 / AEL ZG517)
Session: 8 of 16
Status: Ready for PPT Development
Estimated PPT Slides: 28-30
Total Instructor Preparation Time: 3-4 hours