## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 10: Decision and Quality Management'

## Slide 2: Decision and Quality Management
Session 10 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 10. Today we tackle two interconnected disciplines that separate successful systems engineering from failed projects: Decision Management and Quality Management.
These aren't separate topics - they're two sides of the same coin. Good decisions lead to quality outcomes. Quality metrics inform better decisions.

## Slide 4: Connection to Previous Sessions
Let's connect where we've been:
Session 4: We learned to write requirements - but what if stakeholders want contradictory things? (Decision needed)
Session 5: We learned architecture - but how do we choose between competing designs? (Decision needed)
Session 8: We learned verification and validation - but how do we ensure quality throughout? (Quality management)
Session 9: We learned risk management - risks inform decisions about what to prioritize
Today's focus: How do we make systematic, defensible decisions? How do we ensure quality at every step?

## Slide 5: Why Decision and Quality Management Are Critical
Let me show you sobering data:
Decision-making failures: — 72% of major projects exceed budget due to poor early decisions (McKinsey)
Average cost of poor technical decision: $2.5M in automotive programs
40% of product recalls trace to decisions made under uncertainty without systematic analysis
Quality management impact: — Cost of quality (prevention + appraisal + failure) = 15-25% of total project cost
Cost to fix defects grows 10x at each lifecycle stage (requirements → design → test → production)
Toyota's quality culture saves estimated $1B+ annually compared to competitors
Key insight: You WILL face decisions with incomplete information, conflicting objectives, and high stakes. How you decide determines success or failure.

## Slide 6: Real-World Example - Boeing 737 MAX Decision Failure
Boeing 737 MAX: 346 deaths, $20B+ in losses, 20-month grounding. Let's analyze the decision failures:
Decision Point 1: Engine placement — Trade-off: Fuel efficiency vs flight characteristics
Decision made: Place larger engines forward and higher (efficiency priority)
Consequence: Changed aircraft pitch behavior
Decision Point 2: How to address pitch change — Options:
A) Redesign landing gear (expensive, time-consuming)
B) Software solution (MCAS system - cheap, fast)
Decision made: Option B (software fix)
Analysis used: Cost and schedule only - safety not weighted properly
Decision Point 3: Pilot training requirements — Trade-off: Safety (extensive training) vs marketability (no training difference from 737NG)
Decision made: Minimize training differences
Consequence: Pilots unaware of MCAS system
Quality management failure:
Single point of failure (one AoA sensor)
Inadequate testing of failure modes
No critical parameter monitoring for sensor disagreement
Root cause: Decisions optimized for cost/schedule without systematic multi-criteria analysis including safety. Quality gates failed to catch the gaps.
Today, I'll show you how to avoid these catastrophic decision failures.

## Slide 7: The Battery Selection Challenge
You're the systems engineer for a new electric vehicle. Your manager says:
'Select the battery technology for our new EV. Decision needed by Friday.'
You have three options:
Option A: Lithium Iron Phosphate (LFP) — Cost: $90/kWh (lowest)
Energy density: 160 Wh/kg (lowest)
Safety: Excellent (most stable chemistry)
Lifespan: 3,000+ cycles (longest)
Charging speed: Moderate
Cold weather: Poor performance below -10°C
Supply chain: China-dependent (90% production)
Option B: NMC (Nickel Manganese Cobalt) — Cost: $140/kWh (medium)
Energy density: 250 Wh/kg (highest)
Safety: Good (requires thermal management)
Lifespan: 1,500-2,000 cycles (medium)
Charging speed: Fast
Cold weather: Good performance
Supply chain: Cobalt sourcing concerns
Option C: Solid-State (Emerging) — Cost: $250/kWh (highest, projected to decrease)
Energy density: 400+ Wh/kg (future potential)
Safety: Excellent (non-flammable)
Lifespan: Unknown (new technology)
Charging speed: Very fast (potential)
Cold weather: Excellent (projected)
Supply chain: Limited production capacity
How do you decide? Each stakeholder wants something different:
Finance: Choose LFP (lowest cost)
Marketing: Choose solid-state (best specs for brochure)
Engineering: Choose NMC (proven, balanced)
Safety: Choose LFP or solid-state (safest)
Product planning: Depends on target market (range vs price)
This is exactly what systematic decision analysis solves.

## Slide 8: The Decision Analysis Process
Systematic decision-making follows a proven process. This is the foundation:
Step 1: Frame the decision — What exactly are we deciding?
What is the scope? (Battery chemistry only, or entire energy storage system?)
What is NOT being decided?
Example: 'Select battery chemistry for 75 kWh passenger EV with 400 km range target'
Step 2: Identify objectives — What do we want to achieve?
Fundamental objectives (ends) vs means objectives
Example objectives: Minimize cost, maximize safety, maximize range, ensure supply chain resilience
Step 3: Create alternatives — What are ALL viable options?
Don't eliminate prematurely
Include hybrid approaches
Example: Pure LFP, pure NMC, solid-state, LFP+NMC hybrid, defer decision (wait for solid-state maturity)
Step 4: Establish evaluation criteria — How will we measure each objective?
Must be measurable, objective where possible
Example: $/kWh (cost), Wh/kg (energy density), cycles to 80% capacity (lifespan)
Step 5: Evaluate alternatives — Score each alternative against each criterion
Use data, analysis, simulation, testing
Document assumptions
Step 6: Make decision — Apply decision method (we'll cover several)
Consider uncertainty and risk
Document rationale
Step 7: Implement and monitor — Execute decision
Track performance vs predictions
Be ready to adapt if conditions change
Key principle: The process is as important as the outcome. Traceable decisions that can be explained years later.

## Slide 9: Decision Types and Appropriate Methods
Not all decisions are equal. Different types need different approaches:
Type 1: Simple decisions (Low stakes, clear criteria) — Example: Which supplier for standard bolts?
Method: Simple comparison table, lowest cost with quality threshold
Time investment: Minutes to hours
Type 2: Complicated decisions (Multiple criteria, quantifiable) — Example: Battery chemistry selection
Method: Multi-criteria decision analysis (MCDA)
Time investment: Days to weeks
Type 3: Complex decisions (High uncertainty, many unknowns) — Example: Invest in hydrogen vs battery technology for 2030?
Method: Scenario analysis, real options analysis, decision trees
Time investment: Weeks to months
Type 4: Wicked decisions (Ill-defined problem, conflicting values) — Example: Autonomous vehicle ethical dilemmas (trolley problem)
Method: Stakeholder deliberation, value-focused thinking
Time investment: Months, ongoing
Common automotive examples:
| Decision | Type | Appropriate Method |
|----------|------|-------------------|
| Supplier selection for seats | Simple | Weighted scoring |
| Powertrain architecture (ICE/Hybrid/BEV) | Complicated | MCDA (AHP, TOPSIS) |
| Platform strategy for next generation | Complex | Scenario planning + MCDA |
| ADAS feature prioritization | Complicated | Trade-off analysis + MCDA |
| Autonomous safety policies | Wicked | Value-focused thinking |
Today's focus: Types 2 and 3 - systematic methods for complicated and complex decisions.

## Slide 10: Decision-Making Under Uncertainty
Real engineering decisions are made with incomplete information. We must account for uncertainty:
Types of uncertainty:
1. Parameter uncertainty (We know what matters, but not exact values)
Example: 'Battery cost in 2027 will be $80-150/kWh'
Approach: Sensitivity analysis, Monte Carlo simulation
2. Model uncertainty (We're not sure of the relationships)
Example: 'How does battery degradation relate to fast-charging frequency?'
Approach: Multiple models, expert judgment, testing
3. Scenario uncertainty (Future states of the world)
Example: 'Will governments mandate solid-state batteries by 2030?'
Approach: Scenario planning, decision trees
4. Unknown unknowns (Things we don't know we don't know)
Example: Unforeseen battery chemistry breakthrough
Approach: Robustness analysis (choose options that work across many scenarios)
Decision under uncertainty framework: — Known knowns: Use deterministic analysis
Known unknowns: Use probabilistic analysis (expected value, decision trees)
Unknown unknowns: Use robust decision-making (choose options that don't fail catastrophically)
Automotive example - Range uncertainty:
You're designing for 400 km range, but actual range depends on:
Temperature (-20°C to +40°C) - known distribution
Driving style (aggressive vs eco) - statistical data available
Future regulation (unknown)
Battery degradation over 10 years (model uncertainty)
Approach:
Model parameter uncertainty (Monte Carlo)
Design for 90th percentile worst case (robustness)
Plan for future regulation scenarios
Include margin for degradation uncertainty
This leads to decisions that are defensible even when inputs are uncertain.

## Slide 11
#### Part 2: Multi-Criteria Decision Analysis (MCDA) (Slides 11-14, ~12 minutes)

## Slide 12: What is MCDA and Why It Matters
Most engineering decisions involve MULTIPLE, CONFLICTING objectives. This is where MCDA shines.
Traditional approach (single criterion):
'Minimize cost' → Choose cheapest option
Problem: Ignores safety, quality, performance, schedule, risk
MCDA approach (multiple criteria):
Explicitly consider ALL important criteria
Weight criteria based on stakeholder priorities
Calculate overall score for each alternative
Make transparent, defensible decisions
When to use MCDA: — Multiple objectives that conflict (can't optimize all simultaneously)
Stakeholders with different priorities
Need documented, traceable rationale
High-stakes decisions (regulatory scrutiny, safety-critical)
Automotive applications: — Architecture selection (ICE vs Hybrid vs BEV)
Supplier selection (not just lowest cost)
Feature prioritization (which ADAS features for next release?)
Platform decisions (develop new platform or adapt existing?)
Technology roadmap (which technologies to invest in?)
Key benefit: MCDA forces EXPLICIT discussion of values and trade-offs. No hidden assumptions.

## Slide 13: MCDA Method 1 - Weighted Sum Model (WSM)
The simplest and most common MCDA method: Weighted Sum Model (WSM).
Process:
Step 1: Define criteria and weights — List all evaluation criteria
Assign weights (must sum to 1.0 or 100%)
Weights reflect relative importance
Step 2: Score each alternative — Rate each alternative on each criterion
Use common scale (e.g., 1-10 or 0-100)
Based on data, analysis, or expert judgment
Step 3: Calculate weighted score — Multiply score × weight for each criterion
Sum across all criteria
Alternative with highest total score wins
Example: Battery selection with WSM
Criteria and weights:
| Criterion | Weight | Rationale |
|-----------|--------|-----------|
| Cost | 0.25 | Important but not sole driver |
| Energy Density | 0.20 | Affects vehicle range and mass |
| Safety | 0.30 | Critical for liability and brand |
| Lifespan | 0.15 | Warranty cost impact |
| Technology Maturity | 0.10 | Risk consideration |
| Total | 1.00 | |
Scoring (1-10 scale, higher is better):
| Criterion | Weight | LFP Score | LFP Weighted | NMC Score | NMC Weighted | Solid-State Score | SS Weighted |
|-----------|--------|-----------|--------------|-----------|--------------|-------------------|-------------|
| Cost | 0.25 | 9 | 2.25 | 6 | 1.50 | 2 | 0.50 |
| Energy Density | 0.20 | 5 | 1.00 | 9 | 1.80 | 10 | 2.00 |
| Safety | 0.30 | 10 | 3.00 | 7 | 2.10 | 10 | 3.00 |
| Lifespan | 0.15 | 9 | 1.35 | 6 | 0.90 | 4 | 0.60 |
| Maturity | 0.10 | 10 | 1.00 | 10 | 1.00 | 3 | 0.30 |
| TOTAL | | | 8.60 | | 7.30 | | 6.40 |
Result: LFP wins with this weighting scheme (8.60 vs 7.30 vs 6.40)
Key insight: If we change weights (e.g., energy density becomes 0.35, cost becomes 0.15), NMC might win. This shows how values drive decisions.
Sensitivity analysis: Test how decision changes with different weights. If decision is stable across reasonable weight variations → robust decision.

## Slide 14: MCDA Method 2 - Analytic Hierarchy Process (AHP)
Analytic Hierarchy Process (AHP) — developed by Thomas Saaty, widely used in automotive and aerospace.
Key difference from WSM: AHP derives weights through pairwise comparisons rather than assigning them directly.
Process:
Step 1: Build hierarchy — Goal (top level): Select battery technology
Criteria (middle): Cost, safety, performance, etc.
Alternatives (bottom): LFP, NMC, Solid-State
Step 2: Pairwise comparison of criteria — Compare each criterion to every other
Use Saaty's 1-9 scale:
1 = Equal importance
3 = Moderate importance
5 = Strong importance
7 = Very strong importance
9 = Extreme importance
Example comparison:
'How much more important is Safety compared to Cost?'
→ Answer: Safety is moderately to strongly more important = 4
Step 3: Calculate criteria weights — Build pairwise comparison matrix
Calculate eigenvector (mathematical process)
Normalized eigenvector = criteria weights
Step 4: Check consistency — AHP includes consistency ratio (CR)
CR < 0.10 means judgments are consistent
CR > 0.10 means revisit pairwise comparisons (judgments are contradictory)
Step 5: Repeat for alternatives — For each criterion, compare alternatives pairwise
Calculate scores for each alternative on each criterion
Step 6: Synthesize — Combine criteria weights and alternative scores
Calculate overall priority for each alternative
Example pairwise comparison matrix (criteria):
| | Cost | Safety | Energy Density | Lifespan |
|--|------|--------|----------------|----------|
| Cost | 1 | 1/4 | 2 | 2 |
| Safety | 4 | 1 | 5 | 5 |
| Energy Density | 1/2 | 1/5 | 1 | 2 |
| Lifespan | 1/2 | 1/5 | 1/2 | 1 |
Derived weights (after eigenvector calculation):
Safety: 0.52 (dominant)
Cost: 0.23
Energy Density: 0.14
Lifespan: 0.11
Advantage: Weights emerge from explicit comparisons, easier for stakeholders than directly assigning percentages.
Disadvantage: Time-consuming for many criteria (n criteria requires n×(n-1)/2 comparisons).
Tool support: Expert Choice, Super Decisions, online AHP calculators.

## Slide 15: MCDA Method 3 - TOPSIS
TOPSIS (Technique for Order Preference by Similarity to Ideal Solution) - elegant method used in automotive engineering.
Core concept:
Best alternative is closest to the ideal solution (best score on all criteria)
Best alternative is farthest from the anti-ideal solution (worst score on all criteria)
Process:
Step 1: Create decision matrix — Rows = alternatives
Columns = criteria
Cells = scores
Step 2: Normalize scores — Convert to common scale (0-1)
Accounts for different units (cost in $, weight in kg, etc.)
Step 3: Apply weights — Multiply normalized scores by criterion weight
Step 4: Identify ideal and anti-ideal solutions — Ideal: Best score on each criterion
Anti-ideal: Worst score on each criterion
Step 5: Calculate distances — Euclidean distance from each alternative to ideal
Euclidean distance from each alternative to anti-ideal
Step 6: Calculate relative closeness — Closeness = Distance to anti-ideal / (Distance to ideal + Distance to anti-ideal)
Range: 0 to 1 (higher is better)
Step 7: Rank alternatives — Highest closeness score wins
Example (battery selection):
Assume normalized, weighted scores:
| Alternative | Cost | Safety | Energy | Lifespan | Sum to Ideal | Sum to Anti-Ideal | Closeness |
|-------------|------|--------|--------|----------|--------------|-------------------|-----------|
| LFP | 0.23 | 0.30 | 0.10 | 0.14 | 0.15 | 0.42 | 0.74 |
| NMC | 0.15 | 0.21 | 0.18 | 0.09 | 0.23 | 0.31 | 0.57 |
| Solid-State | 0.05 | 0.30 | 0.20 | 0.06 | 0.28 | 0.25 | 0.47 |
Result: LFP wins (closeness = 0.74, closest to ideal, farthest from anti-ideal)
Advantages:
Mathematically rigorous
Handles any number of alternatives and criteria
Clear visual interpretation (geometric distance)
When to use:
Large number of alternatives (e.g., supplier selection from 20 candidates)
Quantitative criteria dominate
Need defensible, objective ranking
Automotive applications: Material selection, supplier scoring, architecture ranking, technology selection.

## Slide 16
#### Part 3: Trade-off Analysis (Slides 15-17, ~10 minutes)

## Slide 17: Understanding Trade-offs
In engineering, we rarely optimize a single objective. We TRADE OFF between competing goals.
Classic automotive trade-offs: — Performance vs Fuel Efficiency (power vs consumption)
Safety vs Weight (crashworthiness adds mass)
Cost vs Quality (cheaper materials may compromise durability)
Features vs Complexity (more features = more failure modes)
Development Speed vs Robustness (fast development may skip testing)
The Pareto Frontier concept:
A solution is Pareto optimal (or Pareto efficient) if you can't improve one objective without worsening another.
Example: Range vs Cost trade-off in EVs
| Battery Size | Range (km) | Cost ($) | Pareto Optimal? |
|--------------|------------|----------|-----------------|
| 50 kWh | 300 | $20,000 | Yes (cheapest) |
| 60 kWh | 360 | $23,000 | Yes |
| 75 kWh | 450 | $27,000 | Yes |
| 90 kWh | 540 | $32,000 | Yes |
| 65 kWh | 350 | $26,000 | No (dominated by 75 kWh - less range, more expensive) |
All Pareto-optimal solutions lie on the Pareto frontier. Choice among them depends on stakeholder values.
Trade-off analysis process:
Identify conflicting objectives
Generate design alternatives
Evaluate each on both objectives
Plot trade-off curve (Pareto frontier)
Eliminate dominated solutions
Apply decision criteria to choose from Pareto set
Visual: [Show graph with Cost on X-axis, Range on Y-axis, Pareto frontier curve]
Key insight: Don't waste time analyzing dominated solutions. Focus on Pareto frontier.

## Slide 18: Trade-off Analysis Methods
How do we systematically analyze trade-offs? Multiple methods:
Method 1: Parametric Trade Studies — Vary design parameters, observe impact on objectives
Example: Vary battery size from 40-100 kWh, plot range vs cost vs weight
Tools: Excel, MATLAB, Python, design exploration software
Method 2: Utility Theory — Convert multiple objectives to single 'utility' value
Reflect stakeholder preferences mathematically
Example: Utility = w1×Range + w2×(1/Cost) + w3×(1/Weight)
Choose design with maximum utility
Method 3: Design Space Exploration (DSE) — Generate large number of design alternatives (1000s)
Evaluate all on multiple objectives
Visualize in multi-dimensional space
Filter to Pareto frontier
Tools: ModelCenter, Isight, MOEA (Multi-Objective Evolutionary Algorithms)
Method 4: Sensitivity Analysis — How sensitive is the decision to changes in parameters or weights?
Example: If battery cost drops 20%, does the decision change?
Identifies critical assumptions and uncertainties
Method 5: Knee of the Curve Analysis — On trade-off curve, find the 'knee' point
Point of diminishing returns
Example: 75 kWh battery at knee - going to 90 kWh adds 20% range but 35% cost
Automotive example - Aerodynamics vs Cooling trade-off:
Problem: Smaller grille improves aerodynamics (lower drag, better efficiency) but reduces radiator airflow (cooling performance)
Trade study approach:
Parametric variation: Grille sizes from 1000 cm² to 3000 cm²
CFD analysis: Drag coefficient (Cd) vs cooling air mass flow
System simulation: Vehicle performance in hot conditions
Identify Pareto frontier: Designs that balance Cd and cooling
Apply decision criteria: Choose based on target market (hot climate → larger grille; cold climate → smaller grille)
Result: Document WHY specific grille size was chosen, including trade-offs accepted.
This becomes critical when, 2 years later, someone asks: 'Why didn't we make the grille smaller for better efficiency?'

## Slide 19: Real Automotive Case - Tesla Model 3 Trade-offs
Let's examine real trade-off decisions from Tesla Model 3 development:
Trade-off 1: Glass Roof vs Traditional Roof
Objectives in conflict: — Aesthetics / Differentiation (glass roof = premium feel)
Weight (glass heavier than stamped steel + insulation)
Cost (glass roof more expensive)
Thermal management (glass increases solar heat gain → larger AC required)
Crash safety (roof strength requirements)
Tesla's decision: Glass roof standard
Rationale:
Differentiation value outweighs cost/weight (~15 kg penalty)
UV-filtering glass mitigates thermal issue
Single-piece glass simplifies manufacturing (assembly cost offset)
Brand positioning (premium EV)
Trade-off accepted: Higher weight and thermal load for aesthetic/brand value
Trade-off 2: Minimalist Interior (No Instrument Cluster)
Objectives in conflict: — Cost reduction (eliminate instrument cluster = $150-200 savings)
User experience (drivers expect instrument cluster)
Safety (eyes off road to check center screen)
Differentiation (unique Tesla interface)
Tesla's decision: Center screen only, no instrument cluster
Rationale:
Cost savings
Simpler manufacturing
Software flexibility (all UI updates via OTA)
Brand differentiation
Trade-off accepted: User experience concerns for cost/simplicity
Market result: Polarizing - some love it, some hate it (design risk accepted)
Trade-off 3: Range vs Affordability (Battery Size)
Objectives:
Range (more range needs bigger battery)
Affordability (target $35k base price)
Profitability (larger battery reduces margin)
Tesla's approach: Multiple variants
Standard Range: 50 kWh, 260 km, $35k (later discontinued - unprofitable)
Long Range: 75 kWh, 520 km, $46k (Pareto optimal - good range, acceptable cost)
Performance: 75 kWh, 480 km, $56k (range traded for acceleration)
Decision: Optimize product portfolio across Pareto frontier to serve different customer values
Lessons learned:
Trade-offs must align with brand positioning
Different customers value objectives differently → multiple variants
Document trade-off rationale for future reference
Some trade-offs create risk (minimalist interior) - accept knowingly
Quantify trade-offs where possible (weight, cost, range all measurable)

## Slide 20
#### Part 4: Quality Assurance vs Quality Control (Slides 18-20, ~8 minutes)

## Slide 21: QA vs QC - The Critical Distinction
One of the most misunderstood distinctions in engineering: Quality Assurance vs Quality Control. They're complementary but fundamentally different.
Quality Assurance (QA) - PREVENTION — Definition: Process-focused activities to prevent defects
Timing: Throughout development, before defects occur
Approach: Design processes, standards, training, reviews
Question: 'Are we building quality IN?'
Responsibility: Everyone (QA team facilitates)
Quality Control (QC) - DETECTION — Definition: Product-focused activities to identify defects
Timing: During and after development, after defects exist
Approach: Testing, inspection, measurement, validation
Question: 'Are we finding defects OUT?'
Responsibility: QC/Test team (dedicated)
Simple analogy: — QA: Installing guardrails on a mountain road (prevents cars from going off cliff)
QC: Inspecting cars after they've crashed (detecting damage)
You want both, but QA is more cost-effective.
Automotive examples:
| Activity | QA or QC? | Rationale |
|----------|-----------|-----------|
| Design FMEA workshop | QA | Prevents defects by identifying failure modes in design phase |
| Final vehicle inspection before delivery | QC | Detects defects after production |
| Supplier development program | QA | Prevents defects by improving supplier processes |
| Software code review | QA | Prevents defects by catching errors before code is compiled |
| Dynamometer testing | QC | Detects performance defects through testing |
| ISO 26262 compliance process | QA | Prevents safety issues through systematic process |
| X-ray inspection of welds | QC | Detects weld defects after welding |
Cost comparison (Automotive Industry Action Group data):
Prevention (QA): $1 per unit
Appraisal (QC during production): $10 per unit
Internal failure (found before delivery): $100 per unit
External failure (found by customer): $1,000+ per unit
Recall: $10,000+ per unit
Key principle: Shift left - invest in QA to prevent defects rather than relying on QC to catch them.

## Slide 22: Quality Management Systems (QMS)
A Quality Management System (QMS) integrates QA and QC into organizational processes.
QMS purpose: — Ensure consistent quality
Meet regulatory requirements
Enable continuous improvement
Provide objective evidence of quality
Key QMS standards in automotive:
1. ISO 9001 - General Quality Management — Applicable to all industries
Process approach, risk-based thinking
Customer focus, continual improvement
Required for most automotive suppliers
2. IATF 16949 - Automotive Quality Management — Built on ISO 9001, adds automotive-specific requirements
Mandatory for automotive OEM suppliers
Emphasizes defect prevention, variation reduction
Includes customer-specific requirements (GM, Ford, VW, etc.)
Core tools: APQP, PPAP, FMEA, SPC, MSA
3. ISO 26262 - Functional Safety — Quality management for safety-critical systems
V-model process, safety lifecycle
Required for ASIL-rated automotive systems
4. ASPICE - Automotive SPICE (Software Process Improvement and Capability Determination) — Process assessment model for automotive software
Capability levels 0-5 (similar to CMMI)
Many OEMs require suppliers to achieve Level 2 or 3
QMS structure:
Level 1: Quality Policy and Objectives — Top management commitment
Example: 'Zero defects, first-time quality, continuous improvement'
Level 2: Quality Manual — How organization meets QMS standard
Process map, responsibilities
Level 3: Procedures — How specific processes are executed
Example: Design review procedure, change control procedure
Level 4: Work Instructions — Detailed step-by-step instructions
Example: How to perform specific test
Level 5: Records — Evidence that processes were followed
Example: Test reports, inspection records, meeting minutes
Automotive QMS in practice: — Design reviews at phase gates (prevent design defects)
Supplier audits (prevent supply chain defects)
Production Part Approval Process (PPAP) - verify production readiness
Control plans (ensure process capability)
Reaction plans (contain defects quickly)
Lessons learned (prevent recurrence)
Certification: Third-party audits verify QMS compliance (e.g., TÜV, BSI, DNV)

## Slide 23: Quality Gates and Phase Reviews
Quality gates are decision points where projects must demonstrate quality criteria before proceeding.
Purpose: — Prevent defects from propagating to next phase
Ensure readiness before major investment
Provide management visibility
Enforce disciplined process
Typical automotive quality gates (aligned with V-model):
Gate 0: Concept Approval — Entry criteria: Market analysis, business case, preliminary requirements
Quality checks: Requirements completeness, stakeholder alignment, feasibility
Exit criteria: Approved concept, funded program, assigned team
Gate 1: Requirements Review — Entry criteria: Complete stakeholder requirements, system requirements
Quality checks: Requirements quality attributes (clear, verifiable, traceable), RTM completeness
Exit criteria: Baselined requirements, approved for design
Gate 2: Design Review — Entry criteria: System architecture, subsystem designs, interface definitions
Quality checks: Design FMEA complete, design verification plan, traceability to requirements
Exit criteria: Approved design, released for implementation
Gate 3: Implementation Review — Entry criteria: Prototype/software complete, unit tested
Quality checks: Code reviews, unit test results, integration test plan
Exit criteria: Ready for integration testing
Gate 4: Verification Review — Entry criteria: System integrated, test results available
Quality checks: Requirements verification complete, test coverage, defect resolution
Exit criteria: Verified system, ready for validation
Gate 5: Validation Review (Production Readiness) — Entry criteria: Validation testing complete, PPAP submitted
Quality checks: Customer acceptance, manufacturing process capability (Cpk ≥ 1.33), regulatory compliance
Exit criteria: Approved for production launch
Gate 6: Launch Review — Entry criteria: Initial production complete, field monitoring data
Quality checks: Zero major defects, process stability, customer satisfaction
Exit criteria: Ramp-up to full production
Gate criteria example (Requirements Review):
✓ All stakeholder needs documented
✓ System requirements complete (100% of needs traced)
✓ Requirements quality checked (0 ambiguous requirements, 100% verifiable)
✓ Requirements Traceability Matrix complete
✓ Regulatory requirements identified and mapped
✓ Requirements baseline established in configuration management
✓ Stakeholder sign-off obtained
✓ Design FMEA initiated
Gate governance: — Go: Criteria met, proceed to next phase
Conditional Go: Minor issues, proceed with documented actions
No-Go: Significant gaps, do not proceed until resolved
Key principle: Quality gates are non-negotiable. Never skip gates under schedule pressure - that's when defects escape.

## Slide 24
#### Part 5: Critical Parameter Management (Slides 21-22, ~6 minutes)

## Slide 25: What Are Critical Parameters?
Not all parameters are created equal. Critical parameters are the few vital characteristics that determine system success.
Definition: Critical parameters are characteristics that:
Significantly affect customer satisfaction or safety
Have narrow acceptable tolerances
Require special controls to ensure conformance
Can cause system failure or major defect if out of spec
Categories:
Critical-to-Quality (CTQ) Parameters — Directly impact customer-perceived quality
Example: Brake pedal feel, 0-100 km/h acceleration time
Critical-to-Safety (CTS) Parameters — Affect occupant or pedestrian safety
Example: Airbag deployment time, ABS response time
Critical-to-Function (CTF) Parameters — Essential for system to perform intended function
Example: Battery voltage range, sensor accuracy
Critical-to-Process (CTP) Parameters — Manufacturing process variables that affect quality
Example: Welding current, paint booth temperature
Example - Electric Vehicle Battery System:
| Parameter | Type | Specification | Why Critical | Control Method |
|-----------|------|---------------|--------------|----------------|
| Cell voltage | CTF, CTS | 2.5-4.2V | Over-voltage = fire risk, under-voltage = damage | 100% monitoring, BMS cutoff |
| Temperature | CTS | -20 to +60°C | Thermal runaway risk | Thermal sensors, active cooling |
| State of Charge (SOC) accuracy | CTQ | ±3% | Range anxiety if inaccurate | Kalman filter, calibration |
| Isolation resistance | CTS | >100 Ω/V | Electrical shock hazard | Pre-drive check, ISO monitoring |
| Crash deformation limit | CTS | <15mm intrusion | Prevents cell puncture | FEA analysis, crash testing |
Critical parameter characteristics: — Measurable (quantitative specification)
Controlled (monitoring, process controls, inspection)
Documented (control plan, work instructions)
Traceable (linked to requirements and risks)
Pareto principle (80/20 rule):
20% of parameters cause 80% of defects
Identify and control the critical 20%

## Slide 26: Critical Parameter Management Process
Systematic Critical Parameter Management (CPM) ensures vital characteristics are controlled:
Step 1: Identify Critical Parameters — Sources:
Requirements analysis (safety, performance requirements)
FMEA (high RPN failure modes)
Historical warranty data (known problem areas)
Regulatory requirements (crash, emissions, safety)
Customer complaints (VOC - Voice of Customer)
Tool: Critical Parameter Identification Matrix
Step 2: Classify and Prioritize — Rate by criticality (CTS > CTQ > CTF > CTP)
Rate by risk (probability × severity)
Focus control effort on highest priority
Step 3: Define Specifications — Nominal value and tolerances
Based on capability studies and margin analysis
Example: Battery SOC accuracy = 50% ± 3% (nominal ± tolerance)
Step 4: Establish Control Methods
Prevention controls (QA):
Design for robustness (parameter insensitive to variation)
Process capability studies (Cpk ≥ 1.33 for critical params)
Poka-yoke (error-proofing)
Detection controls (QC):
100% inspection for safety-critical parameters
Statistical Process Control (SPC) for process parameters
Automated monitoring (sensors, BMS)
Step 5: Document in Control Plan — Control plan lists all critical parameters
For each: specification, measurement method, frequency, reaction plan
Example Control Plan (Battery Assembly):
| Parameter | Spec | Measure Method | Frequency | Reaction if OOS |
|-----------|------|----------------|-----------|-----------------|
| Cell voltage | 3.6±0.1V | Digital voltmeter | 100% | Reject cell, investigate supplier |
| Torque (busbars) | 8±1 Nm | Torque wrench | 100% | Rework, retorque |
| Isolation resistance | >500 kΩ | Megohmmeter | 100% | Do not ship, investigate |
| Leak test (pass/fail) | Pass | Helium leak detector | 100% | Rework seals, retest |
Step 6: Monitor and React — Real-time monitoring where possible
Immediate reaction if out-of-spec
Root cause analysis for any critical parameter excursion
Step 7: Continuous Improvement — Track trends over time
Reduce variation (Six Sigma approach - Cpk ≥ 2.0 target)
Update control methods based on lessons learned
Tools: — Control charts (SPC)
Process capability studies (Cp, Cpk)
Measurement System Analysis (MSA) - ensure measurement accuracy
Reaction plans (immediate containment)
Automotive standard: AIAG Control Plan methodology, PPAP requirements

## Slide 27
#### Part 6: Metrics and KPIs (Slides 23-24, ~8 minutes)

## Slide 28: Systems Engineering Metrics and KPIs
'You can't manage what you don't measure.' — Peter Drucker
Systems engineering effectiveness must be measured. But measure the RIGHT things.
Metric vs KPI: — Metric: Any quantitative measurement
KPI (Key Performance Indicator): Metric that's critical to success, tracked by management
Categories of SE metrics:
1. Product Quality Metrics — Defect density (defects per 1000 requirements or KLOC)
Defect escape rate (defects found by customer vs total)
Mean Time Between Failures (MTBF)
Warranty claims per 1000 vehicles (CPV - Claims Per Vehicle)
2. Process Performance Metrics — Requirements volatility (% requirements changed after baseline)
Requirements test coverage (% requirements with test cases)
Design review effectiveness (defects found in reviews vs testing)
Phase containment (% defects found in phase where introduced)
3. Schedule Metrics — Schedule variance (actual vs planned)
Milestone achievement rate (% milestones met on time)
Cycle time (time from concept to production)
4. Cost Metrics — Cost variance (actual vs budget)
Cost of quality (prevention + appraisal + failure costs)
Rework cost as % of total development cost
5. Productivity Metrics — Requirements developed per engineer-month
Test cases executed per week
Defect closure rate (defects fixed per week)
Example KPIs for automotive program:
| KPI | Target | Actual (Month 6) | Status |
|-----|--------|------------------|--------|
| Requirements stability | <5% change/month | 3.2% | ✓ Green |
| Test coverage | 100% | 94% | ⚠ Yellow |
| Defect density | <0.5 def/req | 0.7 def/req | ❌ Red |
| Schedule variance | ±5% | -8% (behind) | ❌ Red |
| Defect escape rate | <5% | 3% | ✓ Green |
| Design review participation | >90% | 85% | ⚠ Yellow |
Balanced scorecard approach: Don't optimize one metric at expense of others
Optimizing schedule only → quality suffers
Optimizing cost only → safety compromised
Balance across quality, cost, schedule, innovation

## Slide 29: Case Study - GM Ignition Switch Decision Failure
Let's analyze a catastrophic failure of both decision-making and quality management: GM ignition switch (2003-2014).
Background: — 124 deaths, 275 injuries
30 million vehicles recalled
$4.1B in costs and settlements
Criminal charges against GM
The problem:
Ignition switch could move from 'Run' to 'Accessory' or 'Off' if bumped or with heavy keychain
→ Engine shuts off while driving
→ Power steering and brakes lose assist
→ Airbags disabled (key not in 'Run' position)
Decision failure #1: Component selection (2002)
Trade-off: Ignition switch torque spec
Higher torque = harder to turn, safer (won't slip)
Lower torque = easier to turn, more comfortable
Decision made: Spec = 15±5 cN·m (very wide tolerance, lower end = 10 cN·m)
Decision method: Supplier recommendation, no systematic MCDA
What was missed: No safety analysis of low torque scenario (FMEA failure)
Result: Switches produced at 10 cN·m (low end) → too easy to move accidentally
Quality failure #1: Inadequate testing — QC testing did not include 'bump' scenario or heavy keychain
No validation of worst-case conditions (low torque + vibration + keychain weight)
Decision failure #2: Engineering change (2006)
Engineer discovered problem in 2005, authorized supplier to change switch design (increase torque) WITHOUT:
Formal change control process
New part number (unauthorized, against QMS)
Notification to manufacturing or service
Why this decision was made: Avoid paperwork and documentation
Consequence: Mix of old (defective) and new (fixed) switches in field, impossible to identify which vehicles have which
Quality failure #2: No critical parameter management — Ignition switch torque was NOT identified as critical parameter
No 100% testing of torque value
No statistical process control
Should have been CTS (Critical-to-Safety) with tight control and 100% inspection
Decision failure #3: Response to field reports (2003-2013)
Timeline:
2004: First crash report (airbag didn't deploy)
2005-2007: Multiple reports of stalling, moving ignition
2010: Internal committee reviewed issue → Decided NOT to recall
Trade-off in 2010 decision: — Recall cost: ~$100M (estimated)
Liability risk: Unknown
Brand reputation: Negative publicity
Decision made: Do nothing (no recall)
Decision method: Cost minimization, no systematic risk analysis
What was missed:
Safety consequence severely underestimated
Liability and brand damage severely underestimated
Ethical dimension ignored
Actual cost: $4.1B (41× more than recall would have cost)
Quality failure #3: Metrics didn't surface the problem — Warranty data showed stalling issues, but not aggregated
No KPI for 'airbag non-deployment in crashes' (should have been critical safety metric)
Data siloed in different departments
Root causes:
Decision-making: — No systematic decision framework (MCDA, risk analysis)
Cost prioritized over safety in trade-offs
Individual decisions, no oversight or challenge process
No documentation of decision rationale
Quality management: — Critical parameter (ignition torque) not identified
QMS violated (unauthorized change, no part number change)
Quality gates failed (issue known but not escalated)
Metrics didn't track safety-critical parameters
What should have been done:
2002 (Original design): — FMEA identifying low-torque risk
Ignition torque designated as CTS parameter
Tighter specification (15±2 cN·m)
100% torque testing
2006 (Change): — Formal ECN (Engineering Change Notice)
New part number
Field campaign to replace defective switches
2010 (Field reports): — Systematic decision analysis:
Criteria: Safety, cost, liability, reputation
Weight safety as primary
Decision: Immediate recall
Lessons learned:
Safety must be weighted explicitly in trade-off decisions
Critical parameters must be identified and controlled
QMS is non-negotiable - no shortcuts
Metrics must surface safety issues
Decision rationale must be documented
Cost of prevention << cost of failure

## Slide 30: Common Decision and Quality Pitfalls
Let me show you the systematic failures to avoid:
Decision-making pitfalls:
Pitfall 1: HiPPO decisions (Highest Paid Person's Opinion)
Senior executive overrides systematic analysis based on intuition
Example: 'I drove a competitor's car, we need to match their feature'
Fix: Require data-driven justification for overriding analysis
Pitfall 2: Analysis paralysis — Endless analysis, no decision
Fear of making wrong decision → make no decision
Fix: Set decision deadlines, 'good enough' threshold
Pitfall 3: Sunk cost fallacy — 'We've already invested $10M in this architecture, we can't change now'
Past costs shouldn't drive future decisions
Fix: Evaluate based on future costs/benefits only
Pitfall 4: Confirmation bias — Seeking data that supports preferred option, ignoring contradictory data
Example: Testing scenarios where Option A wins, avoiding scenarios where it fails
Fix: Red team review, devil's advocate, pre-commit to decision criteria
Pitfall 5: Groupthink — Team converges on consensus without critical analysis
No one challenges assumptions
Fix: Assign explicit challenger role, encourage dissent
Pitfall 6: Optimizing single criterion — 'Minimize cost' without considering quality, safety, schedule
GM ignition switch optimized cost → catastrophe
Fix: Multi-criteria decision analysis (MCDA)
Pitfall 7: Not documenting rationale — Decision made, but reasoning not recorded
2 years later: 'Why did we choose this?'
Fix: Decision log with criteria, alternatives, rationale
Quality management pitfalls:
Pitfall 8: Inspection over prevention — Rely on testing to find defects rather than preventing them
'We'll test quality in'
Fix: Shift to QA (prevention) - FMEA, design reviews, process improvement
Pitfall 9: Quality is QA team's job — Engineers think: 'I design, QA ensures quality'
Result: Defects designed in, expensive to fix
Fix: Quality is everyone's responsibility
Pitfall 10: Ignoring non-functional requirements — Focus on functional testing, neglect performance, reliability, safety
Example: Feature works in ideal conditions, fails in extreme temps
Fix: NFR test coverage equal to functional test coverage
Pitfall 11: No critical parameter identification — Treating all parameters equally
Result: Critical safety parameters not controlled
Fix: Systematic CPM process (FMEA-driven)
Pitfall 12: Metrics without action — Dashboards show red KPIs, but no response
'That's just how our metrics always look'
Fix: Define triggers and mandatory actions for out-of-spec KPIs
Pitfall 13: Gaming metrics — Optimizing metric instead of actual quality
Example: Closing bugs as 'not reproducible' to hit closure targets
Fix: Multiple complementary metrics, audit sample of closed bugs
Pitfall 14: No lessons learned — Same mistakes repeated across programs
No institutional memory
Fix: Formal lessons learned process, searchable database, design reviews reference previous failures

## Slide 31: Key Takeaways
Let's consolidate what you've learned today:
1. Systematic Decision-Making — Use structured frameworks (MCDA, trade-off analysis)
Explicitly identify criteria and weights
Document rationale for traceability
Consider uncertainty and risk
2. Multi-Criteria Decision Analysis — WSM: Simple weighted scoring
AHP: Pairwise comparisons for weight derivation
TOPSIS: Distance to ideal solution
Choose method based on decision complexity
3. Trade-off Analysis — Engineering involves conflicting objectives
Pareto frontier identifies optimal solutions
Choice among Pareto options depends on values
Document trade-offs accepted
4. Quality Assurance vs Quality Control — QA = Prevention (design it in)
QC = Detection (test it out)
QA is more cost-effective (10:1 or better)
Both are necessary
5. Critical Parameter Management — Identify vital few (CTS, CTQ, CTF)
Define specifications with margin
Implement controls (prevention + detection)
Monitor and react to excursions
6. Metrics and KPIs — Measure to manage, not to punish
Leading + lagging indicators
Balanced scorecard (cost/schedule/quality)
Define action triggers
7. Integration — Good decisions lead to quality outcomes
Quality metrics inform better decisions
Both require systematic processes and culture
Remember: Boeing 737 MAX and GM ignition switch failures weren't due to technical inability - they were failures of decision-making and quality management. You now have the tools to prevent these catastrophes.

## Slide 32: Connection to Other Sessions and Systems Engineering
Let's place today's learning in the systems engineering context:
Today (Session 10): Decision and Quality Management
Connections to previous sessions:
Session 4 (Requirements): — When stakeholder needs conflict → Decision analysis to prioritize
Requirements quality attributes → Quality management
Critical requirements → Critical parameters
Session 5 (Architecture): — Multiple architecture alternatives → MCDA to choose
Architecture trade-offs → Pareto analysis
Design decisions → Documented rationale
Session 8 (V&V): — Verification = Quality control (detecting defects)
Test coverage = Quality metric
Quality gates at each V-model phase
Session 9 (Risk Management): — Risk informs decisions (uncertain scenarios)
FMEA identifies critical parameters
Risk metrics = KPIs for program health
What comes next:
Session 11 (Agreement and Infrastructure Management): — Supplier selection = MCDA application
Make-vs-buy decisions
Supplier quality management
Session 12 (Safety and Security): — Safety is critical decision criterion
Safety integrity levels → Critical parameters
Functional safety = Quality management for safety
Session 15 (Technical Management): — Configuration management supports quality
Measurement and analysis = Metrics programs
Decision management as technical process
Throughout SE lifecycle: — Every technical process involves decisions
Quality must be managed at every phase
Metrics track progress and inform decisions
Critical parameters flow from requirements through validation
Key integration point: Decision and quality management are ENABLING processes that support all technical processes.

## Slide 33: 📊 PPT DESIGN GUIDANCE
Real Examples to Include:
Practical Exercise (Due before Session 11):
You are the systems engineer for a new Advanced Driver Assistance System (ADAS) that combines Adaptive Cruise Control (ACC) and Lane Keeping Assist (LKA).
Part 1: Decision Analysis (40%)
Scenario: You must select the primary sensor architecture from three alternatives:
Option A: Camera-only — Cost: $150 per vehicle
Range: 100m
Weather performance: Poor (rain/fog degrades)
Object classification: Excellent (can read signs, detect pedestrians)
Redundancy: Single sensor
Option B: Radar-only — Cost: $200 per vehicle
Range: 200m
Weather performance: Excellent (unaffected)
Object classification: Poor (detects objects, can't classify type)
Redundancy: Single sensor
Option C: Camera + Radar fusion — Cost: $350 per vehicle
Range: 200m (radar determines)
Weather performance: Good (radar compensates for camera in bad weather)
Object classification: Excellent (camera provides)
Redundancy: Dual sensor
Your task:
Define decision criteria (minimum 5)
Assign weights to criteria (justify based on stakeholder needs)
Score each alternative on each criterion (1-10 scale, document rationale)
Calculate using WSM (Weighted Sum Model)
Perform sensitivity analysis (test 2 different weighting schemes)
Make recommendation with documented rationale
Part 2: Trade-off Analysis (20%)
For your chosen architecture, analyze the trade-off between:
System cost (sensor + processing)
Performance (detection range, weather capability)
Create trade-off table showing 5 design points
Plot Pareto frontier
Explain which point you would select and why
Part 3: Critical Parameter Management (40%)
Identify 5 critical parameters for the ADAS system
Classify each as CTS, CTQ, or CTF
Justify criticality (link to safety or performance requirements)
For the TOP 2 critical parameters:
Define specification (nominal ± tolerance)
Describe control method (prevention + detection)
Define monitoring approach and reaction plan if out-of-spec
Define 3 KPIs for tracking ADAS system quality during development
Each must be SMART
Define target value and decision trigger
Grading Criteria: — Decision analysis: Criteria completeness, weight justification, scoring rationale
Trade-off analysis: Correct Pareto identification, clear selection rationale
Critical parameters: Appropriate identification, realistic specs, comprehensive controls
KPIs: SMART criteria, actionability, alignment with quality objectives
Professional presentation: Clarity, formatting, traceability
Submission:
Part 1: Decision matrix + sensitivity analysis (2 pages)
Part 2: Trade-off plot + analysis (1 page)
Part 3: Critical parameter table + KPI definitions (2 pages)
Total: 5 pages maximum
Tips: — Research real ADAS systems (Tesla, GM Super Cruise, Mercedes Drive Pilot)
Consider ISO 26262 (functional safety) requirements
Think about regulatory requirements (Euro NCAP, NHTSA)
Reference Session 9 (FMEA) for critical parameter identification
Use real data where possible (sensor costs, performance specs)
Discussion Questions: — How would your decision change if target market is Arizona (sunny) vs Norway (dark, snowy)?
What if regulatory requirements mandate redundant sensors for Level 3 autonomy?
How do you handle the cost vs safety trade-off?
What metrics would indicate your chosen architecture is failing during validation?
30 minutes for your questions. —--
Professional analytical aesthetic: Clean, data-driven, decision-oriented
Color coding:
Blue for Decision Analysis
Green for Quality Assurance (prevention)
Orange for Quality Control (detection)
Red for critical parameters and warnings
Purple for metrics/KPIs
Use real automotive examples: Photos of decision boards, quality control stations, dashboards
Diagrams: Decision trees, Pareto frontiers, control charts, KPI dashboards
Slide 4 (Boeing 737 MAX) - Grabs attention with real consequences
Slide 8 (Decision process) - Systematic framework
Slide 12 (WSM example) - Practical application students will use
Slide 15 (Pareto frontier) - Core trade-off concept
Slide 18 (QA vs QC) - Critical distinction
Slide 21 (Critical parameters) - Automotive application
Slide 25 (GM ignition switch) - Comprehensive failure analysis
Slide 28 (Summary) - Students will photograph this
Slide 6: Build battery options table row by row
Slide 12: Highlight each criterion, then show weighted calculation step-by-step
Slide 15: Animate Pareto frontier curve, highlight dominated solutions
Slide 18: Split-screen animation showing QA (prevention) vs QC (detection) timeline
Slide 25: Timeline animation of GM ignition switch decision points and consequences
Slide 6: Battery comparison table (complete with real specs)
Slide 12: Full WSM calculation example (3 alternatives × 5 criteria)
Slide 22: Control plan example (automotive battery assembly)
Slide 23: KPI dashboard with RAG status
Actual MCDA studies from automotive industry (if public)
ISO 9001/IATF 16949 certification audit checklists
Real control plans from PPAP submissions
Actual automotive KPI dashboards (anonymized)
Cost of quality data from automotive industry

## Slide 34: 🎯 INSTRUCTOR NOTES
Assessment Opportunities:
Start with crisis (Boeing 737 MAX), show systematic solution, return to preventing crisis — Balance theory (MCDA methods) with practice (worked examples) — Emphasize decision documentation and traceability — Connect decision quality to system quality — Use automotive examples throughout
Challenge 1: "Why not just use intuition for decisions?"
How to address: Show Slide 4 (Boeing) and Slide 25 (GM) - intuition failed catastrophically. Emphasize: Intuition for simple decisions is fine; complex multi-stakeholder decisions need systematic analysis. Systematic doesn't mean slow - WSM takes 30 minutes for a well-scoped decision.
Challenge 2: "MCDA seems complicated and time-consuming"
How to address: Show Slide 12 (WSM) - simple spreadsheet, 1-2 hours for important decision. Compare to cost of wrong decision (GM: $4.1B). Frame as insurance. Not every decision needs MCDA - use for Type 2/3 decisions (Slide 9).
Challenge 3: "How do we decide the weights in MCDA?"
How to address: Weights reflect stakeholder values. Use AHP (pairwise comparison) if direct weighting is difficult. Show sensitivity analysis - if decision is same across reasonable weight ranges, weights don't matter much. If decision flips with small weight changes, need careful stakeholder negotiation.
Challenge 4: "QA sounds good, but we don't have time for prevention"
How to address: Show cost multipliers (Slide 18): Prevention $1, Appraisal $10, Failure $100, Recall $10,000. Ask: "Can you afford NOT to do prevention?" QA is faster than fixing defects later. FMEA takes 2 days, but prevents 6 months of rework.
Challenge 5: "We track metrics but nothing changes"
How to address: Slide 24 - metrics without action are waste. Define triggers and mandatory actions. Example: Defect density >0.5 → trigger additional design review. Make metrics part of governance, not just dashboards.
If running short: — Condense Slide 13 (AHP) - mention it exists, focus on WSM
Reduce Slide 14 (TOPSIS) to brief overview
Move some trade-off examples to backup slides
If running long: — Extend Slide 12 (WSM) with live calculation exercise (students participate)
Add interactive exercise: Give students a simple decision, have them do WSM
Show actual MCDA software demo (Expert Choice, AHP-OS)
Core content (must cover - non-negotiable): — Slides 8-12 (Decision process, types, MCDA/WSM)
Slides 15-17 (Trade-offs and Pareto)
Slides 18-20 (QA vs QC, QMS, quality gates)
Slides 21-22 (Critical parameters)
Slide 23 (Metrics and KPIs)
Slides 25-26 (Failure case studies and pitfalls)
Slide 28 (Summary)
Slide 6: Interactive - poll students: "Which battery would you choose?" before showing analysis. See how many choose differently and why.
Slide 12: Work through WSM together - have students suggest criteria and weights, calculate together.
Slide 18: Quick quiz - show 5 activities, ask students to classify as QA or QC.
Slide 25: Case study discussion - "At what point should GM have recalled? What decision framework would have led to the right choice?
Slide 27: Pair exercise - give pairs 3 minutes to identify which pitfalls their organization/project exhibits. Share anonymously.
Quick Poll (Slide 3): "How many have seen important decisions made without systematic analysis?" (normalize the problem)
Decision Exercise (Slide 12): Give students battery decision, 5 minutes to score one alternative, compare results, discuss variance.
QA vs QC Quiz (Slide 18): Present 6 activities, students vote QA or QC, discuss.
Metrics Design (Slide 24): Small groups design 2 KPIs for a given system, share, critique.
Before class: — [ ] WSM calculation spreadsheet template (for students)
[ ] Example AHP pairwise comparison matrix
[ ] Real control plan example (anonymized)
[ ] KPI dashboard template
[ ] Decision log template
Handouts: — [ ] Decision analysis process checklist
[ ] WSM template (Excel)
[ ] Critical parameter identification worksheet
[ ] QA vs QC comparison table
[ ] SMART KPI criteria checklist
Post-class: — [ ] Share slides
[ ] Post exercise assignment with templates
[ ] Post WSM and AHP templates
[ ] Share links to: ISO 9001, IATF 16949, AIAG FMEA handbook
[ ] Create discussion forum: "Share a bad decision you've witnessed and how MCDA would have helped
During lecture: — Quick quiz (Slide 9): "What decision method for supplier selection with 15 candidates and 8 criteria?
Quick quiz (Slide 18): "Is FMEA a QA or QC activity? Why?
Exercise assessment criteria: — Decision analysis: Are criteria comprehensive? Weights justified? Scores documented? Sensitivity analysis performed?
Trade-off analysis: Correct Pareto identification? Clear selection rationale?
Critical parameters: Appropriately identified? Linked to FMEA/requirements? Realistic control methods?
KPIs: Meet SMART criteria? Actionable? Aligned with objectives?
Common student mistakes to watch for: — Assigning weights without justification
Not documenting scoring rationale
Confusing dominated solutions with Pareto optimal
Identifying too many parameters as "critical" (critical means vital few, not everything)
Defining vanity metrics instead of actionable KPIs
Not linking critical parameters to requirements or FMEA

## Slide 35: ✅ Session Success Criteria
Students leave able to:
✓ Apply systematic decision analysis to engineering trade-offs
✓ Use Weighted Sum Model (WSM) for multi-criteria decisions
✓ Identify and visualize trade-offs using Pareto frontier
✓ Distinguish between QA (prevention) and QC (detection)
✓ Identify critical parameters for automotive systems
✓ Define SMART KPIs for systems engineering programs
✓ Recognize decision and quality management failures
✓ Document decision rationale for traceability
Critical outcome: Students can make and defend complex engineering decisions using systematic methods and implement quality management to prevent defects, not just detect them.
Evidence of success: — Student can perform WSM calculation for multi-criteria decision
Student can explain why QA is more cost-effective than QC
Student can identify critical parameters from FMEA and define control methods
Student can define actionable KPIs with decision triggers
Student understands that decision quality and product quality are interlinked

## Slide 36: 📚 Additional Resources for Students
Standards and Guidelines: — ISO 9001:2015: Quality Management Systems - Requirements
IATF 16949:2016: Automotive Quality Management System Requirements
ISO 26262-8:2018: Functional Safety - Supporting Processes
AIAG FMEA Handbook (5th Edition)
AIAG PPAP Manual (Production Part Approval Process)
Decision Analysis: — Keeney, R.L. & Raiffa, H.: "Decisions with Multiple Objectives: Preferences and Value Trade-offs
Saaty, T.L.: "Decision Making with the Analytic Hierarchy Process
Triantaphyllou, E.: "Multi-Criteria Decision Making Methods: A Comparative Study
Quality Management: — Juran's Quality Handbook (7th Edition)
"Out of the Crisis" by W. Edwards Deming
"The Toyota Way" by Jeffrey Liker
ASQ Certified Quality Engineer Handbook
Automotive-Specific: — APQP Manual (Advanced Product Quality Planning) - AIAG
ASPICE (Automotive SPICE) - Process Assessment Model
VDA 6.3 - Process Audit
Online Tools: — AHP-OS (free online AHP calculator)
Super Decisions (free AHP software)
Minitab / JMP (statistical analysis for quality metrics)

## Slide 37: 🔗 Connections to Other Sessions
Builds on: — Session 4: Requirements provide criteria for decisions; quality requirements drive critical parameters
Session 5: Architecture selection is MCDA application; design quality gates
Session 8: V&V is quality control; traceability enables quality management
Session 9: Risk analysis informs decisions; FMEA identifies critical parameters
Leads to: — Session 11: Supplier selection uses MCDA; supplier quality management
Session 12: Safety is critical decision criterion; safety = quality for life-critical systems
Session 15: Configuration management supports quality; measurement = metrics implementation
Key concept thread: — Session 9: HOW do we manage risk? (FMEA, risk analysis)
Session 10: HOW do we make decisions and ensure quality? (This session)
Session 11: HOW do we manage agreements and infrastructure? (Supplier/resource decisions)
Session 15: HOW do we manage information and configuration? (Technical management)
Decision-making appears in: — Session 5 (Architecture selection)
Session 11 (Make-vs-buy, supplier selection)
Session 13 (Life cycle cost trade-offs)
Every session implicitly (engineering is decision-making)
Quality management appears in: — Session 8 (V&V processes)
Session 12 (Functional safety quality requirements)
Session 15 (Quality of technical management processes)

## Slide 38: 🎬 Opening and Closing Strategies
Closing (Last 2 minutes):
Start with Boeing 737 MAX image on screen as students enter. Begin:
Before we start, look at this aircraft. Boeing 737 MAX. 346 people died. $20 billion in losses. 20-month grounding.
This wasn't a technology failure. Boeing knows how to build aircraft. This was a failure of decision-making and quality management.
Today, we're going to learn how to make systematic, defensible decisions and how to build quality in from the start. Because in automotive, the stakes are just as high - and you will be making these decisions.
Welcome to Session 10: Decision and Quality Management.
Return to the opening images (Boeing and GM):
We started with two catastrophic failures: Boeing 737 MAX and GM ignition switch. Both resulted from failures you now know how to prevent:
You can make systematic decisions using MCDA
You can analyze trade-offs and choose from Pareto frontier
You can distinguish QA from QC and emphasize prevention
You can identify and control critical parameters
You can define metrics that drive improvement
The exercise I've given you is your chance to practice. When you're faced with a real decision - sensor architecture, supplier selection, architecture choice - you'll have systematic methods.
Quality and decisions aren't separate from engineering - they ARE engineering. Make them count.
See you in Session 11, where we'll apply these decision methods to supplier selection and make-vs-buy decisions.

## Slide 39: 📈 Learning Objectives Mapping to Assessment
| Session Objective | Assessment Method | Success Criteria |
|-------------------|-------------------|------------------|
| Apply decision analysis techniques | Exercise Part 1 | Correctly applies WSM with documented criteria, weights, scores |
| Use MCDA for complex decisions | Exercise Part 1 | Complete decision matrix with sensitivity analysis |
| Distinguish QA vs QC | In-class quiz + conceptual understanding | Can classify activities correctly; explains prevention vs detection |
| Implement critical parameter management | Exercise Part 3 | Identifies appropriate critical parameters linked to FMEA/requirements; defines realistic controls |
| Define metrics and KPIs | Exercise Part 3 | KPIs meet SMART criteria; actionable decision triggers defined |
| Recognize decision/quality failures | Case study discussion | Can analyze GM/Boeing cases; identifies root causes |
| Select appropriate decision frameworks | Exercise Part 1 + in-class discussion | Chooses method appropriate to decision type; justifies choice |

## Slide 40
End of Session 10 Framework
Next: Session 11 (Agreement and Infrastructure Management)