## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 12: Specialty Engineering - Safety & Security'

## Slide 2: Specialty Engineering - Safety & Security
Session 12 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 12. Today we tackle a critical reality of modern automotive systems engineering: Safety and Security are no longer separate concerns - they are deeply intertwined.
Get safety wrong, and people die. Get security wrong, and your safe system becomes a weapon. Today, we learn how to engineer both simultaneously.

## Slide 4: Connection to Previous Sessions
Let's connect our journey to where we are today:
Session 1: We learned from engineering failures. Many were safety failures - Therac-25, Toyota unintended acceleration.
Session 4: We learned requirements engineering. Safety and security requirements need EXTRA rigor.
Session 8: We learned verification and validation. Safety-critical systems require specialized V&V approaches.
Session 9: We learned risk management and DFMEA. Today, we go deeper into safety-specific risk analysis.
Today's focus: Specialty Engineering - the disciplines that keep systems safe, secure, and usable.

## Slide 5: Why Safety & Security Engineering Is Critical
Let me show you the stakes we're dealing with:
Safety Statistics: — 1.19 million road traffic deaths globally per year (WHO)
10-30% of crashes involve system/component failures
Average recall cost: $300M+ for major OEMs
Legal liability: Multi-billion dollar settlements
Security Incidents: — 2015: Jeep Cherokee hacked remotely, 1.4M vehicles recalled
2016: Tesla Model S hacked via browser exploit
2020: Mercedes E-Class encryption broken
2022: Toyota production halted due to supplier cyberattack
The convergence: — Modern vehicles: 100+ ECUs, 100M+ lines of code
Connected vehicles: Remote attack surface
Autonomous vehicles: Safety + Security + AI uncertainty
Key insight: A cybersecurity breach can CAUSE safety failures. These disciplines must be integrated.
This is why specialty engineering is not optional - it's fundamental to modern automotive systems engineering.

## Slide 6: Real-World Example - The Jeep Cherokee Hack
Remember this case: July 2015, security researchers Charlie Miller and Chris Valasek demonstrated:
The attack: — Remote access via cellular connection
Exploited vulnerability in Uconnect infotainment system
Gained control of steering, brakes, transmission
Attack possible from anywhere in the US (cellular network)
The impact: — 1.4 million vehicles recalled
$1.4 billion settlement fund
NHTSA investigation and new regulations
Fundamental shift in automotive cybersecurity awareness
What failed: — Security failure: Infotainment system connected to CAN bus without isolation
Safety failure: No defense-in-depth - single exploit compromised safety-critical functions
Interoperability failure: Mixing security zones (entertainment + safety-critical)
Human factors failure: No driver indication of compromise
This demonstrates why we need INTEGRATED specialty engineering.
Today, I'll show you how to prevent this through systematic safety and security engineering.

## Slide 7: A Deceptively Complex System
Let me give you a challenge. Your manager says:
'Design an Adaptive Cruise Control system with automatic emergency braking.'
From Session 4, you know how to write requirements. But now, consider the specialty engineering questions:
Safety Questions: — What if the radar sensor fails? (Safety hazard)
What if the system brakes when it shouldn't? (False positive - safety risk)
What if it doesn't brake when it should? (False negative - safety critical)
What's the acceptable failure rate? (Quantitative safety requirement)
What safety integrity level is required? (ASIL classification)
Security Questions: — Can an attacker spoof the radar? (Sensor security)
Can someone remotely disable emergency braking? (System security)
Can they cause unintended braking? (Safety through security)
How do we authenticate sensor data? (Secure communication)
Human Factors Questions: — Will drivers understand when the system is active? (Situational awareness)
Will they over-rely on it? (Automation complacency)
Can they override it in emergencies? (Human-in-the-loop)
Is the interface intuitive under stress? (Cognitive load)
Suddenly, our 'simple' ACC is a complex specialty engineering challenge.

## Slide 8: Safety Analysis - The Systematic Approach
Safety engineering is NOT about testing more. It's about ANALYZING systematically to identify what could go wrong BEFORE it happens.
The safety analysis process:
Step 1: Hazard Identification — What can go wrong? (Brainstorming, historical data, standards)
Example: 'Vehicle accelerates when driver didn't command it'
Step 2: Risk Analysis — How likely? (Probability)
How severe? (Consequence)
Risk = Severity × Probability
Step 3: Risk Evaluation — Is this risk acceptable?
What's our risk tolerance?
Automotive: ISO 26262 defines acceptability criteria
Step 4: Risk Treatment — Eliminate (design out the hazard)
Mitigate (reduce probability or severity)
Accept (if below threshold)
Transfer (insurance, contractual)
Step 5: Verification — Prove the risk has been adequately addressed
Safety testing, analysis, review
Three powerful methods we'll explore:
Fault Tree Analysis (FTA) - Top-down
Failure Mode and Effects Analysis (FMEA) - Bottom-up
HAZOP (Hazard and Operability Study) - Systematic deviation analysis
Let me show you each.

## Slide 9: Fault Tree Analysis (FTA)
Fault Tree Analysis (FTA) is a TOP-DOWN deductive method.
How it works:
1. Start with top event (hazardous situation):
Example: 'Vehicle fails to brake for obstacle'
2. Work backward — what could cause this?
Radar sensor failure OR
ECU processing failure OR
Brake actuator failure OR
Software algorithm failure
3. Continue decomposing each cause:
Radar sensor failure caused by:
Power supply failure AND
No backup sensor available
4. Use logic gates: — AND gate: All inputs must occur (Power fail AND no backup)
OR gate: Any input causes event (Sensor OR ECU OR actuator fail)
5. Calculate probability: — If each component has known failure rate
AND gate: P(A AND B) = P(A) × P(B)
OR gate: P(A OR B) = P(A) + P(B) - P(A)×P(B)
Real automotive example - Brake System FTA:
Top Event: 'Loss of braking function'
├─ OR ─ Hydraulic failure
│ ├─ AND ─ Master cylinder leak
│ │ ├─ Seal degradation
│ │ └─ No brake fluid level warning
│ └─ OR ─ Brake line rupture
├─ OR ─ Electronic control failure
│ ├─ AND ─ ECU failure
│ │ ├─ Software bug
│ │ └─ Watchdog timer disabled
│ └─ OR ─ Sensor failure
└─ OR ─ Driver input failure
└─ Pedal mechanism broken
FTA benefits: — Visual representation of failure paths
Quantitative risk assessment
Identifies single points of failure
Shows where redundancy is needed
FTA limitations: — Time-consuming for complex systems
Requires knowing all failure modes upfront
Complement with bottom-up methods (FMEA)

## Slide 10: Failure Mode and Effects Analysis (FMEA)
FMEA is a BOTTOM-UP inductive method. We looked at this in Session 9 for design. Now we apply it specifically for safety.
FMEA Process:
1. Identify components/functions — Example: ACC radar sensor, ECU, brake actuator
2. For each component, ask: — What are the possible failure modes? (How can it fail?)
What are the effects? (What happens when it fails?)
What are the causes? (Why does it fail?)
How do we detect it? (How do we know it failed?)
3. Rate each failure mode: — Severity (S): 1-10 (1=no effect, 10=catastrophic)
Occurrence (O): 1-10 (1=rare, 10=frequent)
Detection (D): 1-10 (1=certain detection, 10=no detection)
RPN (Risk Priority Number): S × O × D
4. Prioritize actions: — High RPN = high priority for mitigation
Automotive example - ACC Radar Sensor FMEA:
| Component | Failure Mode | Effect | S | Cause | O | Detection | D | RPN | Action |
|-----------|--------------|--------|---|-------|---|-----------|---|-----|--------|
| Radar sensor | No output signal | Loss of ACC/AEB function | 9 | Power supply failure | 3 | Self-diagnostic detects | 2 | 54 | Add redundant power, driver warning |
| Radar sensor | False object detection | Unintended braking | 8 | Rain/snow interference | 5 | Plausibility check with camera | 4 | 160 | Sensor fusion, false positive filtering |
| Radar sensor | Degraded range | Reduced reaction time | 7 | Sensor blockage (dirt) | 6 | Range monitoring | 3 | 126 | Sensor cleaning system, blockage detection |
| ECU | Processing delay >100ms | Late braking response | 9 | CPU overload | 2 | Watchdog timer | 2 | 36 | Task prioritization, WCET analysis |
| Brake actuator | Stuck inactive | No emergency braking | 10 | Mechanical jam | 1 | Actuation monitoring | 3 | 30 | Regular maintenance, redundancy |
ISO 26262 enhancement: — In functional safety FMEA, we add ASIL (Automotive Safety Integrity Level)
ASIL A (lowest) to ASIL D (highest)
Determines required safety measures and verification rigor
Key difference from Session 9: — Design FMEA: Focus on design robustness
Safety FMEA: Focus on hazardous failures with safety consequences — Safety FMEA feeds into HARA (next section)
FMEA benefits: — Systematic, comprehensive
Quantitative prioritization
Cross-functional team exercise
FMEA limitations: — Doesn't capture combinations of failures (use FTA for that)
Time-intensive
Quality depends on team expertise

## Slide 11: HAZOP (Hazard and Operability Study)
HAZOP is a structured brainstorming method using guide words to systematically explore deviations.
HAZOP Guide Words: — NO/NOT: Complete negation (e.g., no braking)
MORE: Quantitative increase (e.g., more braking force)
LESS: Quantitative decrease (e.g., less braking force)
AS WELL AS: Qualitative addition (e.g., braking + steering)
PART OF: Qualitative decrease (e.g., only front brakes)
REVERSE: Opposite (e.g., acceleration instead of braking)
OTHER THAN: Complete substitution (e.g., steering instead of braking)
HAZOP Process:
1. Define system and boundaries — Example: ACC with AEB system
2. Break into nodes/sections — Node 1: Object detection (radar + camera)
Node 2: Decision logic (ECU)
Node 3: Brake actuation
3. For each node, apply guide words: — Design intent: 'Radar detects obstacle at 150m range'
NO: Radar detects NO obstacle → Missed detection → Collision
MORE: Radar range MORE than 150m → Earlier braking → False positives
LESS: Radar range LESS than 150m → Late detection → Insufficient stopping distance
REVERSE: Radar reports object moving toward instead of away → Wrong TTC calculation
4. Analyze each deviation: — Is it hazardous?
What are the causes?
What are the consequences?
What safeguards exist?
What actions are needed?
Example HAZOP for ACC 'Set Speed' function:
| Parameter | Guide Word | Deviation | Cause | Consequence | Safeguard | Action |
|-----------|------------|-----------|-------|-------------|-----------|--------|
| Speed | NO | No speed set | Switch failure | No ACC activation | Driver awareness | Add diagnostic check |
| Speed | MORE | Speed set higher than current | Sensor error | Sudden acceleration | Speed limit check | Add plausibility check |
| Speed | LESS | Speed set lower than current | Software bug | Hard braking | Deceleration rate limit | Code review, testing |
| Speed | REVERSE | Speed increases when should decrease | Control logic inversion | Dangerous acceleration | Independent safety monitor | Add inverse logic check |
HAZOP benefits: — Catches creative failure modes
Good for complex interactions
Team-based (different perspectives)
HAZOP limitations: — Requires experienced facilitator
Can be exhaustive (time-consuming)
Qualitative (not quantitative like FTA/FMEA)
Automotive application: — HAZOP used in early design phases
FMEA used for detailed component analysis
FTA used for critical hazard investigation
All three are complementary - use together for comprehensive safety analysis —--
#### Part 2: HARA and ISO 26262 Functional Safety (Slides 12-15, ~12 minutes)

## Slide 12: ISO 26262 - The Automotive Functional Safety Standard
ISO 26262 is the international standard for functional safety in automotive electrical/electronic systems. It's based on IEC 61508 but tailored for automotive.
What is Functional Safety? — 'Absence of unreasonable risk due to hazards caused by malfunctioning behavior of E/E systems'
Focus: Safety failures caused by SYSTEM MALFUNCTIONS (not physical crashes, driver error, etc.)
ISO 26262 Structure (12 parts): — Part 1: Vocabulary
Part 2: Management of functional safety
Part 3: Concept phase (← HARA is here)
Part 4: Product development - System level
Part 5: Product development - Hardware level
Part 6: Product development - Software level
Part 7: Production and operation
Part 8: Supporting processes
Part 9: ASIL-oriented and safety-oriented analyses
Part 10: Guidelines
Part 11: Semiconductors
Part 12: Motorcycles
Key concepts:
1. Safety Lifecycle (V-Model for safety):
Concept phase → System development → Hardware/Software development → Integration → Testing → Operation
Each phase has safety requirements, activities, and work products
2. ASIL (Automotive Safety Integrity Level): — ASIL A (lowest) → B → C → ASIL D (highest)
Determines rigor of safety requirements and verification
Higher ASIL = more stringent methods, more verification, more independence
3. Safety Mechanisms: — Technical measures to detect/control faults
Examples: Watchdog timers, CRC checks, redundancy, diverse programming
4. Traceability: — Every safety requirement must trace to hazard
Every safety requirement must be verified
Bidirectional traceability (remember Session 4!)
ISO 26262 is MANDATORY for new vehicle developments in most markets.
Let me show you the critical starting point: HARA.

## Slide 13: HARA - Hazard Analysis and Risk Assessment
HARA is the foundation of ISO 26262. It determines WHAT safety measures are needed and HOW rigorous they must be.
HARA Process (4 steps):
Step 1: Hazard Identification — Systematically identify hazards (What can go wrong at vehicle level?)
Focus on E/E system malfunctions
Sources: Brainstorming, FTA, FMEA, historical data, standards
Example hazards for ACC/AEB: — Unintended braking (false positive)
Failure to brake (false negative)
Insufficient braking force
Delayed braking response
Loss of ACC function
Step 2: Situational Analysis — In what driving situations can this hazard occur?
Operational situations: Highway, urban, parking, off-road
Example: — Hazard: 'Unintended full braking'
Situation 1: Highway at 120 km/h
Situation 2: Urban at 50 km/h
Situation 3: Parking lot at 10 km/h
Step 3: Risk Classification (The core of HARA)
For each hazard + situation, rate three parameters:
a) Severity (S) — Consequence of hazard:
S0: No injuries
S1: Light to moderate injuries
S2: Severe/life-threatening injuries (survival probable)
S3: Life-threatening/fatal injuries (survival uncertain)
b) Exposure (E) — Probability of operational situation:
E0: Incredible (<0.1% of operating time)
E1: Very low probability (0.1%-1%)
E2: Low probability (1%-10%)
E3: Medium probability (10%-50%)
E4: High probability (>50%)
c) Controllability (C) — Can driver/others avoid harm?
C0: Controllable in general
C1: Simply controllable (>99% of drivers)
C2: Normally controllable (>90% of drivers)
C3: Difficult/uncontrollable (<90% of drivers)
Step 4: ASIL Determination — Combine S + E + C using ISO 26262 table
Result: ASIL QM (no safety requirements) or ASIL A/B/C/D
ASIL Table (simplified):
| Severity | Exposure | Controllability | ASIL |
|----------|----------|-----------------|------|
| S3 | E4 | C3 | ASIL D (Highest) |
| S3 | E3 | C3 | ASIL D |
| S3 | E4 | C2 | ASIL C |
| S2 | E4 | C3 | ASIL C |
| S3 | E2 | C2 | ASIL B |
| S2 | E3 | C2 | ASIL B |
| S1 | E4 | C2 | ASIL A |
| S1 | E2 | C1 | QM (Quality Management) |
Let me show you a real example.

## Slide 14: HARA Example - Adaptive Cruise Control
Let's work through a complete HARA for an ACC system.
HARA Example - ACC System:
| ID | Hazard | Situation | S | E | C | ASIL | Rationale |
|----|--------|-----------|---|---|---|------|-----------|
| H-ACC-01 | Unintended full braking | Highway 120 km/h, dry road, following vehicle | S3 | E3 | C2 | C | S3: Rear-end collision likely fatal<br>E3: ACC used 20% on highway<br>C2: Most drivers can steer to shoulder |
| H-ACC-02 | Unintended full braking | Urban 50 km/h, intersection | S2 | E2 | C1 | A | S2: Rear-end at lower speed<br>E2: ACC rarely used in urban<br>C1: Driver easily stops/steers |
| H-ACC-03 | Failure to brake for stopped vehicle | Highway 120 km/h, lead vehicle emergency stops | S3 | E4 | C3 | D | S3: Fatal collision likely<br>E4: Common scenario<br>C3: Insufficient time to react |
| H-ACC-04 | Insufficient braking force | Highway 100 km/h, lead vehicle decelerates | S2 | E4 | C2 | B | S2: Minor collision possible<br>E4: Common scenario<br>C2: Driver can brake manually |
| H-ACC-05 | Late braking response (>500ms delay) | Highway 120 km/h, lead vehicle brakes | S3 | E3 | C2 | C | S3: Collision likely severe<br>E3: Moderate frequency<br>C2: Driver can react if alerted |
| H-ACC-06 | Loss of ACC function | Highway cruising | S0 | E4 | C0 | QM | S0: No safety impact (driver takes over)<br>E4: N/A<br>C0: Normal driving |
What this tells us:
ASIL D (H-ACC-03: Failure to brake for stopped vehicle):
Highest rigor required — Independent safety element required
Extensive verification (fault injection, statistical testing)
Tool qualification for software tools
Hardware random failure metrics (PMHF <10 FIT)
Software development per ASIL D (defensive programming, diverse implementation)
ASIL C (H-ACC-01, H-ACC-05):
High rigor (but less than D)
Safety mechanisms required
Comprehensive testing
ASIL B (H-ACC-04):
Moderate rigor
Basic safety mechanisms
Standard testing
ASIL A (H-ACC-02):
Low rigor
Best practices
QM (H-ACC-06):
Quality management (no safety requirements)
Standard development process
Key insight: — Different hazards → Different ASIL → Different development effort
ASIL D functions may require 10x more effort than ASIL A
Architecture must consider ASIL decomposition (break ASIL D into multiple lower ASIL)

## Slide 15: Safety Concept and Requirements
After HARA, we develop the Safety Concept — HOW we'll address each hazard.
From HARA to Implementation:
1. Safety Goals (Top-level)
One safety goal per hazard
Inherits ASIL from hazard
Example (H-ACC-03: Failure to brake): — SG-ACC-03: 'Prevent collision with stopped vehicle ahead' [ASIL D]
2. Functional Safety Requirements (FSR) — Decompose safety goal into specific requirements
Allocate to vehicle functions
Example FSRs for SG-ACC-03: — FSR-ACC-03.1: 'Detect stopped vehicles at ≥150m range with 99.9% probability' [ASIL D]
FSR-ACC-03.2: 'Calculate time-to-collision (TTC) with ≤50ms latency' [ASIL D]
FSR-ACC-03.3: 'Initiate emergency braking when TTC <2.5s' [ASIL D]
FSR-ACC-03.4: 'Achieve minimum deceleration of 6 m/s² within 300ms' [ASIL D]
FSR-ACC-03.5: 'Provide independent monitoring of braking function' [ASIL D]
3. Technical Safety Requirements (TSR) — Allocate FSRs to system architecture
Hardware + Software + Safety Mechanisms
Example TSRs: — TSR-ACC-HW-01: 'Radar sensor shall have dual-channel processing' [ASIL D]
TSR-ACC-SW-01: 'Object detection algorithm shall use sensor fusion (radar + camera)' [ASIL D]
TSR-ACC-SW-02: 'Software shall implement E2E (end-to-end) protection for CAN messages' [ASIL D]
TSR-ACC-SM-01: 'Independent safety monitor shall check TTC calculation with diverse algorithm' [ASIL D]
4. Safety Mechanisms (Examples for ASIL D): — Hardware level: — Dual-core lockstep processor (detects transient faults)
ECC (Error Correcting Code) memory
Watchdog timer with windowed monitoring
Voltage/clock monitoring
Software level: — Plausibility checks (range, rate-of-change)
Defensive programming (assertions, boundary checks)
Control flow monitoring
CRC for data integrity
E2E protection for communication
System level: — Sensor fusion (radar + camera)
Diverse redundancy (different algorithms)
Safe state transition (warn driver, gradual degradation)
Verification per ASIL D: — Back-to-back testing (compare diverse implementations)
Fault injection (test safety mechanisms)
Requirements coverage analysis
Code coverage (MC/DC for ASIL D)
Independent safety assessment
Traceability (critical for ISO 26262):
Hazard → Safety Goal → FSR → TSR → Implementation → Test Cases
Key takeaway:
ISO 26262 provides a SYSTEMATIC framework from hazard identification to verified safe system. It's not bureaucracy - it's disciplined engineering that saves lives.

## Slide 16
#### Part 3: Cybersecurity in Automotive Systems (Slides 16-19, ~12 minutes)

## Slide 17: The Cybersecurity Imperative
Modern vehicles are computers on wheels — and computers can be hacked.
The evolution of automotive attack surface:
1990s vehicle: — Standalone ECUs, no external connectivity
Physical access required for any attack
Attack surface: ~1 (diagnostic port)
2010s vehicle: — 100+ ECUs, connected via CAN/LIN/FlexRay
Cellular (telematics), WiFi, Bluetooth
Attack surface: ~10-20 entry points
2020s+ vehicle: — Vehicle-to-Everything (V2X) communication
Over-the-air (OTA) updates
Cloud connectivity, mobile apps
Third-party app integration
Attack surface: 100+ potential entry points
Why cybersecurity is critical:
1. Safety impact: — Jeep Cherokee: Hacked steering/brakes (safety-critical)
Tesla: Hacked via browser, could control vehicle
Attack on safety function = SAFETY FAILURE
2. Privacy impact: — Vehicles collect location, driving behavior, personal data
GDPR and privacy regulations
Data breach liability
3. Business impact: — Recalls (1.4M Jeep vehicles)
Brand reputation damage
Legal liability
4. Regulatory drivers: — UN R155 (Cybersecurity): Mandatory for new vehicle types (2024+)
UN R156 (Software Updates): Mandatory for OTA updates
SAE J3061: Cybersecurity guidebook
ISO/SAE 21434: Automotive cybersecurity standard (2021)
The convergence of safety and security: — Cybersecurity vulnerability can CAUSE safety hazard
Example: Disable AEB via remote exploit → Collision
ISO 26262 + ISO 21434 must be integrated
This is why we need systematic cybersecurity engineering — not just penetration testing.

## Slide 18: ISO/SAE 21434 - Automotive Cybersecurity Standard
ISO/SAE 21434 (published 2021) is to cybersecurity what ISO 26262 is to functional safety.
Cybersecurity Engineering Lifecycle:
1. Concept Phase: — Asset identification: What are we protecting? (Data, functions, vehicle control)
Threat modeling: What attacks are possible? (STRIDE, attack trees)
Risk assessment: TARA (Threat Analysis and Risk Assessment)
Cybersecurity goals: What must be protected and to what level?
2. Product Development: — Cybersecurity requirements: Derived from cybersecurity goals
Design: Security architecture, defense-in-depth
Implementation: Secure coding, cryptography, key management
Verification: Penetration testing, fuzz testing, vulnerability scanning
3. Production: — Secure manufacturing (prevent supply chain attacks)
Key injection and provisioning
4. Operations: — Vulnerability monitoring (CVE databases)
Incident response
Security updates (OTA)
5. Decommissioning: — Secure data deletion
Certificate revocation
Key concepts:
CAL (Cybersecurity Assurance Level): — Similar to ASIL for safety
CAL 1 (low) → CAL 4 (high)
Determined by attack feasibility and impact
Higher CAL = more rigorous security measures
TARA (Threat Analysis and Risk Assessment): — Parallel to HARA for safety
Identify assets → Threats → Attack paths → Risk rating → Cybersecurity goals
Let me show you how TARA works.

## Slide 19: TARA - Threat Analysis and Risk Assessment
TARA is the cybersecurity equivalent of HARA. It identifies threats and determines required security levels.
TARA Process (5 steps):
Step 1: Asset Identification — Assets: What has value and must be protected?
Example (ACC/AEB system): — Asset 1: Vehicle control (braking, acceleration)
Asset 2: Driver personal data (location, routes, behavior)
Asset 3: Vehicle identity (VIN, authentication credentials)
Asset 4: Software/firmware integrity
Step 2: Threat Scenario Identification — Use STRIDE model or attack libraries
STRIDE Model: — Spoofing (fake identity)
Tampering (modify data/code)
Repudiation (deny actions)
Information disclosure (data leak)
Denial of service (make unavailable)
Elevation of privilege (gain unauthorized access)
Example threats for ACC: — T1: Spoof radar sensor data (S - Spoofing)
T2: Tamper with ECU software to disable AEB (T - Tampering)
T3: Intercept and modify CAN messages (T - Tampering)
T4: Denial of service on brake control (D - DoS)
T5: Extract encryption keys from ECU (I - Information disclosure)
Step 3: Attack Path Analysis — How can attacker achieve threat?
Attack vector: Entry point (cellular, OBD-II, Bluetooth, etc.)
Attack feasibility: How difficult?
Example (T2: Tamper with ECU software): — Attack path:
Exploit vulnerability in infotainment system (cellular connection)
Pivot to internal vehicle network (CAN bus)
Send malicious CAN messages to ACC ECU
Exploit buffer overflow in ECU to inject code
Modify safety-critical braking function
Attack Feasibility Rating (per ISO 21434): — Elapsed time: Minutes to months
Specialist expertise: Layman to expert
Knowledge of system: Public to confidential
Window of opportunity: Unlimited to limited
Equipment: Standard to bespoke
Feasibility: Very High / High / Medium / Low / Very Low
Step 4: Impact Rating — Safety impact: Could cause injury/death? (S0-S3, like HARA)
Financial impact: Cost of attack
Operational impact: Vehicle unusable?
Privacy impact: Data exposure
Step 5: Risk Determination — Combine Attack Feasibility + Impact — Result: CAL (Cybersecurity Assurance Level) 1-4
Risk Matrix (simplified):
| Impact | Attack Feasibility | CAL |
|--------|--------------------|-----|
| Severe (Safety) | High | CAL 4 |
| Severe (Safety) | Medium | CAL 3 |
| Major (Operational) | High | CAL 3 |
| Moderate | Medium | CAL 2 |
| Minor | Low | CAL 1 |
Example TARA for ACC:
| Threat ID | Threat | Attack Feasibility | Impact | CAL | Cybersecurity Goal |
|-----------|--------|--------------------|--------|-----|---------------------|
| T1 | Spoof radar sensor data | Medium (requires RF equipment) | Severe (false braking or no braking) | CAL 3 | CG-1: Protect sensor data integrity |
| T2 | Tamper with ECU software | High (remote via cellular) | Severe (disable AEB) | CAL 4 | CG-2: Prevent unauthorized software modification |
| T3 | Modify CAN messages | High (access via OBD-II) | Severe (vehicle control) | CAL 4 | CG-3: Authenticate and protect CAN messages |
| T4 | DoS on brake control | Medium (requires CAN access) | Severe (loss of braking) | CAL 3 | CG-4: Ensure availability of safety functions |
| T5 | Extract encryption keys | Low (requires physical access + expert) | Major (enables other attacks) | CAL 2 | CG-5: Protect cryptographic material |
From cybersecurity goals to requirements (like safety):
CG-2: Prevent unauthorized software modification [CAL 4]
→ CSR-2.1: 'ECU shall implement secure boot with cryptographic verification of firmware integrity'
→ CSR-2.2: 'Software updates shall be authenticated using asymmetric cryptography (RSA-2048 or ECC-256)'
→ CSR-2.3: 'ECU shall detect tampering attempts and enter secure mode within 500ms'
Key takeaway:
TARA provides systematic framework to identify threats, assess risk, and determine cybersecurity requirements - parallel to HARA for safety.

## Slide 20: Cybersecurity Architecture - Defense in Depth
The key principle of cybersecurity architecture is Defense in Depth — multiple layers of protection.
Layered Security Architecture for Automotive:
Layer 1: Perimeter Security — Goal: Prevent unauthorized external access
Mechanisms:
Firewall between external interfaces (cellular, WiFi) and vehicle network
Intrusion Detection System (IDS) monitoring network traffic
Whitelisting of allowed communication patterns
Example: Gateway ECU filters all external-to-CAN traffic
Layer 2: Network Security — Goal: Protect communication between ECUs
Mechanisms:
Network segmentation (separate safety-critical from infotainment)
Message Authentication Code (MAC) on CAN messages
End-to-End (E2E) protection (crypto + sequence counter)
Encrypted communication for sensitive data
Example: ACC ECU verifies MAC on all received CAN messages
Layer 3: ECU Security — Goal: Protect individual ECUs from compromise
Mechanisms:
Secure boot: Verify firmware integrity before execution (cryptographic signature)
Runtime integrity: Monitor for code tampering
Memory protection: Isolate safety-critical code (MPU - Memory Protection Unit)
Secure storage: Encrypted key storage (HSM - Hardware Security Module)
Example: ACC ECU uses secure boot - won't execute unsigned firmware
Layer 4: Application Security — Goal: Prevent exploitation of software vulnerabilities
Mechanisms:
Secure coding: MISRA C, buffer overflow protection
Input validation: Sanitize all external inputs
Least privilege: Functions run with minimum necessary permissions
Sandboxing: Isolate untrusted code
Example: Radar processing validates all sensor data ranges before use
Layer 5: Data Security — Goal: Protect confidential and personal data
Mechanisms:
Encryption at rest (stored data)
Encryption in transit (transmitted data)
Access control (who can read what)
Data anonymization
Example: Driver location data encrypted using AES-256
Layer 6: Monitoring and Response — Goal: Detect attacks and respond
Mechanisms:
IDS (Intrusion Detection): Detect anomalous behavior
Logging: Record security events
Incident response: Automated reaction to attacks
OTA updates: Patch vulnerabilities
Example: Vehicle logs all authentication failures, reports to cloud for analysis
Real Architecture Example - ACC/AEB System:
External Interface (Cellular/WiFi) ↓ [Firewall/IDS in Gateway ECU] ← Layer 1 ↓ CAN Bus with MAC/E2E ← Layer 2 ↓ [ACC ECU with Secure Boot + HSM] ← Layer 3 ↓ [Safety-Critical Software with Input Validation] ← Layer 4 ↓ [Encrypted Data Storage] ← Layer 5 ↓ [Anomaly Detection + Logging] ← Layer 6
Security Mechanisms Mapped to CAL:
CAL 4 (highest): All 6 layers required
Secure boot + HSM mandatory
E2E protection on all messages
Independent security monitoring
Penetration testing by external experts
CAL 3: Layers 1-5 required
Secure boot recommended
MAC on critical messages
Code review and static analysis
CAL 2: Layers 1-4 required
Basic authentication
Input validation
CAL 1: Layers 1-3 required
Basic firewall
Standard secure coding
Integration with Safety: — Safety-critical functions (ASIL D) typically also CAL 3-4
Security failure → Safety failure
Example: If attacker disables AEB (security breach), collision occurs (safety hazard)
ASIL D + CAL 4 = Maximum rigor
Key principle:
No single layer is perfect - assume each can be breached. Defense in depth ensures attacker must breach MULTIPLE layers.

## Slide 21
#### Part 4: Interoperability Engineering (Slides 20-21, ~8 minutes)

## Slide 22: Interoperability - Connecting Systems Safely
Modern vehicles don't operate in isolation - they're part of a complex ecosystem. Interoperability is the ability of systems to work together.
The Interoperability Challenge:
Internal interoperability (within vehicle):
100+ ECUs from multiple suppliers
Different communication protocols (CAN, LIN, FlexRay, Ethernet)
Mixed criticality (ASIL D + QM on same network)
Different update cycles (infotainment changes yearly, powertrain lasts 10+ years)
External interoperability (beyond vehicle):
V2V (Vehicle-to-Vehicle): Collision avoidance, platooning
V2I (Vehicle-to-Infrastructure): Traffic lights, road signs, tolling
V2P (Vehicle-to-Pedestrian): Smartphone detection
V2N (Vehicle-to-Network): Cloud services, OTA updates
Collectively: V2X (Vehicle-to-Everything)
Interoperability Requirements:
1. Protocol Compatibility — Standards-based communication (IEEE 802.11p, C-V2X, DSRC)
Consistent message formats (SAE J2735 for V2X messages)
2. Semantic Interoperability — Same meaning of data across systems
Example: What is 'vehicle speed'? GPS speed? Wheel speed? CAN speed?
Coordinate systems: Different ECUs may use different reference frames
3. Timing and Synchronization — Critical for distributed control
Example: Sensor fusion requires synchronized timestamps
IEEE 1588 (Precision Time Protocol) for automotive Ethernet
4. Security Interoperability — Trust across organizations (OEM ↔ Infrastructure provider)
PKI (Public Key Infrastructure) for authentication
Certificate management (issuance, revocation, renewal)
5. Safety Interoperability — Fail-safe behavior across systems
Example: If V2I signal is lost, vehicle must degrade gracefully
Real-world example - V2X for Emergency Braking:
Scenario: Lead vehicle emergency brakes, sends V2V alert
Interoperability requirements: — Protocol: Both vehicles use same V2V protocol (C-V2X)
Message: Standard 'Emergency Electronic Brake Lights' message (SAE J2735)
Timing: Message received within 100ms (latency requirement)
Security: Message authenticated (prevent spoofing)
Safety: Receiving vehicle verifies with onboard sensors (defense in depth)
Human factors: Driver alerted appropriately (avoid distraction)
Standards enabling interoperability: — SAE J2735: Message set dictionary for V2X
SAE J2945: Dedicated Short Range Communications (DSRC) applications
3GPP C-V2X: Cellular V2X communication
ISO 20077: Extended Vehicle (ExVe) - standardized data exchange
AUTOSAR: Standardized software architecture for ECUs
Challenges: — Fragmentation: Different regions use different standards (US vs EU vs China)
Legacy compatibility: New vehicles must work with old infrastructure
Graceful degradation: System must work even if interoperability fails
Key design principle: — Don't rely solely on external systems for safety — Example: V2V alert is supplementary; onboard sensors are primary
This is defense in depth applied to interoperability

## Slide 23: AUTOSAR - Automotive Open System Architecture
AUTOSAR (Automotive Open System Architecture) is a key enabler of interoperability within vehicles.
What is AUTOSAR? — Standardized software architecture for automotive ECUs
Developed by OEMs and suppliers (partnership)
Goal: Portability, reusability, interoperability
AUTOSAR Layered Architecture:
Layer 1: Application Layer — Software components (SWCs)
Business logic (e.g., cruise control algorithm)
Standardized interfaces (ports)
Layer 2: Runtime Environment (RTE) — Communication abstraction
SWCs communicate via RTE (don't know about hardware)
Layer 3: Basic Software (BSW) — Services: Operating system, communication, diagnostics, memory
ECU Abstraction: Hides hardware details
Microcontroller Abstraction: Driver layer
Layer 4: Microcontroller — Hardware (CPU, peripherals)
Benefits for interoperability:
1. Supplier independence: — SWCs are portable across different ECU hardware
Example: ACC algorithm from Supplier A runs on ECU from Supplier B
2. Standardized communication: — CAN, LIN, FlexRay, Ethernet handled by BSW
Application layer doesn't need to know protocol details
3. Configuration over coding: — System integration via configuration files (ARXML)
Less error-prone than manual coding
4. Diagnostics and calibration: — Standardized diagnostic services (UDS - Unified Diagnostic Services)
Standardized calibration interfaces (XCP, CCP)
AUTOSAR for Safety (AUTOSAR Safety Extensions): — E2E protection: End-to-end communication safety
Timing protection: OS-level monitoring of task execution
Memory protection: MPU configuration
Supports ISO 26262 compliance
AUTOSAR Adaptive (for high-performance ECUs): — Service-oriented architecture (SOA)
Dynamic configuration
POSIX OS (e.g., Linux)
For ADAS, autonomous driving, high-performance compute
Real impact: — Without AUTOSAR: Every OEM-supplier pair has custom integration (N×M problem)
With AUTOSAR: Standardized interfaces (N+M problem)
Reduces integration effort by orders of magnitude
Interoperability enabled: — ECUs from different suppliers work together
Software reusable across vehicle platforms
Faster time-to-market, lower cost
AUTOSAR is foundational to modern automotive systems engineering - not just for interoperability, but for managing complexity.

## Slide 24
#### Part 5: Human Factors Engineering (Slides 22-23, ~8 minutes)

## Slide 25: Human Factors - Designing for Real Humans
We've engineered safety and security. But if humans can't use the system correctly, all that engineering is wasted.
Human Factors Engineering (also called Ergonomics or Human-Machine Interface design) ensures systems are:
Usable: Humans can operate them effectively
Safe: Humans don't make dangerous errors
Efficient: Humans can perform tasks quickly
Satisfying: Users have positive experience
Why human factors matter in automotive:
Failure cases: — Tesla Autopilot crashes: Drivers misunderstood automation level (thought it was Level 4 when it's Level 2)
NHTSA study: 94% of crashes involve human error
Toyota unintended acceleration: Pedal misapplication (human error) + poor floor mat design (design error)
The challenge: — Drivers have limited attention — Drivers have limited training (no engineering degree required!)
Drivers operate under stress (emergencies)
Drivers have diverse capabilities (young, elderly, disabled)
Drivers over-trust automation (complacency)
Drivers under-trust automation (disuse)
Key human factors principles for automotive:
1. Situational Awareness — Driver must understand system state at all times
Example: Is ACC active? What speed is set? Is AEB enabled?
Design: Clear visual indicators, consistent location
2. Mode Confusion Prevention — Different modes must be visually distinct
Bad example: Autopilot icon looks similar whether active or standby
Good example: Active = green border + animation, Inactive = gray icon
3. Attention Management — Don't overload driver with information
Prioritize critical information
Example: Collision warning gets central display + sound + haptic, non-critical info on side screen
4. Affordances and Mappings — Controls should suggest their function
Example: Steering wheel buttons for speed control (intuitive location)
Bad example: Touchscreen-only controls (no tactile feedback, requires looking away)
5. Error Tolerance — System should prevent/recover from human errors
Example: If driver accidentally presses SET while speeding, system limits to legal maximum
Example: Confirmation required for critical actions
6. Feedback and Transparency — System provides clear feedback for user actions
Example: Audible beep when cruise speed is set, visual confirmation on display
Let me show you specific examples.

## Slide 26: Human Factors Analysis - Automation Levels
One of the most critical human factors issues in modern automotive: Understanding automation levels.
SAE J3016 - Levels of Driving Automation:
Level 0 - No Automation — Human does everything
Human factors: Traditional vehicle ergonomics
Level 1 - Driver Assistance — System: Either steering OR speed control (not both)
Example: Traditional cruise control, lane keeping assist
Human: Monitors environment, ready to take over immediately
Human factors challenge: Knowing when system is active
Level 2 - Partial Automation — System: Both steering AND speed control simultaneously
Example: Tesla Autopilot, GM Super Cruise, ACC with lane centering
Human: MUST monitor environment constantly, hands on wheel
Human factors challenge: Over-reliance, distraction, 'it's driving itself' misconception
Critical requirement: Driver monitoring system (camera watching driver)
Level 3 - Conditional Automation — System: Full driving in specific conditions (e.g., highway traffic jam)
Human: Can disengage (look at phone) but must respond to takeover request
Example: Audi A8 Traffic Jam Pilot (limited deployment)
Human factors challenge: Transition time - how long does driver need to regain situational awareness?
Design requirement: Minimum takeover time (typically 10+ seconds)
Level 4 - High Automation — System: Full driving in defined conditions, no human intervention needed
Human: Passenger (can sleep)
Fallback: System handles emergencies (e.g., pulls over safely)
Example: Waymo robotaxis (geo-fenced areas)
Human factors challenge: What happens at boundary of operational design domain (ODD)?
Level 5 - Full Automation — System: Drives anywhere, anytime
Human: Just a passenger
Not yet available
The Level 2-3 Transition Problem:
Level 2: Driver MUST monitor constantly
Level 3: Driver CAN disengage but must respond to takeover
Human factors issue: — Humans are TERRIBLE at vigilance tasks (monitoring with no action)
After 10-20 minutes of no intervention, driver attention drifts
Studies show takeover performance degrades severely after distraction
Design solutions: — Driver monitoring: Eye tracking, head position, steering wheel sensors
Escalating warnings: Visual → Audible → Haptic (seat vibration) → Automatic pullover
Clear mode indication: Large, central, unambiguous display of automation level
Training: Educate drivers on system capabilities and limitations
Real example - GM Super Cruise: — Level 2 system
Human factors engineering: — Eye tracking camera on steering column (monitors driver attention)
Light bar on steering wheel (green = hands-free OK, red = hands required)
Escalating alerts if driver not attending
Automatic pullover if driver unresponsive
Geo-fenced to mapped highways only (clear ODD)
Name avoids 'autopilot' misconception
Key human factors requirements for ADAS:
1. Mode awareness: — REQ-HF-01: 'System shall display automation level on primary instrument cluster with ≥99% visibility'
2. Attention management: — REQ-HF-02: 'Level 2 system shall monitor driver attention with ≤2s detection latency'
REQ-HF-03: 'System shall issue escalating alerts if driver attention not detected for >5s'
3. Takeover performance: — REQ-HF-04: 'System shall provide ≥10s warning before requiring driver takeover'
REQ-HF-05: 'Takeover request shall use multi-modal alert (visual + audible + haptic)'
4. Transparency: — REQ-HF-06: 'System shall explain limitations and operational design domain in owner's manual and in-vehicle tutorial'
5. Error tolerance: — REQ-HF-07: 'If driver fails to respond to takeover request, system shall execute safe stop maneuver'
Human factors engineering is NOT an afterthought - it must be integrated from concept phase.
NHTSA and Euro NCAP now include human factors assessment in safety ratings.

## Slide 27
#### Part 6: Integration - Bringing It All Together (Slide 24, ~4 minutes)

## Slide 28: Case Study - Designing a Secure, Safe, Usable ACC System
Let's walk through a complete example integrating everything we've learned.
Project: Design an Adaptive Cruise Control (ACC) system with Automatic Emergency Braking (AEB) for a passenger vehicle.
Step 1: Hazard and Threat Analysis (Parallel)
HARA (Safety): — Hazard: 'Failure to brake for stopped vehicle' → ASIL D
Hazard: 'Unintended braking at high speed' → ASIL C
Hazard: 'Insufficient braking force' → ASIL B
TARA (Security): — Threat: 'Remote attacker disables AEB' → CAL 4
Threat: 'Attacker spoofs radar sensor' → CAL 3
Threat: 'Attacker causes false braking' → CAL 3
Human Factors Analysis: — Use case: Highway driving, driver partially attentive (Level 2)
Risk: Driver over-relies on system, doesn't monitor
Risk: Driver doesn't understand when system is active
Interoperability Analysis: — Interface: CAN bus to brake ECU (existing vehicle network)
Interface: V2V communication (future capability)
Constraint: Must work with existing vehicle architecture
Step 2: Goals and Requirements
Safety Goal [ASIL D]: — SG-ACC-01: 'Prevent collision with stopped or slow-moving vehicle ahead'
Cybersecurity Goal [CAL 4]: — CG-ACC-01: 'Prevent unauthorized modification of braking function'
Human Factors Goal: — HFG-ACC-01: 'Enable driver to maintain situational awareness of system state and limitations'
Interoperability Goal: — IOP-ACC-01: 'Integrate with existing vehicle CAN network without disrupting other functions'
Derived Requirements (integrated):
Detection & Decision: — REQ-ACC-010: 'System shall detect stopped vehicles at ≥150m with 99.9% probability' [ASIL D, Functional]
REQ-ACC-011: 'Radar sensor data shall be authenticated using AES-128 MAC' [CAL 4, Security]
REQ-ACC-012: 'System shall use sensor fusion (radar + camera) with diverse algorithms' [ASIL D, Safety]
Braking: — REQ-ACC-020: 'System shall command braking within 200ms of detecting collision risk' [ASIL D, Safety]
REQ-ACC-021: 'Brake commands shall use E2E protection per AUTOSAR' [ASIL D + CAL 3, Safety + Security]
Fail-Safe: — REQ-ACC-030: 'Upon sensor failure, system shall transition to safe state within 300ms' [ASIL D, Safety]
REQ-ACC-031: 'System shall detect firmware tampering at boot using secure boot' [CAL 4, Security]
Driver Interface: — REQ-ACC-040: 'System shall display ACC status on instrument cluster with ≥12mm icon' [Human Factors]
REQ-ACC-041: 'System shall monitor driver eye gaze every 500ms' [Level 2, Human Factors]
REQ-ACC-042: 'If driver not attending for >10s, system shall issue escalating alerts' [Safety + Human Factors]
Interoperability: — REQ-ACC-050: 'System shall communicate via CAN FD at 2 Mbps per ISO 11898-1' [Interoperability]
REQ-ACC-051: 'System shall support future V2V using SAE J2735 message set' [Interoperability]
Step 3: Architecture (Integrated)
[External: V2V (future)] ← Interoperability ↓ [Gateway ECU with Firewall + IDS] ← Security Layer 1 ↓ [CAN FD Bus with E2E Protection] ← Safety + Security Layer 2 ↓ ┌─────────────────────────────────────┐ │ ACC ECU (ASIL D + CAL 4) │ ← Integrated Safety + Security │ - Dual-core lockstep CPU │ ← Safety (ASIL D) │ - HSM (Hardware Security Module) │ ← Security (CAL 4) │ - Secure Boot │ ← Security (CAL 4) │ - Watchdog Timer │ ← Safety (ASIL D) │ - Sensor Fusion Algorithm (diverse) │ ← Safety (ASIL D) │ - Plausibility Checks │ ← Safety + Security └─────────────────────────────────────┘ ↓ (authenticated messages) [Radar Sensor] [Camera Sensor] ← Safety (redundancy) ↓ [Brake ECU] ← Safety (ASIL D) ↓ ┌─────────────────────────────────────┐ │ Driver Interface │ ← Human Factors │ - Instrument Cluster (ACC status) │ │ - Eye Tracking Camera │ │ - Audible + Haptic Alerts │ └─────────────────────────────────────┘
Step 4: Verification (Integrated Testing)
Safety Testing: — Fault injection: Simulate sensor failures, verify safe state transition
Edge cases: Test at ASIL D coverage (MC/DC code coverage)
Independent assessment: External safety auditor
Security Testing: — Penetration testing: Try to remotely disable AEB
Fuzz testing: Send malformed CAN messages, verify robustness
Secure boot verification: Attempt to load unsigned firmware
Interoperability Testing: — CAN conformance: Verify message timing, format per ISO 11898
Integration testing: Test with actual brake ECU from vehicle
Human Factors Testing: — Usability study: 50 drivers, measure comprehension of system state
Cognitive workload: Assess driver attention during ACC operation
Takeover testing: Measure response time to alerts
Integrated Scenario Testing: — Scenario: Cyberattack attempts to spoof radar sensor (security) during actual stopped vehicle ahead (safety) with distracted driver (human factors)
Expected result:
MAC verification detects spoofed data (security defense)
Plausibility check flags inconsistency (safety + security)
Camera sensor provides redundant detection (safety)
System brakes based on camera data (safety)
Driver monitoring detects inattention, issues alert (human factors)
Attack logged for incident response (security)
This is integrated specialty engineering in action - safety, security, interoperability, and human factors working together, not in silos.

## Slide 29: Key Takeaways
Let's consolidate what you've learned today:
1. Safety Analysis Methods — FTA (top-down): Start with hazard, find causes
FMEA (bottom-up): Start with components, find effects
HAZOP: Systematic deviation analysis
Use all three for comprehensive safety analysis
2. ISO 26262 and HARA — HARA: Hazard + Situation → Severity + Exposure + Controllability → ASIL
ASIL (A-D) determines rigor of safety engineering
Safety goals → FSR → TSR → Implementation → Verification
Traceability is mandatory
3. Cybersecurity — TARA: Assets → Threats → Attack paths → Risk → CAL
Defense in depth: Multiple layers of security
Security failure can cause safety failure
ISO 21434 provides systematic framework
4. Interoperability — Modern vehicles are part of ecosystem (V2X)
Standards enable interoperability (AUTOSAR, SAE, ISO)
Design for graceful degradation
Interoperability ≠ safety (verify with onboard sensors)
5. Human Factors — Design for real human capabilities and limitations
Automation levels (SAE J3016) have different human factors needs
Level 2: Driver monitoring essential
Mode awareness, attention management, error tolerance
6. Integration — Safety + Security + Interoperability + Human Factors must be co-designed
Unified architecture and requirements
Integrated testing scenarios
Remember: These specialty engineering disciplines are not bureaucracy - they are life-saving, systematic approaches that prevent disasters like Toyota unintended acceleration and Jeep Cherokee hacks.

## Slide 30: Connection to Systems Engineering V-Model
Let's place specialty engineering in the systems engineering context.
Left side of V-Model (Development):
Concept Phase: — Safety: HARA, safety goals
Security: TARA, cybersecurity goals
Human Factors: User research, task analysis
Interoperability: Interface identification
System Requirements (Session 4): — Integrate safety (FSR with ASIL), security (CSR with CAL), HF, and interoperability requirements
Traceability to hazards and threats
System Design (Session 5): — Architecture addresses safety (redundancy, fail-safe), security (defense in depth), interoperability (standards), HF (interface design)
Implementation: — Safety mechanisms, secure coding, AUTOSAR integration, HMI implementation
Right side of V-Model (Verification & Validation):
Component Testing: — Unit tests with safety and security coverage
Integration Testing: — Interoperability testing, fault injection, penetration testing
System Testing: — ASIL-specific testing, CAL-specific testing, usability testing
Validation: — Prove safety goals met, cybersecurity goals met, user needs met
Throughout lifecycle (Session 9, 15): — Configuration management: Baseline safety and security requirements
Change management: Impact analysis for safety and security
Measurement: Safety metrics (residual risk), security metrics (vulnerabilities found), HF metrics (usability scores)
Specialty engineering is NOT a separate process - it's integrated into the systems engineering lifecycle at every phase.

## Slide 31: Connection to Other Sessions
Today's session connects to many others:
Builds on: — Session 1: Failures (Therac-25, Toyota) were specialty engineering failures
Session 4: Requirements engineering - specialty requirements need extra rigor
Session 8: V&V - specialty engineering requires specialized verification
Session 9: Risk management and FMEA - HARA extends these concepts for safety
Leads to: — Session 13: Life cycle cost analysis includes cost of safety/security failures
Session 14: Case study 2 will apply specialty engineering concepts
Session 15: Technical management includes safety and security configuration management
Integration points: — MBSE (Session 3): SysML has safety and security extensions
Architecture (Session 5): Safety and security drive architecture decisions
Quality (Session 10): Safety and security are quality attributes
Agreements (Session 11): Supplier contracts must address safety and security responsibilities
Key concept thread: — Session 4: WHAT requirements are needed (including safety/security)
Session 9: HOW to analyze risk (DFMEA → HARA)
Session 12 (today): HOW to systematically engineer safety, security, interoperability, human factors
Session 8: HOW to verify specialty requirements
Specialty engineering is foundational to modern automotive systems engineering.

## Slide 32: 📊 PPT DESIGN GUIDANCE
Real Examples to Include:
Practical Exercise (Due before Session 13):
You are the systems engineer for a Level 2 Autonomous Lane Keeping Assist (LKAS) system for a highway vehicle.
Part 1: Safety Analysis (30%) — Identify at least 5 hazards
Conduct HARA for each (Severity, Exposure, Controllability → ASIL)
For the highest ASIL hazard, create an FMEA table (minimum 5 failure modes)
Define safety goal and 3 functional safety requirements
Part 2: Security Analysis (25%) — Identify at least 3 assets
Conduct TARA for at least 3 threats
Determine CAL for each threat
Define cybersecurity goal and 3 cybersecurity requirements
Part 3: Human Factors Analysis (25%) — Define the automation level (per SAE J3016)
Identify 3 human factors risks (e.g., mode confusion, over-reliance)
Define 3 human factors requirements to mitigate these risks
Sketch HMI mockup showing system status
Part 4: Integration (20%) — Create integrated architecture diagram showing safety mechanisms, security layers, and HMI
Create traceability matrix: Hazards/Threats → Goals → Requirements (Safety + Security + HF)
Define 1 integrated test scenario combining safety, security, and human factors
Grading Criteria: — Correct application of HARA methodology
Correct application of TARA methodology
Quality of safety and security requirements (clear, verifiable, traced)
Human factors analysis depth
Integration and traceability
Professional formatting
Submission:
Part 1: 2 pages (HARA table + FMEA + safety requirements)
Part 2: 1.5 pages (TARA table + security requirements)
Part 3: 1.5 pages (HF analysis + requirements + HMI sketch)
Part 4: 2 pages (Architecture diagram + traceability matrix + test scenario)
Total: 7 pages
Tips: — Research real LKAS systems (Euro NCAP requirements, Tesla, GM Super Cruise)
Use ISO 26262 ASIL table correctly (don't guess S/E/C)
Consider realistic attack vectors (cellular, OBD-II, sensor spoofing)
Think about driver monitoring (how do you ensure driver is attentive?)
Discussion Questions: — How would ASIL change if this was Level 3 (conditional automation) instead of Level 2?
What's the relationship between safety ASIL and security CAL for the same function?
How do you prevent drivers from over-relying on a Level 2 system?
What interoperability standards would be needed if this system used V2V data?
30 minutes for your questions. —--
Professional safety/security aesthetic: Clean, technical, serious tone
Color coding:
Red for hazards and threats
Blue for safety measures and requirements
Green for security measures
Orange for human factors
Purple for integration points
Use real automotive examples: Photos of ACC systems, HMI interfaces, attack demonstrations
Diagrams: HARA tables, TARA tables, FTA/FMEA, architecture diagrams
Slide 4 (Jeep Cherokee hack) - Real-world consequences
Slide 9-11 (Safety analysis methods) - Core techniques
Slide 13 (HARA process) - Foundation of ISO 26262
Slide 18 (TARA process) - Foundation of ISO 21434
Slide 19 (Defense in depth) - Security architecture
Slide 23 (Automation levels + HF) - Critical for modern vehicles
Slide 25 (Integrated case study) - Putting it all together
Slide 27 (Summary) - Students will photograph this
Slide 9: Build fault tree from top event downward
Slide 13: Step-by-step HARA process with example values appearing
Slide 18: Step-by-step TARA process
Slide 19: Layer-by-layer defense in depth (reveal each layer sequentially)
Slide 24: Integration flow showing parallel to convergence
Slide 25: Case study flow with requirements appearing in stages
Slide 10: FMEA table template (automotive example)
Slide 13: ASIL determination table (ISO 26262)
Slide 14: Complete HARA example (ACC system)
Slide 18: TARA table with attack feasibility rating
Slide 25: Integrated requirements table (ASIL + CAL columns)
Jeep Cherokee hack details (2015)
Tesla Autopilot crashes (human factors)
ISO 26262 ASIL table (actual standard)
ISO 21434 attack feasibility table
GM Super Cruise driver monitoring (good HF example)
AUTOSAR architecture diagram
SAE J3016 automation levels

## Slide 33: 🎯 INSTRUCTOR NOTES
Assessment Opportunities:
Start with real failure (Jeep hack), show systematic methods, return to how methods prevent failure — Parallel structure: Safety (HARA) and Security (TARA) taught in parallel to show similarities
Integration emphasis: Constantly reinforce that these disciplines must work together
Industry standards focus: ISO 26262, ISO 21434, SAE J3016 - use actual standards terminology
Hands-on mindset: Students should be able to conduct HARA and TARA after today
Challenge 1: "Why do we need both safety AND security engineering?"
How to address: Use Jeep Cherokee example - security breach CAUSED safety failure. Modern vehicles are connected, so security vulnerabilities create safety hazards. They are no longer separate concerns.
Challenge 2: "HARA and TARA seem complicated - can't we just test more?"
How to address: Testing can only find what you think to test. HARA/TARA systematically identify hazards/threats you didn't think of. Show Toyota example - inadequate hazard analysis led to missing critical failure modes. Analysis PRECEDES testing.
Challenge 3: "How do I determine ASIL or CAL accurately?"
How to address: Use ISO 26262 tables exactly as specified - don't guess. Severity, Exposure, Controllability have defined criteria. When uncertain, consult with safety experts, use conservative (higher) rating. Show worked examples (Slides 13-14).
Challenge 4: "This seems like it adds a lot of development cost"
How to address: Compare cost of HARA (maybe 40 hours of engineering time = $5K) vs cost of recall (1.4M vehicles = $1.4B). Prevention is 1000x cheaper than failure. Also, ISO 26262 and UN R155 are MANDATORY - not optional. Frame as risk reduction investment.
Challenge 5: "How do safety and security requirements interact?"
How to address: Use Slide 24 integrated example. Some requirements address both (e.g., E2E protection provides safety integrity AND security authentication). Some conflict (e.g., encryption latency vs real-time safety). Architecture must resolve conflicts through design (e.g., dedicated safety channel).
If running short: — Condense Slide 11 (HAZOP) - brief overview, details in reading
Reduce Slide 20-21 (interoperability) to overview only
Move some FMEA examples to backup slides
If running long: — Extend Slide 25 (case study) with more detailed walkthrough
Add live demo of HARA/TARA worksheet
Show video of GM Super Cruise or Tesla Autopilot HMI
Core content (must cover - non-negotiable): — Slides 8-10 (Safety analysis methods: FTA, FMEA)
Slides 12-14 (ISO 26262 and HARA)
Slides 16-18 (Cybersecurity and TARA)
Slide 19 (Defense in depth)
Slide 23 (Automation levels and human factors)
Slide 25 (Integrated case study)
Slide 27 (Summary)
Slide 4: Ask "Has anyone experienced a software bug in a vehicle?" (normalize the issue)
Slide 7: Interactive - "What could go wrong with ACC?" - let students brainstorm hazards before showing analysis
Slide 13: Work through HARA together - give a hazard, have students rate S/E/C before revealing ASIL
Slide 18: Work through TARA together - identify attack path for one threat
Slide 23: Poll - "How many would trust Level 2 automation on a highway?" (segue to human factors discussion)
Quick Exercise (Slide 14): Give students a new hazard for ACC (e.g., "Vehicle accelerates instead of braking"), have them determine S/E/C/ASIL in pairs (3 minutes), then discuss.
Group Discussion (Slide 19): "If you could only implement 3 of the 6 security layers, which would you choose and why?" (trade-off thinking)
Case Analysis (Slide 26): "What would you do differently in the Toyota case?" (apply lessons learned)
Before class: — [ ] ISO 26262-3 ASIL table (official or recreated)
[ ] ISO 21434 attack feasibility table
[ ] HARA worksheet template
[ ] TARA worksheet template
[ ] SAE J3016 summary (automation levels)
[ ] Jeep Cherokee hack case study materials
[ ] Example FMEA for automotive component
Handouts: — [ ] HARA worksheet template (Excel/PDF)
[ ] TARA worksheet template
[ ] FTA symbols reference
[ ] FMEA template
[ ] SAE J3016 one-pager
[ ] Defense in depth checklist
Post-class: — [ ] Share slides
[ ] Post exercise assignment with templates
[ ] Post ISO 26262 and ISO 21434 overview documents
[ ] Post links to UN R155 (cybersecurity regulation), UN R156 (software updates)
[ ] Create discussion forum: "Share safety or security analysis examples
During lecture: — Quick quiz (Slide 14): "What ASIL would you assign to this hazard?
Quick quiz (Slide 18): "What's the attack feasibility for this threat?
Exercise assessment criteria: — HARA correctness (Did they apply S/E/C criteria correctly?)
TARA correctness (Did they identify realistic threats and attack paths?)
Requirements quality (Traceable to hazards/threats? Verifiable? Include ASIL/CAL?)
Integration (Is architecture coherent? Does traceability matrix connect everything?)
Common student mistakes to watch for: — Confusing ASIL with CAL
Guessing S/E/C values instead of using criteria
Writing safety/security requirements without traceability to hazards/threats
Treating safety and security independently (not integrating)
Forgetting human factors entirely

## Slide 34: ✅ Session Success Criteria
Students leave able to:
✓ Apply FTA, FMEA, HAZOP methods to identify hazards
✓ Conduct HARA per ISO 26262 and determine ASIL
✓ Conduct TARA per ISO 21434 and determine CAL
✓ Design defense-in-depth security architecture
✓ Define interoperability requirements using standards
✓ Apply human factors principles to automation systems
✓ Integrate safety, security, interoperability, and human factors into unified system design
✓ Understand that specialty engineering is systematic, not ad-hoc
Critical outcome: Students understand that safety, security, interoperability, and human factors are not add-ons - they are foundational to automotive systems engineering and must be integrated from concept phase.
Evidence of success: — Student can conduct HARA and determine correct ASIL
Student can conduct TARA and identify realistic threats
Student can explain why security failures cause safety failures
Student can design architecture integrating safety mechanisms and security layers
Student understands SAE automation levels and associated human factors risks

## Slide 35: 📚 Additional Resources for Students
Standards and Guidelines: — ISO 26262:2018: Road Vehicles - Functional Safety (Parts 1-12)
ISO/SAE 21434:2021: Road Vehicles - Cybersecurity Engineering
SAE J3061: Cybersecurity Guidebook for Cyber-Physical Vehicle Systems
SAE J3016: Taxonomy and Definitions for Terms Related to Driving Automation Systems
UN Regulation No. 155: Cyber Security and Cyber Security Management System
UN Regulation No. 156: Software Update and Software Updates Management System
Safety Analysis: — IEC 61025: Fault Tree Analysis (FTA)
IEC 60812: Failure Mode and Effects Analysis (FMEA and FMECA)
IEC 61882: Hazard and Operability Studies (HAZOP)
Interoperability: — AUTOSAR (Automotive Open System Architecture) specifications
SAE J2735: Dedicated Short Range Communications (DSRC) Message Set Dictionary
ISO 20077: Extended Vehicle (ExVe) - Standardized access to data
Books: — "ISO 26262 - A Practical Guide" by Jürgen Mottok
"Automotive Cybersecurity Engineering Handbook" by Dr. Ahmad MK Nasser
"The Car Hacker's Handbook" by Craig Smith (security perspective)
"Introduction to Human Factors and Ergonomics" by Robert Bridger (HF fundamentals)
Online Resources: — NHTSA Cybersecurity Best Practices
SAE International webinars on functional safety
ISO 26262 training courses (TÜV, SGS)
MISRA C coding guidelines (secure coding)

## Slide 36: 🔗 Connections to Other Sessions
Builds on: — Session 1: Engineering failures (Therac-25, Toyota) were specialty engineering failures
Session 2: ISO/IEC 15288 life cycle includes specialty engineering processes
Session 4: Requirements engineering - safety/security requirements need traceability
Session 8: V&V - specialty engineering requires specialized verification methods
Session 9: Risk management and DFMEA - HARA extends FMEA for safety
Leads to: — Session 13: LCC/TCO includes cost of safety/security failures and recalls
Session 14: Case Study 2 will apply safety, security, and human factors analysis
Session 15: Technical management includes safety/security configuration management
Key concept thread: — Session 9: Risk management basics (DFMEA)
Session 12 (today): Specialty engineering for safety, security, interoperability, human factors
Session 15: Technical processes supporting specialty engineering
Specialty engineering appears in: — Session 5 (architecture driven by safety/security)
Session 8 (safety/security verification)
Session 10 (quality includes safety/security)
Session 13 (cost of safety/security failures)

## Slide 37: 🎬 Opening and Closing Strategies
Closing (Last 2 minutes):
Start with image of Jeep Cherokee on screen as students enter. Begin:
Before we start, look at this vehicle. In July 2015, security researchers remotely took control of its steering, brakes, and transmission. 1.4 million vehicles recalled. $1.4 billion settlement.
The attack was possible because safety and security were engineered separately. The infotainment system had no firewall to the safety-critical CAN bus. One exploit, total vehicle control.
Today, we learn how to prevent this through integrated specialty engineering: safety, security, interoperability, and human factors.
Welcome to Session 12: Specialty Engineering - Safety & Security.
Return to the opening image:
We started with the Jeep Cherokee - a catastrophic failure of integrated specialty engineering. You now have the knowledge to prevent this:
You can conduct HARA to systematically identify safety hazards and determine ASIL
You can conduct TARA to identify security threats and determine CAL
You can design defense-in-depth architectures integrating safety and security
You understand that human factors and interoperability must be engineered, not assumed
The exercise I've given you is your chance to practice integrated specialty engineering. Imagine you're the engineer responsible for a Level 2 LKAS system. Lives depend on getting safety, security, and human factors right.
Because in automotive, specialty engineering is not optional. It's the difference between life and death.
See you in Session 13, where we'll analyze the cost of getting this wrong.

## Slide 38: 📈 Learning Objectives Mapping to Assessment
| Session Objective | Assessment Method | Success Criteria |
|-------------------|-------------------|------------------|
| Apply safety analysis methods | Exercise Part 1 (HARA + FMEA) | Correctly applies S/E/C criteria, determines ASIL, creates FMEA with RPN |
| Conduct HARA per ISO 26262 | Exercise Part 1 | At least 5 hazards identified, correct ASIL determination, safety requirements traced |
| Apply cybersecurity principles | Exercise Part 2 (TARA) | Identifies realistic threats, correct attack feasibility rating, determines CAL |
| Define interoperability requirements | Discussion + exercise integration | Mentions standards (AUTOSAR, V2X), defines interface requirements |
| Incorporate human factors | Exercise Part 3 | Identifies HF risks, defines HF requirements, creates HMI mockup |
| Integrate specialty engineering | Exercise Part 4 | Unified architecture, integrated traceability matrix, combined test scenario |

## Slide 39
End of Session 12 Framework
Next: Session 13 (Life Cycle Cost and Total Cost of Ownership)