## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 13: Life Cycle Cost & Total Cost of Ownership (TCO)'

## Slide 2: Life Cycle Cost & Total Cost of Ownership (TCO)
Session 13 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title Slide
Instructor Narration:
Welcome to Session 13. Today we're talking about money. Not just the sticker price, but the TOTAL cost of a vehicle system across its entire life. Because here's what most people don't realize: the purchase price is usually less than 20% of total ownership cost.
As systems engineers, every decision you make - from requirements to architecture to component selection - affects costs that will ripple through decades. Today, you'll learn to see and manage those costs.
PPT Content:
AUTOMOTIVE SYSTEMS ENGINEERING AE ZG517 / AEL ZG517 Session 13: Life Cycle Cost & Total Cost of Ownership (TCO) Instructor: Sajeeth Kumar Duration: 120 minutes
Learning Outcomes: LO2, LO4, LO5

## Slide 4: The Cost Iceberg
Instructor Narration:
Let me show you the cost iceberg. When someone buys a vehicle, they see the purchase price - that's the tip of the iceberg above water. But beneath the surface?
Fuel costs over 10+ years
Maintenance and repairs
Insurance premiums
Depreciation
Financing costs
Registration and taxes
End-of-life disposal
For manufacturers, the iceberg looks different but equally massive:
Development costs
Manufacturing costs
Warranty and recalls
Regulatory compliance
Supply chain costs
End-of-life take-back obligations
Most of these costs are LOCKED IN by early engineering decisions.
That's why systems engineers must understand life cycle costs.
PPT Content:
THE COST ICEBERG VISIBLE (20%): Purchase Price • Initial vehicle cost • Customer sees this HIDDEN (80%): Life Cycle Costs • Operating costs (fuel, electricity) • Maintenance and repairs • Insurance • Depreciation • Financing • Registration and taxes • End-of-life disposal MANUFACTURER PERSPECTIVE: • R&D and development • Manufacturing and tooling • Supply chain • Warranty and recalls • Regulatory compliance • Service and support • End-of-life responsibilities → 70-80% of life cycle costs are determined in the first 20% of design phase
Learning Outcomes: LO2, LO5

## Slide 5: Case Study Opening - Two Electric Vehicles
Instructor Narration:
Let me tell you a story about two electric vehicles.
Vehicle A: Purchase price: $45,000
Vehicle B: Purchase price: $52,000
Customer walks into dealership. Which one looks like the better deal? Obviously Vehicle A, right? $7,000 cheaper.
But let's look at life cycle costs over 10 years, 150,000 miles:
Vehicle A Total Cost of Ownership: — Purchase: $45,000
Electricity: $6,000
Maintenance: $8,500 (frequent battery cooling system repairs)
Battery replacement (year 7): $12,000
Insurance: $15,000 (higher rates due to repair costs)
Depreciation: Loses 70% value
TOTAL: $86,500
Vehicle B Total Cost of Ownership: — Purchase: $52,000
Electricity: $5,200 (more efficient)
Maintenance: $4,000 (better reliability)
Battery replacement: $0 (warranty covers 10 years)
Insurance: $12,000 (lower repair costs)
Depreciation: Loses 55% value (better resale)
TOTAL: $73,200
Vehicle B, which cost $7,000 MORE upfront, saves the customer $13,300 over its life.
This is life cycle cost thinking. And as engineers, YOU determine which vehicle gets built.
PPT Content:
CASE STUDY: Two Electric Vehicles VEHICLE A VEHICLE B Purchase Price $45,000 $52,000 10-Year TCO: Electricity $6,000 $5,200 Maintenance $8,500 $4,000 Battery Replacement $12,000 $0 Insurance $15,000 $12,000 Depreciation (70%) (55%) TOTAL COST $86,500 $73,200 WINNER: Vehicle B saves $13,300 over life LESSON: Lowest purchase price ≠ Lowest total cost
Learning Outcomes: LO2, LO5

## Slide 6: Why LCC Matters - Stakeholder Perspectives
Instructor Narration:
Different stakeholders care about different costs:
Customers: Total cost of ownership - they pay for everything across vehicle life
Fleet operators: Even more sensitive - operating hundreds of vehicles, TCO directly affects profitability
Manufacturers: Life cycle cost of product development and support - affects competitiveness and profit margins
Society: Environmental costs - externalities like emissions, resource depletion, end-of-life waste
Regulators: Compliance costs and consumer protection
As systems engineers, you must balance ALL these cost perspectives. A decision that saves manufacturing cost might increase customer TCO. An engineering change that increases upfront cost might dramatically reduce warranty costs.
Systems thinking is cost thinking.
PPT Content:
WHY LIFE CYCLE COST MATTERS CUSTOMER PERSPECTIVE: • Seeks lowest total ownership cost • Values reliability (reduces repair costs) • Values efficiency (reduces fuel/energy costs) • Considers resale value FLEET OPERATOR PERSPECTIVE: • TCO is critical to profitability • Uptime is paramount (downtime = lost revenue) • Fuel/energy costs magnified across fleet • Maintenance predictability matters MANUFACTURER PERSPECTIVE: • Development costs must be recovered • Manufacturing costs affect competitiveness • Warranty costs directly hit profit • Reputation affects future sales SOCIETY/REGULATORY PERSPECTIVE: • Environmental externalities • Resource consumption • End-of-life impacts • Safety and emissions compliance → Systems engineer must optimize across ALL stakeholder cost perspectives
Learning Outcomes: LO2, LO4

## Slide 7: Today's Learning Journey
Instructor Narration:
Here's our journey today:
Part 1: Life Cycle Cost Fundamentals - What is LCC, why it matters, cost categories
Part 2: Total Cost of Ownership (TCO) - Customer perspective analysis
Part 3: Cost Estimation Techniques - How to predict and calculate costs
Part 4: Cost-Driven Design - Engineering decisions that affect LCC
Part 5: Cost-Benefit Analysis and Trade Studies - Making economically sound engineering decisions
By the end, you'll be able to evaluate engineering decisions not just technically, but economically across the entire system life cycle.
PPT Content:
TODAY'S JOURNEY 1. LCC Fundamentals (15 min) • Definitions and concepts • Cost categories across life cycle 2. Total Cost of Ownership (20 min) • TCO models for automotive • Customer and fleet perspectives 3. Cost Estimation (20 min) • Parametric and analogy-based methods • Uncertainty and risk in cost estimates 4. Cost-Driven Design (20 min) • How engineering decisions affect LCC • Design for cost optimization 5. Cost-Benefit Analysis (15 min) • Trade studies with cost • Economic decision-making Goal: Engineer systems that are economically optimal across their entire life
Learning Outcomes: LO2, LO4, LO5

## Slide 8: Defining Life Cycle Cost (LCC)
Instructor Narration:
Let's define our terms precisely.
Life Cycle Cost (LCC): The total cost of a system throughout its entire life cycle, from conception to disposal.
Total Cost of Ownership (TCO): The total cost to acquire, operate, and dispose of a system from the OWNER'S perspective.
LCC is broader - includes manufacturer costs. TCO focuses on customer/operator costs.
The system life cycle includes:
Conception and Development: Research, design, testing, certification
Production and Construction: Manufacturing, tooling, quality control
Operation and Support: Use, maintenance, repair, training
Retirement and Disposal: Decommissioning, recycling, waste management
Every stage has costs. Systems engineers must consider ALL of them.
PPT Content:
LIFE CYCLE COST (LCC) - DEFINITION LCC = Total cost of system across entire life cycle LIFE CYCLE STAGES: 1. CONCEPTION & DEVELOPMENT • Research and development • Requirements engineering • Design and architecture • Prototyping and testing • Certification and compliance 2. PRODUCTION & CONSTRUCTION • Manufacturing tooling • Component production • Assembly and integration • Quality control • Logistics and distribution 3. OPERATION & SUPPORT • Energy/fuel consumption • Routine maintenance • Repairs and replacements • Training and documentation • Spare parts inventory 4. RETIREMENT & DISPOSAL • Decommissioning • Recycling and material recovery • Waste disposal • Environmental remediation LCC = C_development + C_production + C_operation + C_disposal
Learning Outcomes: LO2

## Slide 9: LCC Components - Detailed Breakdown
Instructor Narration:
Let me break down each cost category in detail for automotive systems:
Development Costs: — Engineering labor (requirements, design, testing)
Prototyping and tooling for prototypes
Testing facilities and equipment
Certification and regulatory compliance
Software development and validation
Intellectual property and licensing
Production Costs: — Manufacturing tooling and equipment
Material and component costs
Direct labor
Quality control and inspection
Logistics and supply chain
Factory overhead
Operating Costs: — Energy consumption (fuel, electricity)
Routine maintenance (scheduled services)
Repairs and unscheduled maintenance
Spare parts
Insurance
Taxes and registration
Support Costs: — Warranty claims
Technical support and customer service
Training materials and programs
Documentation updates
Recalls and field campaigns
End-of-Life Costs: — Disassembly labor
Hazardous material handling
Recycling and material recovery (can be revenue)
Disposal of non-recyclable materials
Environmental compliance
For a typical automotive system, operating costs are 40-60% of total LCC.
PPT Content:
LCC COMPONENTS - AUTOMOTIVE BREAKDOWN DEVELOPMENT (Typically 10-15% of LCC): • Engineering: $200M-$500M for new vehicle program • Prototyping: $50M-$150M • Testing and validation: $100M-$200M • Certification: $20M-$50M PRODUCTION (Typically 30-40% of LCC): • Tooling: $500M-$1B for new platform • Parts and materials: 60-70% of vehicle price • Labor: 10-15% of vehicle price • Quality control: 2-5% OPERATION (Typically 40-60% of LCC): • Fuel/Energy: $15,000-$30,000 over 10 years (ICE) $5,000-$10,000 over 10 years (EV) • Maintenance: $5,000-$15,000 over 10 years • Insurance: $10,000-$20,000 over 10 years • Taxes/fees: $1,000-$3,000 per year SUPPORT (Typically 5-10% of LCC): • Warranty: $500-$2,000 per vehicle • Service network: Infrastructure costs • Recalls: Highly variable ($100M-$5B+ per major recall) END-OF-LIFE (Typically 1-5% of LCC): • Disposal: $200-$500 per vehicle • Recycling: Can offset costs (aluminum, copper recovery) • Environmental: Depends on regulations TOTAL LCC EXAMPLE (Mid-size ICE vehicle, 10 years): Purchase: $35,000 | Operation: $45,000 | Total: $80,000+
Learning Outcomes: LO2, LO5

## Slide 10: LCC Formula and Modeling
Instructor Narration:
Let's formalize this mathematically. The basic LCC equation is:
LCC = CRDT + CProd + COps + CDisposal
Where:
C_RDT = Research, Development, Test & Evaluation
C_Prod = Production and Manufacturing
C_Ops = Operation and Support
C_Disposal = End-of-Life and Disposal
But we need to account for TIME. A dollar today is not worth the same as a dollar in 10 years. So we use Net Present Value (NPV):
LCC = Σ(C_t / (1+r)^t)
Where:
C_t = Cost in year t
r = Discount rate (typically 3-8% for automotive)
t = Time period
Example:
A maintenance cost of $1,000 in year 5, with 5% discount rate:
NPV = $1,000 / (1.05)^5 = $784
This is critical: Far-future costs are discounted. This can lead to undervaluing long-term consequences. As systems engineers, be aware of this bias.
PPT Content:
LCC MATHEMATICAL MODELING BASIC LCC EQUATION: LCC = C_RDT + C_Prod + C_Ops + C_Disposal NET PRESENT VALUE FORMULATION: LCC = Σ(C_t / (1+r)^t) for t = 0 to n Where: • C_t = Cost in time period t • r = Discount rate (time value of money) • t = Time period (years) • n = System lifetime DISCOUNT RATE SELECTION: • Corporate: 8-12% (reflects opportunity cost of capital) • Government: 3-7% (social discount rate) • Customer: 5-10% (personal finance rate) EXAMPLE CALCULATION: System with 10-year life, 6% discount rate Year 0 (Development): $1,000,000 → NPV = $1,000,000 Year 1 (Production): $500,000 → NPV = $471,698 Year 2 (Production): $500,000 → NPV = $445,094 Year 3-10 (Operation): $100,000/yr → NPV = $590,169 Year 10 (Disposal): $50,000 → NPV = $27,919 TOTAL LCC (NPV) = $2,534,880 KEY INSIGHT: Higher discount rates favor low upfront costs Lower discount rates favor low operating costs
Learning Outcomes: LO2, LO5

## Slide 11: LCC Analysis Process
Instructor Narration:
How do you actually conduct an LCC analysis? Here's the systematic process:
Step 1: Define Objectives and Scope — What decision are you supporting?
What alternatives are being compared?
What's the time horizon? (typically vehicle useful life: 10-15 years)
Whose perspective? (manufacturer, customer, society)
Step 2: Establish Cost Breakdown Structure — Decompose system into cost elements
Align with Work Breakdown Structure (WBS)
Identify all cost categories
Step 3: Identify Cost Drivers — What factors most affect costs?
Examples: weight (materials cost), complexity (assembly cost), reliability (warranty cost)
Step 4: Estimate Costs — Use estimation techniques (we'll cover these)
Include uncertainty ranges
Document assumptions
Step 5: Apply Time Value of Money — Select appropriate discount rate
Calculate NPV for all costs
Step 6: Conduct Sensitivity Analysis — Which assumptions most affect results?
Test different scenarios (fuel prices, failure rates, etc.)
Step 7: Document and Communicate — Present results with uncertainty
Support decision-making
Update as better data becomes available
This is an iterative process. Early estimates are rough, refined over time.
PPT Content:
LCC ANALYSIS PROCESS 1. DEFINE OBJECTIVES & SCOPE ✓ Decision to be supported ✓ Alternatives to compare ✓ Time horizon ✓ Stakeholder perspective ✓ Boundaries (what's included/excluded) 2. ESTABLISH COST BREAKDOWN STRUCTURE ✓ Hierarchical decomposition ✓ Aligned with WBS ✓ Complete and mutually exclusive categories 3. IDENTIFY COST DRIVERS ✓ Technical parameters affecting cost ✓ Operational factors ✓ External factors (regulations, market) 4. ESTIMATE COSTS ✓ Data collection (historical, vendor quotes) ✓ Estimation techniques (parametric, analogy) ✓ Uncertainty quantification 5. APPLY TIME VALUE OF MONEY ✓ Select discount rate ✓ Calculate NPV for each cost element ✓ Sum to total LCC 6. CONDUCT SENSITIVITY ANALYSIS ✓ Vary key assumptions ✓ Identify cost drivers with highest impact ✓ Assess risk and uncertainty 7. DOCUMENT & COMMUNICATE ✓ Assumptions log ✓ Visualize results ✓ Support decision-making → Iterate as design matures and better data becomes available
Learning Outcomes: LO2, LO4

## Slide 12: Cost vs. Value - Important Distinction
Instructor Narration:
Before we go further, distinguish between COST and VALUE.
Cost: Resources consumed (money, time, materials)
Value: Benefit delivered to stakeholders
The goal is NOT minimum cost. The goal is MAXIMUM value.
Example: Safety features add cost but deliver enormous value (lives saved, liability avoided).
Value Engineering: Systematic approach to improving value by:
Reducing costs without reducing performance
Increasing performance without increasing costs
Reducing costs WHILE increasing performance (ideal)
Four Scenarios:
| Cost | Performance | Value | Example |
|------|-------------|-------|---------|
| Low | Low | Poor | Cheap components that fail frequently |
| High | High | Good | Premium features customers value |
| Low | High | Excellent | Engineering innovation |
| High | Low | Poor | Over-engineered, gold-plating |
As systems engineers, you seek the third quadrant: Low cost, high performance.
This requires creativity, systems thinking, and life cycle perspective.
PPT Content:
COST vs. VALUE DEFINITIONS: • Cost = Resources consumed (inputs) • Value = Benefits delivered (outputs) • Value = Performance / Cost GOAL: Maximize Value (NOT minimize cost) VALUE ENGINEERING APPROACHES: 1. REDUCE COST, MAINTAIN PERFORMANCE • Standardization (fewer unique parts) • Design for manufacturing • Material substitution 2. INCREASE PERFORMANCE, MAINTAIN COST • Innovation and technology • Systems integration • Better requirements 3. REDUCE COST, INCREASE PERFORMANCE • This is engineering excellence • Requires deep systems thinking • Example: Electric powertrains (fewer parts, better performance) 4. AVOID: INCREASE COST, REDUCE PERFORMANCE • Over-complexity • Gold-plating • Poor requirements AUTOMOTIVE EXAMPLES: LOW COST, HIGH VALUE: • LED lighting (lower power, longer life, better visibility) • Turbocharging (smaller engine, better efficiency and power) • Over-the-air updates (eliminate recall costs, improve functionality) HIGH COST, HIGH VALUE: • Advanced driver assistance systems (safety value justifies cost) • Battery thermal management (extends battery life significantly) The cheapest system is not always the best. Optimize for life cycle value.
Learning Outcomes: LO2, LO5

## Slide 13: TCO Model - Consumer Vehicle
Instructor Narration:
Let's build a TCO model for a typical consumer vehicle. Assume:
Mid-size sedan, $35,000 purchase price
10-year ownership, 15,000 miles/year
Gas price $3.50/gallon, 30 mpg average
TCO Calculation:
1. Depreciation: $24,500 (vehicle worth ~$10,500 after 10 years)
2. Fuel: $17,500 (150,000 miles ÷ 30 mpg × $3.50/gal)
3. Insurance: $15,000 ($1,500/year average)
4. Maintenance & Repairs: $10,000 (increases with age)
5. Financing: $6,000 (5-year loan, 6% APR on $30,000)
6. Taxes & Fees: $3,000 ($300/year registration + initial sales tax)
Total 10-Year TCO: $76,000
Breakdown: — Depreciation: 32% of TCO
Fuel: 23% of TCO
Insurance: 20% of TCO
Maintenance: 13% of TCO
Financing: 8% of TCO
Taxes/Fees: 4% of TCO
Key insight: Fuel and depreciation together are 55% of TCO. Engineering can affect both significantly.
PPT Content:
TCO MODEL: CONSUMER VEHICLE ASSUMPTIONS: • Vehicle: Mid-size sedan • Purchase Price: $35,000 • Ownership: 10 years, 150,000 miles • Fuel: Gasoline, $3.50/gal, 30 mpg • Insurance: $1,500/year • Financing: 60-month loan, 6% APR, 20% down TCO BREAKDOWN (10 years): 1. DEPRECIATION: $24,500 (32%) • Year 1: -20% ($7,000) • Years 2-5: -10% average/year • Years 6-10: -5% average/year • Residual value: $10,500 2. FUEL: $17,500 (23%) • 15,000 miles/year ÷ 30 mpg = 500 gal/year • 500 gal × $3.50 × 10 years = $17,500 3. INSURANCE: $15,000 (20%) • $1,500/year × 10 years 4. MAINTENANCE & REPAIRS: $10,000 (13%) • Years 1-3: $500/year (basic maintenance) • Years 4-7: $1,000/year (wear items) • Years 8-10: $2,000/year (major repairs) 5. FINANCING: $6,000 (8%) • $28,000 loan @ 6% APR, 60 months • Total interest paid 6. TAXES & FEES: $3,000 (4%) • Initial sales tax: $2,000 • Registration: $200/year × 10 = $2,000 • Inspections, emissions: $1,000 TOTAL 10-YEAR TCO: $76,000 TCO per mile: $0.51/mile TCO per year: $7,600/year ENGINEERING IMPACT: • Fuel efficiency: 10% improvement saves $1,750 • Reliability: Reduce maintenance 20% saves $2,000 • Depreciation: Better quality improves resale (complex)
Learning Outcomes: LO2, LO5

## Slide 14: TCO Comparison - ICE vs. EV
Instructor Narration:
Let's compare ICE vs. EV using TCO analysis. This is how you make informed engineering and policy decisions.
ICE Vehicle: Mid-size sedan, $35,000 purchase, 30 mpg
EV Vehicle: Similar size, $42,000 purchase, 3.5 miles/kWh
Assumptions: — 10 years, 15,000 miles/year
Gas: $3.50/gallon
Electricity: $0.13/kWh
EV qualifies for $7,500 federal tax credit
TCO Comparison:
| Cost Element | ICE | EV | Difference |
|--------------|-----|-----|------------|
| Purchase Price | $35,000 | $42,000 | +$7,000 |
| Tax Credit | $0 | -$7,500 | -$7,500 |
| Net Purchase | $35,000 | $34,500 | —$500 |
| Fuel/Energy | $17,500 | $5,600 | -$11,900 |
| Maintenance | $10,000 | $5,000 | -$5,000 |
| Insurance | $15,000 | $16,500 | +$1,500 |
| Depreciation | -$24,500 | -$27,000 | -$2,500 |
| Taxes/Fees | $3,000 | $2,500 | -$500 |
| TOTAL TCO | $76,000 | $63,600 | —$12,400 |
EV saves $12,400 over 10 years despite higher upfront cost.
This is the power of TCO analysis - revealing true economic value.
PPT Content:
TCO COMPARISON: ICE vs. ELECTRIC VEHICLE VEHICLE SPECIFICATIONS: • ICE: Mid-size sedan, $35,000, 30 mpg • EV: Similar size, $42,000, 3.5 mi/kWh, 75 kWh battery • Both: 10 years, 150,000 miles DETAILED TCO BREAKDOWN: ICE EV Δ Purchase Price $35,000 $42,000 +$7,000 Tax Credit $0 -$7,500 -$7,500 NET PURCHASE $35,000 $34,500 -$500 Energy Costs: • ICE: 150k mi ÷ 30 mpg × $3.50/gal = $17,500 • EV: 150k mi ÷ 3.5 mi/kWh × $0.13/kWh = $5,600 $17,500 $5,600 -$11,900 Maintenance: • ICE: Oil changes, filters, exhaust, transmission = $10,000 • EV: Brakes (regen saves), tires, coolant = $5,000 $10,000 $5,000 -$5,000 Insurance: • EV higher due to higher vehicle value $15,000 $16,500 +$1,500 Depreciation: • Both lose ~70% in 10 years -$24,500 -$27,000 -$2,500 Registration/Taxes: • Some states offer EV incentives $3,000 $2,500 -$500 TOTAL 10-YEAR TCO $76,000 $63,600 -$12,400 EV SAVES: $12,400 (16% lower TCO) BREAKEVEN ANALYSIS: • EV monthly payment higher: +$100/mo • EV monthly energy savings: -$100/mo • EV monthly maintenance savings: -$42/mo • Net savings: $42/month from day 1 • Payback on extra upfront cost: Immediate (with tax credit) SENSITIVITY: What if... • Gas prices rise to $5/gal? EV saves $21,000 • Battery replacement needed year 8 ($8,000)? EV saves $4,400 • Drive 25,000 mi/year? EV saves $20,000
Learning Outcomes: LO2, LO5

## Slide 15: Engineering Decisions That Drive LCC
Instructor Narration:
Every engineering decision you make affects life cycle costs. Let me show you the most impactful decisions:
1. Architecture Selection — Modular vs. integrated architectures
Number of components and complexity
Example: Tesla's battery pack architecture reduces manufacturing cost by 30%
2. Component Selection — Cost vs. reliability trade-off
Cheap components have high failure rates → high warranty costs
Example: Choosing premium capacitors adds $5 but saves $500 in warranty
3. Material Selection — Upfront cost vs. weight vs. manufacturability
Example: Aluminum body panels: +$800 material cost, -100 lbs weight, +3 mpg → saves $3,000 in fuel
4. Manufacturing Process — Tooling investment vs. per-unit cost
Example: Die casting saves $50/part at 100k+ volume, but costs $5M tooling
5. Maintenance Access — Design for serviceability
Example: Easy access to battery pack reduces labor cost from $2,000 to $500
6. Failure Modes and Reliability — MTBF (Mean Time Between Failures) directly affects warranty and TCO
Example: Improving MTBF from 50k to 100k miles cuts warranty costs in half
7. Software vs. Hardware Solutions — Software has near-zero marginal cost but high development cost
Example: OTA updates replace recall campaigns (saves millions)
8. Standardization and Commonality — Fewer unique parts reduce inventory, training, tooling costs
Example: Using same climate control module across 5 models reduces cost 40%
The systems engineer's job: Optimize across ALL these decisions for minimum LCC.
PPT Content:
ENGINEERING DECISIONS THAT DRIVE LCC 1. ARCHITECTURE SELECTION Decision: Centralized vs. Distributed computing architecture Cost Impact: • Centralized: Lower harness cost (-$200), higher compute cost (+$500) • Distributed: Higher harness (+$200), lower compute (-$500) • But: Centralized enables OTA updates → saves recall costs 2. COMPONENT SELECTION (Reliability vs. Cost) Example: Power supply capacitors • Standard grade: $2 each, MTBF 50k hours → 20% failure rate in 10 years • Premium grade: $7 each, MTBF 200k hours → 2% failure rate • Warranty cost per failure: $500 • LCC winner: Premium (saves $400/vehicle in warranty) 3. MATERIAL SELECTION Example: Body panels (Aluminum vs. Steel) • Steel: Baseline, $500/vehicle • Aluminum: +$800 material cost • Weight savings: -100 lbs • Fuel savings: +2 mpg → $1,750 over 10 years • LCC winner: Aluminum (saves $950 over life) 4. MANUFACTURING PROCESS Example: Battery pack assembly • Manual assembly: $0 tooling, $200/pack labor • Automated: $10M tooling, $50/pack labor • Breakeven: 67,000 units • At 200k units/year: Automation saves $30M/year 5. DESIGN FOR MAINTAINABILITY Example: Battery pack access • Poor access: 8 hours labor → $800 cost per service • Good access: 2 hours labor → $200 cost per service • Expected services: 2 over 10 years • TCO impact: $1,200 savings per vehicle 6. RELIABILITY ENGINEERING Example: Inverter MTBF • MTBF 80k miles: 60% failure rate by 150k miles • MTBF 200k miles: 15% failure rate by 150k miles • Replacement cost: $2,000 • Cost to improve MTBF: $100/vehicle • LCC savings: $800/vehicle 7. SOFTWARE vs. HARDWARE Example: Feature updates • Hardware upgrade: $500/vehicle + retrofit logistics • Software OTA: $5M development ÷ 100k vehicles = $50/vehicle • LCC winner: Software (saves $450/vehicle) 8. STANDARDIZATION Example: Climate control modules • Custom per model: 5 variants × $2M tooling = $10M, $150/unit • Standardized platform: 1 variant × $3M tooling = $3M, $100/unit • At 200k units: Saves $7M + $50/unit KEY PRINCIPLE: Every dollar spent on better design can save $5-10 in life cycle costs. But you must analyze and quantify to make informed decisions.
Learning Outcomes: LO2, LO4, LO5

## Slide 16: Design for Cost (DFC) Principles
Instructor Narration:
Design for Cost is a systematic approach to minimizing LCC. Here are the key principles:
1. Simplicity — Fewer parts = lower cost (design, manufacturing, inventory, service)
Example: Tesla Model Y rear casting replaces 70 parts with 1 → saves $600/vehicle
2. Standardization — Use common components across products
Reduces tooling, inventory, training costs
Example: Volkswagen MQB platform shares 60% of parts across 10 models
3. Design for Manufacturing (DFM) — Easy to manufacture = lower labor and scrap costs
Minimize unique processes and tooling
Example: Snap-fit vs. fasteners saves $5/assembly
4. Design for Assembly (DFA) — Reduce assembly time and complexity
Mistake-proof designs (poka-yoke)
Example: Reducing assembly time by 1 minute saves $1/vehicle at scale
5. Design for Serviceability (DFS) — Easy access to wear items
Modular replacement vs. complete assembly
Example: Replaceable vs. sealed battery modules
6. Design for Reliability — Prevent failures at source (cheaper than fixing later)
Use proven components and de-rating
Example: 50% de-rating on voltage extends life 10x
7. Design for Testability — Built-in diagnostics reduce troubleshooting time
Example: OBD-II codes cut diagnostic time from hours to minutes
8. Design for End-of-Life — Easy disassembly for recycling
Valuable material recovery
Example: Aluminum recovery pays for disposal
All of these are systems engineering practices that drive down LCC.
PPT Content:
DESIGN FOR COST (DFC) PRINCIPLES 1. SIMPLICITY ✓ Minimize part count ✓ Reduce design complexity ✓ Eliminate non-value-added features Example: Reduce assembly from 200 parts to 50 → -40% assembly cost 2. STANDARDIZATION ✓ Common parts across product lines ✓ Use industry-standard components ✓ Platform strategies Example: VW MQB platform saves $1,500/vehicle through commonality 3. DESIGN FOR MANUFACTURING (DFM) ✓ Minimize manufacturing steps ✓ Use standard processes ✓ Reduce tight tolerances where possible ✓ Design for automated assembly Example: Redesign to eliminate welding step → saves $25/vehicle 4. DESIGN FOR ASSEMBLY (DFA) ✓ Reduce assembly time ✓ Top-down assembly ✓ Self-locating/aligning parts ✓ Minimize fasteners Example: Snap-fit vs. screws: -30 seconds/assembly = $0.50 savings 5. DESIGN FOR SERVICEABILITY (DFS) ✓ Easy access to serviceable parts ✓ Modular design for quick replacement ✓ Clear service procedures ✓ Minimize special tools Example: Quick-connect vs. clamps: -15 min service = $15 labor savings 6. DESIGN FOR RELIABILITY ✓ Use proven components ✓ De-rate components (operate below max ratings) ✓ Robust design (insensitive to variation) ✓ Eliminate failure modes at source Example: Premium bearings cost +$20, save $500 in warranty 7. DESIGN FOR TESTABILITY (DFT) ✓ Built-in self-test (BIST) ✓ Accessible test points ✓ Clear fault indicators ✓ Diagnostic-friendly architecture Example: Built-in diagnostics save 30 min troubleshooting = $30/repair 8. DESIGN FOR END-OF-LIFE (DFEOL) ✓ Easy disassembly ✓ Material labeling ✓ Recyclable materials ✓ Minimize hazardous materials Example: Modular battery design enables cell-level recycling DFC METHODOLOGY: 1. Establish cost targets (top-down) 2. Allocate targets to subsystems 3. Design to cost targets 4. Estimate actual costs 5. Identify cost drivers 6. Iterate design to reduce costs 7. Verify through prototyping TOOLS: • Cost modeling software • Should-cost analysis • Value engineering workshops • Teardown analysis (benchmark competitors)
Learning Outcomes: LO2, LO4

## Slide 17
[Continuing with remaining slides...]
Created Session 13 and 14.