## Slide 1
---
marp: true
theme: engineering
paginate: true
math: katex
header: 'Session 14: Case Study 2 - Tesla Autopilot System Analysis'

## Slide 2: Case Study 2 - Tesla Autopilot System Analysis
Session 14 | Automotive Vehicles (AEL ZC441)

## Slide 3: Title
Welcome to Session 14, our second major case study. In Session 6, we analyzed the Boeing 737 MAX MCAS disaster - an aerospace automation failure that killed 346 people.
Today, we analyze Tesla Autopilot - an AUTOMOTIVE automation system involved in multiple fatalities and hundreds of crashes.
This is not an anti-Tesla session. Tesla pioneered advanced driver assistance in consumer vehicles. But their approach reveals critical systems engineering lessons about automation, human factors, testing, and regulation.
Our goal: Understand what went wrong, why, and how systems engineering principles can prevent similar failures in your future work on autonomous and semi-autonomous vehicles.
PPT Content:
AUTOMOTIVE SYSTEMS ENGINEERING AE ZG517 / AEL ZG517 Session 14: Case Study 2 - Tesla Autopilot System Analysis Comparing Aerospace vs. Automotive Automation Failures Learning from Incidents to Build Safer Autonomous Systems Instructor: Sajeeth Kumar Duration: 120 minutes

## Slide 4: Case Study Overview - The Facts
Let's establish the facts we'll be analyzing:
October 2015: Tesla Autopilot launches (Version 1.0, Mobileye-based)
May 2016: First fatal crash (Joshua Brown, Florida) - Autopilot fails to detect white truck against bright sky
October 2016: Tesla announces 'Full Self-Driving' capability (hardware, software pending)
March 2018: Walter Huang fatal crash (Mountain View, CA) - Autopilot steers into barrier
March 2019: Jeremy Banner fatal crash (Florida) - Similar to 2016, truck crossing path
NHTSA Investigations (as of 2023): — 40+ investigations into Tesla Autopilot crashes
17+ fatalities attributed to Autopilot engagement
736 crashes involving Autopilot (since 2019 data collection)
Pattern: Autopilot disengages seconds before impact (liability question)
Key Issues Identified: — Driver monitoring inadequate (detects hands on wheel, not attention)
System operates outside Operational Design Domain (ODD)
Confusing nomenclature ('Autopilot', 'Full Self-Driving')
Inadequate testing and validation for edge cases
Regulatory gaps in ADAS oversight
Total impact: — 17+ confirmed deaths (likely more)
Hundreds of injuries
Multiple NHTSA investigations
Recalls affecting 2+ million vehicles
Legal liability cases ongoing
Industry-wide implications for ADAS regulation
Our mission: Analyze this through systems engineering lens and compare to 737 MAX.

## Slide 5: Connection to Your Learning Journey
Why are we studying BOTH an aerospace case (737 MAX) and automotive case (Tesla Autopilot)?
Because the systems engineering failures are remarkably similar:
| Aspect | Boeing 737 MAX | Tesla Autopilot |
|--------|----------------|-----------------|
| System Type | Flight automation | Driving automation |
| Failure Mode | Single sensor dependency | Inadequate sensor fusion |
| Human Factors | Pilots unaware of system | Drivers misunderstand capability |
| Naming | MCAS hidden from pilots | 'Autopilot' implies full autonomy |
| Testing | Inadequate failure mode testing | Inadequate edge case validation |
| Regulation | FAA delegation to Boeing | NHTSA reactive, not proactive |
| Stakeholders | Commercial pressure > safety | Market pressure > validation |
| Result | 346 deaths | 17+ deaths, hundreds of crashes |
Same systems engineering failures, different domain.
Today you'll learn: — How SE principles apply across industries
Why human-automation interaction is critical
How to design and verify ADAS systems properly
Regulatory challenges for novel technologies
Lessons for your work on autonomous vehicles

## Slide 6: Learning Approach for Today
Today's structure mirrors Session 6:
Part 1 (Slides 1-10): Case presentation - Technical system, incidents, facts
Part 2 (Slides 11-18): Guided SE analysis - Requirements, architecture, V&V, human factors
Part 3 (Slides 19-21): Comparative analysis - 737 MAX vs. Autopilot lessons
Part 4 (Slides 22-25): Group work - Analyze specific aspects
Part 5 (Slides 26-28): Synthesis - Lessons for autonomous vehicle development
Ground rules: — Technical analysis, respectful to victims
Focus on SYSTEMS failures, not individual blame
Use SE frameworks from entire course
Compare lessons across aerospace and automotive domains

## Slide 7: Incident 1 - Joshua Brown (May 2016)
Let's examine the first fatal crash in detail.
Date: May 7, 2016
Location: Williston, Florida (US Highway 27A)
Vehicle: 2015 Tesla Model S with Autopilot 1.0 (Mobileye-based)
Victim: Joshua Brown, 40, Tesla enthusiast
Sequence of Events:
13:40: Vehicle traveling 74 mph (9 mph over limit) with Autopilot engaged
13:40:05: Tractor-trailer begins left turn across highway (crossing vehicle's path)
13:40:06-10: Autopilot does NOT detect truck and does NOT brake
Camera fails to distinguish white truck against bright sky
Radar sees truck but classifies as 'overhead object' (false positive suppression)
13:40:10: Vehicle collides with truck at full speed, passes underneath trailer
Result: Joshua Brown dies from injuries, vehicle continues 100+ yards off road
Technical Failure Analysis:
Sensor Failure Modes:
Camera: High contrast scene (white truck, bright sky) - vision system failed to detect
Radar: Detected truck but classified as overhead sign/bridge (tuned to ignore)
Sensor Fusion: Failed - neither sensor triggered braking
Driver Monitoring Failure: — Driver's hands detected on wheel periodically (satisfied monitoring)
Driver was watching movie (found playing on laptop after crash)
System did NOT detect driver's lack of visual attention
System Design Issues:
Over-reliance on camera in challenging lighting
Radar tuned to minimize false positives (missed true positive)
Inadequate sensor fusion (should vote between sensors)
Driver monitoring only checks hands, not eyes/attention
No functional limitation on where Autopilot can engage
NHTSA Investigation Findings: — Tesla's Autopilot performance 'not defective'
But: Recommended better driver monitoring
Driver misuse of system (watching video while driving)
Systems Engineering Question: Is 'driver misuse' an acceptable answer, or a systems design failure?

## Slide 8: Incident 2 - Walter Huang (March 2018)
Second fatal crash reveals a DIFFERENT failure mode.
Date: March 23, 2018
Location: Mountain View, CA (US Highway 101)
Vehicle: 2017 Tesla Model X with Autopilot 2.5
Victim: Walter Huang, 38, Apple engineer
Sequence of Events:
09:27: Vehicle traveling on Highway 101 with Autopilot engaged
09:27:15: Highway splits - left lanes continue 101, right exit to 85
Lane markings faded at gore point (triangular barrier area)
09:27:18: Autopilot steers LEFT toward barrier (follows left lanes)
Should have detected barrier and disengaged
09:27:19: Vehicle accelerates from 62 to 71 mph approaching barrier
09:27:20: Autopilot disengages 1 second before impact (no driver input detected)
09:27:21: Vehicle strikes barrier at 71 mph, battery fire
Result: Walter Huang dies at hospital, vehicle destroyed
Critical Details: — Huang had complained to family about Autopilot steering toward this same barrier previously
He continued using Autopilot despite known issue
Tesla data shows Huang's hands off wheel for 6 seconds before impact
Huang was likely using phone (not confirmed, device damaged in fire)
Technical Failure Analysis:
Perception Failure:
Lane detection: Confused by faded markings at gore point
Barrier detection: Failed to classify concrete barrier as obstacle
Path planning: Chose to follow lane lines (left) instead of road geometry
Deceleration → Acceleration: System accelerated approaching stopped traffic (trying to maintain set speed)
Driver Monitoring Failure: — Hands off wheel for 6 seconds (system allows this)
No detection of phone use or distraction
System Design Issues:
Autopilot operates on roads outside ODD (highway splits, gore points)
Lane-following algorithm prioritizes lane lines over obstacle detection
System disengages 1 second before crash (appears to shift liability to driver)
Inadequate driver monitoring - doesn't ensure driver ready to take over
NTSB Investigation Findings (2020): — Tesla's Autopilot design 'contributed to crash'
Autopilot allowed use outside ODD
Driver monitoring insufficient
Driver was distracted (probable phone use)
Recommended: Improve driver monitoring, limit Autopilot to appropriate roads
Systems Engineering Question: Who is responsible when automation works outside its design domain and driver doesn't supervise?

## Slide 9: Framework for Analysis - SE Lens
Now we apply our systems engineering frameworks, exactly as we did for 737 MAX.
Our Analysis Framework:
1. Requirements Engineering Failures — What requirements existed for Autopilot?
What requirements were missing?
Were they complete, verifiable, traceable?
2. System Architecture & Design — Sensor architecture - redundancy and diversity
Perception algorithms - failure modes
Human-automation interaction design
3. Verification & Validation Failures — What testing was done?
What edge cases were missed?
Real-world validation gaps
4. Human Factors Failures — Driver understanding of system capabilities
Driver monitoring design
Naming and marketing implications
5. Regulatory and Standards Gaps — How did Tesla get approval for deployment?
Where did oversight fail?
Comparison to aerospace regulation
6. Systems Thinking Failures — Optimizing for feature deployment vs. safety validation
Fleet learning vs. individual vehicle safety
Let's work through each systematically, then compare to 737 MAX. —--

## Slide 10: Analysis Part 1 - Requirements Failures
Let's analyze Tesla Autopilot through requirements engineering lens.
Critical Safety Requirements That Should Have Existed:
SR-1: Operational Design Domain
❌ Missing: 'Autopilot shall only operate within defined ODD (divided highways, good weather, clear markings)'
What exists: System can activate anywhere
Consequence: Operates in scenarios it wasn't designed for (city streets, poor markings, complex intersections)
SR-2: Obstacle Detection
❌ Inadequate: 'Autopilot shall detect and avoid all obstacles in path'
What exists: Optimized for moving traffic, poor at stationary objects
Consequence: Crashes into barriers, parked vehicles, trucks
SR-3: Driver Monitoring
❌ Inadequate: 'System shall ensure driver is attentive and ready to take control'
What exists: Torque sensor on steering wheel (hands on wheel)
Should be: Eye tracking, head pose, attention monitoring
Consequence: Drivers use phone, sleep, watch movies while 'supervising'
SR-4: Safe Handoff
❌ Missing: 'System shall provide adequate time and warning for driver to resume control'
What exists: Disengages with minimal warning, sometimes 1 second before crash
Consequence: Driver cannot react in time
SR-5: Fail-Safe Behavior
❌ Inadequate: 'System shall bring vehicle to safe stop if failure detected'
What exists: Disengages, expects driver to take over immediately
Should be: Detect driver readiness before handoff, execute safe stop if driver unresponsive
SR-6: Sensor Redundancy
⚠️ Partial: 'Critical perception shall use diverse, redundant sensors'
What exists: Camera + radar + ultrasonics (but radar removed in some versions)
Issue: No LiDAR (single technology - vision only in newer models)
Consequence: Failures when vision fails (lighting, contrast, occlusion)
SR-7: System Capability Communication
❌ Absent: 'System shall clearly communicate limitations to driver'
What exists: Name 'Autopilot' and 'Full Self-Driving' imply full autonomy
Consequence: Driver misunderstanding, over-reliance, complacency
Requirements Quality Analysis:
| Attribute | Status | Evidence |
|-----------|--------|----------|
| Complete | ❌ FAIL | Missing ODD, driver monitoring, safe handoff requirements |
| Verifiable | ❌ FAIL | No clear verification criteria for 'ensure driver attention' |
| Traceable | ❌ FAIL | Requirements not traced to ISO 26262 safety goals |
| Realistic | ❌ FAIL | Expects driver to supervise indefinitely (not realistic) |
| Unambiguous | ❌ FAIL | 'Autopilot' naming is ambiguous about capability |
Comparison to 737 MAX: — Both: Missing critical safety requirements
Both: Inadequate requirements for human interaction
Both: Requirements didn't account for realistic human behavior
Difference: 737 MAX had aerospace standards (failed to follow), Tesla had no equivalent mandatory automotive ADAS standard

## Slide 11: Analysis Part 2 - Architecture & Design Failures
Now examine the system architecture through SE lens.
Sensor Architecture Analysis:
Original Autopilot (HW1, 2015-2016): — 1 forward camera (Mobileye)
1 forward radar
12 ultrasonic sensors
Issue: Single camera for critical perception (SPOF)
Autopilot 2.0-2.5 (2016-2019): — 8 cameras (360° coverage)
1 forward radar
12 ultrasonic sensors
Improvement: Camera redundancy
Issue: Still relies heavily on vision, radar as secondary
Autopilot 3.0+ / FSD (2019+): — 8 cameras (higher resolution)
No radar (removed in 2021+ models)
12 ultrasonic sensors (removed in 2022+ models)
Vision-only approach — Issue: Single sensing modality (eliminates sensor diversity)
Architecture Principles Violated:
❌ Sensor Diversity: Removed radar, relies only on vision
Industry standard: Camera + radar + LiDAR (diverse physics)
Tesla: Vision only (affected by lighting, weather, contrast, occlusion)
❌ Graceful Degradation: System disengages abruptly when confused
Should: Detect degradation, alert driver with adequate time, execute safe stop if needed
Actually: Sudden disengagement, immediate handoff to driver
❌ Defense in Depth: No backup safety layers
If vision fails, no backup (removed radar)
If driver not paying attention (common), no backup supervision
⚠️ Redundancy: Dual FSD computers (processing redundancy)
Good: Two independent processors
But: Both run same algorithms on same sensor data (common mode failure)
Perception Algorithm Design Issues:
1. Optimized for False Positive Minimization — Tuned to avoid phantom braking (customer complaints)
Result: Misses true positives (actual obstacles)
Classic SE trade-off: False negatives (misses) vs. false positives (false alarms)
2. Lane-Following vs. Obstacle Avoidance Priority — System prioritizes staying in lane over avoiding obstacles
Walter Huang crash: Followed lane into barrier
Should: Obstacle avoidance overrides lane following
3. Neural Network Black Box — Deep learning-based perception
Hard to verify all scenarios
No formal proof of safety
Driver Monitoring Architecture:
Current Design: — Torque sensor on steering wheel
Periodic checks (every 30-60 seconds)
Driver can satisfy by moving wheel slightly
Inadequacies: — Doesn't detect visual attention (eyes on road)
Doesn't detect head pose (facing forward)
Doesn't detect drowsiness
Easily defeated (weights on wheel, etc.)
Industry Best Practice (e.g., GM Super Cruise): — Eye tracking (infrared camera)
Head pose detection
Hands on wheel
Geofencing (only works on pre-mapped highways)
Comparison to 737 MAX Architecture: — Both: Removed redundancy for cost/simplicity (MAX: single AOA, Tesla: removed radar)
Both: Inadequate human monitoring
Both: System can operate outside design intent
Difference: Tesla uses learning-based perception (harder to verify than MAX's deterministic code)

## Slide 12: Analysis Part 3 - Verification & Validation Failures
How was Autopilot tested and validated? Let's analyze through V&V lens.
Verification (Are we building the system right?):
Unit Testing:
✓ Individual components tested (cameras, radar, computer)
✓ Software modules tested in simulation
Integration Testing:
⚠️ Partial - components integrated incrementally
❌ Issue: Limited testing of sensor fusion edge cases
System Testing:
⚠️ Partial - tested on test tracks and public roads
❌ Issue: Edge cases (crossing trucks, faded markings, barriers) not systematically tested
Validation (Are we building the right system?):
Does it meet stakeholder needs? — ✓ Customers: Want convenience features (Yes, delivers)
❌ Safety regulators: Want guaranteed safety (No, crashes occur)
❌ Society: Want safe roads (No, crashes involving Autopilot)
Critical V&V Gaps:
Gap 1: Edge Case Testing — Autopilot tested in 'typical' scenarios
Edge cases (crossing vehicles, stationary objects, gore points) not systematically validated
These edge cases are where crashes occur
Gap 2: Real-World Operational Testing — Tesla uses 'shadow mode' - system runs in background, logs what it would do
But: Not same as active intervention testing
Customers are de facto beta testers (not informed consent for safety-critical system)
Gap 3: Driver Behavior Validation — System assumes driver will supervise attentively
Reality: Drivers become complacent, distracted
No validation that driver monitoring is adequate for realistic driver behavior
Gap 4: Independent Verification — No independent third-party testing before deployment
NHTSA does not pre-approve ADAS systems (unlike FAA for aircraft)
Self-certification by manufacturer
Gap 5: Statistical Safety Validation — How many test miles needed to prove safety?
Industry estimate: Billions of miles for autonomous safety proof
Tesla's approach: Deploy early, learn from fleet
Question: Is this ethical for safety-critical system?
Gap 6: Scenario Coverage — No evidence of systematic scenario analysis (HAZOP, FMEA)
Crashes suggest scenarios not anticipated:
Crossing vehicle in high-contrast lighting
Faded lane markings at highway splits
Emergency vehicles with flashing lights
Gap 7: Compliance to Standards — ISO 26262 (Automotive Functional Safety) - voluntary, not mandated for ADAS in US
No evidence Tesla follows ISO 26262 ASIL D process
Contrast: Aviation follows DO-178C (mandatory)
Fleet Learning Approach (Tesla's Defense):
Tesla argues: — Fleet of 3M+ vehicles collects massive data
Neural networks improve with real-world data
Continuous improvement through OTA updates
SE Critique: — Fleet learning doesn't replace systematic V&V
Individual vehicles are not validated before learning applied
Updates can introduce new failure modes
No safety case for each OTA update
Comparison to 737 MAX V&V: — Both: Inadequate edge case testing
Both: Self-certification (Boeing ODA, Tesla no oversight)
Both: Optimistic assumptions about human behavior
Difference: Aerospace has mandatory standards, automotive ADAS does not (in US)

## Slide 13: Analysis Part 4 - Human Factors Catastrophic Failures
This is where Tesla Autopilot most profoundly fails - human factors engineering.
Human Factors Principle: 'Design systems for how humans actually behave, not how we wish they would behave.'
Autopilot's Human Factors Failures:
Failure 1: Automation Complacency (Documented Phenomenon)
Psychology of Automation: — Humans are poor at sustained vigilance (monitoring tasks)
When automation works well, trust increases, attention decreases
This is not 'misuse' - it's predictable human behavior
Autopilot Design Assumes: — Driver will remain attentive for entire trip
Driver will be ready to take over instantly
Driver will not become complacent
Reality: — Drivers become complacent within minutes
Drivers use phones, eat, sleep
Drivers cannot resume control instantly from distraction
SE Failure: System designed for idealized human, not actual human
Failure 2: Mode Confusion (What is the system doing?)
Autopilot has multiple modes: — TACC only (adaptive cruise, no steering)
Autosteer (cruise + lane keeping)
Navigate on Autopilot (plus lane changes)
Full Self-Driving (city streets)
Driver Confusion: — Which mode am I in?
What will the system do?
What do I need to do?
Evidence from Crashes: — Drivers unsure when Autopilot is engaged
Drivers unsure what Autopilot can/cannot handle
Mode transitions not clearly communicated
Failure 3: Misleading Nomenclature
'Autopilot' implies: — Aircraft autopilot (works without pilot intervention for extended periods)
Full automation
Can handle all situations
'Full Self-Driving' implies: — Complete autonomy (SAE Level 5)
No driver intervention needed
Reality: — Both are SAE Level 2 (partial automation)
Driver must supervise constantly
System can fail at any moment
Comparison to Aviation: — Aircraft autopilot operates in controlled airspace
Pilots are trained professionals
Strict operational limitations
Autopilot is NOT used during critical phases (takeoff, landing)
Automotive Autopilot: — Operates in uncontrolled environment (public roads)
Drivers are general public (untrained)
No operational limitations (can use anywhere)
Used during most critical scenarios (highway merges, intersections)
The naming is a systems engineering failure - sets wrong expectations
Failure 4: Inadequate Driver Monitoring
What's needed for Level 2 automation: — Verify driver is visually attentive (eyes on road)
Verify driver is cognitively engaged (ready to intervene)
Provide adequate takeover time (4-7 seconds minimum)
What Tesla provides: — Torque sensor (hands on wheel)
30-60 second check intervals
1-2 second takeover time (inadequate)
Comparison to GM Super Cruise: — Eye tracking (infrared camera)
Head pose monitoring
Geofencing (only on pre-mapped highways)
If driver not attentive: escalating warnings → safe stop
Failure 5: Training and Education Gap
Driver Training for Autopilot: — Brief in-car tutorial
Written warnings in manual (most don't read)
On-screen disclaimers (click-through)
What's needed: — Formal training (like pilot training for aircraft autopilot)
Testing/certification
Recurrent training
Clear operational limitations
SE Principle Violated:
'Safety-critical systems require trained operators' - violated by consumer ADAS
Root Cause Analysis - Human Factors:
Tesla optimized for: — User experience (ease of use, minimal training)
Feature deployment speed (beat competitors)
Customer satisfaction (minimize false alarms)
Tesla did NOT optimize for: — Realistic human behavior modeling
Safety margins for human error
Clear communication of limitations
This is the fundamental human factors systems engineering failure.
Comparison to 737 MAX: — Both: Assumed humans would perfectly supervise automation
Both: Inadequate human monitoring
Both: Insufficient training
Both: Marketing/naming implied more capability than existed
Same human factors failures, aerospace and automotive

## Slide 14: 737 MAX vs. Tesla Autopilot - Side-by-Side Comparison
Let's now directly compare the two case studies. The parallels are striking.
Systems Engineering Failure Comparison:
| SE Area | Boeing 737 MAX MCAS | Tesla Autopilot |
|---------|---------------------|-----------------|
| System Purpose | Pitch stability augmentation | Driver assistance / partial automation |
| Automation Level | Hidden from pilots | Visible but capabilities unclear |
| Human Role | Pilots supervise, can override | Drivers supervise, can override |
| Failure Mode | Single AOA sensor failure → nose down | Vision/radar failure → crashes into obstacles |
| Stakeholder Priority | Airlines (training cost) > Safety | Market speed > Validation |
| Requirements | Missing redundancy req's | Missing ODD, driver monitoring req's |
| Architecture | Single sensor (SPOF) | Single modality (vision only), removed radar |
| Verification | Inadequate failure mode testing | Inadequate edge case validation |
| Human Factors | Pilots unaware of system | Drivers misunderstand capability |
| Training | None provided | Minimal tutorial |
| Naming | 'MCAS' hidden in docs | 'Autopilot', 'FSD' misleading |
| Regulation | Self-certification (Boeing ODA) | No pre-market approval |
| Result | 346 deaths, 2 crashes | 17+ deaths, 736+ crashes |
Commonalities - Root Causes:
1. Commercial Pressure Over Safety: — Both prioritized speed to market over thorough validation
Both cut corners on requirements and testing
2. Single Points of Failure: — Both removed redundancy (MAX: 1 AOA sensor, Tesla: vision only)
Both violated defense-in-depth principles
3. Inadequate Human Factors: — Both assumed perfect human supervision
Both provided inadequate training
Both had misleading nomenclature
4. Failed Verification: — Both inadequately tested edge cases / failure modes
Both relied on self-certification
Both lacked independent validation
5. Regulatory Gaps: — Both exploited weak regulatory oversight
Both self-certified safety
Both deployed before comprehensive safety validation
Differences:
| Aspect | 737 MAX | Tesla Autopilot |
|--------|---------|-----------------|
| Domain | Aerospace | Automotive |
| Standards | Exist (DO-178C) but violated | No mandatory standard (US) |
| Training | Pilots are professionals | Drivers are general public |
| Environment | Controlled airspace | Uncontrolled public roads |
| Deployment | Few aircraft | Millions of vehicles |
| Iteration | Expensive to update | Easy OTA updates |
| Consequence | Grounding possible | Recall difficult to enforce |
Key Insight:
Same systems engineering failures manifest across industries.
The SE principles are universal - requirements, architecture, V&V, human factors, standards.
If automotive follows aerospace path: — Current: Permissive, deploy first
After major disaster: Reactionary regulation
Future: Mandatory standards, pre-market approval
The question: Will automotive learn from aerospace failures, or repeat them at larger scale?

## Slide 15: Lessons Learned - Comparative Analysis
What can we learn by comparing these failures?
LESSON 1: Systems Engineering Principles Are Universal — Same SE failures (requirements, architecture, V&V, human factors) cause disasters in aerospace AND automotive
SE frameworks apply across domains
Your takeaway: SE skills transfer across industries
LESSON 2: Automation Without Human Factors is Dangerous — Both cases: Assumed humans would perfectly supervise automation
Reality: Humans are poor at monitoring tasks
Your takeaway: Design for realistic human behavior, not idealized
LESSON 3: Single Points of Failure Are Never Acceptable — MAX: Single AOA sensor
Tesla: Vision-only perception (removed radar)
Your takeaway: Safety-critical systems require redundancy and diversity
LESSON 4: Edge Cases and Failure Modes Must Be Systematically Tested — Both missed critical edge cases in testing
Both deployed without comprehensive validation
Your takeaway: Use FMEA, HAZOP, systematic scenario analysis
LESSON 5: Marketing and Naming Affect Safety — 'MCAS' hidden from pilots → lack of awareness
'Autopilot' / 'Full Self-Driving' → over-reliance
Your takeaway: System naming and communication are SE responsibilities
LESSON 6: Self-Certification Creates Conflict of Interest — Both relied on self-certification under commercial pressure
Both needed independent verification
Your takeaway: Independent V&V is not optional for safety-critical systems
LESSON 7: Regulations Lag Technology — Aerospace: Standards existed, were circumvented
Automotive: Standards don't exist (for ADAS in US)
Your takeaway: Engineers must self-impose rigorous SE even when not required
LESSON 8: Incremental Deployment ≠ Safety Validation — Tesla argument: Fleet learning improves safety
Reality: Each vehicle must be validated before deployment
Your takeaway: Data-driven improvement doesn't replace systematic V&V
LESSON 9: Cost of Failure Far Exceeds Cost of Proper SE — MAX: $20B+ costs, brand damage, criminal charges
Tesla: Ongoing investigations, recalls, legal liability
Your takeaway: Invest in SE upfront, avoid catastrophic costs later
LESSON 10: Engineers Have Professional and Ethical Responsibility — Both cases: Engineers raised concerns, were overruled
Both: Lives lost because safety was deprioritized
Your takeaway: Speak up when safety is compromised. It's your professional duty.

## Slide 16: Group Work Instructions
Now it's your turn. You'll work in groups to analyze specific aspects of Autopilot and propose solutions.
Group Activity (30 minutes):
Step 1: Form groups (4-5 students)
Step 2: Choose one topic:
Topic 1: Requirements Rewrite — Write complete safety requirements for Level 2 driving automation
Include: ODD, sensor requirements, driver monitoring, fail-safe behavior
Make them complete, verifiable, traceable
Topic 2: Architecture Redesign — Propose sensor architecture with redundancy and diversity
Design driver monitoring system
Define fail-safe behaviors
Topic 3: V&V Plan — Create comprehensive V&V plan for ADAS
Include scenario analysis (edge cases to test)
Define acceptance criteria
Topic 4: Human Factors Improvement — Redesign driver-automation interaction
Propose driver training program
Create clear communication strategy
Topic 5: Regulatory Framework — Propose mandatory ADAS standard for US
Compare to UN R157, ISO 26262
Include enforcement mechanisms
Topic 6: Comparative Analysis — Compare Autopilot to GM Super Cruise, Waymo, other ADAS
Identify what makes a system safer
Propose best practices
Deliverable: 3-minute presentation with SE-backed recommendations

## Slide 17: Group Presentations and Discussion
(Instructor facilitates presentations and synthesis)

## Slide 18: Final Synthesis - Key Takeaways
Let's synthesize what we've learned across both case studies.
Session 6 (737 MAX) + Session 14 (Autopilot) = Universal SE Lessons:
✓ Requirements engineering is critical — incomplete requirements kill people
✓ Human factors cannot be ignored — design for realistic humans
✓ Single points of failure are unacceptable — redundancy saves lives
✓ Verification must be independent — self-certification fails
✓ Edge cases must be systematically tested — crashes happen at edges
✓ Standards exist for a reason — follow them rigorously
✓ Commercial pressure cannot override safety — ethical responsibility
✓ Automation changes human role — must be carefully designed
✓ Naming and communication affect safety — be accurate and honest
✓ SE processes prevent disasters — skipping them invites tragedy
For Your Career in Automotive SE:
You will work on ADAS, autonomous vehicles, connected systems. You will face:
Time to market pressure
Cost constraints
Cutting-edge technology
Regulatory uncertainty
Your responsibility: Apply rigorous SE to save lives.
Remember: — 346 people died because aerospace SE was compromised
17+ people died because automotive ADAS SE was inadequate
Future deaths can be prevented by YOU applying SE properly
That's why you're learning this. That's why it matters. —--

## Slide 19: 📊 PPT DESIGN GUIDANCE
Assignment (Due before Session 15):
Comparative Case Study Analysis Paper (4-5 pages):
Choose ONE of the following:
Compare 737 MAX and Tesla Autopilot failures - identify common SE failures
Analyze another ADAS system (GM Super Cruise, Waymo, Comma.ai) - what makes it safer?
Propose comprehensive SE framework for Level 4 autonomous shuttle deployment
Required Elements: — SE analysis using frameworks from Sessions 1-14
Requirements, architecture, V&V, human factors analysis
Lessons learned and recommendations
Professional presentation with references
Next Session (Session 15): Technical Management Processes — Configuration management
Risk management deep dive
Quality assurance
Lessons from case studies inform technical management
Final Sessions: — Session 16: Emerging Trends (AI, digital engineering, autonomous systems)
Session 17: Course synthesis and future of automotive SE
Questions? —--
(Similar to Session 6 framework)

## Slide 20: 🎯 INSTRUCTOR NOTES
Timing Management:
Comparative case study learning: Analyze automotive failure, compare to aerospace
Pattern recognition: Same SE failures across domains
Application: Students apply SE frameworks to real-world automotive system
Professional development: Understand ethical responsibilities in ADAS/AV development
Respectful treatment of real tragedies
Balance between technical analysis and human impact
Empower students to prevent future incidents
Core content: 60 minutes
Group work: 30 minutes (strictly enforced)
Presentations: 3 min per group
Synthesis: 10 minutes

## Slide 21: ✅ Session Success Criteria
Students leave able to:
✓ Analyze ADAS systems using complete SE framework
✓ Compare aerospace and automotive automation failures
✓ Identify human factors failures in automation design
✓ Understand regulatory gaps in ADAS oversight
✓ Propose SE solutions for safe autonomous vehicle development
✓ Recognize professional responsibility in safety-critical automotive systems
Most Importantly:
Students understand that ADAS and AV development requires rigorous SE. Shortcuts kill people. Their future work will determine whether automotive repeats aviation's mistakes or learns from them.

## Slide 22
End of Framework